## Slide 1: Long parallel MD on July 20
Giovanni, Giulia, Hannes, Ingrid, Jonathan, Niky, Rama
Many thanks to PSB, PS and SPS OP, as well as HiRadMat

## Slide 2: Long parallel MD on July 20
Organized on short notice as HiRadMat had completed its program on Wednesday (Thanks!)
Absence of many experts after that
Thanks to Jonathan for changing his holidays to come to the CCC with us!
Goal: increase intensity gradually and observe impact on wire scanners

## Slide 3: Overview of the MD
Dumped intensity
Vertical scanner
Horizontal scanner
1.5e11 p/b
1.7e11 p/b
1.9e11 p/b
2.0e11 p/b
2.15e11 p/b

## Slide 4: Overview of the MD
Dumped intensity
Vertical scanner
Horizontal scanner
1.5e11 p/b
1.7e11 p/b
1.9e11 p/b
2.0e11 p/b
2.15e11 p/b

## Slide 5
Bunch length 1.6 ns with 1.6 1011 p/b
Beyond, bunch length larger (1.7 to 1.8 ns)
Longitudinal instabilities could not be stabilized
2.1 1011 p/b
1.7 1011 p/b
1.4 1011 p/b

## Slide 7
 Reproducible monotonous pattern

## Slide 8
 Spikes start to appear at higher intensity

## Slide 9: Power measured from the coupler (Rama)
 Significant power is coming out, mainly from 160 MHz and 800 MHz mode

## Slide 10: Power from 160 MHz mode

## Slide 11: Power from 800 MHz mode

## Slide 12: MD summary
Continued with pushing intensity to study at the same time the behaviour of the newly installed wirescanners in a controlled manner. At lower intensities the bunch length (at flat top) was close to 1.6 ns At higher intensities, achieved bunch length was around 1.8 ns. We had to increase the longitudinal blowup but even then we were consistently suffering from longitudinal instabilities in the ramp. Scanned intensity from 1.5e11 p/b until 2.15e11p/b. The vertical wirescanner behaved nicely. Instead, the horizontal wirescanner reached temperatures triggering thermo-ionic emission, but in a much less severe state than before their upgrade. Nevertheless, both wire scanners show no damage. The brightness of the measurements is close to the LIU target. Some spikes were observed in the MKDH and MKP but no interlocks were crossed.

## Slide 13: To do next
Compare simulated power loss extracted from the coupler to what is coming out in measurements
Wait for Ivan to be back