## Slide 1: Deep learning based uncertainty prediction of DIR for dose accumulation in radiotherapy
Andreas Smolders :: PhD Student :: Paul Scherrer Institute
From Physics to Medicine: XAI workshop , November 2023
This project has received funding from the European Union's Horizon 2020 Marie Skłodowska-Curie Actions under Grant Agreement No. 955956

## Slide 2: Content
The problem of DIR uncertainty
Unsupervised learning for predicting Gaussian DIR uncertainty
Evaluating DIR uncertainty

## Slide 3
Part 1: DIR uncertainty

## Slide 4: In conventional radiotherapy, treatment is fractionated
Reference CT
Manual contouring
Daily Delivery
Planning
QA checks
N times

## Slide 5: Anatomical changes cause target margin requirement

## Slide 6: In adaptive therapy the treatment is reoptimized every day
Daily CT
Contouring
Delivery
Planning
QA checks
Daily patient appointment
N times

## Slide 7: We cannot sum up doses corresponding to different scans
Dose accumulation
Fraction 1
Fraction 2
Fraction N
All different anatomies

## Slide 8: Deformable registration (DIR) maps one image onto another one
Contour propagation
Dose accumulation
(synCT generation)
Applications in (adaptive) radiotherapy
Notes: Step by step image with DVFs
Research question?

## Slide 9: DIR is also necessary for dose accumulation in deforming anatomy (2)
Dose accumulation
Fraction 1
Fraction 2
Fraction N
DIR
DIR
DIR
Reference Anatomy

## Slide 10: DIR differ in some regions but agree in others
Can we quantify the uncertainties associated with DIR solutions and propagate them to clinically interpretable and usable metrics?
Qualitatively, DIR uncertainty is large if:
  Large deformation
  Low contrast
  DIR failure
    Non-correspondence
    Sliding tissue wall
Quantitatively accurate:
  DIR uncertainty
  Contour uncertainty
  Dose uncertainty
Notes: Step by step image with DVFs
Research question?

## Slide 11
Part 2: Unsupervised learning

## Slide 12: The method assumes Gaussian DIR uncertainty
σx
σy
: the output of a given DIR algorithm
: predict with deep learning

## Slide 13: Standard deviation is predicted based on CT images and DVF itself

## Slide 14: The DIR problem can be phrased as a Bayesian problem
: fixed image
: moving image
: DVF
Model
Prior
Evidence
]
Mean
Max a posteriori
Max likelihood
z
Normal DIR
Approximate entire
Posterior

## Slide 15: Imposing a gaussian posterior and minimizing KL divergence avoids intractability
Model posterior probability
Assumptions
+
= Intractable
Impose gaussian posterior
Minimize "distance" between distributions
(1) Dalca, Adrian V., et al. "Unsupervised learning of probabilistic diffeomorphic registration for images and surfaces." Medical image analysis 57 (2019): 226-236.

## Slide 16: Minimizing KL divergence is similar to classic DIR approaches
==> Mean squared error
Target optimization equations
Interpretation
==> regularization for smooth DVF
==> uncertainty prediction term
Lam = 10
Lam = 1
Lam = 0.5
Σ
Loss
f = fixed image
m = moving image
zk = DVF sample

## Slide 17: Intuitively the uncertainty depends on the contrast
Low contrast
High contrast
Low MSE
Low uncertainty loss
Fixed
Moving
Fixed
Moving
σp
High MSE
Low uncertainty loss
σp
Low MSE
High uncertainty loss

## Slide 18: Advantage of decoupling mean and uncertainty estimation
First mean, then uncertainty
Mean and uncertainty together
First the mean, good average registration
Low uncertainty
Fixed
Moving
Fixed
Moving
To lower the loss, predict higher uncertainty
Mean registration is affected to minimize MSE
σp
σp

## Slide 19: An unsupervised deep learning method estimates the DVF uncertainty
Moving
image
Existing DIR algorithm
…
Fixed
image
z = μ + GCσε
Images
DVF
Spatial transformer network
3D UNet
μ
G
ε ~ N(0,1)
Loss
μ

## Slide 20
Part 3: Evaluating DIR uncertainty

## Slide 21: We evaluate 3 methods for DIR uncertainty estimation in 4 different ways
Supervised
Unsupervised
Combined
Visual inspection
DIRLAB landmark uncertainty
Contour uncertainty
Dose accumulation uncertainty
Models
Evaluation techniques

## Slide 22: Visual inspection highlights difference between models
Input
Unsupervised
Supervised
Combined

## Slide 23: Predicted DIR uncertainty matches landmark uncertainty
1
2
3
4
5

## Slide 24: Dose uncertainty is also created using sampling
Accumulated Dose
Dose uncertainty
Dose uncertainty [%]
Dose [%]

## Slide 25: The encompassed volume fraction (EVF) is close to the expected 95%
EVF [%]
Other DIR algorithms
Probabilistic DVH

## Slide 26: Conclusion
DIR uncertainty large if:
  Large deformation
  Low contrast
  DIR failure
    Non-correspondence
    Sliding tissue wall
Quantitatively accurate:
  DIR uncertainty
  Contour uncertainty
  Dose uncertainty
https://github.com/AndreasSmolders/DIRUncertainty
More details in:
Smolders, A et al, PMB (2023), https://doi.org/10.1088/1361-6560/ad0282