## Slide 1
„Study of Non-Evaporable Getter Pumps for Medical Applications: the Case of MedAustron.”

## Slide 2: Content
NEXTorr pump
Motivation
Characterization of pumping speed
MC Simulation
Saturation
Ultimate vacuum
MedAustron
Further studies

## Slide 3: NEXTorr pump
NEG pump combined with ion pump

## Slide 6: Motivation
Compact pump
Relatively high pumping speed
Volume ~15 smaller than ion pump with same pumping speed
Applicable in setups where space is limited
  Medical application
  CLIC

## Slide 7: Characterization Pumping speed
Fischer-Mommsen Dome
Fully baked
Activation NEG at 450oC/1h

## Slide 8: Characterization Pumping speed

## Slide 9
Gas | initial Pumping Speed |  | 
 | Tmp valve open | Tmp valve closed | Tmp valve closed ion pump off
H2 | 71.3 | 65.6 | 47.5
N2 | 28 | 27.1 | 19.7
CO | 98.1 | 89.6 | 93.2
CH4 | 11.7 | 11 | 0.75

## Slide 10: MC Simulation

## Slide 11: MC Simulation

## Slide 12: MC Simulation

## Slide 13
Gas | initial Pumping Speed |  | 
 | W tmp | w/o tmp | w/o tmp io
H2 | 71.3 | 65.6 | 47.5
N2 | 28 | 27.1 | 19.7
CO | 98.1 | 89.6 | 93.2
CH4 | 11.7 | 11 | 0.75

## Slide 14: Saturation

## Slide 15: Ultimate vacuum

## Slide 16: Ultimate Vacuum

## Slide 17: Ultimate vacuum

## Slide 19: Med Austron
Wanted: 1 10-7 mbar in 1h
Given: Degassing rate
Surface
Total degassing rate
Pumping speed

## Slide 20: MedAustron
Scaling down to NEXTorr with 100l/s

## Slide 21: Med Austron

## Slide 22: Med Austron

## Slide 25: Further Studies
Ageing
Reproduce saturation measurement
MC simulation of influence TMP position