## Slide 1
Task 9.2 progress @
1.3 GHz cavities deposition facility
10th IFAST WP9 online meeting
14/09/2023
Alessandro Salmaso

## Slide 2: Objective recap
«Hybrid» coating system for 1.3GHz cavities
  Rectangular magnetron & rotating cavity
  Post magnetron configuration with Nb3Sn cylindircal target produced via dipping
COIL

## Slide 3: Coating system design
Commisioned a 80cm long chamber to reduce the number of flanges (to be delivered mid-october)
Prototype system assembled to test the pumping system and other components

## Slide 4: Coating system design
«Utilities» on the lower part
  Pump unit
  Gauges
  Gas inlets
  Electrical and water feedthrough

## Slide 5: Cavity stand
Cavity suspended from rotating ferrofluidic vacuum feedtrough
Stand designed to center the cavity and minimize deformation due to high temperature deposition
Torque: 80Nm
Load: 60 kg
Stand weight: 8kg (max)

## Slide 6: Deformation at 700°C
Solidworks static simulation of the cavity at 700°C
Deformation along cavity axis about 1mm at the cell
To be simulated and tested whole thermal cycle:
Room T
x hours @ deposition T
Room T
Deformation axis (mm)

## Slide 7: Rectangular magnetron
Magnetron fixed on the lower flange
Design still ongoing

## Slide 8: Centering system
Magnetron and cavity will be aligned on the same axis by means of centering system: two disks tangent to three vertical rods with small tolerance

## Slide 9: Heating system
4 IR lamps (max)
Copper shield will reduce the heat-up of the chamber

## Slide 10: Next steps
Assemble vacuum system ASAP
Commission Magnetron
In the meantime
Test vacuum components already available
Test thermal cycle of the cavity

## Slide 11
Thanks for your attention
alessandro.salmaso@lnl.infn.it