## Slide 1: QFib Test Beam
Suat OZKORUCUKLU
Berkan Kaynak, Onur Potok, Buse Duran, Selbi Hatipoglu, Ali Tosun, Aldo Penzo
10 August 2023

## Slide 2
Beam defining counters
Beam defıned as 5mm diameter or 10x10mm2 according to combination of coincidence of beam counters
DUT: Detector Under Test
1.5m long HF-PPP fibers + MCP-PMT/PMT
2.5m long HF fiber bundle + MCP-PMT
12cm Polymicro fiber bundle + MCP-PMT
8cm Polymicro High NA fiber bundle + MCP-PMT
12cm Polymicro fiber array(7x7) + MCP-PMT
TRS: Time Reference System
SB1-2: MCP-PMT + Qbar doublets (two 5x5x100mm3), 45o to the beam
TRC: MCP-PMT + Qblock (12x12x25mm3)/UVT Plexi (12x12x20mm3), Head on
QFib Test Beam Setup

## Slide 3
100, 120, 140, 180 GeV pion beam was used.
Mainly 180 GeV pion beam was used.
In total, 57 Runs and 29 Scans were taken.
More than 61.5 Million event were taken.
TRS calibrated with the scans.
Attenuation and time difference in the different fibers are investigating with DUT study.
Data Taking Conditions
Scalers | Counts
#1 (1x1 Coinc.) | 5.62E+04
#2 (1x1 Coinc.) | 5.54E+04
#3 (Anti-Coinc.) | 1.30E+04

## Slide 4
TRS Amplitudes
TRC - Ch1
Beam
SB2
SB1
180 GeV Pions
TRC – With 12x12x25mm3 QBlock
SB1 - Ch2
SB2 - Ch3

## Slide 5
Beam
SB2
SB1
180 GeV Pions
TRC – With 12x12x25mm3 QBlock
DUT Fibers
MCP-PMT
Timing measurement was performed using both short and long fibers for different distances and angles to the photodetector.
For the High NA fiber time resolution, we obtain ~26 ps. (Next page)
Analysis still on going.
DUT Setup

## Slide 6
Timing Measurements
Sigma_1-2 
19.1 0.113 ps
Sigma_1-3 
22.8 ps
Sigma_1-4 
26.1 ps
Sigma_2-3 
26.4 ps
Intrinsic time resolutions
  Sigma1(TRC) 
  7.14 2.19 ps
  Sigma2(SB1) 
  19.44 0.80 ps
  Sigma3(SB2) 
  0.72 ps
SB1 -> 5 cm
SB2 -> 5 cm
Beam
SB2
SB1
180 GeV Pions
TRC – With 12x12x25mm3 QBlock
High NA Polymicro Fiber