## Slide 1: Irradiation Facilities Team: Highlights of 2022/2023
Pierre Pelissou on behalf of the IRRAD team
https://indico.cern.ch/event/1314868/

## Slide 2: Outline
Team presentation
IRRAD facility overview
IRRAD statistics 2022
IRRAD news 2023
IRRAD Beam Profile Monitors (BPMs)
Evaluate Beam Dump Facility (BDF) irradiation opportunities

## Slide 3: 1. Team presentation
  Team Responsible
  IRRAD Coordinator, Facilities EXSO
  Facilities Manager, GIF++ EXSO
  Users Supervisor
Giuseppe, STAFF
  GIF++ Physics Coordinator
Martin, STAFF (50% ATLAS)
Federico, STAFF
Blerina, FELL
Jaroslaw, PhD
  AIDAinnova, RADNEXT, EURO-LABS (EU-projects)
  Computing M&O / R&D
  Machine Learning R&D
  RADNEXT EU-project
Pierre, FELL
  Facilities R&D
  RADNEXT EU-project
Maurice, HONO (retired)
  Team consultant

## Slide 4: 2. IRRAD facility overview: PS East Area b.157 (renewed during LS2)
T09
T10
T11
North side: Test-beam Areas
© EA renovation celebration event (03/2022)
CHARM (mixed-field)
South side: Irradiation Facility
T08
IRRAD
CHARM
Location: PS East Area b.157 (renewed during LS2)
20/09/2023
Pierre Pelissou - EP-DT-DD Section Meeting

## Slide 5: 2.1. Schematic view of the IRRAD beam line at CERN
30m
T08-BEAM
LHe Cryostat 1.9K
Shuttle System
IRRAD Tables
Beam Profile
Monitors (BPM)
Tracking
detectors
Electronics/full
detector systems
Calorimetry
detectors
CHARM
Cryogenic line
20/09/2023
Pierre Pelissou - EP-DT-DD Section Meeting
https://ps-irrad.web.cern.ch/ps-irrad/
Testing components of HEP experiments
24 GeV/c, Gaussian 12×12 mm2 FWHM
Spills of 400 ms every ~10 s
Fluence of 1,4×1016 p/cm2/week (avg 2023)
Scanning also in dimensions of 10×10 cm2
Low-temperature irradiation (-25°C)

## Slide 6: 3. IRRAD statistics 2022
EXPERIMENTS R&D (IRRAD)
SYSTEM-LEVEL TEST (CHARM)
CRYOGENIC TEST (IRRAD)
IRRAD (EP):
  54 experiments registered
  >600 samples processed:
    LHC Experiments: ATLAS, CMS, LHCb Phase II upgrade
    R&D & expt. support: EPRD, RD53, RD50, EP-ESE / DT
    CERN ATS Projects: TE-MSC, EN-EL, R2E
    EU-projects & external: AIDAinnova, CNES (FR)
  ~50% requests exceeding 1016 p/cm2
    cold (-25C), cryogenic & large areas often required
    irradiations to 1017 p/cm2 level require ~1 year!
CHARM (BE):
  29 users scheduled
  39 system-level & 13 component tests:
    ATS: SY-BI / EPC / STI, TE-MPE / VSC, BE-CEM
    RCS: EP-DT, CMS, ATLAS, Caen, Wiener
    EU-projects: RADNEXT (3 users)
  increasing number of requests
CHARM COMPONENTS TEST CAMPAIGNS
2022
20/09/2023
Pierre Pelissou - EP-DT-DD Section Meeting

## Slide 7: 4. IRRAD news 2023
Run 2023 (25w. p+ and 12d. for CHIMERA):
  1× week RP run @ CSBF/CHARM: week 37
  ~3× weeks LHe Cryo run @ IRRAD: from 20/09
  Proton run ends on 18/10, ion run ends on 31/10
Wednesday Machine Development periods:
  2× HI beam for CHIMERA/HEARTS: 30/08 and 06/09
Beam Instrumentation:
  T08.XSEC measurement run on 03/04/2023, confirms the calibration of 2022 within ~4-5%
IRRAD/CHARM Safety Files Update:
  Descriptive / Demonstrative parts (4 “old” doc’s): OK
  Operational Part (1 new doc): OK
  To be presented to Host States authorities on 27/09
High Intensity EAST T8 (8E11 pps):
  Preliminary tests by BE-OP and HSE-RP validation: OK
  New calculations for CHARM target (SY-STI): ongoing
  ECR in preparation
Now also available in: https://bpt.web.cern.ch/ps/EAST/T8/2023/
20/09/2023
Pierre Pelissou - EP-DT-DD Section Meeting

## Slide 8: 4.1. IRRAD user experiments (until July 2023)
20/09/2023
Pierre Pelissou - EP-DT-DD Section Meeting
IRRAD:
  150 samples processed
  26 experiments registered in IDM (330 samples), others to come …
    ATLAS ITk pixel & strips, ATLAS HGTD, CMS pixel, LHCb ECAL, RD53, RD50, EP-ESE, TE-MSC, SY-BI, AIDAinnova, …
  Several other experiments being discussed: probable need of assigning priorities after summer!
CHARM:
  21 experiments performed + components testing in user racks and overhead conveyer
  44 experiments registered in the planning
  All slot reserved in 2023
TE-MSC
EP-ESE, RD50, …
CMS Pixel
ATLAS-HGDT
ATLAS-ITk
CHARM RACK

## Slide 9
20/09/2023
Pierre Pelissou - EP-DT-DD Section Meeting
  Definition: devices based on nanometric metal-layers on ultra-thin polymer carriers:
  Original IRRAD BPM Cu/FR4 (140/600mm) used in 2014-2018 had several drawbacks:
    Limited sensitivity, low radiation hardness, high material activation, etc.
  NEW small pattern (9ch.) BPM Al/Kapton (0.3/25mm): produced and operational
    >30× reduced material budget, X0 < 1%, improved for low-penetration beams (e.g., heavy-ions)
  NEW large pattern (39ch.) BPM Al/Kapton (0.2/25mm): prototypes tested; R&D ongoing
39ch. BPM device
9ch. BPM device
~20mm×20mm
~40mm×30mm
5. IRRAD Beam Profile Monitors (BPMs)

## Slide 10: 5.1. Ongoing Beam Profile Monitors (BPMs) R&D
20/09/2023
Pierre Pelissou - EP-DT-DD Section Meeting
  2 possible BPM candidates manufactured at CERN:
Chrome- based BPM
3D-printed BPM

## Slide 11: 6. Beam Dump facility – a new possible parasitic test area station
20/09/2023
Pierre Pelissou - EP-DT-DD Section Meeting
Key parameters:
Location: SPS ECN3 beam facility - North area (Prevessin site)
Beam direction

## Slide 12: 6.1 Technical comparison of radiation field characteristics
20/09/2023
Pierre Pelissou - EP-DT-DD Section Meeting
Facility | Dose Level (Gy/y) | HEH fluence (cm-2/y) | Si 1MeVeq fluence (cm-2/y)
CHARM – R10 ( POT/y) |  |  | 
NTOF_NEAR N1 ( POT/y) |  |  | 
NTOF i-NEAR ( POT/y) | [1.2;2.5] |  | (The total neutron fluence)
ISOLDE Irradiation station ( POT/y) | ≥ |  | 
IRRAD in beam ( POT/y) |  | protons | /
BDF P1 ( POT/y) |  |  | 
BDF P2 bis |  |  | 
BDF P3 |  |  | 
BDF P4 bis (10 cm away from the beam pipe) |  |  | 
BDF P4 (in beam with R=50mm dilution and gaussian shape of 8 mm2 sigma) |  | protons | /
Facility | Dose Level (Gy/y) | HEH fluence (cm-2/y) | Si 1MeVeq fluence (cm-2/y)
 |  |  | /
BDF P2 bis |  |  | 
BDF P3 |  |  | 
BDF P4 bis (10 cm away from the beam pipe) |  |  | 
BDF P4 (in beam with R=50mm dilution and gaussian shape of 8 mm2 sigma) |  |  | /
~ Today’s IRRAD
~ CHARM but op. constraints
Potentially relevant for future detectors studies

## Slide 13: Irradiation Facilities Team: Highlights of 2022/2023
Pierre Pelissou on behalf of the IRRAD team
https://indico.cern.ch/event/1314868/