## Slide 1: Radiation Tolerant RISC-V processor and SoC platform
Implementing DRD7: an R&D Collaboration on Electronics and On-detector Processing.
2nd workshop
25 September 2023
Kostas Kloukinas

## Slide 2: Introduction
Project intentions
  Rad-Tol RISC-V based System-on-Chip design
Participating institues, as of today (in order of presentations)
  CERN
  KU LEUVEN
  Fachhochschule Dortmund
  UK Consortium

## Slide 3: CERN
EP-R&D WP5.2 Rad-Tol SoC Ecosystem activity
  Motivation
    Tackle design complexity in future experiments
    Control development cost on advanced nodes
    Facilitate on-detector “intelligence”
    Enable reconfigurable, retargetable FE ASICs
  Propose a SoC ASIC design methodology
    Introduce an abstract design methodology
    Develop reusable IP blocks
    Standardized interconnects for IP blocks
    Replace state machines with a control processor (RISC-V based)
    Programmable, flexible logic blocks (SoC Ecosystem, cores, eFPGA, NoCs)
    Enhance Hierarchical Digital Implementation and Verifications

## Slide 4: SoC Radiation Tolerant Ecosystem Conceptual Diagram
I2C
I2C
I2C
I2C
SPI
SPI
SPI
SPI
JTAG
GPIO
DAC
DAC
DAC
DAC
ADC
ADC
ADC
ADC
any-Link
any-Link
Slow Control Interfaces
Analog functions
High Speed Interfaces
e-Links
e-Links
e-Links
e-Link
FE channel
FE channel
RISC-V
SRAM
eFPGA fabric
Programmable Logic
FE analog blocks
Interconnect Bus
SRAM
micro-code
data

## Slide 5: SoC Generator Tool
SoCMake
  SoC generator tool
  SystemRDL language to automatize the generation of:
    Hardware design
    Software toolchain
    Verification platform
    Documentation
  Generate custom SoCs
  Rapid SoC prototyping
  Work in progress

## Slide 6: Demonstrator ASIC
Alessandro Caratelli
Marco Andorno
Anvesh Nookala
Davide Ceresa
Risto Pejasinovitc

## Slide 7: Plans & Resources
Timeline
  SoC activity started in 2021, during EP R&D phase I
  Approved to continue in phase II, for at least four more years
Scope
  Open platform for Rad-Tol SoC ASIC design
  SoC & core architecture, Verification, Implementation
Resources
  1 fellow, 2 students, 3 part-time staff
Start of SoC activity

## Slide 8: DRD7 Workshop Radiation Tolerant RISC-V Processors

## Slide 9: Motivation behind our research
Spatial redundancy techniques
  TMR, DMR, dual lockstep systems, ...
Pipeline rollback
  Register encoding/decoding
  Pipeline rollback when non-recoverable error occurs
Radiation hardening by software techniques
  Instruction replay or checkpoint recovery
Simple to understand
Reliability failure reduces by orders of magnitude
Can be automatized
Large area and power overhead (> 2x/3x)
difficult to implement (RTL and physical constraints)
Increases critical path delay
Latency penalty when rollback
Complex to implement
Low area overhead
Can mitigate SETs and SEUs
Low area overhead
Low critical path delay overhead
Can be fully implemented in software
Significally complicates the software stack
Performance loss (lost cycles)
Memory requirement for checkpoint recovery

## Slide 10: In-situ SEE error detection and correction
Single-Event Effect (SEE) error detection
  Double sampling error detection flip-flop
  Parallel error detection flip-flop
  Test chip created
Single-Event Effect (SEE) error correction
  Fully configurable
2023
Notes: TD = transition tedection
Fully configurable
  Different flavours of error correction code
  Clock phase offset
  Number of bits to target
  Floorplanning methods to increase radiation hardening

## Slide 11: SEE mitigation in DNN accelerators
Memories: 50-70% area
  SEC-DED code to harden
Data path: 30-50% area
  Software/hardware mitigation
  Software-based DNN tolerance
  Hardware checker neurons
Control logic: 2-5% area
  TMR
Control logic
Data path
Memories
DNN accelerator

## Slide 12: Long term goal
Any RISC-V core can be targeted
  Hell, any design for that matter
Fueled by FuseSoC and Edalize
  Achieving the power of vendor and tool independence
In-Situ SEE error detection and correction library
SEU inject test platform
  In simulation testing
  At runtime (FPGA) testing
  Formal verification?

## Slide 13: Contributions and resources
Contributions
  Rad-hard RISC-V SoC development on TSMC 28nm HPC+ or 22nm FDSOI technology
Resources
  5 person team for 3 years
    3 persons already funded
      3 * 3FTE, resources already available
    2 persons to be funded
      2 * 3 FTE, resources considering asking

## Slide 14
25.09.2023
2nd DRD7 workshop
Michael Karagounis
A radhard RISC-V micorocontroller implementation

## Slide 15: Motivation
First thoughts about the usefulness of a radiation-hard µC arose during the development of the MOPS (Monitoring of Pixel) chip
  MOPS digitizes pixel module voltage and temperature and communicates via CANOpen
  CANOpen is usually implemented in software but was implemented in hardware for MOPS
Many custom ASICs have a similar structure:
Design of hardwired custom ASIC is complex and time consuming
  Big verification effort
  Bugfixes detected in silicon need redesign and new production cycle
Adaptation to new projects is difficult
  hardwired logic needs full redesign
Idea: replace internal data processing logic with radiation-hard RISC-V core
  Adaptation to new application and bugfixes via software updates
AD / DA Converter
Internal Logic
Communication Interface
Data Acquisition
Data Transfer
Data Processing

## Slide 16: Design of TMR protected RISC-V microcontroller
Fully TMR protected RV32-IMC Core designed in TSMC 65nm
  3 stage pipeline with multiplication and compressed instruction set extension
1.2V Core & I/O supply and 50 MHz clock
three SRAM instances protected with scrubbing algorithm
SEU detection & counting logic
Read SRAM Row
Compare 3 Instances
Write SRAM Row
Increase SRAM Row
SEU Register
Periph Counter
Core Counter
SRAM Counter
SRAM
SRAM
SRAM
SRAM
Refresh
Periph Instances
Voter
1
Voter
2
Voter X
≥1
Core Instances
Voter
1
Voter
2
Voter X
≥1

## Slide 17: TID & SEE Characterization
X-ray irrdiation at -20°C
TID of 1 Grad reached
SRAM leakage current main driver of increased current consumption
cross section of corrected SEUs extracted by SEU counter circuit
SEFI cross section is three orders of magnitude smaller than SEU cross section
Heavy ion irradiation for study of SEE
A. Walsemann, M. Karagounis, A. Stanitzki, D. Tutsch, A radiation hard RISC-V microprocessor for high-energy physics applications, Nuclear Instruments and Methods in Physics Research Section A, vol. 1056, p. 168633, 2023

## Slide 18: Futur Plans & Resources
Overall project goal is an open-source Zero SEFI microcontroller at LHC inner layer SEE rates
  Are there additional architecture level protection measures necessary apart from TMR?
Development of a well-elaborated verification suite
  Verification of functionality and TMR implementation
  study of cycle accurate golden models and/or virtual prototypes
Improve diagnose capability during SEE radiation testing
  Not only detect SEFIs but also cause of SEFIs
Resources
  0.67 FTE (PhD student) for 1+3 years
  Funds for Submission of chip prototypes

## Slide 19: UK Consortium Contribution
UK (STFC) Consortia
  Royal Holloway, Birmingham, Warwick, Bristol, Manchester, RAL.
Motivation
  Develop common interface ASIC to couple a range of specialised FE ASICs to a common industry-standard off-detector interface.
Plans for DRD7.2.b
  Study/design of processor
  Verification/testing of cores
  Evaluate SoC platform
  Software Ecosystem
Contribution
  Q4 2023: requests for funds
  >1 FTE for 4 years
Proposed common interface ASIC for detector readout, timing, and control

## Slide 20: Towards a Project Proposal
Develop a Rad-Tol RISC-V based SoC ASIC design platform for HEP experiments
  Standardized Architectures
  Implementation Methodologies
  Verification Methodologies
  IP block Repository
  Propose standardized solutions to the HEP community
Establish regular meetings
  Kick-off meeting in late October 2023
  Identify areas of expertise
  Define fields of contribution
Finalize Project Proposal

## Slide 21
Thank You