## Slide 1: FECOS Status overview
matej.sekoranja@cosylab.com
miha.vitorovic@cosylab.com
luka.sepetavc@cosylab.com
the best people make cosylab
Matej Šekoranja
Miha Vitorovič
Luka Šepetavc

## Slide 2: Task overview (completed)
New command interface to WinCC OA
  Reduced number of data points elements per Component
EnteringState/LeavingState callbacks
  Each state has two methods called before entering and after leaving it
  More in-line with the WinCC OA approach
FECOS XML parser
  Native LabVIEW XML parser not working on real-time targets
  Will enable FECOS to parse RMS generated configuration
Design FECOS real-time capabilities
  Based on discussion of real-time requirements with Anton Kerschbaum
Notes: for command interface with now less DPEs (array of values) instead of multiple DPEs
there used to be only “transition”, now all transitions have leaving previous state/entering next state; leaving state tells you which command you received, which state you are leaving and which is the next state
FECOS XML built from scratch, using external libraries for parsing text with regular expressions
>XML parser will have a set of helper functions to help with processing standard fml structures, e.g. for PCC
define how to write real-time capable functions that are inline with FECOS

## Slide 3: Task overview (completed)
Implementation of the Basic Device
  Simpler state machine
  No command interface to WinCC OA
  Controlled by some other Component (state driven device)
Notes: -it’s not possible to send commands from PVSS (no command interface) – not even Reset, Reset can only be send internally or by another component
„Basic device“ there was problem in the specification/design/approval process, so we have to reopen and fix (1MD)

## Slide 4: Task overview (work in progress)
FECOS dynamic Component loading and instantiation
  No need to statically link Components into FECOS
  Single FECOS core image deployed on all PXIs
  All specific functionality (Components) deployed separately
  PXI functionality dictated by configuration
  FECOS only loads what is needed
Implement FECOS real-time capabilities
FECOS EA model
Define stability and performance test cases for FECOS XML parser
Notes: -FECOS EA will include requirements...

## Slide 5: Task overview (to do)
Evaluate and document FECOS real-time performance
Perform stability and performance test cases for FECOS XML parser
Report stability and performance test cases for FECOS XML parser
Design and implementation of scratchpad
Remote logging (log4j)
Notes: -scratchpad will allow modifications of cycle dependent data; quite complex
-implement remote logging; will use log4j formatting
-> FECOS will provide logging services to all FECOS components

## Slide 6: Task overview (to do)
Design and implementation of data retrieval (HTTP)
Addition of real-time capabilities to FECOS user manual
Add Basic Device to FECOS user manual
Adding wizards and FECOS palettes to LabVIEW
  Ease of development
Notes: -create programming user manual for real-time programming
-wizards will simplify for example implementation of getters and setters (simplify the use of data value references)
-add FECOS palettes to user libraries (right click)