## Slide 1: FELIX read-out with ITkPix Wael Alkakhi In consultation with Prof. Arnulf Quadt II. Physikalisches Institut, Georg-August-Universität Göttingen ATLAS-D Annual meeting 2023, Bonn Parallel Sessions I: Detector Physics 2

## Slide 2: Introduction: HL-LHC & ITk detector
HL-LHC target is to perform at high energies collisions, luminosity ~ 7x1034 cm-2s-1
Current inner detector system will be replaced with a new all-silicon tracking system ITk (Inner TracKer).
Properties: High range cover (|η| < 4), High trigger rate (1 MHz), High pile up events (200), High resolution (50µm x 50µm pixel size)
Consists of pixel sub-detector surrounded by strips sub-detector.
Pixel subdetector consists of Inner Barrel and Endcap, Outer Barrel and Outer Endcap.

## Slide 3: ITK Pixel Readout
Current Read-out chain is RD53A-Optoboard-Felix-YARR.
Felixcore application and Netio protocol in the read-out chain.
Target: Switching to Felix-star and NetioNext for better performance and reading out ITkPix front-ends (Yarr(NetioNext-felixstar)/ Felix/ Optoboard/ ITkpix).
FELIX-STAR application
NetIO-Next
RD53A chips -> ITkPix chips

## Slide 4: Felix Read-out Chain Data Handling
Felix-star application is the central process of a Felix system and replaces Felixcore.
It handles all its tasks in a single thread.
It handles the communication between one or more FELIX Cards on one side and a set of Netio-next clients on the other side.
Netio-next is A fast communication protocol for data messaging between Felix-Star and Felix clients.

## Slide 5: Netio/Felixcore vs Felix-star/Netio-Next
Felix-star
Felixcore
Mutlipule thread
Uses Netio
Single thread
Uses Netio-Next

## Slide 6: ITk Read-out system building blocks
FELIX is a “data router”. Sends commands and triggers to detector front-end (FE) electronics and receives data packets from them. Hosts a FPGA supporting 48 high speed optical links.
Optoboard is an interface between FELIX and front-ends
  4 GBCRs (recovers the signal after twinax cables).
  4 lpGBTs (multiplexes/de-multiplexes the high-speed uplinks/downlinks).
  1 VTRx+ (coverts highspeed signals from electrical to optical and vice-versa).

## Slide 7: Motivation & Work Plan
Aim: Validate YARR-Felix-Optoboard-ITkPix Read-out chain using Netio-Next and Felix-star.
Start point(RD53A read-out):
  Yarr Branch: devel_rd53a_felixNetioNext, using Vldb (GBT) and Felix VC709 board through felix-star/Netio-Next.
  Yarr Branch: devel_rd53a_felixNetio, using Vldb+ (lpGBT) and Felix-712 Card through felixcore/Netio.
Intermediate step :
  Validate YARR-Felix-Optoboard-RD53A Read-out chain using Netio-Next and Felix-star.

## Slide 8: Yarr/Felix/Optoboard/RD53A Lab Setup
Power
Optoboard
Rd53A SCC
To FELIX PC

## Slide 9: Example of Achieved Results
YARR-Felix-Optoboard-RD53A Read-out chain using Netio-Next and Felix-star works.

## Slide 10: Conclusion & Outlook
Towards achieving the YARR/Felix/Itkpix readout system:
  First: YARR/Felix/Optoboard/RD53A read-out validated.
    New branch created on YARR gitlab repo devel_rd53a_felixNetioNext-lpGBT-debugging .
    Merging to Master branch is undergoing.
  Next: Move to ITkPix, (different in encoding/decoding scheme → need a new Firmware for Felix).
Future plans: Integrate the achieved developments in the final Atlas read-out system including the ITk software (YARR) and the new Felix application FelixClient.
Thank you for your Attention

## Slide 11: Back up

## Slide 12: RD53A SCC
The width is 20mm and 400 pixels, the height is 11.6mm and 192 pixels
Pixel size is 50 µm × 50 µm
3 types of pixel readouts in chip (linear, differential, Synchronous)
Power
Display port (Output data)
RD53A Chip

## Slide 13: Issues & Solutions
Building Yarr SW was not working because of recent initializations in Netio-Next:
=> solved through re-initialization some variables in Yarr
During scans, connection was refused during loading configs stage:
=> solved by updating libfabric.
Wrong representation of link fid discovered in Felix-star Felix-toflx application
=> Representation was corrected.
Truncation error in libfabric,
  =>Fixed by increasing used buffers size in YARR.
Added headers by Netio-Next in data messages
=> Extract headers in readData function before forwarding data to YARR dataprocesser (avoiding doing so in callback function).
Lost data packages addresses
=> Retrieve correct related rx from extracted headers, use it as data package address .