## Slide 1: Cost model for the SRF system for the muon collider RCSs
Alexej Grudiev
with a lot of help of Akira Yamamoto, Heiko Damerau
11/09/2023

## Slide 2: Outline
Motivation
ILC cost and parameter summary of Akira’s summary
RCS parameter summary based on (one of the) last Fabians table
Zero-order cost model
  RF voltage
First order cost model
  RF voltage
  Beam power
  Duty factor
Conclusions

## Slide 3: Motivation
Provide simple parametric cost model of the SRF systems for the RCS chain
Will be used for optimization of the magnetic ramp of the RCS to find a correct balance between installed RF voltage and magnetic ramp profile: linear versus sinusoidal.
It is based on the ILC cost estimate

## Slide 4: Summary of the ILC cost summary
Akira Yamamoto kindly provided summary of the ILC cost developed for the ESPPU-2020:
  RCS RF system Cost discussion (20 July 2023) · Indico (cern.ch)
The figure form the summary which will be used in the cost model summarized below:
  Total cost of ILC250 at 31.5 MV/m: 5260 MU
  Cryogenics: 6%, High power RF: 8%, SRF and Cryomodule: 28%
  Power couplers cost 18% of the SRF and Cryomodule
  Total RF voltage 250 GV, Rep. rate: 5Hz, beam train length 0.73 ms, beam current: 5.8 mA
  No scaling is done from ILC@31.5MV/m to RCS@30MV/m

## Slide 5: Summary of the RCS parameters
RSC |  | 1 | 2 | 3 | 4 | ILC
Inj/ej energy | GeV | 63/313.8 | 331.8/750 | 750/1500 | 1500/5000 | 250
Acc. Time | ms | 0.34 | 1.1 | 2.4 | 6.4 | 0.73
Energy gain per turn | GeV | 14.8 | 7.9 | 11.4 | 63.6 | 250
RF voltage per turn | GV | 20.9 | 11.2 | 16.1 | 90 | 250
Number cavities 9-cells, 1.3GHz, 30MV/m |  | 696 | 374 | 536 | 3000 | 8000
Peak Beam current per beam | mA | 21.7 | 19.5 | 9.9 | 3.1 | 5.8
Energy gain per cavity (RF phase 45 deg) | MV | 21.2 | 21.2 | 21.2 | 21.2 | 31.5
Peak Beam power per cavity for 2 beams | kW | 920.08 | 826.8 | 419.76 | 131.44 | 182.7
Duty factor (filling time ~1 ms is included) | 1.00E-03 | 6.7 | 10.5 | 17 | 37 | 8.65
Average beam power/cav for 2 beams | kW | 6.16 | 8.68 | 7.14 | 4.86 | 1.58

## Slide 6: Zero-order cost model and RSC cost
ILC | rel cost | abs cost
paramter | [%] | [MU]
Total | 100 | 5260
HPRF (klystrons, WG) | 8 | 420.8
SRf and cryomodule | 28 | 1472.8
Cryogenics | 6 | 315.6
Sum | 42 | 2209.2
Total voltage | [GV] | 250
Zero-order cost model |  | 
Cost per GV: C0 | [MU/GV] | 8.8368
RSC |  | 1 | 2 | 3 | 4 | All
RF voltage per turn | GV | 20.9 | 11.2 | 16.1 | 90 | 
C0 | MU | 185 | 99 | 142 | 795 | 1221
Very simple, TOO simple probably, since the beam parameters are very different and pulse structure is different in some of the RCS form the ILC ones

## Slide 7: First-order cost model refinement
HPRF (klystrons, WG) | MU | 420.8
energy gain | [GV] | 250
peak beam current | mA | 5.8
Cost per GV per mA: C1P cost of HPRF: C1P*V*cosPhi*Ib | MU/(GV*mA) | 0.29
SRf and cryomodule | MU | 1472.8
FPC (18%) | MU | 265.104
Cost per GV per mA: C1FPC cost of FPC: C1FPC*V*cosPhi*Ib | MU/(GV*mA) | 0.18
cavities and CM (82%) | MU | 1207.7
Cost per GV: C1SRF cost of SRF: C1SRF*V | [MU/GV] | 4.83
Cryogenics | MU | 315.6
train length :tb | ms | 0.73
filling time: tf | ms | 1
repetition frequency | Hz | 5
Duty factor: (tb+tf)*frep | 1.00E-03 | 8.65
Cost per GV per 1e-3: C1C Cost of Cryogenics: C1C*V*DutyF | [MU/GV/1e-3] | 0.146
RSC |  | 1 | 2 | 3 | 4 | All
Acc. Time | ms | 0.34 | 1.1 | 2.4 | 6.4 | 
Energy gain per turn | GeV | 14.8 | 7.9 | 11.4 | 63.6 | 
RF voltage per turn | GV | 20.9 | 11.2 | 16.1 | 90 | 
Peak Beam current per beam | mA | 21.7 | 19.5 | 9.9 | 3.1 | 
Peak Beam power per cavity for 2 beams | kW | 920 | 827 | 420 | 131 | 
Duty factor with fill. time 1 ms | 1E-3 | 6.7 | 10.5 | 17 | 37 | 
C1P | MU | 186 | 89 | 66 | 114 | 456
+ |  |  |  |  |  | 
C1FPC | MU | 117 | 56 | 41 | 72 | 287
+ |  |  |  |  |  | 
C1SRF | MU | 101 | 54 | 78 | 435 | 668
+ |  |  |  |  |  | 
C1C | MU | 20 | 17 | 40 | 486 | 566
= |  |  |  |  |  | 
Total C1 | MU | 425 | 217 | 224 | 1107 | 1974
More accurate cost model gives almost x2 higher cost for the RCSs

## Slide 8: Conclusions
Zero-order parameterized cost model has been proposed. It does not reflect any differences in the beam power between ILC and MC RCSs.
First-order parameterized cost model has been developed considering difference in the beam power and duty factor between ILC and MC RCS.
  Cost of high power RF and FPC is propositional to the beam peak power
  Cost of cryogenic is proportional to the duty factor
It gives very rough cost estimate but provide some dependence of the cost on the main parameters of the RCSs. That is the main objective for the RCS optimization