## Slide 1
Design Optimization Approach for the 6D Cooling Magnets
Siara Fabbri, Luca Bottura

## Slide 2: Motivation
Beam Optics Ideal Set of Magnets
Magnet Engineering Analysis (OK, not OK)
Beam Optics Ideal Constrained Set of Magnets
Magnet Engineering Analysis (*Optimization)
*Initial Constraint Space of Magnets

## Slide 3: Motivation
How to best iterate with beam optics
  (Ex. constrain the feasible peak field on axis for an allowed space)
  Set of guidelines for coil dimensions (Ex. Longer over thicker)
How to best optimize a configuration of solenoids given a desired on-axis field.
  US-MAP Solenoids display big challenges such as large stresses, forces, stored energy…

## Slide 4: Review: US-MAP Cells
 |  |  | A1 | A2 | A3 | A4
 |  |  | 01 | 01 | 01 | 01
Input Parameters | Inner Bore Radius | mm | 450 | 410 | 270 | 220
 | Magnet Thickness | mm | 100 | 130 | 110 | 140
Geometry | Magnet Length | mm | 210 | 260 | 110 | 90
 | Current Density |  | 63.25 | 126.6 | 165 | 195
 | Cell Length | m | 2 | 1.32 | 1 | 0.8
 |  |  | A1 | A2 | A3 | A4
 |  |  | 01 | 01 | 01 | 01
Input Parameters | Inner Bore Radius | mm | 450 | 410 | 270 | 220
 | Magnet Thickness | mm | 100 | 130 | 110 | 140
Geometry | Magnet Length | mm | 210 | 260 | 110 | 90
 | Current Density |  | 63.25 | 126.6 | 165 | 195
 | Cell Length | m | 2 | 1.32 | 1 | 0.8
B1 | B2 | B3 | B4 |  | B5 |  | B6 |  | B7 |  | B8 |  | 
01 | 01 | 01 | 01 | 02 | 01 | 02 | 01 | 02 | 01 | 02 | 01 | 02 | 03
770 | 500 | 410 | 175 | 410 | 113 | 217 | 84 | 215 | 50 | 210 | 45 | 140 | 250
150 | 150 | 150 | 200 | 240 | 88 | 165 | 92 | 160 | 74 | 145 | 65 | 80 | 120
500 | 360 | 370 | 92 | 320 | 100 | 196 | 100 | 177 | 100 | 170 | 120 | 80 | 100
69.8 | 90 | 123 | 94 | 70.3 | 157 | 168 | 185 | 155.1 | 198 | 155 | 220 | 135 | 153
2.75 | 2 | 1.5 | 1.27 |  | 0.806 |  | 0.806 |  | 0.806 |  | 0.806 |  | 
18 unique coil types (2 to 6 coils per cell)
B4 has 2 unique coil types: B4-01, B4-02
…
B8 has 3 unique coil types: B8-01, B8-02, B8-03
2954 Solenoids

## Slide 5: Review: US-MAP Cells
Cell B8
Stresses
Hoop:
Radial:
Longitudinal:
Repeating cells…

## Slide 6: New Optics Initial Draft
898 Solenoids

## Slide 7: New Optics Initial Analysis

## Slide 8: New Optics: Magnetic Properties (Lattices)
Above 17 T no longer convenient HTS solution
100 MJ/ typical HiLumi magnets
US-MAP maximum
US-MAP maximum
US-MAP maximum

## Slide 9: New Optics: Mechanical Calculations (Lattices)
US-MAP
300 MPa hoop stress is current limit for FC solenoid, corresponds to peak 600 MPa in SS/alloy part of conductor
US-MAP

## Slide 10: New Optics: Mechanical Calculations (Lattices)
US-MAP

## Slide 11: Solenoid in Cell Optimization program (SiCO)
I. Define Simulation Grid of small elements
Minimum gap between coils and min/max
Minimum gap between coils and min/max 𝑅
II. Compute
On axis field for each element (element in lattice of alternating polarity elements)
On axis field 𝑩_𝒛 for each element (element in lattice of alternating polarity elements)
Harmonics: H1, H2, H3,
III. Filter and Optimize
Desired harmonics
Desired magnet parameters
Step size in z
Step size in r
All Coil geometry possibilities
Cell Length
III. Filter and Optimize
Desired harmonics
Desired magnet parameters
Small pixel elements in lattice
H1, H2, H3, …
FFT
on axis
,
,
…
(*) values given by beam physics
Example filter parameters
(volume, peak stresses, forces, …)
Current limitations (*to be implemented in future):
*2 solenoids per cell only
*No off-axis components
Peak fields/stresses in conductor for single coils, full cell in COMSOL

## Slide 12: Brief review: Key Analytic Equations
Rewriting this as…
It can be expressed as an infinite sum of alternating polarity solenoids:
Validated
On-axis field from one Finite Coil :
,
,
.

## Slide 13: Brief review: Field Analysis
FFT
Oscillating field from a lattice

## Slide 14
+
-
-
+
Define grid & simulate small elements of same current density

## Slide 15
Define grid & simulate small elements of same current density

## Slide 16
Calculate summed field for each possible coil block arrangement
Example

## Slide 17
More Examples
In this 3x5 grid, 90 possible rectangle configurations!

## Slide 18
Filter
Harmonic Filter
….and higher harmonics
Scaled Current Density Filter

## Slide 19
Th
Limitations: calculation of peak fields and therefore stresses make semi-empirical assumptions and can be inaccurate when coil length is small compared to inner radius (see additional slides)
Cell/Coil Parameter Calculator
Full-Cell Calculations:
Stored Magnetic Energy
Total Coil Volume
Single Coil Calculations:
Peak Fields
Stresses
COMSOL
Full-cell stress and field calculations

## Slide 20: What to optimize around?
Cost
Stored Magnetic Energy
Stresses

## Slide 21: SIMULATIOn Example Cell B1

## Slide 22: Simulation Example, Cell B1
1. Define your grid
Grid element sizes: dz = 10 mm, dr = 10 mm
Minimum gap between two neighboring coil surfaces = 100 mm
Min mm, Max mm
2. Compute field/ harmonic contribution of each element
How many unique rectangles can be made from this grid?
3. Generate unique rectangle combinations from grid
63x127 squares = 8001 tiny squares of current
B1 Coil
for for , …
A/mm2, A/mm2
4. Filter
Number of geometries accepted: 29k
  16,386,048
With smart size constraints & 1h later: 5.4 M unique rectangles

## Slide 23: B1 Select Distributions
(single coil)
(1 Cell)
B1 baseline values

## Slide 24: B1 Select Geometries and On-Axis Fields
Select on-axis field from 10 geometries

## Slide 25: Results: All US-MAP Cells (in Lattice)

## Slide 26
Cost
Stored Magnetic Energy
Stresses
Volume of Coils / Cell
Results
SiCO

## Slide 27
Cost
Stored Magnetic Energy
Stresses
SiCO
Stored Magnetic Energy (1 Cell)
Results

## Slide 28
SiCO
Hoop stresses
Results
Cost
Stored Magnetic Energy
Stresses

## Slide 29
Cost
Stored Magnetic Energy
Stresses
SiCO
SiCO
Tensile
Compressive
Radial stresses
Results

## Slide 30
US-MAP
coil geom
on axis
Example: on-axis field and coil geometry comparison using minimum hoop stress solutions
SiCO
on axis
coil geom
US-MAP + SiCO
US-MAP

## Slide 31: New Optics: Initial Optimization of Stage 5 and 10 Analysis
Radial Stress
Volume
Peak Hoop Stress

## Slide 32: Next Steps
Iteration with beam optics
Define allowed parameter ranges (peak stresses, fields), and complexity (more than two solenoids for high field cells? Multiple conductor types?)
Define guideline for initial solenoid creation
Simulation program
More constraints: RF Cavity sizes, structural and cryo space required around a coil
Factor in off-axis field quality
Integrate quench detection considerations

## Slide 33: Thank you!

## Slide 34: Simulation Study: Analytic Formulas for a Single Coil
Parameter | Parameter | Equation | References /comments
1 | Self Inductance |  | [1] where,
2 | Radial Stress | = | [2] and [3]
3 |  | = | [2] and [3]
5 | Peak field at of a single ideal coil |  | [3]
6 | Peak field at inner radius of a single ideal coil |  | [3]
7 | Mutual Inductance |  | [1] Eqs. 1, 29 and 33
Parameter | Parameter | Equation | References /comments
1 |  |  | 
2 |  |  | [2] and [3]
3 |  |  | [2] and [3]
5 |  |  | [3]
6 | Peak field at inner radius of a single ideal coil |  | [3]
7 | Mutual Inductance |  | [1] Eqs. 1, 29 and 33
[1] Rosa, Edward Bennett, and Frederick Warren Grover. Formulas and tables for the calculation of mutual and self-inductance. No. 169. US Government Printing Office, 1948.
[2] Wilson, Martin N. "Superconducting magnets." (1983).
[3] Iwasa, Yukikazu. Case studies in superconducting magnets: design and operational issues. Springer science & business media, 2009.

## Slide 35: Technology Options – Table of Stages and Coils

## Slide 36: Cell B5
141 mm
113 mm
196 mm
mm
z
r
 |  |  | B5 | 
 |  |  | 01 | 02
Input Parameters | Inner Bore Radius | mm | 113 | 217
 | Magnet Thickness | mm | 88 | 165
Geometry | Magnet Length | mm | 100 | 196
 | Current Density |  | 157 | 168
 | Cell Length | m | 0.806 | 
 |  |  | B5 | 
 |  |  | 01 | 02
Input Parameters | Inner Bore Radius | mm | 113 | 217
 | Magnet Thickness | mm | 88 | 165
Geometry | Magnet Length | mm | 100 | 196
 | Current Density |  | 157 | 168
 | Cell Length | m | 0.806 | 
100 mm
mm
01
217 mm
02
98 mm
mm
524 mm
610 mm

## Slide 37: Results Part 1: Characterization of all Coil Types 3/4 Mechanical Properties
(-) Compression
(-) Compression
(+) Tension

## Slide 38: Results Part 3: Characterization of all Stages, 1/4 Magnetic Properties – Cells and Lattices
For comparison purposes an LHC dipole stores ~7 MJ
Above 17 T (B5 to B8), highest performance required & difficult for

## Slide 39: Results Part 3: Characterization of all Stages, 2/4 Mechanical Calculations in Lattices
Maximum and minimum values of hoop stress
Coils with >150MPa will probably require reinforcement
Multi-radius-coil cells (B4-1, B5-1, B6-1, B7-1, B8-1, B8-2): the hoop stress decreases monotonically radially
For all other coils (A1 to B3, B4-2, B5-2, B6-2, B7-2, B8-3): there is a local minimum in hoop stress

## Slide 40: Results Part 3: Characterization of all Stages, 2/4 Mechanical Calculations in Lattices
Maximum and minimum values of radial stress
Multi-radius-coil cells (B4-1, B5-1, B6-1, B7-1, B8-1, B8-2): tensile saddle-like profile on inner coil. To go towards a compressive stress profile these coils would need to be wound in independent layers!
For all other coils (A1 to B3, B4-2, B5-2, B6-2, B7-2, B8-3): compressive ‘parabolic-like’ profile, with a minimum stress in the center

## Slide 41: Results Part 3: Characterization of all Stages, 2/4 Mechanical Calculations in Lattices – Longitudinal Stress
Maximum and minimum values of longitudinal stress
As expected, the stresses are all compressive based on the roller positioning

## Slide 42: Results Part 3: Characterization of all Stages, 2/4 Mechanical Calculations in Lattices - Forces
A support structure for a 37 MN axial force (3700 tons) will be a design challenge

## Slide 43
B1

## Slide 44: I. Define grid of tiny coil elements
Example:
Grid element sizes: dz = 10 mm, dr = 10 mm
Minimum gap between two neighboring coil surfaces = 100 mm
Min mm, Max mm
Grid for small coil elements symmetrically placed at opposite polarity
B1 Coil
B1 Coil

## Slide 45: I. Harmonic Profile of each Grid Element

## Slide 46: II. Rectangle (Coil) Possibilities in the space
z
r
63x127 squares = 8001 tiny squares of current
Examples
Every unique rectangle represents a unique configuration of alternating polarity coils
How many unique rectangles can be made from this grid?
  16,386,048
With imposed constraints:
  mm
  mm
  1h later: 5.4 M unique rectangles

## Slide 47: III. Parse the Geometries
Harmonic Acceptance:
… same for , ,
Constraints:
A/mm2, A/mm2
Number of geometries accepted: 29k