## Slide 1: Target System
IMCC and MuCol Annual Meeting 2024
12-15 March 2024, CERN
Rui Franqueira Ximenes | CERN-SY-STI-TCD
rui.Franqueira.Ximenes@cern.ch
M. Calviani, D. Calzolari, A. Lechner, F. Saura, J. Manczak, C. Mucher et al CERN – Systems Department, Sources Targets Interaction (STI), Targets Collimators Dumps (TCD)

## Slide 2: Content
Target studies
Carbon Target system overview & status update
  C-Target
  P+ Beam Window
  Target Shielding
Conclusions and prospects

## Slide 3: Target system
WP4.2 - Target system development
Establish a baseline target
Identify technological limits and R&D.
Define a system conceptual design
Estimate pion yield, target lifetime, heat load on the surrounding magnets.
Define the required shielding and associated magnet aperture

## Slide 4: Targetry options
CERN leading C-Target system studies & liquid-Pb option with ENEA. RAL & Warwick University leading fluidized W option.
C-Target & target system
CERN
Liquid Pb Target
ENEA & CERN
Fluidized W-Target
RAL & Warwick Uni.
C. Densham, J.J. Back, W. Bishop, D. Wilcox, et al.
C. Carrelli, M. Tarantino, I.Di Piazza, P.C. Puviani et al.
R. F. Ximenes, M. Calviani, D. Calzolari, A. Lechner, F. Saura, J. Manczak, C. Mucher et al

## Slide 5: Targetry options
Pb-Liquid Target
Opportunities
Known liquid-Pb / LBE thermo-hydraulics
Cooling outside vacuum chamber.
Radioisotopes mostly retained.
No degradation of target material.
Synergies between different projects at CERN such as FCCee.
Challenges
Liquid-Pb containment vessel and windows (material, temperatures, DPA).
MHD interaction.
Cavitation-induced erosion.
Temperature and dynamic effects.
Dynamic multi-phase flow simulation complexity
Conceptual designs
Pipe flow.
Vertical curtain.
Jet stream.
C. Carrelli, M. Tarantino, I.Di Piazza, P.C. Puviani et al.

## Slide 6: Targetry options
W-Fluidized Target
Advantages
No cavitation, corrosion, radiochemistry damage.
High thermal-shock resistance.
Heat removal.
Challenges
Erosion management & powder handling.
Reduced experience in operational facilities
Offline tests at RAL & HiRadMat beam test
Test rig built and operated at Rutherford Appleton Laboratory from 2009-2018
Response of various size spherical tungsten particles to 2x1011 p+ at HiRadMat (CERN)
C. Densham, J.J. Back, W. Bishop, D. Wilcox, et al.

## Slide 7: Carbon target & target systems considerations
  Energy deposition & dpa studies on the Target, windows, shielding, magnets, chicane
  Parameterization study in view of pion/muon yield optimization
  Conceptual Engineering study of Target & Target Systems, shielding, p+ dump -> feasibility
  ++ iteration loops with p+ driver, magnets, cooling
Production target
Tapering region
Chicane
Eventually p+ dump

## Slide 8: Carbon Target System
MuC target & shielding schematic (not at scale) [units in mm]

## Slide 9: Carbon Target System

## Slide 10: C-Target

## Slide 11: C-Target
Target Baseline parameters (recap)
Pion-yield studies (reported in at the 2023 annual meeting) + target engineering calculations converged into a set of baseline parameters
Pion yield studies by Daniele Calzolari:
https://indico.cern.ch/event/1250075/contributions/5342888/attachments/2668976/4625922/target_calzolari_annual_meeting_2023.pdf
CERN’s CNGS Target

## Slide 12: C-Target
Vessel Temperature – Serpentine Concept
Vessel Temperature & velocity vectors – Flow separator concept
Map Mach number, pumping power, HTC, wall temperature f (P, mf)
Target Cooling CFD study
Flow separator: (Initial concept)
  Simple. Low pumping power
  High recirculation and hotspots
Serpentine concept:
  Mapped HTC, Mach nr, pumping power and wall temperature Vs mass flow & pressure. He at 20 bar, 0.1 kg/s
  More complex. Pumping power around 37 kW
  Temperatures reduced by a factor of 2
  Thermo-structural static safety factor = 1.68 (cantilever fixation)

## Slide 13: C-Target
Target Cooling CFD study
Possibility of protecting the titanium vessel from the target radiative heat
Use of the carbon support substructure
Assumed external serpentine cooling with uniform HTC
Heat deposition on internal thermal radiation shield (ITRS) was not included
No significant differences were found because of the high emissivity of carbon
Low emissivity surface: ↓T vessel but ↑↑ T target
Not a meaningful solution to reduce the vessel temperature
Vessel T – without ITRS
Vessel T – with large ITRS
Vessel T – with medium ITRS
Target vessel 3D concept

## Slide 14: P+ beam window

## Slide 15: P+ beam window
Double layer window concept
Cooling helium at 1 bar & 5 g/s
Parametric study for Ti & Be windows (0.1 - 1 mm)
  More thickness, better mechanical resistance but higher energy deposited and temperature
  250 microns best compromise
  Beryllium has a higher safety factor & less radiation damage
Chart: Window Thickness
| 1 | 0.25 | 0.1
Safety Factor | 0.72 | 1.33 | 0.88
Temperature | 677 | 317 | 121
Chart: Material
| Titanium | Berylium
Safety Factor | 1.3255 | 1.4148
Temperature | 317 | 175
Parametric analysis in steady state. Thickness & Material
Convection cooling concept
Helium side
-1 bar -High Helium Temperature -Natural convection -Radiation
Vacuum side
-Vacuum -Radiation
1 bar, 5 g/s
116 W (0.25 mm)
DPA on Ti windows for 1 MW and baseline proton beam parameters

## Slide 16: P+ beam window
Point max T Point max stress
Window dynamic response
Radiative heat
from target
Window
Beam
Cooling Flow 2.5 bar, 0.5 g/s
Support
Helium side
-1 bar -High Helium Temperature -Natural convection -Radiation
Vacuum side
-Vacuum -Radiation
Conduction cooling concept
44 W (0.25 mm)
Chart: Temperature (˚C)
Safety Factor | 1.1544 | 0.7498 | 0.43186
Max T | 248 | 524 | 714
Single window concept
Conduction cooling from He cooled support
Beryllium window
Single beam shot far from failure (SF =1.17)
Pulling window away from target helps reducing the radiative heating from the target
Smaller window radius bring closer the heat sink to the beam and reduce maximum temperature

## Slide 17: P+ beam window
Beam dilution at the p+ window
Still work to be done to assess the fatigue (at high temperature and after irradiation)
Radiation damage is a challenge. Dilution mechanisms to be explored

## Slide 18: Target Shielding

## Slide 19: Target Shielding
19
Conceptual Design
Holding the assembly (23 t).
  Self-holding assembly, e.g. puzzle-like shape.
  Alignment pins & structural rods
He distribution
Water moderator & neutron absorber
He plenum
He return outlet
H2O moderator
Inlet guide plate & tubes
Boron carbide

## Slide 20: Target Shielding
Helium velocity on pipes across shielding
Pressure distribution
Helium distribution
Target Shielding CFD
RT Helium cooling
Plenum optimization in view of:
Study the effect of:
  Having homogeneous flow
  Study the effect of plenum size
  Define location of cooling return
Pressure loss: 52.4 kPa
Not coupled with thermal solver
  ∆T on coolant is high, but the HTC change is not so important
Useful insights to validate the use of analytical tools to estimate flow properties
  Thermal analysis using fluid cell elements to capture fluid T change

## Slide 21: Target Shielding
# Tungsten yield @ 500°C = 854 MPa
# Tungsten ultimate tensile stress @ 15°C = 1432 MPa
Max stress on external cooling pipe (169 MPa) center
Min stress on internal cooling pipe (374 Mpa) center
Shielding Temperature > 400 °C
Target shielding: thermo-mechanical study
Only thermal load (weak springs BC)
Longitudinally segmented slices (TCC ~100 W/m2K - frictional contacts)
At T < 400 °C , tungsten behaves as brittle (looking at failure via max principal stress)
Temperatures in acceptable range
  Interface temperature with solenoid reasonable
Slicing helps to decrease stresses

## Slide 22: Conclusions & Prospects
Status/Updates
Target vessel cooling ongoing and soon finalized. Further studies foreseen to better reduced Titanium vessel temperature.
P+ Beam window advancing towards a single window cooled with He.
Target shielding cooling study converging into a design proposal, although further refinement is still required.
What is in the pipeline to have a complete concept for the C-Target system ?
Dynamic response of the Target + supporting structure + target vessel
Complete modelling of Target cooling, particularly with integrated piping
Design of the target vessel support in the cryostat/target shielding.
Conceptualization of the target alignment
Complete target shielding cooling studies & vessel design.
Detail the structural assessment of the target shielding

## Slide 23: Conclusions & Prospects
What is in the pipeline to have a complete concept for the C-Target system ?
Detail the thermo-mechanical study of the window and do its conceptual design
Installation/maintenance & handling study of the target systems in the cryostat.
More in-depth study on radiation damage and fatigue considerations for the target system components and materials. -> Define R&D needed
What else?
Definition of the radiation shielding and cooling requirements for the chicane
Definition of the proton dump extraction
Proton dump conceptual design.
Studies on other frontend absorbers (as required such as masks, p+ absorber at the start of cooling section, etc)
Support the studies for alternative target concepts (as required)
Keep actively working on integration with the magnets team
Pursue alternative target options (Liquid Pb Target and Fluidized W Target)
Special thanks to Francisco and his key contributions these last 3 years 

## Slide 24
Many thanks!
Special thanks to Francisco and his key contributions these last 3 years 

## Slide 25: Carbon Target: engineering feasibility
  Target Cooling
  Due to high T and sublimation of graphite, an enclosed ‘pressurized’ atmosphere is required.
  However, active cooling can be made indirectly. Heat dissipation mostly via radiation and natural convection. → target confinement / separation of cooling system is advantageous (maintenance, RP, disposal, cooling services requirements).
Maximum temperature and power deposition for 1.5 MW as function of the beam sigma.
Direct cooling considerations
Old concepts

## Slide 26: Carbon target & target systems considerations
++ Other requirements
Target Physics requirements
Solenoid / Double Horn
Shielding
Carbon Target
Integration
Operation / Maintenance / Disposal
Radio Protection
Services
Target Engineering requirements
Proton driver
Cooling &
Capture
Production
Dynamic load
High temperature & average power
Fatigue
Radiation damage
Sing/multiple rods
Length / λ
Diameter
Tilt
Target vessel size
Beam windows
Design
Material / alloy
Availability
Properties
Radiation damage
Material
Type of cooling
Passive/active
Parameters
Dedicated/shared
Cooling
Pulse intensity
Pulse length
Pulse frequency
Beam size
Beam energy
Pion/Muon yield
Emittance
++…
P+
µ