## Slide 1
  C. Bartoli1, M. Breschi1, A. Macchiagodena1, P. L. Ribani1, H. De Gersem2, D. Moll2, F. Boattini3, L. Bottura3
  1Alma Mater Studiorum – Università di Bologna, Italy
  2University of Darmstadt, Germany
  3CERN, Geneva, Switzerland

## Slide 2: Outline
Options of fast-ramped resistive magnets for the accelerator
Advances in the modeling of the H-type magnet
Advances in the dynamic modeling of the resistive magnets
Preliminary thermal analysis of the hourglass magnet

## Slide 3: Outline
Options of fast-ramped resistive magnets for the accelerator
Advances in the modeling of the H-type magnet
Advances in the dynamic modeling of the resistive magnets
Preliminary thermal analysis of the hourglass magnet

## Slide 4: Analyzed configurations
Hourglass H-magnet
Magnet specifications: 1) Magnetic field in the aperture 1.8 T 2) Good field region (30 mm * 100 mm) 3) 1 ms ramp from -1.8 to + 1.8 T
Two magnet configurations identified by optimization of the total magnet energy
Vacoflux 48 or M235-35A
Vacoflux 48
M235-35A
M235-35A

## Slide 5: Outline
Options of fast-ramped resistive magnets for the accelerator
Advances in the modeling of the H-type magnet
Advances in the dynamic modeling of the resistive magnets
Preliminary thermal analysis of the hourglass magnet

## Slide 6: Magnetic circuit model of the H-type magnet
To reduce the computation time wrt the FEM model, an equivalent circuit model of the H-type magnet was developed
The circuit was solved with mesh analysis

## Slide 7: Magnetic circuit model of the H-type magnet
The field in the gap and the total flux linked to the winding were computed with both the magnetic circuit and a 2D FEM model (FEMM), obtaining a good agreement.
Field Flux

## Slide 8: Analytical assessment of iron losses
The losses measured in the two selected ferromagnetic materials were fitted by Bertotti formula to retrieve the values of khyst, keddy, and kaddit parameters.
Vacoflux 48
M235-35A
The parameters were found at f = 400 Hz

## Slide 9: Magnetic circuit model of the H-type magnet
The magnetic energy and total losses in the iron were also computed with the FEMM model and the magnetic circuit.
Energy Iron losses
FEMM linearization

## Slide 10: Comparison between magnetic circuit and FEMM
A parametric study was launched to compare FEMM and magnetic circuit with different geometries.
175 configurations studied, computing the maximum error with 10 values of transport current on Bgap, Etot, F.
13% peak error on the flux
Computation time is reduced from 177 s to 1.5 s
 | Min. (mm) | Max (mm) | Number of values
Gap width | 80 | 120 | 5
Gap height | 25 | 35 | 5
Coil width | 39.5 | 69.5 | 7

## Slide 11: Outline
Options of fast-ramped resistive magnets for the accelerator
Advances in the modeling of the H-type magnet
Advances in the dynamic modeling of the resistive magnets
Preliminary thermal analysis of the hourglass magnet

## Slide 12: Dynamic modeling
Objective: Simulate fast-ramped magnets
PRESENT
2D FEM
Transient solver
Circuit coupling
  Magnet as multi-port element
Calculation of
  Coil losses
  Core losses
  …
FUTURE
Temperature effects
Hysteresis
3D end effects
Software:
Pyrit

## Slide 13: Verification
Static Transient
H-Type
model_000

## Slide 14: Core losses
Hysteretic material model:
  Reversible:
  Irreversible: ,
Core loss:
  Steinmetz:

## Slide 15: Pulse duration & losses
Long pulse low core losses
Short pulse low coil losses
Total losses uneffected: 240 J/cycle/m
Hourglass model_002

## Slide 16: Energy densities
Losses for one cycle (J/m³) Max. stored energy (J/m³)
5ms pulse

## Slide 17: Outline
Options of fast-ramped resistive magnets for the accelerator
Advances in the modeling of the H-type magnet
Advances in the dynamic modeling of the resistive magnets
Preliminary thermal analysis of the hourglass magnet

## Slide 18: Thermal model of the hourglass magnet
Bar Width | Bar Thickness | Magnet Length (L) | Initial temperature (Ti) | Cooling edges temperature (T0)
0.1403 m | 0.007 m | 1 - 2 m | 293 - 283 K | 293 K
To study the conduction cooling from the magnet ends, a 1D model (THEA) was developed. Only one copper bar is simulated, neglecting the interaction with other magnet parts.

## Slide 19: Thermal model results
Pulse = 5 ms, ∆Tmax = 41 K
P = 129 W/m
To reduce the computation time, the heat generated during the pulsed operation is averaged over the cycle and treated as a constant value.
The analytical solution at steady state regime is in agreement with the numerical simulation.
Pulse = 5 ms, ∆Tmax = 157 K
P = 129 W/m
L = 1 m L = 2 m
Temperature rise above 150 degrees for L = 2 m: challenging for conduction cooling from the magnet ends.

## Slide 20: Conclusions
The design of fast ramped resistive magnets for the Muon Collider accelerator is ongoing
A magnetic circuit model of the H-type magnet was developed, which includes the analytical computation of the iron losses
Transient 2D FEM models of both H-type and hourglass type magnet were developed, which allow coupling with the external circuit
In perspective, analytical formulae for the losses in the copper windings will be added to the circuit model
Temperature effects, 3D end effects and hysteresis will be added to the FEM models

## Slide 22: Additional slides

## Slide 23: Considered geometries
Hourglass H-Type

## Slide 24: Pulse duration
Map Dipole | Transient T=5ms | Harmonic f=200Hz | Transient T=2ms | Harmonic f=500Hz
Bgap [T] | 1.8 | 1.8 (Static) | 1.8 | 1.8 (Static)
Mmf [kAt] | 47.4 | 47.4 | 47.4 | 47.4
Core losses (yoke) [J/cycle-m] (M235-35A, k=9e-3, m=1.3, n=1.9) | 48.4 | 64.3 | 83.4 | 84.6
Core losses (pole) [J/cycle-m] (M235-35A, k=9e-3, m=1.3, n=1.9) | 60.1 | 71.6 | 102.5 | 94.3
Coil Losses [J/cycle-m] | 56.2+47.3=103.5 | 60.5+52=112.5 | 32.2+18.8=51 | 43.8+23.8=67.6
Total losses [J/cycle-m] | 212 | 248 | 238 | 247
Stored energy (total / gap) [J/m] | 6720 / 3800 | 6720 / 3800 (Static) | 6720 / 3800 | 6720 / 3800 (Static)

## Slide 25: Magnet simulation
Magnet as N-port element
  Unknowns:
    N voltages, N currents
    Magnetic vector potential (DOFs N)
  N source equations required Current sources
Transient: ,
  Static: ,
  Harmonic: , ,

## Slide 26: Coil losses
Power density:
Statics:
Dynamics:
  Skin effect

## Slide 27: Core losses - post-processing
and : pair on hysteresis loop
  Distinct elements = distinct hysteresis loops
Steinmetz formula:
  Post-processing
  Only for sinusoidal quantities
  No phase lag or amplitude effect
  attributed to hysteresis

## Slide 28: Thermal model assumptions
To reduce the computation time, the heat generated during pulsing operation conditions is averaged in the cycle period and treated as a constant value.
Pulse time = 5 ms,
peak power loss = 5.175 kW/m
P= 129 W/m

## Slide 29: Thermal model results
Magnet lengths above 1 m determine temperature rises above 150 degrees and seem challenging for the conduction cooling from the magnet ends.
Energy [J/cycle/m] | Pulse duration [ms] | Conductor length [m] | Initial temperature [K] | ∆Tmax [K]
12.75 | 2 | 1 | 293 | 20.3
25.875 | 5 | 1 | 293 | 41.3
12.75 | 2 | 2 | 293 | 77
25.875 | 5 | 2 | 293 | 157
12.75 | 2 | 1 | 283 | 20.3
25.875 | 5 | 1 | 283 | 41.3