## Slide 1: Magnets and Powering System Cost Evaluation and Plan for the Accelerators
Fulvio Boattini (CERN)
IMCC and MuCol Annual Meeting 2024
CERN, 14/03/2024

## Slide 2
Outline of the presentation
Presentation of the cost model for Power Converters and Magnets;
Cost computation (pu values)
Planning proposal
Conclusions
Magnets and Powering System Cost Evaluation and Plan for the Accelerators / Fulvio Boattini/ CERN

## Slide 3: Cost model layout
The cost model is based on the computation of capital and operational cost.
Capital costs includes:
Material
Construction
Infrastructures.
Magnets and Powering System Cost Evaluation and Plan for the Accelerators / Fulvio Boattini/ CERN

## Slide 4: Cost model layout
The cost model is based on the computation of capital and operational cost.
Capital costs includes:
Material
Construction
Infrastructures.
Several components of the cost model still to be implemented
Infrastructure costs are strongly dependent upon the location of the power converters (surface or tunnel). In the following computations we will consider installation on surface
Several components of the cost model still to be implemented
Magnets and Powering System Cost Evaluation and Plan for the Accelerators / Fulvio Boattini/ CERN

## Slide 5: Cost Models: Power converters. Bottom-up model Capital costs
HP: installation on surface. Unified cell to load connection. One powering system per sector.
Identify Nseries/Nparallel power cells.
Compute the size and cost of IGBTs/Diodes and stacks.
Identify size and cost of the power cell cabinet. Included fabrication costs
Compute the size and cost of Boost (left) and preload(right) capacitors.
Identify size and cost of the technical building and capacitor containers
1
2
3
4
5
Magnets and Powering System Cost Evaluation and Plan for the Accelerators / Fulvio Boattini/ CERN

## Slide 6: Cost Models: NC Magnets. Bottom-up model Capital costs
The simplified cost approach is taken from “Basic design and engineering of normal-conducting, iron-dominated electromagnets” by Th. Zickler.
Cost figures are adapted for 3% of inflation over the last 14 years and the highest value of the range is taken.
The material costs for Vacoflux 48 are estimated values in consultation with magnet experts.
Much simpler model because of lack of expertise in magnet construction. Briefly discussed with magnet expert but requires verification.
Magnets and Powering System Cost Evaluation and Plan for the Accelerators / Fulvio Boattini/ CERN

## Slide 7: Cost Computation
 | RCS1(***) | RCS2 | RCS3 | RCS4 | Totals
NC Magnets cost (*) [MEu] | 0.6% | 0.4% | 0.7% | 4.2% | 5.9%
SC Magnets cost [MEu] | 0.0% | 4.0% | 8.6% | 15.5% | 28.1%
PC cost: power cells [MEu] | 1.3% | 1.3% | 1.7% | 7.4% | 11.7%
PC cost: capacitors [MEu] | 0.1% | 0.1% | 0.3% | 1.3% | 1.8%
PC cost: building [MEu] | 0.9% | 0.9% | 1.1% | 4.5% | 7.3%
Operation cost (losses NC+PC) (**) [MEu] | 0.5% | 0.5% | 0.8% | 3.4% | 5.2%
Totals | 3.4% | 7.2% | 13.1% | 36.4% | 60.0%
(*) to be verified by magnets’ experts
(**) 20years 6000h/year. Cable losses and cryogenic power are not included
(***) computed as 70% of the linear cost for RCS2. Except for the magnets
Using the above cost models we computed the following costs. They are shown in pu wr2 the total cost of the magnets (WP7).
Courtesy of Siara Fabbri and Luca Bottura
Magnets and power converters for the accelerators represents 60% of the total magnet costs
20.8%
13.2%
Magnets and Powering System Cost Evaluation and Plan for the Accelerators / Fulvio Boattini/ CERN

## Slide 8: Construction hypothesis
The unified cell to load connection option requires the construction of one building with capacitor containers for each sector, for the installation of the power cells. Cables connect the surface power converters with the tunnel NC magnets.
Considered in this presentation
Alternative
The cell-load cascade connection option would be an alternative. Makes sense if power cells and capacitors are installed in the tunnel. Could reduce overall cost:
Surface building not required anymore (but tunnel alcove required…)
Shorter cables
Lower voltage to gnd
All magnets in series, easier control problem
Buildings
Containers
Magnets and Powering System Cost Evaluation and Plan for the Accelerators / Fulvio Boattini/ CERN

## Slide 9: Planning
Construction of High frequency magnetic demonstrator for validating losses calculation.
Additional budget: 60kEu Material
This is required for the string test with power converters. It allows validating the interleaving powering concept and the current control behavior.
Eight 0.5m long magnets with eight circuits. Estimated cost 500kEu.
Magnets and Powering System Cost Evaluation and Plan for the Accelerators / Fulvio Boattini/ CERN

## Slide 10: Planning
Capacitors are not a big cost figure. Nevertheless, it can be important to optimize the volume particularly if installation in the tunnel is foreseen.
Budget estimate: 200kEu
Test of one full scale Power Cell on dummy load
Budget estimate: 100kEu
To be reviewed by magnets experts
Magnets and Powering System Cost Evaluation and Plan for the Accelerators / Fulvio Boattini/ CERN

## Slide 11: Planning
To be reviewed by magnets experts
Large number of power converters and buildings.
Difficult to keep the target.
Magnets and Powering System Cost Evaluation and Plan for the Accelerators / Fulvio Boattini/ CERN

## Slide 12: Conclusions
The powering system and nc magnets of the accelerator are very much connected, and a global optimization should be pursued. Work is in progress.
The NC magnets cost model is a first test based on existing literature. No experts’ eye verified it (carefully).
Preliminary evaluations, point to the SC magnets and Power Converters as the main cost factors among those presented here. Accelerators shows to be the biggest contributor. As the optimization proceed, data can radically change.
The pc cost model has a granularity in the selection of the components that may bring to a non cost optimal solution. The model should be improved in this respect. A cross check with FCC cost models for pc will be helpful.
A lot of uncertainty still exists on the “cahier de charge” of the Power Converters, particularly concerning the accuracy that is required to the control. This can greatly influence the topology and cost of the pc. More precise data should be provided.
Magnets and Powering System Cost Evaluation and Plan for the Accelerators / Fulvio Boattini/ CERN

## Slide 14: Spare Slides

## Slide 15
Several cells are powering one sector
Several stacks build up one power cell
Several IGBTs and DIODEs build up one stack
Several capacitor containers required for the Cboost and Cpreload
Cost Models: Power converters. Bottom-up model Capital costs

## Slide 16
Several cells are powering one sector
Several stacks build up one power cell
Several IGBTs and DIODEs build up one stack
Several capacitor containers required for the Cboost and Cpreload
Cost x joule
Surface x joule
No of Power Cells depends upon total voltage / current in the magnets
Cost Models: Power converters. Bottom-up model Capital costs

## Slide 17: Cost Models: Power converters. Bottom-up model Capital costs
Safe Operating Area
Current in magnet
Voltage Cpreload
Voltage Cboost
Min = -5450A
Max = 5450A
Min = 90V
Max = 560V
Min = 3000V
Max = 3600V
Is1=5.5kA
Is2=-5.5kA
Vce1=2.9kV
Toscill=12ms
Several stacks build up one power cell
Several IGBTs and DIODEs build up one stack
The Number of IGBTs and Diodes, depend upon the levels of commutated current and voltage of the power cell
Power Cell

## Slide 18: Backup Slide1: Capacitor costs and surface
HP:
All capacitors are stored in Marine Containers 12m(long) x 2.7m(wide) x 2.5m(high)
Available surface for capacitors in one container is 32.4m2 but only 42% of it is occupied by capacitors (POPS experience).
PP film capacitors dimensions and cost are taken from the POPS experience;
ELCO capacitors dimensions and costs are taken from the SIRIUS experience;
Four ELCO’s chassis are piled up in the container.
PP film capacitors are derated differently if the applications requires voltage polarity reversal or not. Switched resonance doesn’t require it.
ELCOs cannot reverse polarity.
The cost model for capacitors returns the cost per joule and the occupied surface x joule. Nevertheless, since the capacitors are installed in containers, the cost of the land is not factored in.
POPS container 12mx2.7mx2.5m; 26tons; 0.5MCHF;

## Slide 19: Backup Slide2: Power converters cost and surface
Define performance of the IGBTs and diodes
Define number of stacks and mechanical dimensions
Define cost of the stacks
Cost and dimensions computation for the IGBT stacks
HP: press-pack component selected
Granularity is poor as very few sizes exists. For this reason, we may have excessive cost estimation
Stacks cabinet
DC caps cable input
Mags cable output
STACK
STACK
STACK
STACK
STACK
STACK
One power Cell
Control cabinet

## Slide 20: Backup Slide2: Power converters cost and surface
Define the cost and dimensions of one power cell with cabinet and stacks
Define the number of sectors in the accelerator and the number of power cells required in each sector
Compute the cost of all required power cells and the cost of the building.
The total cost is the sum of the two
Stacks cabinet
DC caps cable input
Mags cable output
STACK
STACK
STACK
STACK
STACK
STACK
One power Cell
Control cabinet
Once the cost and dimensions of the stacks are known, the model proceeds by defining the size and cost of the hosting cabinet and accessory hardware. One cabinet corresponds to one power cell.
In addition the cost model also evaluate the cost of the building surface included with services (cooling and electric auxiliaries) that are required to operate the power cells.
These costs are based on the construction of the B245 for the POPSB power converter (2018 CERN)

## Slide 21: Setting the stage: some important definitions
The Bref is created by the connection of two different sinusoids named here Preload and Ramp. The power electronic does that.
Playing with the Preload circuit Tpulse can be varied;
Playing with the Boost circuit, Bref_dot max can be changed;
Preload
Preload
Ramp
Bref
Bref dot
Tpulse
Bref_dotmax
Mmf current
Mmf current harmonics
The first harmonic of the magnet current has a frequency of 1/Tpulse
The next most important harmonic is the second.
The magnet losses reported in this presentation are computed with AC simulation with the first harmonic only
Transient simulation necessary to simulate proper losses
Short Tpulse requires high power in the converter

## Slide 22: Setting the stage: some important definitions
Losses are calculated by considering the energy lost per cycle and per meter or the average power losses
Conductor current density used for magnet design is defined as this relates to the
Water cooled conductors: ; Tpulse = 5ms and Trepet = 200ms 
Air cooled conductors: ; Tpulse = 5ms and Trepet = 200ms 
Magnetic dimension of the magnet
decreases less than linearly with Tpulse
increases linearly with Tpulse
decreases more than linearly with Tpulse
increases linearly with Tpulse

## Slide 23
Setting the stage: Power Converters – magnets connection
~5000V
~1’000’000V
Cell-load connection (SPS): the voltage to ground is limited by the PC voltage  can connect all mags of the accelerator in one single sector  current will be the same everywhere
Unified cell connection (LHC): the voltage to ground is the sum of series connected PC  must divide in several sectors  current will not be the same everywhere (control problem is harder)
Should be distributed into the tunnel to minimize cabling (and cable losses)
Interleaving connection makes the impedances of each circuit the same. We can treat the single circuit as if the same current was flowing and the same voltage applied (ideal case). We could treat FEM computation as current controlled in each circuit.
…an MMC but at much higher frequency!

## Slide 24: MMC: a similar topology for a different application
640 kVdc
2 GW
Hundreds of connected cells
Basic cell:

## Slide 25: Optimization of power converters and dipole magnets
The ultimate goal of the optimization is minimizing the overall costs. The following costs are included:
Magnet costs (material + manufacturing)
Capacitor costs including containers
Power electronics cost including peripherals and building (no cables)
Operational costs (Losses in magnets and IGBTs) for 20 years of operation with 6000h per year
base_input_parameters={'Maximum B field in air[T]': 1.8,'Maximum B field in joke[T]': 1.4,
'B field ratio in poles[Bp/Bg]':0.6 ,'Total length of normal conducting dipoles [m]':2540,
'Number of sectors for powering': 48,'Number of parallel circuits': 8,
'Acceleration ramping time [s]':0.0011, 'Pulse cycling time [s]':0.2,'Pulse duration time [s]':0.007,
'RMS current density [A/mm2]':5,'Conductor thickness [m]':0.003,'Insulation thickness [m]':0.001,
'Joke steel type':"steel_M235_35A.json",'Poles steel type':"steel_M235_35A.json",'gap height [m]':0.03,
'gap width [m]':0.1,'Aspect ratio of conductor hc/wc':1,
'Aspect ratio of the conductor window h1i/w1i':3,'Cooling water flow in conductor [m3/h]':0.1,
'Cooling water speed in conductor [m/s]':3,'Filling factor of conductor window':0.5
All based on FEMM computing…very slow

## Slide 26
Optimization: minimize the losses of magnets only
Benchmark: Hourglass type with 30x100mm gap
h1=500 mm
w1=738 mm
wj= 163mm
hc=16.5 mm
sc= 3.8 mm
sis=4.8 mm
Tpulse= 2 ms
σrms= 3 A
mmf= 46115 At
ElossIron= 136 J/m/pulse
Elosscu= 161 J/m/pulse
NRGstored= 7577 J/m
Optimization Losses only: sc, sis, water cooling section
Optimization Losses only: Bratio_pole, AsRatwdw
h1=560 mm
w1=800 mm
wj= 163mm
hc=12.5 mm
sc= 2 mm
sis=15 mm
Tpulse= 2 ms
σrms= 7 A
mmf= 47270 At
ElossIron= 160 J/m/pulse
Elosscu= 196 J/m/pulse
NRGstored= 7654 J/m
h1=570 mm
w1=850 mm
wj= 163mm
hc=140 mm
sc= 2x3.5 mm
sis=10 mm
Tpulse= 2 ms
σrms= 2.7 A
mmf= 53000 At
ElossIron= 153 J/m/pulse
Elosscu= 91 J/m/pulse
NRGstored= 7084 J/m
We can have two dipole topologies:
Air cooled with flat conductors
Water cooled with hollow conductors
Here Tpulse = 2 ms

## Slide 27
External dimensions [mm x mm] | 460 x 322
Joke cross section [dm2] | 11.35
Pole cross section [dm2] | 1.21
Coil cross section [mm2] | 285.39
Number of parallel coils | 4
Bgap [T] | 1.80
Gap size [mm x mm] | 100 x 30
MMF [kAt] | 47.49
Sigma_RMS (pulse) [A / mm2] | 29.41
Sigma_RMS (cycle) [A / mm2] | 4.41
Iron losses (joke) [J / (cycle * m)] | 48.29
Iron losses (pole) [J / (cycle * m)] | 10.22
Coil losses [J / (cycle * m)] | 447.47
Total losses [J / (cycle * m)] | 505.98
Energy (total) [J / m] | 6386.12
Energy (gap) [J / m] | 3830.48
230 mm
161 mm
96 mm
96 mm
71 mm
50 mm
19.2 mm
9.2 mm
Coil current of
AC analysis
Tpulse = 4.5 ms
Ipeak = 11.87 kA
Steel M235-35A
Steel
M235-35A
Optimization: minimize the total cost of Magnets and power converters
Steel: M235-35A everywhere
Here Tpulse = 4.5 ms

## Slide 28
External dimensions [mm x mm] | 442 x 312
Joke cross section [dm2] | 10.55
Pole cross section [dm2] | 1.09
Coil cross section [mm2] | 285.39
Number of parallel coils | 4
Bgap [T] | 1.78
Gap size [mm x mm] | 100 x 30
MMF [kAt] | 43.92
Sigma_RMS (pulse) [A / mm2] | 27.20
Sigma_RMS (cycle) [A / mm2] | 4.59
Iron losses (joke) [J / (cycle * m)] | 38.12
Iron losses (pole) [J / (cycle * m)] | 8.70
Coil losses [J / (cycle * m)] | 434.89
Total losses [J / (cycle * m)] | 481.71
Energy (total) [J / m] | 5773.80
Energy (gap) [J / m] | 3702.65
Coil current of
AC analysis
Tpulse = 5.6 ms
Ipeak = 10.98 kA
221 mm
156 mm
93 mm
93 mm
63 mm
50 mm
19.2 mm
9.2 mm
Steel M235-35A
Vacoflux 48
Optimization: minimize the total cost of Magnets and power converters
Steel: M235-35A for the joke, Vacoflux 48 for the Poles
Here Tpulse = 5.6 ms

## Slide 29: Comparisons
 | Hollow conductors water cooled |  | Flat conductors air cooled
 | Optimization for loss in magnets | Optimization for overall cost in Power Converters + Magnets | Flat conductors Hourglass. Not optimized
Total losses [J/m/pulse] | 381 | 506 | 230
Total NRG [J/m] (DC equivalent) | 7577 | 6386 | 7084
Outer Dimensions wxh [mm] | 738 x 500 | 442 x 312 | 850 x 163
Tpulse [ms] | 5 | ~ 5 | 5
Lower losses and higher NRG and dimensions
Higher losses and lower NRG and dimensions
Recomputed to Tpulse=5 ms
A good compromise?

## Slide 30: Results cost optimization
 | H-type (full steel) | H-type (Vacoflux + steel)
Costs pole [pu] | 0.012 | 0.042
Costs joke [pu] | 0.111 | 0.103
Costs conductors [pu] | 0.019 | 0.019
Total magnet costs [pu] | 0.142 | 0.164
Costs capacitors [pu] | 0.050 | 0.047
Costs power electronics1 [pu] | 0.611 | 0.567
Cost losses magnets2 [pu] | 0.151 | 0.150
Cost losses PE2 [pu] | 0.041 | 0.043
Total costs [pu] | 0.995 | 0.971
Costs are calculated for RCS2 which consists of 2540m of normal conducting dipole magnets.
2 Operational costs are considered only for the losses in the IGBTs and the magnet (no cables). The assumption is 20 years of operation with 6000h per year and costs of 90 U/MWh.
1 Due to the discrete IGBT model in the overall cost model the costs are slightly overestimated and probably can be reduced by 30% to 40%.