## Slide 1: Magnet systems development and production schedule & cost estimate
B. Caiffi2, A. Bersani2, S. Farinon2,
S. Mariotto3 , D. Novelli1,2 , A. Pampaloni 2, T. Salmi4 , L. Bottura5, ...
1Sapienza University of Rome , 2INFN – Genoa , 3INFN – Milan , 4Tampere University , 5CERN

## Slide 2: Magnet requirements
Task 7.4 Collider Ring Magnets (INFN)
Courtesy of Patricia Borges de Sousa
https://indico.cern.ch/event/1250075/contributions/5357594/
10 TeV collider (10 km ring):
15T /150 mm (REBCO, hybrid)
5 m length
1200 magnets
3 TeV collider (5 km ring):
11T/150 mm (Nb3Sn)
5 m length
600 magnets
,
TBM according to lattice
,
TBM according to lattice
Radial build
With REBCO @ 20 K Wabs can be 3 cm thick (P<10 W/m)
What about 2 cm? Would the dose be acceptable?
138 mm
Courtesy of Anton Lechner

## Slide 3: Tentative Schedule (3 TeV collider)
Models |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Prototypes |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Pre-series |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Series |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041
demonstrator (1)
models (10)
3x200 dipole
magnets
R&D and
demonstrators
  ARC DIPOLES 11T/158mm
  (quadrupoles and IR still not included)
+ 4 years
Models |  |  |  |  |  |  |  |  |  |  |  |  | 
Prototypes |  |  |  |  |  |  |  |  |  |  |  |  | 
Pre-series |  |  |  |  |  |  |  |  |  |  |  |  | 
Series |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037
R&D and
demonstrators
demonstrator
models
full length prototypes
3x90 dipole magnets
3x200 dipole magnets
Aggressive time schedule, 13 years from R&D to end of construction
  Initial proposal
  Revised proposal
4 years (+1)
6 years (+ 1)
4 years (+ 1)
5 years (+ 1)
Nb3Sn demonstrator program 6 years
LHC: 13 short models in 11 years, 6 prototypes in 4 years, pre-series 4 years, series 4 years
3 years
5 years
4 years
3 years
4 years
4 years
17 years from R&D to end of construction
3x30 dipole magnets
full length prototypes (5)

## Slide 4: Tentative Schedule (10 TeV collider)
R&D and demonstrators |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Models |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Prototypes |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Pre-series |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Series |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Specifications and concept development
demonstrator model ( 1 per concept)
models (10)
full length prototypes (5)
3x30 dipole magnets
+3 years
  ARC DIPOLES 15T/138 mm
  (quadrupoles and IR still not included)
  Initial proposal
  Revised proposal
26 years from R&D to end of construction
3x400 dipole magnets
Models |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Prototypes |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Pre-series |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Series |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047
Specifications and concept development
R&D and demonstrators
23 years from R&D to end of construction
demonstrator
models
full length prototypes
3x30 dipole magnets
3x400 dipole magnets
3 years
5 years
7 years
3 years
5 years
6 years
4 years (+1)
6 years (+1)
8 years (+1)
4 years (+1)
4 years (-1)
5 years (-1)
More emphasis on demonstrator and short model phase (REBCO or hybrid solutions still to be studied)

## Slide 5: Cost Model
Bore
Coil
Structures
Iron
Optimization of the cross section still ongoing.
Cost estimate performed on a simplified geometry with a sector coil dipole and iron and steel structure modelled as circular crowns.
R bore, wcoil, wiron and wstruct optimized to fulfil beam optics requirements, margin on the load line, acceptable stress on the conductor and effectiveness of the quench protection (see D. Novelli presentation [ref])
(FCC-hh [ref])
(as FCC, 2xLHC)
where
(D2 HL-LHC as benchmark)
(D2 HL-LHC as benchmark)
Material | 
Sn | 
aspirational value | 
aspirational value | 
Material | 
aspirational value | 
aspirational value | 
Escalated price in 2016
The right value in 2016
Corresponds to the FCC target
The value of today (2023)
A realistic projection for the next years

## Slide 6: Cost Estimate (3TeV)
Rbore= 79 mm
wcoil= 80 mm
wstruct= 50 mm
wiron=350 mm
  11T /158 mm (Nb3Sn)
€/kg iron | €/kg struct | €/kg conductor *
8 | 10 | 700
* 7€/kAm, FCC target 5€/kAm
Iron [Kg/m] | Structure [kg/m] | Coil [kg/m]
6587 | 450 | 223
Iron cost [k€/m] | Structure cost [ k€/m] | Coil cost [k€/m]
53 | 4.5 | 156
Tot. Material k€/m | 84 | 30%
Tot. Assembly k€/m | 40 | 14%
Tot. Conductor k€/m | 156 | 56%
Tot. Cost k€/m | 280 | 
TOTAL COST: 6.7% O.M.B. (overall magnets budget)
200 k€/magnet ( 2FTE)
Dipoles of the arc for the series production
(quadrupoles and IR not included)
Coordination, design and follow-up: 4 FTE x 4 years= 16 FTE-years (1.6 MEur)
Disclaimer: cryostat, specific tooling (e.g. oven for thermal treatment of Nb3Sn) W absorber not taken into account
fstruct = 1.5
Tot. Material = (Ciron+ Cstruct)*fstruct
Notes: J= 3 e8

## Slide 7: Cost reduction learning curve
How to rescale for the other steps (pre-series, prototypes, short models, demonstrators)?
Learning curve
Wright's law
Applied to LHC magnets works perfectly! [ref]
b: learning percentage
b=0.8
 | 3 TeV |  | 10 TeV | 
 | N units (cumulative) | cost (A.U.*) | N units (cumulative) | cost (A.U.*)
demostrator | 1 | 3.36 | 1 | 7.13
short model | 11 | 1.55 | 11 | 3.29
proto | 16 | 1.38 | 16 | 2.92
pre series | 46 | 0.98 | 46 | 2.08
series | 246 | 0.57 | 446 | 1.00
*w.r.t. cost of 10 TeV series magnet

## Slide 8: Cost Estimate (3TeV)
Iron cost [k€/m] | Structure cost [ k€/m] | Coil cost [k€/m]
91 | 8 | 269
Tot. Material k€/m | 144 | 30%
Tot. Assembly k€/m | 69 | 14%
Tot. Conductor k€/m | 269 | 56%
Tot. Cost k€/m | 481 | 
Iron cost [k€/m] | Structure cost [ k€/m] | Coil cost [k€/m]
127 | 11 | 377
Tot. Material k€/m | 201 | 30%
Tot. Assembly k€/m | 96 | 14%
Tot. Conductor k€/m | 377 | 56%
Tot. Cost k€/m | 674 | 
Pre-series
Prototypes
Short Models
Demonstrators
Iron cost [k€/m] | Structure cost [ k€/m] | Coil cost [k€/m]
143 | 12 | 425
Tot. Material k€/m | 227 | 30%
Tot. Assembly k€/m | 109 | 14%
Tot. Conductor k€/m | 425 | 56%
Tot. Cost k€/m | 761 | 
Iron cost [k€/m] | Structure cost [ k€/m] | Coil cost [k€/m]
310 | 27 | 919
Tot. Material k€/m | 491 | 30%
Tot. Assembly k€/m | 235 | 14%
Tot. Conductor k€/m | 919 | 56%
Tot. Cost k€/m | 1645 | 
N units | length [m] | N years | cost FTE-y [k€] | Total cost [o.m.b*]
90 | 5 | 4 | 1600 | 1.70%
N units | length [m] | N years | cost FTE-y [k€] | Total cost [o.m.b*]
5 | 5 | 5 | 2000 | 0.15%
N units | length [m] | N years | cost FTE-y [k€] | Total cost [o.m.b*]
10 | 1.5 | 6 | 3000 | 0.11%
N units | length [m] | N years | cost FTE-y [k€] | Total cost [o.m.b*]
1 | 1.5 | 4 | 12000 | 0.03%
*overall magnets bugdet

## Slide 9: Cost Estimate (10 TeV)
Rbore= 69 mm
wcoil= 58 mm
wstruct= 30 mm
wiron= 300 mm
  15T /138 mm (REBCO)
€/kg iron | €/kg struct | €/kg conductor *
8 | 10 | 2500
  *50 €/kAm: 1/3 of today prize (150€/kAm)
  Also based on projection of ref
  A. Molodyk and C. Larbalestier, Science, 2023
Iron [Kg/m] | Structure [kg/m] | Coil [kg/m]
4512 | 209 | 121
Iron cost [k€/m] | Structure cost [ k€/m] | Coil cost [k€/m]
36 | 2.1 | 304
Tot. Material k€/m | 56 | 14%
Tot. Assembly k€/m | 40 | 10%
Tot. Conductor k€/m | 304 | 76%
Tot. Cost k€/m | 400 | 
Dipoles of the arc for the series production
(quadrupoles and IR not included)
TOTAL COST: 19.0% O.M.B. (overall magnets budget)
200 k€/magnet ( 2FTE)
Coordination, design and follow-up: 4 FTE x 4 years= 16 FTE-years (1.6 MEur)
Disclaimer: cryostat, specific tooling, W absorber not taken into account
fstruct = 1.5
Tot. Material = (Ciron+ Cstruct)*fstruct
Notes: J=3.5 10^8 A/m2

## Slide 10: Cost Estimate (10TeV)
Iron cost [k€/m] | Structure cost [ k€/m] | Coil cost [k€/m]
75 | 4.3 | 633
Tot. Material k€/m | 116 | 15%
Tot. Assembly k€/m | 42 | 5%
Tot. Conductor k€/m | 632 | 80%
Tot. Cost k€/m | 790 | 
Iron cost [k€/m] | Structure cost [ k€/m] | Coil cost [k€/m]
105 | 6.1 | 888
Tot. Material k€/m | 163 | 15%
Tot. Assembly k€/m | 58 | 5%
Tot. Conductor k€/m | 888 | 80%
Tot. Cost k€/m | 1109 | 
Pre-series
Prototypes
Short Models
Demonstrators
Iron cost [k€/m] | Structure cost [ k€/m] | Coil cost [k€/m]
119 | 7 | 1000
Tot. Structure k€/m | 185 | 15%
Tot. Material k€/m | 183 | 15%
Tot. Assembly k€/m | 66 | 5%
Tot. Conductor k€/m | 1000 | 80%
Tot. Cost k€/m | 1250 | 
Iron cost [k€/m] | Structure cost [ k€/m] | Coil cost [k€/m]
257 | 15 | 2168
Tot. Material k€/m | 397 | 15%
Tot. Assembly k€/m | 143 | 5%
Tot. Conductor k€/m | 2168 | 80%
Tot. Cost k€/m | 2708 | 
N units | length [m] | N years | cost FTE-y [k€] | Total cost [o.m.b*]
90 | 5 | 4 | 1600 | 2.80%
N units | length [m] | N years | cost FTE-y [k€] | Total cost [o.m.b*]
5 | 5 | 5 | 2000 | 0.24%
N units | length [m] | N years | cost FTE-y [k€] | Total cost [o.m.b*]
10 | 1.5 | 8 | 4000 | 0.18%
N units | length [m] | N years | cost FTE-y [k€] | Total cost [o.m.b*]
1 | 1.5 | 6 | 24000 | 0.05%
*overall magnets bugdet

## Slide 11: Tentative Schedule (3 TeV collider)
Models |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Prototypes |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Pre-series |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Series |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041
R&D and
demonstrators
  ARC DIPOLES 11T/150mm
  (quadrupoles and IR still not included)
4 FTE/y, 0.08 ‰ o.m.b.*
5 FTE/y, 0.19‰ o.m.b.*
4 FTE/y, 0.30‰o.m.b.*
4 FTE/y,16.6 ‰ o.m.b.*
4 FTE/y, 4.31 ‰ o.m.b.*
4 years
6 years
4 years
5 years
4 years
TOTAL: 8.67% o.m.b.*
*overall magnets bugdet

## Slide 12: Tentative Schedule (10 TeV collider)
R&D and demonstrators |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Models |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Prototypes |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Pre-series |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Series |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Specifications and concept development
  ARC DIPOLES 15T/150 mm
  (quadrupoles and IR still not included)
4 years
6 years
8 years
4 years
4 years
5 years
2 FTE/y, 0.016‰ o.m.b.*
4 FTE/y, 0.09‰ o.m.b.*
5 FTE/y, 0.22‰ o.m.b.*
4 FTE/y, 0.47‰ o.m.b.*
4 FTE/y, 7.06‰ o.m.b.*
4 FTE/y, 47.5‰ o.m.b.*
TOTAL: 22.3% o.m.b.*
*overall magnets bugdet

## Slide 13: Cost Profile
8
0.8
0.08
0.008
*overall magnets bugdet

## Slide 14: R&D priorities
Our goal: make magnets! Our R&D must be magnet- oriented!
We want to achieve the desired magnetic field and gradient but keeping the stress acceptable and the protection feasible!
How we deal with stress?
  Which concept (block, cos-theta)?
  Which mechanical structure (bladder & key,
  collaring, stress management)?
  Which cable (Roebel, CORC, tape)?
How we protect the magnet?
  Insulated, not insulated, metal insulated?
  At which Top?
DEMOSTRATORS CONSTRUCTION AND TEST of paramount importance to validate design choices!
Not only REBCO! (e.g Iron-based? Xxx?)
R&D on the cable
  Improve reproducibility and uniformity in batch length beyond 1 km
  Optimization of industrial HTS tape mechanical and thermal properties
  Improvement of robustness and reproducibility of cable concept (CORC, ROEBEL)
  Development of novel technique of control of the inter-turn resistance
If we work at 20/30K, can we use indirect cooling or forced gas cooling solutions ?

## Slide 15
Thank you for your attention

## Slide 17: Magnet requirements for Lattice
10TeV collider[ref] - preliminary
Final Focusing
ARC
Several magnet typology needed (dip, quad, combined, etc) , but optimization & definition of requirements still on going
Chromatic correction
Courtesy of Kyriakos Skoufaris