## Slide 1: Status of Recirculating Linacs (RLAs)
Avni Aksoy

## Slide 2: Collider Concept
Short, intense proton bunch
Ionisation cooling of muon in matter
Acceleration to collision energy
Collision
Fully driven by muon lifetime
Protons produce pions which decay into muons, muons are captured
Acceleration
from 0.25 GeV to 63 GeV

## Slide 3: Low Energy Acceleration Complex

## Slide 4: High efficient low cost acceleration for low energy Muons
‘Dogbone’ Recirculating Linear Accelerator is proposed to accelerate beam at low energy (Alex Bogacz)
Single linac is used to accelerate consecutive µ- and µ+ bunches in one RF pulse with many passes
Independent arcs due to large energy variation between passes.

## Slide 5: Beam Parameters along the acceleration chain
Very long bunch after final coolling (375 mm)
  One can use induction linacs in injection. However bunch needs to be compressed at least by factor 10.
10 % emittance growth in the transverse and longitudinal planes, both for 3 and 10 TeV.
  Very tight tolerance with given longitudinal emittance!
Very large energy spread
  Chromatic aberrations even by quadrupoles at low energy
Both longitudinal and transverse emittance has to be preserved
  Quasi-Isochronous arcs are necessary (with flexible momentum compaction)
Consecutive two bunches with opposite charge
  Good matching for both bunches (i.e. round beam at injection/extraction to arcs)
Very high bunch charge
  Minimization of beam loading and wakefield..
Rapid acceleration
...

## Slide 6: Previous study for RLA2

## Slide 7: Choice of RF frequency in linacs
If we have RMS ~ 30 mm Gaussian bunch  200 mm full length
Typically the total bunch length should be < 10% of λRF
To preserve longitudinal emittance lower frequency is preferable but we can use linearizers
Reasonable frequency would be SC 352 MHz cavity (LEP cavity)
200MHz
350MHz
650MHz

## Slide 8: RLA2
Energy gain : 11.6GeV / pass
Total acceleration time ~25 μs
  No RF parameters are possible to change within one RF pulse
Minimum number of pulsed magnets
  Preferred not to use any
5-pass RLA 5-63 GeV
μ+
μ-
μ+
μ-
16.6 GeV
39.8 GeV
28.2 GeV
51.4 GeV
The goal is accelerating two bunches (μ+,μ-) spaced by λRF (n-1/2) from 5 to 63 GeV
FODO type lattice with fixed gradient quadrupoles in linac

## Slide 9: Beam Dynamics in Linac
Large initial energy spread causes emittance growth due to chromatic effects by quadrupoles
We need to use weak quadrupoles to preserve emittance
  Drawback: Sensitive to transverse wakefield effects
W/O linearizer
With linearizer

## Slide 10: Droplet Arcs
Arcs consists of two symmetric sections (-50º and 140º) and total turn is 380º, net turn is 180º
The curvature changes with energy
Large energy acceptance
  we still have large energy spread at the exit of first pass
    σΔp ~ 500 MeV → σΔp/p 3% (16.6 GeV ± 1.2 GeV)
Longitudinal emittance ≤≥ bunch length needs to be preserved/controlled
  Small Momentum compaction factor (R56 ≈ L αc)
We also need small dispersion in bending magnets to preserve transverse emittance
Small betatron oscillation to minimize chromaticity

## Slide 11: Basic arc cell
Different lattice configuration has been studied
  FODO, Triplet. TME : The sign of R56 is fixed. Control of bunch length can be done only with RF.
DB(A)-lattice allows to control R56 with quadrupole strength as well as the chromaticity (Flexible Momentum compaction)
Basic cell for arcs
Bending angle/cell =10o
Bmax =7T
Aperture =50mm

## Slide 12: Arc Lattices
40o bending section of first arc
Dispersion is suppressed with half bending angle
Sextupoles are optimized with second order optics.
Dispersion suppression and matching
Basic cell

## Slide 13: Beam dynamics in arcs
Start to end simulation in first arc (tracking)
Extraction
40o bending
Straight section
140o bending
By-pass section
µ-
µ+

## Slide 14: Start to end RLA2
1st pass
1st arc
5th pass
4th arc
….
2nd pass

## Slide 15: Start to end simulation for RLA2

## Slide 16: New DBA Lattice for Arcs
Strong high order effects due to large energy spread
Nonlinear optimization based on tracking to minimize higher terms (dispersion + chromaticity + ..)
  Thanks to Andrea
Emittance evaluation for 360o turn

## Slide 17: Injector study

## Slide 18: Low Energy Acceleration Layout
In order to use more realistic particle distribution in RLAs we focused on injector.
Expected beam parameters from final cooling channel
EK = 255 MeV
εz = 0.0225 eVs
σz = 400 mm
εx,y = 20 mm.mrad

## Slide 19: Initial beam distribution
Parameter | Unit | Value
Initial beam energy | MeV | 255
Final beam energy | GeV | 1.5
Initial bunch charge | nC | 650
Transverse emittance | μm.rad | 20
Longitudinal emittance | eVs (m.MeV) | 0.0255 (6.75)
Initial RMS (full) bunch length | mm | 400 (~1800)
Final RMS bunch length | mm | < 30
Final energy spread | % | <10
Very long bunch needs to use “very” low frequency
Maximum transmission
  Rapid acceleration
...

## Slide 20: Considerations
Accelerator frequencies in RLA1 and RLA2 is 352 MHz  We can use sub-harmonic frequencies i.e. 88 MHz and 176 MHz as well as 352 MHz
Low initial energy  We can use solenoids up to a reasonable beam energy
Bunch compression
  Velocity compression, magnetic compression
Very high bunch charge
  Relatively large beam when the beam has low energy
High transmission requirement
  Avoid beam loss (minimize tails) and minimize long drifts…
…

## Slide 21: Frequency choice
The bunch length 1800 mm requires more than 88 MHz
  For RF @88MHz the length of Δφ =±90 deg is ~ 1.7 m
  Lower is preferable but 44 MHz would have very low gradient??
Instead of using single frequency one can use combination of frequencies to control longitudinal emittance and force bunch synchrotron motion in RF bucket

## Slide 22: RF cavities
G. Arnolds-Mayer et.al. 'RADIO FREQUENCY SUPERCONDUCTIVITY AT CERN: A STATUS REPORT', The Third Workshop on RF Superconductivity, Argonne National Laboratory, Illinois, USA
C. Rossi, et.al. "HIGH GRADIENT TESTS OF AN 88 MHZ RF CAVITY FOR MUON COOLING" , Proceedings of EPAC 2006, Edinburgh, Scotland
The 176 MHz also assumed to be single cell with same length of 88 MHz
The gradients
  15 MV/m for 352 MHz
  9 MV/m for 176 MHz
  5 MV/m for 88 MHz
88 and 176 MHz
352MHz

## Slide 23: Injector simulations
Different frequencies are distributed along beamline
Magnetic bunch compressor is also used
Solenoid focusing
88 MHz & 176 MHz
Magnetic
Compressor
FODO focusing
88,176 & 352MHz

## Slide 24: Injector simulations
Very low average acceleration due to manipulation of the phase space
>90% muon survival

## Slide 25: Injector simulations
Achieved bunch length : 40 mm
Longitudinal emittance is more less preserved

## Slide 26: Conclusion
In addition to improve arc lattice we focused on injector simulation to find out a “realistic” bunch distribution at the entrance of first RLA
  First iteration has been performed.
Due to long bunch length we started with 88 MHz acceleration frequency and used combination of higher frequencies.
The final bunch length and longitudinal emittance is still beyond acceptance of 352 MHz cavity
  ~ 20 % higher than we need in terms of bunch length..
Due to acceleration about zero-cross we have very low effective acceleration in the injector which causes low transmission.
  ~1.25 MeV/m
Relaxing longitudinal emittance (i.e. 10-20%) would increase the performance of injector significantly
  Better transmission, shorter machine etc..
We will continue optimization until we reach target beam parameters.

## Slide 27: Thank you for your attention.