Investigating Eddy Current Effects within the RCS Vacuum Chamber
Erik Kvikne
David Amorim, Fabian Batsch, Fulvio Boattini, Heiko Damerau, Marco Gast, Elias Metral, Leonard Sebastian Thiele
IMCC and MuCol Annual Meeting 2024
14-03-2024

---
Eddy Currents & Motivation
- Rapid changes in the magnetic field strength of the RCS NC magnet will induce significant Eddy currents within a metallic vacuum chamber.
- The dissipated power due to these currents scales with the ramp rate squared.
- The objective of this work is to get a first order estimation of the loss using analytical formulas.
- The losses puts restrictions on chamber material and geometry which is important for the beam coupling impedance study.
(Tentative Parameter list for the IMCC)
[Speaker Notes: Eddy currents are generated in conducting materials when we have a rapid change in the magnetic field The power lost due to these eddy currents scale with the square of the ramp rate, which is worrying for the accelerator chain as the ramp rates go as high as 4200. We therefore wanted to try and estimate the power loss and temperature increase in the vacuum chamber by using analytical formulas.]

---
The simplest case: Thin plate
The formula for the ohmic loss per unit length in a rectangular thin plate due to Eddy currents can be derived analytically:
The following conditions must be fulfilled:
– B field vertical to the plate, with constant ramp rate.
– Plate magnetically thin: a << penetration depth δ.
– Plate geometrically thin: d << a
– Plate long enough to neglect the ends: a,d << L
– Steady-state conditions.
P/L: Ohmic loss per unit length
d: Plate thickness
a: Plate width
σ: Electrical conductivity
B: Magnetic field
(G. Moritz)
d
a

---
Rectangular Vacuum Chamber
The ohmic loss per unit length due to Eddy currents in a rectangular vacuum chamber is:
(A. Lachaize)
P/L: Ohmic loss per unit length
d: Wall thickness
a: Chamber width
b: Chamber height
σ: Electrical conductivity
B: Magnetic field
b
d
a
[Speaker Notes: I started off by investigating a vacuum chamber with a rectangular cross section. By assuming a uniform magnetic field we have this simple formula for the power loss per unit length. Note that we see that it scales with the square of the ramp rate and has a term that scales with the width to the third power, as well as linearly with the chambers conductivity and thickness Assume uniform magnetic field.]

---
Stainless Steel Rectangular Vacuum Chamber
Stainless steel vacuum chamber:
- Conductivity: 1.1 × 106 S/m
- Height and width: 30X100mm*
- Thickness: 0.3mm
30 mm
0.3 mm
100 mm
Power loss in the MW/m range
*(Tentative Parameter list for the IMCC)
[Speaker Notes: To get an approximation of the power loss I assumed a … Plotting the power loss as a function of the ramp rate we can see that the loss is of the order mega watts per meter. The highest one being the RCS1 with 7.44 MW/m.]

---
Electromagnetic Simulation
- Uncertainties arise regarding the analytical formula's applicability due to the rapid ramp rates of the RCS.
- Ansys Maxwell2D was used to validate the analytical formula by comparing with electromagnetic simulations for conditions similar to the ones of the RCS.
- In these simulations a uniform magnetic field is created between two large conducting plates, excited by an alternating current with frequency f. The field strength at any point is approximately given by:

---
Electromagnetic Simulation
The Ansys Eddy current solver computes the time averaged ohmic loss. In order to compare simulated results with our analytical formula we need to calculate the time average.
Thin plate:
d: Thickness
a: Width
b: Height (Rectangular beam pipe only)
σ: Electrical conductivity
B0: Magnetic field amplitude
f: B field’s frequency of oscillation
Rectangular beam pipe:

---
Stainless Steel thin plate
Stainless steel plate:
- Conductivity: 1.1 × 106 S/m
- Width: 100mm
- Thickness: 0.3mm
Simulation result is less than 0.2% smaller than analytical
100 mm
0.3 mm
[Speaker Notes: To get an approximation of the power loss I assumed a … Plotting the power loss as a function of the ramp rate we can see that the loss is of the order mega watts per meter. The highest one being the RCS1 with 7.44 MW/m.]

---
Stainless Steel Rectangular Vacuum Chamber
Stainless steel:
- Conductivity: 1.1 × 106 S/m
- Height and width: 30X100mm*
- Thickness: 0.3mm
30 mm
0.3 mm
100 mm
*(Tentative Parameter list for the IMCC)
Simulation result is 22% larger than analytical
[Speaker Notes: To get an approximation of the power loss I assumed a … Plotting the power loss as a function of the ramp rate we can see that the loss is of the order mega watts per meter. The highest one being the RCS1 with 7.44 MW/m.]

---
Energy loss
The energy loss per cycle can be estimated by using the ramp time (Tramp) from the tentative parameters list.
RCS:	2	3	4
Tramp [ms]	1.1	2.37	6.37
And by assuming the magnetic field of one cycle can be modeled as a sine wave with a period of 2Tramp.
Energy loss per cycle rectangular beam pipe:
RCS:	2	3	4
Energy loss [J/cycle/m]	2462	1143	425
Where Q is the energy loss per cycle in the rectangular vacuum chamber due to Eddy currents.

---
Energy loss
The energy loss per cycle can be estimated by using the ramp time (Tramp) from the tentative parameters list.
RCS:	2	3	4
Tramp [ms]	1.1	2.37	6.37
And by assuming the magnetic field of one cycle can be modeled as a sine wave with a period of 2Tramp.
Energy loss per cycle rectangular beam pipe:
RCS:	2	3	4
Energy loss [J/cycle/m]	2462	1143	425
Larger than total energy loss of magnet! (F. Boattini, M. Gast)
A continuous conducting beam pipe will cause too large losses.
Where Q is the energy loss per cycle in the rectangular vacuum chamber due to Eddy currents.

---
Reducing Eddy Current Losses
A vacuum chamber made of a material with low conductivity, like ceramic (σ ~10-12 S/m), would eliminate the problem of Eddy currents.
But RF shield is necessary to keep the chamber impedance low.
Since the losses within a plate is proportional to the cube of its width, we can significantly reduce the losses by segmenting the beam pipe into thin parallel strips.

---
Longitudinal striped design
Instantaneous:
(The proton driver design study, 2000)
Time averaged:
w: Stripe width
d: stripe thickness
NH: Number of horizontal stripes (top + bottom)
NV: Number of vertical stripes (left + right)
σ: Electrical conductivity
Instantaneous:
B: Magnetic field strength
Time averaged:
B0: Magnetic field amplitude
f: B field’s frequency of oscillation
[Speaker Notes: Only the metal necessary for the shielding is kept inside the magnet, the rest (“vacuum skin”) is moved outside]

---
Longitudinal striped design
Instantaneous:
(The proton driver design study, 2000)
Time averaged:
w: Stripe width
d: stripe thickness
NH: Number of horizontal stripes (top + bottom)
NV: Number of vertical stripes (left + right)
σ: Electrical conductivity
Instantaneous:
B: Magnetic field strength
Time averaged:
B0: Magnetic field amplitude
f: B field’s frequency of oscillation
[Speaker Notes: Only the metal necessary for the shielding is kept inside the magnet, the rest (“vacuum skin”) is moved outside]

---
Longitudinal striped design
Instantaneous:
(The proton driver design study, 2000)
Time averaged:
w: Stripe width
d: stripe thickness
NH: Number of horizontal stripes (top + bottom)
NV: Number of vertical stripes (left + right)
σ: Electrical conductivity
Instantaneous:
B: Magnetic field strength
Time averaged:
B0: Magnetic field amplitude
f: B field’s frequency of oscillation
[Speaker Notes: Only the metal necessary for the shielding is kept inside the magnet, the rest (“vacuum skin”) is moved outside]

---
Longitudinal striped design
Instantaneous:
NH/2
(The proton driver design study, 2000)
Time averaged:
w
Nv/2
w: Stripe width
d: stripe thickness
NH: Number of horizontal stripes (top + bottom)
NV: Number of vertical stripes (left + right)
σ: Electrical conductivity
Instantaneous:
B: Magnetic field strength
Time averaged:
B0: Magnetic field amplitude
f: B field’s frequency of oscillation
Nv/2
NH/2
[Speaker Notes: Only the metal necessary for the shielding is kept inside the magnet, the rest (“vacuum skin”) is moved outside]

---
Longitudinal striped design
By changing to a striped design, while keeping the thickness unchanged, we see a reduction of ohmic loss of 2-3 orders of magnitude depending on the width of the stripes.
This assumes the parallel stripes to be touching. In reality we would have some spacing between them. This will in turn reduce the number of stripes and thus the ohmic loss further.

---
Energy loss
Energy loss per cycle for the longitudinally striped design:
	RCS:	2	3	4
10 mm stripe width	Energy loss [J/cycle/m]	16.01	7.43	2.76
5 mm stripe width	Energy loss [J/cycle/m]	4.01	1.86	0.69
2 mm stripe width	Energy loss [J/cycle/m]	0.65	0.30	0.11
Energy loss per cycle for rectangular beam pipe:
RCS:	2	3	4
Energy loss [J/cycle/m]	2462	1143	425

---
Example from J-PARC
(Michikazu Kinsho, 2005)

---
Full magnet under vacuum
Dipole magnet
Metallic stripes
Vacuum skin
Insulating substrate
- Only the necessary amount of metal for shielding is placed inside the magnet.
- “Vacuum skin” moved outside of magnet
(The proton driver design study, 2000)

---
Conclusion and next step
- Large metallic surfaces in the RCS vacuum chamber leads to unacceptable Eddy current losses.
- By using a ceramic vacuum chamber with a RF shield consisting of thin longitudinal stripes on the outside we can reduce the Eddy current losses significantly.
- Next steps:
  - Look into the feasibility of a ceramic design from a vacuum perspective.
  - Further investigate the beam coupling impedance of a ceramic beam pipe with longitudinal conducting stripes on the outer surface.

---
Thank you for your attention!

---
Backup

---
Overview of the magnet (dipole) model: Losses calculation
(F. Boattini, M. Gast)

---
Analytical vs simulation loss with ratio
Thin plate:
Rectangular beam pipe:

---
Elliptical Vacuum Chamber
(Xu & Wang, 2012)
b
a
- B is the magnetic field
- a is the chamber half-width
- b is the chamber half-height
- σ is the chamber’s electrical conductivity
- d is the chamber thickness
d
[Speaker Notes: I started off by investigating a vacuum chamber with a rectangular cross section. By assuming a uniform magnetic field we have this simple formula for the power loss per unit length. Note that we see that it scales with the square of the ramp rate and has a term that scales with the width to the third power, as well as linearly with the chambers conductivity and thickness]