## Slide 1: A preliminary design of a 704 MHz cavity and related power coupler for the MC demonstrator
Juliette Plouin
CEA Paris-Saclay
On behalf of D. Giove, D. Sertore, M.R. Masullo INFN Milano-LASA and Napoli
Guillaume Ferrand, Claude Marchand, Juliette Plouin
CEA-Saclay
IMCC Meeting 12-15 march 2024

## Slide 2: RF cavities for muon cooling cells
Real estate gradient is 22 MV/m
Average on the whole cell
Half of the length is not for RF
Carmelo Barbagallo,

## Slide 3

Vacuum model simulated in CST according to the beam dynamics specification given by
Chris Rogers.
Transit time factor is 0.83
Enom = 44 MV/m means
Eacc = 36.44 MV/m

## Slide 4: Pill box type cavity simulated by INFN
In the last weeks at INFN we developed few tools (Ansys and CST based) to carry out the design of a 704 MHz cavity for the first proposal of a cooling channel for the MC demonstrator. This work has been dictated by the requirement to provide a contribution to the overall analysis of the congruence of the BD requirements vs the technological constrains due to this kind of cavities.
It has been used to verify our tools with a positive result.
D. Giove, D. Sertore, M.R. Masullo INFN Milano-LASA and Napoli
Window radius Rw = 60 mm
Cavity in copper
Without beryllium window
Field on axis
2/3 x Emax at the iris
Emax

## Slide 5: Pill-box type cavity simulated by CEA
beryllium
copper
 | 2D with losses | 3D w/o losses | Carmelo
Frequency (MHz) | 702,72 | 702,72 | 704
beta | 0,884 | 0,884 | 0,884
Transit time factor | 0,83 | 0,83 | 
shunt impedance (Ω) | 157,87 | 157,85 | 159,32
quality factor | 20262 | Inf | 20200
Emax/Eacc | 1,21 | 1,53 | 
Emax @36,44 MV/m | 44,1 | 55,8 | 44,22
Bmax/Bacc (mT/MV/m) | 3,06 | 3,07 | 
Bmax @36,44 MV/m | 111 | 111 | 110,63
2D with losses
3D w/o losses
Window radius Rw = 120 mm

## Slide 6: External coupling
External coupling calculation
(2 ports for S-parameters calculations)
WR975
= 605 MHz
WG 50/100 mm = 1.5 GHz
is the power
from/to outside
is the stored energy

## Slide 7: Qext calculations
Chart: Frequency (Hz)
Chart: Frequency (Hz)
BW = 800 kHz
= 864
L =10 mm
BW = 2.6 kHz
= 2.65 105
L =100 mm

## Slide 8: A study for a preliminary “nose” version of a cavity @ 704 MHz
D. Giove, D. Sertore, M.R. Masullo INFN Milano-LASA and Napoli
beta=0,884 |  |  | 
f | 704.06 | MHz | gap=60mm
Q | 21394 |  | height=153 mm
Rsh/Q | 127.15 | Ohm | bore radius= 50 mm
Rsh | 2.72 | MOhm/m | length=125 mm with two piece of pipes
Ratio Emax/E0 axis | 1.86 |  | 
1/2 x Emax at the iris
Emax

## Slide 9: Cavity implementation in the cooling cell
1 m
0.125 x 4 =0.5 m
Chris Rogers,
WP8 Meeting #16
05/03/2024
Epeak = 44 MV/m

## Slide 10: Cavity implementation in the cooling cell
1 m
0.125 x 3 ~ 0.4 m
Chris Rogers,
WP8 Meeting #16
05/03/2024
Epeak = 55 MV/m

## Slide 11: Magnetic field on cavity
Normal conducting cavities
Short RF pulses (~𝜇𝑠)
High acceleration gradients (~30 MV/m)
High magnetic solenoidal field (up to14 T)
Creates problematics of break-down that needs to be mitigated
See talk from Claude Marchand

## Slide 12: Cavity shape must minimize electron emission risks
Electrons are emitted by the high E field area of surface 1 … and hit the high E field area of surface 2
min
max
surface 1
surface 1
surface 1
surface 2
surface 2
surface 2
Electrons are emitted by the high E field area of surface 1 … and do not hit the high E field area of surface 2

## Slide 13: Calculations of electron emission in presence of an RF field with CST particle studio
100 mm
200 mm
300 mm
Very simple cavity model at 900 MHz

## Slide 14: Emission of a DC current
10 mm
Face 1 (emission)
Face 2
Face 1 (emission)
Face 2

## Slide 15: Oscillation of the electrons in the RF field
The number of electrons arriving on Face 2 depends on RF field pattern
Face 1 (emission)
Face 2
Some electrons never hit Face 2

## Slide 16: RF engineer position @ CEA-Saclay see MuCol website