## Slide 1: Funded by the European Union (EU). Views and opinions expressed are however those of the author only and do not necessarily reflect those of the EU or European Research Executive Agency (REA). Neither the EU nor the REA can be held responsible for them.
Carmelo Barbagallo, Alexej Grudiev
IMCC and MuCol Annual Meeting 2024
12-15 March 2024, CERN
704 MHz cavity studies for the Muon Cooling Demonstrator

## Slide 2: Outline
Introduction
  Motivation of the study
Eigenmode RF simulations in CST Studio Suite®
  704 MHz pillbox cavity
  704 MHz cavity for the Muon Cooling Demonstrator
RF-thermo-mechanical simulations in COMSOL Multiphysics®
  Coupled RF-thermo-mechanical studies on the cavity
  Lorentz Force Detuning (LFD) analysis
Conclusions and Perspectives

## Slide 3: Motivation of the study
Build a conceptual RF design and Multiphysics numerical model of a 704 MHz pillbox-type cavity for the Muon Cooling Demonstrator
Normal conducting cavities
MHz
Short RF pulses ()
High peak accelerating gradient ()
High peak solenoid field (up to 14 T)
Preliminary Cooling Cell Concept
Solenoid + Dipole
RF cavities
Absorber
2 m
Chris Rogers

## Slide 4: 704 MHz Pillbox cavity
Vacuum model simulated in CST according to the beam dynamics specification given by Chris Rogers.
Lcav
Rcav
E-field
H-field
Parameter | Unit | Pillbox - Cu | Description
f0 | [MHz] | 704 | Operating frequency
Lcav | [mm] | 125 | Cavity length
Rcav | [mm] | 163.10 | Cavity radius
Enom | [MV/m] | 44 | Average Nominal gradient
Vnom | [MV] | 5.50 | Nominal voltage
β | [-] | 0.884 | Relativistic beta
TTF | [-] | 0.83 | Transit-time factor
Vacc | [MV] | 4.56 | Accelerating voltage
Eacc | [MV/m] | 36.44 | Accelerating gradient
Nominal and accelerating voltage
with
Transit-Time factor
Beam dynamics specifications

## Slide 5: 704 MHz Pillbox cavity – Pulse shape and power dissipation
The voltage profile was calculated for a short beam pulse, considering the coupling factor βc=1.2
The average power dissipation was computed from the obtained duty factor (DF)
Parameter | Unit | Pillbox Cu | Description
f0 | [MHz] | 704 | Operating frequency
Q0 | [-] | 2.84e+04 | Intrinsic quality factor
*R/Q | [Ω] | 194.73 | Geometric shunt impedance
R/Q·Q0 | [MΩ] | 5.53 | Shunt impedance (σCu = 5.8e+07 S/m)
Pdiss | [MW] | 3.75 | Peak power dissipated on the cavity walls
βc | [-] | 1.2 | Coupling factor
 | [us] | 14.51 | Total filling time
 | [-] | 5.49e-05 | Beam duty factor (frep = 5 Hz)
 | [W] | 206.41 | Average power
Parameter | Unit | Pillbox Cu | Description
f0 | [MHz] | 704 | Operating frequency
Q0 | [-] | 2.84e+04 | Intrinsic quality factor
*R/Q | [Ω] | 194.73 | Geometric shunt impedance
R/Q·Q0 | [MΩ] | 5.53 | Shunt impedance (σCu = 5.8e+07 S/m)
Pdiss | [MW] | 3.75 | Peak power dissipated on the cavity walls
βc | [-] | 1.2 | Coupling factor
 | [us] | 14.51 | Total filling time
 | [-] | 5.49e-05 | Beam duty factor (frep = 5 Hz)
 | [W] | 206.41 | Average power
Duty factor
Filling time and injection time
Bunch train

## Slide 6: 704 MHz Pillbox cavity – Pulse shape and βc dependency
Voltage and power profiles for different coupling factor βc. Higher βc means lower filling time tf
Higher βc means lower average power Pave and duty factor DF for the cavity
Parameter | Unit | Pillbox - Cu | Description
Vnom | [MV] | 5.50 | Nominal voltage
βc | [-] | 1.2 | Coupling factor
tf | [us] | 14.51 | Total filling time
Pdiss | [MW] | 3.75 | Peak power dissipated on the cavity walls
 | [W] | 206.41 | Average power
 | [-] | 5.49e-05 | Beam duty factor (frep = 5 Hz)
Parameter | Unit | Pillbox - Cu | Description
Vnom | [MV] | 5.50 | Nominal voltage
βc | [-] | 1.2 | Coupling factor
tf | [us] | 14.51 | Total filling time
Pdiss | [MW] | 3.75 | Peak power dissipated on the cavity walls
 | [W] | 206.41 | Average power
 | [-] | 5.49e-05 | Beam duty factor (frep = 5 Hz)
Notes: Higher beta means lower filling time, but also lower average power and duty factor

## Slide 7: Power from the generator - 704 MHz Pillbox cavity
For higher βc (lower filling time), more power is required from the generator to fill the cavity faster
Power required from the generator
Generator Duty Factor
βc=1.2 is a reasonable compromise between average dissipated power and power required from the generator.
Parameter | Unit | Pillbox - Cu | Description
Pg | [MW] | 4.5 | Generator power
βc | [-] | 1.2 | Coupling factor
Pg,ave | [W] | 329 | Average generator power
g | [-] | 4.38e-05 | Beam duty factor (frep = 5 Hz)
Parameter | Unit | Pillbox - Cu | Description
Pg | [MW] | 4.5 | Generator power
βc | [-] | 1.2 | Coupling factor
Pg,ave | [W] | 329 | Average generator power
 | [-] | 4.38e-05 | Beam duty factor (frep = 5 Hz)
Notes: From the other hand

## Slide 8: 704 MHz cavity for the Muon Cooling Demonstrator
Proposed design: 704 MHz cavity with circular profile on the high-magnetic field region and elliptical profile on the iris to lower the local surface field.
Be window
Vacuum
Copper
RF cavity
Lacc
Ri
Rcav
Rc
Rv
tw
Be window
a
b
Beryllium (Be) window:
  60 mm (3σbeam) radius
  60 um thickness (tw) (very thin to minimize the beam scattering)
Why do we need a cavity with closed apertures?
Pros
  Cavity design close to pillbox
  Preserve the E-field on axis
  Maximize the geometrical shunt impedance
Cons
  High mechanical deformations under Lorentz Force leading to cavity frequency detuning
  Risk of cavity contamination in case of rupture under fatigue

## Slide 9: 704 MHz cavity for the Muon Cooling (MC) Demonstrator
Parameter | Unit | Pillbox Cu | MC cavity | Description
Rcav | [mm] | - | 195.06 | Cavity radius
Rv | [mm] | 163.10 | 177.33 | Vacuum radius
Ri | [mm] | - | 60 | Iris radius
Lacc | [mm] | 125 | 125 | Accelerating length
Rc | [mm] | - | 57.5 | Radius of the circular profile
a | [mm] | - | 5 | Minor semi-axis of iris ellipse
b | [mm] | - | 11 | Major semi-axis of iris ellipse
Rw | [mm] | - | 60 | Window radius
tw | [um] | - | 60 | Window thickness
Parameter | Unit | Pillbox Cu | MC cavity | Description
f0 | [MHz] | 704 | 704 | Operating frequency
Q0 | [-] | 2.84e+04 | 2.98e+04 | Intrinsic Quality Factor
R/Q | [Ω] | 194.73 | 179.53 | Geometric shunt impedance
R/Q·Q0 | [MΩ] | 5.53 | 5.36 | Shunt impedance
Pdiss | [MW] | 3.75 | 3.89 | Peak dissipated power
 | [-] | 5.49e-05 | 5.77e-05 | Beam duty factor
Pave | [W] | 206.41 | 224.50 | Average power
Epeak | [MV/m] | 44.00 | 45.19 | Peak surface electric field
Bpeak | [mT] | 85.46 | 92.94 | Peak surface magnetic flux density
Parameter | Unit | Pillbox Cu | MC cavity | Description
f0 | [MHz] | 704 | 704 | Operating frequency
Q0 | [-] | 2.84e+04 | 2.98e+04 | Intrinsic Quality Factor
R/Q | [Ω] | 194.73 | 179.53 | Geometric shunt impedance
R/Q·Q0 | [MΩ] | 5.53 | 5.36 | Shunt impedance
Pdiss | [MW] | 3.75 | 3.89 | Peak dissipated power
 | [-] | 5.49e-05 | 5.77e-05 | Beam duty factor
Pave | [W] | 206.41 | 224.50 | Average power
Epeak | [MV/m] | 44.00 | 45.19 | Peak surface electric field
Bpeak | [mT] | 85.46 | 92.94 | Peak surface magnetic flux density
Geometrical parameters
RF figures of merit
Similar performance to the ideal pillbox
R/Q is 7% lower than pillbox
Pave 8% higher than pillbox
Epeak 2.6% higher and Bpeak 8% higher than pillbox
Notes: Update duty factor based on the recent calculations

## Slide 10: Peak E and H fields on the cavity
Maximum E-field is localized on the cavity iris, while maximum H-field on the upper part of the cavity
Peak E-field needs to be minimized to reduce the risk of RF-breakdown
Peak H-field needs to be reduced for the RF-heating
E-field
H-field

## Slide 11: RF-thermo-mechanical simulations
Thermal expansion
(upper walls)
with
Power losses (Heat source on lossy walls)
2nd RF Eigenmode
RF eigenmode
PMC (symmetry planes)
Lossy walls
Stationary thermal simulation
Non-linear thermo-mechanical simulation
Displacement field
Spatial mesh displacement
On symmetry planes
Roller condition

## Slide 12: Power loss and Temperature Gradient
at
Power loss on the cavity walls [kW/m2]
Power loss on the windows [W/m2]
Average power losses
Pdiss,ave,walls=217.94 W
Pdiss,ave,Windows=2.33 W
Temperature gradient
Temperature [K]
Tmax=313 K
Tc=300 K
ΔT = 13 K
at

## Slide 13: Thermal stress, displacement and frequency shift
von Mises Stress vs Yield strength
von Mises Stress on the cavity walls [MPa]
MAX
von Mises Stress on the windows [MPa]
Thermally induced total displacement
The frequency shift is lower than the 3 dB bandwidth.
Thermally-induced frequency shift
Total displacement [um]
No plastic deformations, good safety margin to failure.

## Slide 14: Lorentz Force Detuning (LFD) - RF-mechanical simulations
RF field pressure (Boundary load walls)
2nd RF Eigenmode
RF eigenmode
PMC (symmetry planes)
Lossy walls
Non-linear mechanical simulation
Displacement field
Spatial mesh displacement
On symmetry planes
Roller condition

## Slide 15: Lorentz Force Detuning: RF field pressure and stress
Radiation pressure on the cavity walls [mbar]
Radiation pressure on the windows [mbar]
RF field pressure
(Compression)
(Traction)
Significant pressure on the 60 mm thick windows
(Compression)
(Traction)
von Mises Stress vs Yield strength
No plastic deformations. Only factor two margin in the interconnection between the window and the cavity (risk of failure under fatigue)

## Slide 16: Preliminary results: LFD on the cavity walls and Be windows
Total displacement
Frequency shift
at
The frequency shift is higher than the 3 dB bandwidth. This is principally due to the large deformation and displacement detected at the Be windows. A new stiffer design for the Be windows must be addressed.
The implemented LFD model is based on the Slater theorem, which is valid only for small deformation.
The used linear elastic assumption is typically valid within the 2-3% of deformations. Even the model includes geometric non-linearity, the assumption that a purely elastic material can undergo arbitrary large deformations may not be entirely valid.
Lorentz Force-induced total displacement [mm]
Deformed geometry (x20)
3dB bandwidth
max 0.988 mm

## Slide 17: Conclusions and Perspectives
A conceptual RF design and Multiphysics model of a copper 704 MHz cavity operating at 44 MV/m for the Muon Cooling Demonstrator was built based on beam dynamics specification.
RF figures of merit were computed for a design including Be windows, having 60 mm radius and 60 u thickness. The design show similar performance to the ideal pillbox.
RF thermo-mechanical and Lorentz Force Detuning simulations:
  Most of the power is dissipated on the Cu cavity walls (217.94 W), while 2.33 W are dissipated on the Be windows. The maximum temperature of 313 K is reached on the window under ideal cooling condition (Tc = 300 K).
  The maximum thermally-induced total displacement is 28.9 μm on the Be window. The von Mises stress is lower than the yield stress for both materials (no risk of rupture). The thermally-induced frequency shift is 39.77 kHz, which is lower than the cavity bandwidth.
  A significant RF field pressure of ranging from -41.2 mbar to 5.2 mbar was detected on the Be window.
  The von Mises stress is lower than the yield stress for both materials. However, only factor two margin for the Be window (risk of failure under fatigue)
  The maximum total displacement induced by Lorentz forces is 0.988 mm on the Be window, which induces a frequency shift of 0.94 MHz, which is higher than the bandwidth.
Larger Be window and mechanical deformations need to be addressed. The implementation of a more accurate numerical model for simulating Lorentz Forces in the large deformation regime might be necessary.

## Slide 18
Thank you
for your attention

## Slide 19
Additional studies

## Slide 20: Maximum displacement on a thin and flexible membrane
Roark's Formulas for Stress and Strain for a thin flexible circular membrane
Deflection y (mm) (verify that )
S = maximum allowed stress (MPa)
Stress (MPa) (verify that )
r = membrane radius (mm)
p = applied pressure (MPa)
E = Young’s modulus (MPa)
t = thickness (mm)
(Fermilab)

## Slide 21: Maximum displacement on a thin and rigid membrane
Roark's Formulas for Stress and Strain for a thin rigid circular membrane
Deflection y (mm) (verify that )
Stress (MPa) (verify that at the edge)
= Poisson’s ratio
with
with
at the center
at the border

## Slide 22: Maximum displacement on a thin and flexible membrane
Roark's Formulas for Stress and Strain for a thin flexible circular membrane
The found deflection in the simplified model is roughly the same of the one found in the cavity window.
r = 60 mm (membrane radius)
p = 4.21e-03 MPa (applied pressure)
E = 303 GPa (Young’s modulus)
t = 0.06 mm (membrane thickness)
(under uniform pressure p)
1.06 mm (linear elastic model under uniform pressure p)
Deflection y (mm) (verify that )