## Slide 1
High Efficiency Klystrons for MuCol
G. Burt for HE project team at CERN & Lancaster:
Igor Syratchev
Nuria Catalan
Zain Un Nisa
Anis Baig

## Slide 2
The klystron is a key element of almost all particle accelerators.
LHC
LHC
FCCee
CLIC, Muon_C
ILC
DESY
PSI
SACLA
SLAC
CLIC’k
SLAC-BF
Industrial/Medical
PAL
e-rings
injectors
IOT
single beam
SSA tower
Magnetron
(oscillator)
Frequency, GHz
Peak power, MW
electron & proton rings
SC e/p Linacs
electron Linacs
high intensity
high gradient
Klystrons
Pulsed
Continuous Wave
MBK
FNAL
Tetrode
KEK
NLC
J-PARC
ESS
CEPC
HE klystrons at CERN
Beam diagnostic,
X-FEL
High Efficiency klystrons project at CERN is targeted to improve efficiency and performance of these devices for various applications.
In fabrication
DEFT
Ultimate limit
Muon Collider

## Slide 3
A. Grudiev MC RF WG meeting #9:
March 22

## Slide 4: What is available now at MC frequencies?
ESS have
2.9 MW klystrons at 352 MHz (see below)
1.5 MW klystrons at 704 MHz CPI VKP-8292A and Canon E37504 (would need two per cavity)

## Slide 5: Muon cooling demonstrator layout High peak power klystron: 24 MW
RF for cooling: Max. gradient 30 MV/m
32m
RF for 144 cavities at
~30 MV/m
30mx14m
18 RF stations
14m
Building -> Gallery :
(underground might be possible)
30m x 15m
Height: 8-10 m
modulator
klystron
24MW
cavity
WG
WG distribution with phase adjustment to feed 2 x 4 cavities
cavity
cavity
cavity
cavity
cavity
cavity
cavity
WG
A. Grudiev and R. Losito
MC RF WG meeting #5: Sept 21

## Slide 6: Existing tubes
While tubes >24 MW exist they are all above 3 GHz
There are 10-20 MW tubes developed for CLIC drive beam and ILC at 1-1.3 GHz
Nothing of this power exists at 325 or 650 MHz
Issue is typically that to get high power means high voltage which makes the tubes longer
For scaling at low frequency this used to not be feasible as length is inversely proportional to frequency for constant beam
New developments may change that……..
Chart: frequency (GHz)
| 0.32500000000000001 | 0.65
MuCol requirements | 24 | 24
Developmental | 0.35 | 1.2 | 10 | 10 | 50 | 50 | 0 | 0.5 | 0.4 | 0.5 | 0.4 | 25 | 50 | 25 | 20

## Slide 7
Canon E37503
Thales TH1803
High power L-band Multi Beam Klystrons (MBK). Commercial tubes.
Frequency: 1.0 GHz
Peak RF power: 20 MW
Efficiency: 70%
Frequency: 1.3 GHz
Peak RF power: 10 MW
Efficiency: 65%
Thales TH1801
Toshiba E3736
CPI VKL-8301

## Slide 8: Collector
A large chunk of a klystron’s length is the collector
In DC mode the collector must absorb the entire beam power, and dissipate the heat load without heating up too much
The Canon E37503 had a max heat load of 300 kW and was 1.5m long (ie half the tubes length)
The DC heat load for the muon collider klystron is sub-5 kW and hence a much shorter collector can be used (30 cm may be fine).

## Slide 9: Scaling Klystrons (PSP)
Key numbers in klystron scaling is the electron wavelength, Beta, and the bunching parameter, A,
If we scale a klystrons voltage, current, or frequency certain relationships need be maintained
In our case scaling from 1 GHz to 350 MHz, while keeping A constant would mean the length increases by a factor of 3

## Slide 10
F= 999,5 MHz
P max= 20.2 MW
T = 150 µsec
V= 159.4 kV
I total = 180 A
Eff.= 70.5 %
uP= 0.47 µAxV-3/2/beam
Gain = 53.9 dB
P average (50Hz)= 150kW
Scaling the Canon tube to 0.7GHz, 24MW and 30 µsec.
Canon E37503
6 beams MBK
F= 700 MHz
P max= 24 MW
T = 30 µsec
V= 171 kV
I total = 200 A
Eff.= 70.0 %
uP= 0.47 µAxV-3/2/beam
Gain = 53.9 dB
P average (5Hz) = 3.6kW
Mu-tube, 0.7 GHz
6 beams MBK
‘Quick’ extrapolation
To our experience such a scaling is a ‘low’ risk development:
For the fixed micro perveance, the tube length is proportional to the frequency
Lower cathode current density (55%) and increased life time.
Much lower average power (simpler collector)
Marginal (~10%) increase of the modulator voltage and current.
Cost and schedule:
The CLIC tube prototypes were designed/built about 10 years ago; Canon: iiiii and Thales : iiiiii. Mu-tube cost will be within this range, as the companies shall do it not from scratch, but could scale it from exiting ones. Though, today there is no market for such devices, thus the cost of ‘unique’ prototype could be even higher.
Similar to the CLIC tubes, it will take about 24 month to design, built and test the first Mu-tube prototype. Additional budget will be needed for the testing infrastructure (like RF loads etc.).

## Slide 11
Two-Stage Multi Beam Klystron (TS MBK) technology.
Bunching at a low voltage (high perveance). Very compact RF bunching circuit.
Bunched beam acceleration and cooling (reducing p/p) along the short DC voltage post-accelerating gap.
Final power extraction from high voltage (low perveance) beam. High efficiency.
For pulsed tubes, the second HV stage can be operated in DC mode. Thus simplifying the modulator topology. (cost/volume) and increasing the modulator efficiency.
Simplified feedback for the first stage pulsed voltage. Improved klystron RF phase and amplitude stability.
Specific features
Additional advantages:
V1
V2
Stage 1
Stage 2
HV insulators
Post accelerating gap
TS HE MBK
Efficiency 85%
V
V1+V2
Commercial HE MBK
Efficiency 70%
Drawbacks:
Reflected electrons from the output cavity and collector shall be avoided at any cost.
RF radiation into DC gap has to be sealed.
Requires special HV isolated RF feedthrough to inject RF signal into input cavity.
GOOD FOR:

## Slide 12
Only single beam shown
FCC Two-stage MBK klystron: CW, 400MHz, 1.28MW.
Pic 3D model
Particles velocity animation
Very Efficient: 84%
Compact: ~2.5m length in total
Low voltage: 60kV+12kV
High saturated power gain: 46dB
Power gain curve at nominal voltage (PIC results)
10 beams
Total current 21A
1st stage:
60kV/floating
RF length 1.6m
DC accelerating gap
2nd stage
Collector
At ground
Cathode
+12kV

## Slide 13
CLIC Two-stage MBK klystron: Pulsed, 1.0 GHz, 24 MW

## Slide 14
TS MBK
E37503
Local oil tank
Main solenoid
Cathode ceramic (25 kV)
PA gap
2nd HV insulating ceramic (115 kV)
Magnetic circuit
Output waveguide
Beam collector
Collector coil
1st stage
2nd stage
Output coil
CLIC Two-stage MBK klystron: Pulsed, 1.0 GHz, 24 MW

## Slide 15: Example 352 MHz
(Incomplete) design of a 12 MW 352 MHz klystron.
RF circuit is 1.55 meters long, total length inc. collector will be around 2 m
Further work needed to get to 24 MW by adding more beamlets (CLIC was 30 this is only 20) and improving efficiency

## Slide 16: Conclusion
Current 352 and 704 MHz klystrons are limited to 2.9 and 1.5 MW respectively, requiring a lot of klystrons for a muon collider.
704 MHz tube may well be within scaling range of the CLIC tubes at 24 MW
The 352 MHz tube would be very long if scaled from the same tube
Two-stage technologies significantly shorten low frequency, high power tubes and is suitable for 352 MHz solution
KlyC simulations show that 12 MW klystron is possible in under 2 m, and further work should push this to 24 MW.
Significant synergy with CLIC and FCC developments