## Slide 1: Front End Buncher and φ-E Rotator
David N
IMCC
Mars 2024

## Slide 2: Outline
Introduction + history
  Motivation:
    Proton beam on Hg target –small
    Drift + Rotate to small δE for cooling
    High- frequency buncher and phase rotator
IDS “Neutrino Factory” 200 MHz (2011)
Front End for MAP - Muon Collider (2014)
  325 MHz baseline
Major changes
  Chicane and absorber –C Rogers
  Helical Snake 6-D Cooler Y. Alexahin
Optimization
Inverse phase-energy rotator
  Bunch recombiner
Future Variations

## Slide 3
(v-1)

## Slide 4: INTRODUCTION
Drift + “rf” Buncher after target
  R. Palmer -1994
    Short bunch, large δE  long bunch, small δE
    But long bunch means low freq. rf (< ~20 MHz)
  High frequency rf forms train of bunches (>200 MHz)
    match rf phase, mismatch frequency ??- 2000
  Fixed frequency Rotator  adiabatic vernier rotator
    D Neuffer – A. van Ginneken PAC 2001 TPPH16
  Works for both signs μ+ μ- !!

## Slide 5: IDS Baseline Buncher and φ-E Rotator
Drift (π→μ)
“Adiabatically” bunch beam first (weak 320 to 232 MHz rf)
Φ-E rotate bunches – align bunches to ~equal energies
  232 to 202 MHz, 12MV/m
Cool beam 201.25MHz ~15 MV/m rf
Captures and Cools both μ+ and μ-
18.9 m
~60.7 m
FE Target
Solenoid
Drift
Buncher
Rotator
Cooler
~33m
42 m
~80 m
p
π→μ

## Slide 6: 325MHz System “Collider”-MAP
Drift
  20T 2T
Buncher
  Po=250MeV/c
  PN=154 MeV/c; N=12
  Vrf : 0 15 MV/m
    (2/3 occupied)
  fRF : 490 365MHz
Rotator
  Vrf : 20MV/m
    (2/3 occupied)
  fRF : 364 326MHz
  N=12.045
  P0, PN245 MeV/c
Cooler
  245 MeV/c
  325 MHz
  25 MV/m
  2 1.5 cm LiH absorbers
  /0.75m

## Slide 7: Chicane
Initial version was open from target to cooler
  Accepts μ+, μ- at ~250 MeV/c
  Also accepts everything else p, e+-
Introduce chicane + absorber to filter out unwanted particles (C. Rogers, et al.)
  Chicane cuts out P > 500 MeV/c
  Absorber stops protons, electrons, pi, ….
    30 cm Be
Can we introduce without destroying front end ??
SREGION ! Bent solenoid
6.5 1 1e-2
1 0. 1.0
BSL
1 2.0 0.0 1 0.283 0.0 0.058181 0.0 0.0 0.0 0. 0. 0. 0. 0.
VAC
NONE
0. 0. 0. 0. 0. 0. 0. 0. 0. 0.

## Slide 8: 325 “Collider “ w Chicane/Absorber
Add 30 m drift after chicane
  *6.5m  +21.67°,-21.67º
Add chicane + absorber
    particle 1-283 MeV/c
    particle 2-194 MeV/c
  absorber at 54m
    10cm Be
    particle 1-250 MeV/c
    particle 2-154 MeV/c
  Bunch (N=12) 015 MV/m :490 365 MHz
  Rotate (N=12.045 )– 20MV/m : 365  326.5 MHz
  Cool -325MHz -25 MV/m
    pref=245 MeV/c
Chicane + Absorber

## Slide 9: Simulation Results
N :0.15<P<0.35 GeV/c
N: εT<0.03; AL<0.2
N: εT<0.015; AL<0.2
Simulation obtains
  ~0.12 μ/p within acceptances
  ~2014 MARS
  8 GeV proton source
FOFO cooling
  Cools transversely
  By factor of 3
    ~10 in 6-D phase space
Useful
cooling

## Slide 10: Compare without/with chicane
0 GeV/c
1600 GeV/c
0m (production target)
66m (after chicane/absorber)
88m (after drift)
109m (after buncher)
132m (after rotator)
190m (after cooling)
-30m
50m
0m
57m
79m
102m
152m
1600 GeV/c
0 GeV/c
-30m
-50m
21 bunches for Collider

## Slide 11: Rf Buncher/Rotator requirements
Buncher -21m  17.5 m
  37 cavities (14 frequencies)
  13 power supplies (~1—3MW)
RF Rotator -24m
  64 cavities (16 frequencies)
  20 MV/m, 0.25m
  ~2 MW (peak power) per cavity
Cooling System – 325 MHz
  200 0.25m cavities (75m cooler), 25MV/m
  ~4MW /cavity
Front End section | Length | #rf cavities | frequencies | # of freq. | rf gradient | rf peak power requirements
Buncher | 21m | 42 | 484 to 365 | 14 | 0 to 16 | 0—1.34 MW/cavity
Rotator | 24m | 56 | 364to 326 | 16 | 20 | ~2.4 MW/cavity
Cooler | 75m | 200 | 325 | 1 | 25 MV/m | ~3.7MW/cavity
Total df+bxr+rttr | ~134m | 93 |  | 30 | ~500MV | 140MW
6-D cooler | 126m | 360 | 325 MHz | 1 | 25 MV/m | ~3.7 MW

## Slide 12: Simulation Results
N :0.15<P<0.35 GeV/c
N: εT<0.03; AL<0.2
N: εT<0.015; AL<0.2
Simulation obtains
  ~0.12 μ/p within acceptances
  ~2014 MARS
  8 GeV proton source
FOFO cooling
  Cools transversely
  By factor of 3
    ~10 in 6-D phase space
Useful
cooling

## Slide 13: Table of rf cavities, power
Buncher frequency (MHz) | Buncher gradient (MV/m) | RF Power /cavity (MW) (4 cavities)
488.42 | 0.80 | 0.001
478.17 466.42 455.24 444.56 434.45 424.70 | 1.33/1.87 2.40/2.94 2.94/3.48 4.55/5.08 5.62/6.15 6.64/7.23 | 0.007 0.015 0.053 0.086 0.13 0.19
415.39 | 7.76/8.30 | 0.27
406.49 397.97 389.80 381.95 374.42 | 8.83/9.37 9.90/10.4 11.2/11.5 12.0/12.6 13.1/13.7 | 0.35 0.46 0.58 0.71 0.86
367.18 | 14.2/14.8 | 1.0
Rotator frequency (MHz) | Rotator gradient (MV/m) | RF Power /cavity (MW) (4 cavities)
361.67 | 20 | 2.06
355.70 350.60 346.23 342.48 339.27 336.54 | 20 20 20 20 20 20 | 2.1 2.14 2.19 2.23 2.26 2.28
334.23 | 20 | 2.30
332.27 330.62 329.35 328.30 327.50 | 20 20 20 20 20 | 2.31 2.32 2.33 2.34 2.35
326.92 | 20 | 2.36
326.54 | 20 | 2.37
326.37 | 20 | 2.37
First few buncher cavities are very low gradient;
should be removed, grouped or increased in strength

## Slide 14: Table of rf cavities 352 match
Buncher frequency (MHz) | Buncher gradient (MV/m) | RF Power /cavity (MW) (4 cavities)
502.96 489.98 477.65 465.93 | 2.94/3.48 4.55/5.08 5.62/6.15 6.64/7.23 | 0.053 0.086 0.13 0.19
454.76 | 7.76/8.30 | 0.27
444.12 433.97 424.27 414.99 406.11 | 8.83/9.37 9.90/10.4 11.2/11.5 12.0/12.6 13.1/13.7 | 0.35 0.46 0.58 0.71 0.86
398.35 | 14.2/14.8 | 1.0
Rotator frequency (MHz) | Rotator gradient (MV/m) | RF Power /cavity (MW) (4 cavities)
391.39 | 20 | 2.06
384.81 379.21 374.42 370.37 366.84 363.88 | 20 20 20 20 20 20 | 2.1 2.14 2.19 2.23 2.26 2.28
361.37 | 20 | 2.30
359.28 357.56 356.18 355.60 354.67 | 20 20 20 20 20 | 2.31 2.32 2.33 2.34 2.35
353.99 | 20 | 2.36
353.55 | 20 | 2.37
353.35 | 20 | 2.37
25 frequencies

## Slide 15: 6-D Alexahin cooler
Initial version had transverse-only cooler
Helical FOFO snake
  Alternating tilted solenoids
126 m long
  2 cavities every 0.7m
  160 0.25m cavities 25 MV/m
Cools longitudinally and transversely
  L  1/3, 1  1/6 , 2 1/5
  ~1/100  (6-D cooling)
Cools both + and -

## Slide 16: Some Optimizations (H. Sayed)
Adiabatic transition from high-field to low field ?
  20T  2 T in 15m?
  Shorter transition is better
Focusing field in channel
  2T constant field in baseline
More Field is better
  234 T
  Alternating gradient ?

## Slide 17: Optimization (H. Kamal Sayed)
Buncher +Rotator-31 cavity sets
  Changed frequency, rf gradient
Optimized using NERSC supercomputer using evolutionary optimization algorithm, 100’s of simulations
  Increase Erf in Buncher
    By ~4 MV/m
    Higher gradient better
      10—20 MV/m Buncher ~5—10% more
  Rf reaches 325 MHz faster …
    Could use shorter system ?
    Could start further downstream
H. Kamal Sayed, NIM A 794 (2015) 193–199
Buncher
Rotator

## Slide 18: Recombiner options
MAP 2014
  3 longitudinal
  7 transverse

## Slide 19: Summary Front End Design
Buncher/Rotator scenario parameters developed semiempirically
  Guided by simulations, extrapolation, intuition
Neutrino Factory Scenarios, Muon Collider scenarios done similarly
Tweaked to include chicane absorber
Should develop less empirically ??

## Slide 20: Scenario Construction
Parameters available in ICOOL constrain method
Start with final rf frequency
  325 MHz
Select 2 reference particles
  Initial momentum 250 MeV/c / 180 MeV/c
Select number of bunches (between references)
  n = 12
Buncher length, rf gradients
  21 m 016 MV/m
Rotator length, rf gradient
  N =12.05, 24m, 20 MV/m
  Icool parametrization not ideal
    Ref particle accelerations  245 MeV/c
Adjust lengths to match
Match to cooling

## Slide 21: Large number of parameters
Target + collection magnet
  20 T  2? T
Chicane + absorber
  Location, strength of
  Chicane and Absorber
Buncher / Rotator
  B = const or alternating solenoid ?
Match into cooling
  Initial cooling
    4-D or 6-D
    Alexahin-type

## Slide 22
Thank you
for your attention

## Slide 23: Time –reversed version
Bunch-Recombiner
  Start with train of bunches
    Cooled beam after initial cooler
  Vernier rf to bunch train
Can recombine bunch train after initial cooler to single bunch for final cooler
Looks cleaner than Front-end
  Starts with cold muons-only
  C. Yoshikawa, C. Ankenbrandt, D. Neuffer, K. Yonehara
  IPAC2012, TUPPD013
  MuCOOL note 548 (2010)

## Slide 24: Bunch merge
Bunch Merge
Longitudinal Merge
Transverse Merge
eT
st
Trans
Compare 1-D bunch merge
  And 3-D