## Slide 1: Magnets for a Muon Collider
Presented by L. Bottura, CERN
on behalf of the Muon Magnets Working Group
Funded by the EU under Grant Agreement 101094300

## Slide 2: Outline
The muon collider in the HEP landscape
The magnet challenges of the muon collider
Magnet development targets
Summary and perspective

## Slide 3: Collider Choices
Hadron collisions: compound particles
  LHC collides 13.6 TeV protons
  Protons are mix of quarks, anti-quarks and gluons
  Very complex to extract physics
  But can reach high energies
Lepton collisions: elementary particles
  LEP reached 0.205 TeV with electron-positron collisions
  Clean events, easy to extract physics
  Lepton collisions  precision measurements
  Hard to reach high energies
e+e-

## Slide 4: Energy Limit
Electron-positron rings (multi-pass colliders) are limited by synchrotron radiation
Electron-positron linear colliders avoid synchrotron radiation, but are single pass
Typically cost proportional to energy and power proportional to luminosity,
Novel approach: the muon collider
Large mass suppresses synchrotron radiation => circular collider, multi-pass
Fundamental particle yields clean collisions, requires less energy than protons
But lifetime at rest only 2.2 μs (increases with energy)
Hence present energy frontier is probed by proton rings
N
S
N
S
accelerating cavities
magnets
The muon collider is part of the European Accelerator R&D Roadmap
e-: 0.511 MeV
m: 106 MeV
p+: 938 MeV

## Slide 5: Muon Collider: Physics ?
Equivalence between proton (hadron) and muon (lepton) center of mass energy at collision for selected production and decay channels
https://doi.org/10.48550/arXiv.2203.07261
Muon collisions in the range of 10 TeV have comparable discovery potential to hadron collision in the range of 100 TeV

## Slide 6: Muon Collider: Sustainable ?
K.Long et al, Nature Physics, v.17, p.289, 2021
A muon collider at 10 TeV can provide the highest integrated luminosity per unit energy consumption

## Slide 7: Muon Collider: Affordable ?
D. Neuffer and V. Shiltsev 2018 JINST 13 T10003
A 10 TeV muon collider profiting from the LHC infrastructure could be the most cost-effective energy frontier collider

## Slide 8: Proton-driven Muon Collider Concept
Produce a low emittance muon beam…
… collide !
… accelerate muons…
Steady state
Steady state
Pulsed
Steady state
Pulsed
Time
Beam intensity
100…200 ms
protons
muons
pions

## Slide 9: Muon Collider magnets
> 40 T, 60 mm
RCS
20 T, 200 mm
Radiation heat load ≈ 5…10 kW
Radiation dose: 80 MGy
NC ±1.8 T, 400 Hz 100 mm x 30 mm
SC < 10T
100 mm x 30 mm
SC dipole
NC dipole
NC dipole
SC dipole
16 T peak, 160 mm
Radiation heat load ≈ 5 W/m
Radiation dose ≈ 20…40 MGy

## Slide 10: Target and capture solenoid (20 T)
Operating field: 20 T
Operating temperature: 20 K
M. Takayasu et al., IEEE TAS, 21 (2011) 2340
Z. S. Hartwig et al., SUST, 33 (2020) 11LT01
MIT “VIPER” conductor
A Portone, P. Testoni, J. Lorenzo Gomez, F4E
MuCol HTS conductor
Operating current: 61 kA
See A. Portone, et al., 2PoA01-02 on Tuesday 12/9/2023

## Slide 11: Final cooling (40 T) magnetics
  Modular pancake design with supporting ring and plates to manage hoop, radial and vertical stresses
  Free bore 50 mm
  Inner ring thickness 5 mm
  Coil winding thickness 60 mm
    Je = 632 A mm-2  40 T
  Outer ring thickness 60 mm
    Outer radius 150 mm
  Horizontal plate thickness 2 mm
  46 identical ‘modular’ pancakes and 6 ‘correction’ pancakes are used to straighten the field lines at the solenoid ends
Inner Ring
Outer Ring
‘Modular’ Coil
1 % Field Homogeneity
Bore
Support Plate
‘Correction’ Coil
Magnetic Field Modulus, T
lines represent the field direction
Cross Section of ¼ Solenoid
Courtesy of B. Bordini and A. Dudarev, CERN
smax = 600 MPa

## Slide 12: Final cooling (40 T) mechanics
  Preloading, a radial precompression of ~ 200 MPa is essential to limit the conductor hoop stress to acceptable values and to prevent tensile radial stress.
  Electro-mechanical design and tests are in progress to validate the concept and identify issues/solutions towards assessing the performance limits.
Radial Stress, MPa
Hoop Stress, MPa
Solenoid not Energized
Radial Stress, MPa
Hoop Stress, MPa
Solenoid Energized to 40 T
Courtesy of B. Bordini and C. Accettura, CERN

## Slide 13: Final cooling (40 T) quench
  At this magnet scale (i.e. stored energy and size) a non-insulated winding seems to be a good option for quench management.
  Transverse resistance control in a range suitable for operation, balancing protection, mechanics, ramp time and field stability will be crucial (priority R&D)
Courtesy of T. Mulder, CERN
  Singe and stacked pancake tests are planned to validate the concept and identify issues/solutions towards assessing the performance limits.

## Slide 14: Accelerator magnets (±1.8 T)
F. Boattini, CERN
5.07 kJ/m
5.65…7.14 kJ/m
5.89 kJ/m
Warm dipoles are pulsed from
-Bmax to +Bmax at high speed (0.35 to 6.37 ms) every 200 ms
Cold dipoles provide a steady baseline field of about 10 T
The main challenge is the management of the power in the resistive dipoles (several tens of GW):
Minimum stored magnetic energy
Highly efficient energy storage and recovery
HTS flat racetracks
Rectangular magnet bore 100 mm x 30 mm
peak field
10.4 T
b3 = -7.2 units
b5 = -1.4 units
b7 = -0.03 units
A simple HTS racetrack dipole could match the beam requirements and aperture
See M. Breschi, et al., 4PoA02-04 on Thursday 14/9/2023

## Slide 15: Collider magnets limits – A-B plots
Work in progress to provide analytical expression for the magnet design limits (including protection and cost)
Nb3Sn falls short of required performance because of operating margin and peak stress (at affordable cost !)
HTS falls short of required performance because of peak stress and protection (at affordable cost !) – Need to devise alternative protection schemes
Margin limit
Stress limit
Protection limit
Protection limit
Stress limit
Aspirational cost: 700 EUR/kg
Peak stress: 150 MPa
Hot spot tempeature: 350 K
Design range
Aspirational cost: 2500 EUR/kg
Peak stress: 300 MPa
Hot spot tempeature: 200 K
See D. Novelli, et al., 5PoM01-04 on Friday 15/9/2023
Design range
Margin limit

## Slide 16: Collider magnets limits – A-B range
A reduction of HTS cost will result in wider design A-B range
  Reducing unit cost by a factor four doubles the allowable magnet aperture at 16 T
  A reduction of one order of magnitude would be required to reach (16 T, 150 mm)
Operation in the range of temperature 10 K…20 K (above liquid helium) will reduce magnet aperture requirements
  Acceptable heat loads is increased by a factor 2…4, thus reducing the need for shielding
Present cost
Cost reduction factor
1/3
1/2
1/1
1/4
Design range
Iterate with beam physics as the nominal optics and adjust design targets in accordance. Typical A-B range can be (12 T,160 mm) to (16 T, 100 mm)
Include quadrupoles in the analytical evaluation of A-B limits
See D. Novelli, et al., 5PoM01-04 on Friday 15/9/2023
1/10

## Slide 17: HTS needs for a muon collider
Total length required (whole collider complex): 300,000 km
R&D and demonstration:
100…200 km/year
Series production:
10…20 Mm/year
Massive, but not unreasonable: LHC wire was the same order of magnitude

## Slide 18: Magnet development targets
Complex | Magnet | Aperture (mm) | Length (m) | Field (T) | Ramp rate (T/s) | Temperature (K)
Target, decay and capture channel | Solenoid | 1200 | 19 | 20 | SS | 20
6D cooling channel | Solenoid | 90…1500 | 0.08…0.5 | 4…15 | SS | 4.2/20
Final cooling channel | Solenoid | 50 | 0.5 | > 40 | SS | 4.2
Rapid cycling synchrotron | NC Dipole | 30x100 | 5 | ± 1.8 | 4200 | 300
Rapid cycling synchrotron | SC Dipole | 30x100 | 1.5 | 10 | SS | 4.2/20
Collider ring | Dipole | 160 | 10 | 12 | SS | 4.2/20
 |  | 100 |  | 16 |  | 

## Slide 19: Summary and perspective
A muon collider is one of the very interesting options for high energy physics at the energy frontier
  Precision and energy frontier, small footprint, cost, sustainability
High temperature superconductors may be the best technology to make a muon collider affordable and efficient
  Target high engineering current density (up to 1000 A/mm2) and operation at high cryogenic temperature (up to 20 K)
There are many challenges and crucial developments ahead
However…
Magnet technology R&D for a muon collider:
  Has close and tight relation to the advances needed for other science and societal applications (e.g. fusion, material and life sciences, NMR, energy)
  Will provide a sure return of investment
Notes: The reason for this talk is that we have received a strong recommendation from the group that proposes priority for particle physics in Europe. The recommendation, received in March 2020 and approved at the Council session of June 2020, contains a very strong statement on the need to ramp-up R&D effort on high-field accelerator magnets

## Slide 20
C. Accettura, N. Amemiya, B. Auchmann, J.S. Berg, A. Bersani, A. Bertarelli, F. Boattini, B. Bordini, M. Breschi, B. Caiffi, X. Chaud, F. Debray, A. Dudarev, M. Eisterer, S. Fabbri, S. Farinon, P. Ferracin, H. De Gersem, A. Kario, A. Kolehmainen, J. Kosse, J. Lorenzo Gomez, R. Losito, S. Mariotto, M. Mentink, T. Mulder, R. Musenich, D. Novelli, T. Ogitsu, M. Palmer, J. Pavan, H. Piekarz, A. Portone, L. Quettier, E. Rochepault, L. Rossi, T. Salmi, H. Schneider-Muntau, C. Senatore, M. Statera, P. Tavares, H.H.J. Ten Kate, P. Testoni, G. Vallone, A. Verweij, M. Wozniak, A. Yamamoto, Y. Yang, Y. Zhai, A. Zlobin, and the Muon Magnets Working Group
Grateful thanks to many !

## Slide 22: HEP Landscape - Circular Colliders
HL-LHC (CERN)
Installation 2026
Commissioning 2029
EIC (BNL)
In construction
CD4 June 2030
FCC-ee (CERN)
FCC-hh (CERN) – 2070-2090
CEPC (IHEP)
SppC (IHEP) > 2040
m Collider > 2040

## Slide 23: HEP Landscape - Linear Colliders
ILC
250 GeV…1 TeV
TBD
CLIC (CERN)
500 GeV…3TeV
TBD
C3 (SLAC)
250 GeV…500 GeV
TBD

## Slide 24: Muon beam generation and cooling
Absorber
RF field
“cooled” muon
Decreased p⊥
Increased p//
p⊥
p//

## Slide 25: The need for energy
CERN uses today 1.3 TWh per year of operation, with peak power consumption of 200 MW (running accelerators and experiments), dropping to 80 MW in winter (technical stop period)
Electric power is drawn directly from the French 400 kV distribution, and presently supplied under agreed conditions and cost
Supply cost, chain and risk are obvious concerns for the present and future of the laboratory

## Slide 26
Future helium supply is limited and entails a substantial economical and availability risk
Courtesy of F. Ferrand, CERN

## Slide 27: Energy efficient cryogenics
The 60…80 K range would be a dream…
LHC
(FCC)
ESS
Need efficient cryo-plant and heat removal scheme in the range of 10…20 K (see work at ESS)
This could be the best range of operating temperature of a future HEP collider
RHIC
Tevatron
HERA
LHC
HTS may be the only path towards a future collider
Nb-Ti
8T
5T
Nb3Sn
16T
12…14T
HTS
40…60T
20…40T
a few T
1.9
4.2
77
Credits to P. De Sousa and R. Van Weelderen, CERN
W/Q = (Th-Tc)/Tc

## Slide 28: Conductor cost
Grateful thanks to fusion !
Impressive cost reduction in HTS !
Based on CERN orders and requests for quotations 2010-2022
Normalised costs are not aligned to currency, nor corrected for inflation

## Slide 29: Compact HTS windings
350 A/mm2
500,000 km
950 A/mm2
150,000 km
Need to increase the winding current density to fall in a reasonable range of tape length
Unresolved issues:
Winding geometry for tapes and stacks (ends, alignment, transposition, …)
Mechanics of coils under the exceptional electromagnetic loads (600 MPa longitudinal, 400 MPa transverse)
Quench management at high current and energy density (up to 300 MJ/m3)
Radiation hardness of materials and coils (40…80 MGy and 1022 n/m2)

## Slide 30: The HEP push towards HTS
Reduce energy consumption
(FCC-ee 350 MW, FCC-hh 580 MW)
Increase energy efficiency
(COP at 1.9 K is about 1000)
Risk with helium supply chain
(FCC-hh would require 900 tons of lHe)
Infrastructure (magnet) cost
(FCC-hh quoted at 9 BCHF)
Operate SC magnets at higher cryogenic temperature (gas)
Avoid large liquid helium bath and operate with gas (lower density)
Reduce SC cost per unit length and current
Increase coil current density to decrease conductor inventory
Compact HTS windings
Target JE 1000 A/mm2
Operation in gaseous He
Range of 15…25 K
5 T at 2800 A
JE = 250 A/mm2
16 T at 2800 A
JE = 850 A/mm2
Calculation example
(T. Lecrevisse, CEA)

## Slide 31: Muon collider vs. high field magnets
HTS insert of NHMFL all SC 32 T
32 T in 40 mm (15 T LTS + 17 T HTS)
NHMFL HTS Little Big Coil
45.5 T in 14 mm (14.5 T HTS + 31 T resistive)
LNCMI/CEA Nougat
HTS insert
32.5 T in 50 mm
(12. 5 T HTS + 20 T resistive)
Sunam NI one-body
HTS magnet
26.4 T in 35 mm
(26.4 T HTS multi-width)
Muon final cooling magnet
40 T at 4.2 K, 60 mm

## Slide 32: Muon collider vs. fusion
Muon collider target magnet
20 T at 20 K, 1.2 m
10 kW, 80 MGy
ITER Central Solenoid Model Coil
13 T at 4.5 K, 1.7 m (LTS)
MIT/CFS SPARC TF Coil prototype
20 T at 20 K (HTS)
Large bore solenoids, large heat and radiation

## Slide 33: Muon collider vs. life science
Muon final cooling magnet
40 T at 4.2 K, 60 mm
14 T HTS MRI
800 mm
28.2 T LTS+HTS
54 mm
Push field performance beyond state-of-the-art

## Slide 34: Muon collider vs. power generation
HTS dipole designs
10…20 T, 50 mm
Develop compact saddle HTS windings
Small-size stator for PM generator
Design of 10 MW HTS wind generator
Saddle coils design for generator