## Slide 1: Microbulk detectors for the BabyIAXO experiment
Authors: Ana Quintana García oh behalf of IAXO
Micromegas detector group
RD51 Collaboration Meeting, 04-dec-2023

## Slide 2: Content
IAXO/BabyIAXO Physics
Microbulk detectors
IAXO-D1- Saclay at CEA-Saclay
Characterization
Tests performed at CEA-Saclay: position scanning
Solar axions
Microbulk Micromegas detector
BabyIAXO Microbulk X-ray detectors
Prospect
Summary
BabyIAXO
X-ray detector requirements

## Slide 3: The International AXion Observatory (IAXO): Physics
AXIONS → Predicted solution of the strong CP problem.
→ Dark matter candidate.
Well into the QCD axion region
Production: axions are produced from thermal photons via the Primakoff effect inside the stars.
Detection: axions converted back into photons in the presence of an intence magnetic fields.
Expected X-ray excess when the magnet points to the Sun.
Expected solar axion flux

## Slide 4: BabyIAXO
Intemediate-scale version of IAXO with physics potential
Detector + shielding
Active shielding: plastic scintillator as a cosmic muon veto.
Passive shielding: several centimeters of lead around the detector
IAXO collaboration, Conceptual design of BabyIAXO, the intermediate stage towards the International Axion Observatory, JHEP 05 (2021) 137 [2010.12076].
Magnet
Optics
Detectors
Tracking system

## Slide 5: X-ray detector for BabyIAXO
High detection efficiency in the RoI: 0-10 keV.
Very low background (<10 keV): 10-7 c/keV/cm2/s.
  Shielding (pasive + active)
  Radiopurity of construction materials
  Advanced event discrimination stragedies
Time Projection Chamber (TPC) with Microbulk readout.
X-ray window
3 cm
Vacuum pipe to magnet
8.5 mm

## Slide 6: Microbulk Micromegas detector
Prototypes:​
IAXO-D0 at Zaragoza​
IAXO-D1-LSC at the Underground Laboratory of Canfranc​
IAXO-D1-Zgz at Zaragoza​
IAXO-D1-Saclay at CEA-Saclay
Microbulk readout:​
Intrinsic radiopurity.
Very homogeneous amplification gap, uniform gain.
Good energy resolution @5.9keV (55Fe peak).​
Pixelized readout gives topological information.
High power to discriminate X-rays signal from background events.
Cu (5mm)
Kapton (50mm)
Strips in 2D
Micromegas readout:
120 x 120 strips
Pitch = 0.5 mm
(6 x 6 cm2)
Micromesh grid
S. Andriamonje et al. JINST 2010 5 P02001

## Slide 7: Background rejection in BabyIAXO
Radiopurity: inner components.
Passive shielding: lead shell.
Active shilding: muon vetos (PMT scintillators).
Event discrimination strategies: G4 simulation and prototype measurments.
CAST background measurement,
NATURE PHYSICS (2017)
Background evolution in CAST

## Slide 8: IAXO-D1 at CEA-Saclay
r = 30 mm
Characterization of a new Micromegas detector design IAXO-D1
Window replaced -> be able to illuminate most the Micromegas surface
AGET card
Flat cable
Detector chamber:
Ar-ISO mixture
Fe55 Source
Characterizations and tests:
Gain, transparency and resolution: mesh & strips.
Position scan over the window (mapping).
Stability over time.
Mesh acquisition:
  + PA ORTEC
  + Shaper
  + MCA
Strip acquisition:
+ AGET chip: S. Anvar et al., AGET, the get front-end asic, for the readout of the time projection chambers used in nuclear physic experiments, IEEE Nucl. Sci. Symp. Conf. Rec. (2011)
  + REST framework: REST-for-Physics, a ROOT-based framework for event oriented data analysis and combined Monte Carlo response, Comput. Phys. Commun. 273 (2022) 108281 [2109.05863]

## Slide 9
IAXO-D1-Saclay: characterization (mesh)
Ar-ISO(5%)
Standard behaviour
Gains over 104
Resolution @5.9 keV -> 16% (FHWM) with Ar + 5% ISO

## Slide 10
IAXO-D1-Saclay: characterization (strips)
Gain concordance between different dynamic ranges (AGET gains).
240 fC gives better resolution that the other dynamic ranges.
The energy resolution is worse than expected: noise not completely controlled.
Study of the gain and resolution at different AGET gains (dynamic ranges)
Gain 0x0 (120 fC)
Gain 0x1 (240 fC)
Gain 0x2 (1 pC)
Vm = 350 V, Ed = 100 V/cm

## Slide 11: IAXO-D1-Saclay: position scan
0º
90º
y
x
Readout
RIM
Study of the uniformity of the gain and resolution in the different positions over the window.
Only with the readout powered
Adding the RIM
Connecting the field shapers
Field shapers

## Slide 12: IAXO-D1-Saclay: position scan
+ RIM
+ Field Shaper

## Slide 13: IAXO-D1-Saclay: position scan
+ RIM
+ Field Shaper

## Slide 14: IAXO-D1-Saclay: position scan
Applying the Vmesh to the RIM
Increase in the number of events away from the center
The general behavior is the same
+ RIM
+ Field shapers
Applying the (Vcath-Vmesh)/2 to the field shapers
The sensitive zone is wider
Slightly improvement on the center resolution

## Slide 15: IAXO-D1-Saclay: position scan
+ RIM
+ Field shapers
Applying the Vmesh to the RIM
Increase in the number of events away from the center
The general behavior is the same
Applying the (Vcath-Vmesh)/2 to the field shapers
The sensitive zone is wider
Slightly improvement on the center resolution

## Slide 16: IAXO-D1-Saclay: position scan
+ RIM
+ Field shapers
Applying the Vmesh to the RIM
Increase in the number of events away from the center
The general behavior is the same
Applying the (Vcath-Vmesh)/2 to the field shapers
The sensitive zone is wider
Improvement on the point-shape of the source

## Slide 17: IAXO-D1-Saclay: position scan
+ RIM
+ Field shapers
Applying the Vmesh to the RIM
Increase in the number of events away from the center
The general behavior is the same
Applying the (Vcath-Vmesh)/2 to the field shapers
The sensitive zone is wider
Improvement on the point-shape of the source

## Slide 18: Summary and prospects
Summary:
Axions searches with helioscopes requires ultra-low background x-ray detectors -> Microbulk Micromegas
Characterization: gain, resolution, uniformity and stability are being performed on the IAXO-D1-Saclay prototype.
Prospects:
Complete the characterization of the test set-up with gain stability tests and optimization of the shapping time of the electronics.
Estimation of the background level: first in this set-up, then placing it insde the lead-shielding and finally covering it with the muon vetos.
Continue the effort of optimising the algorithms for background rejection in order to reach the BabyIAXO background requirement.
IAXO-D0/IAXO-D1-Zgz
IAXO-D1-LSC
Xe:
Ar:
IAXO-D1-Saclay