## Slide 1: RFQ2 Tuning Update
L. Millar, A. Grudiev
SY-RF-MKS
RFQ2 45th Meeting - 21/09/2023
Notes: https://indico.cern.ch/event/1327955/

## Slide 2: Overview
Since last time:
Ridge1 machined and installed.
Cavity tuned (results in the slides which follow).

## Slide 3: RFQ2 Tuning Summary

## Slide 4: Tuning Summary
Sum and difference of the quadrants is calculated to obtain:
Q = (Q1 - Q2 + Q3 - Q4) / 4
1st dipole = (Q1 - Q3) / 2
2nd dipole = (Q2 - Q4) / 2
Ideally, there would be no dipole components and a flat quadrupole component.
Sampling windows shown in grey.

## Slide 5: Tuning Summary
Current parameters:
Q: 100 ± 0.4%. ✅
Dipole 1 (Ds): ± 0.82%. ✅
Dipole 2 (DT): ± 0.41%. ✅
f0 = 352.2043 MHz @ 25° in vacuum. ✅

## Slide 6: Tuning Summary
Current parameters:
Q: 100 ± 0.4%. ✅
Dipole 1 (Ds): ± 0.82%. ✅
Dipole 2 (DT): ± 0.41%. ✅
f0 = 352.2043 MHz @ 25° in vacuum. ✅

## Slide 7: Tuning Summary
Current parameters:
Q: 100 ± 0.4%. ✅
Dipole 1 (Ds): ± 0.82%. ✅
Dipole 2 (DT): ± 0.41%. ✅
f0 = 352.2043 MHz @ 25° in vacuum. ✅

## Slide 8: Tuning Summary – Q Factor
Results for the 352.2 MHz operating mode:
Q0 = 6127 (8.65% lower than RFQ1)
Qext = 4106
β = ~1.49
Qext is 6% higher than anticipated, while Q0 increased by ~3% after copper ridge installation.
β is 2% lower than the planned 1.52 value (critically coupled with a 70 mA beam).

## Slide 9: Tuning Summary
Displacement relative to “nominal” starting position.
Max retraction (+ve): 3.77 mm
Max insertion (-ve): 4.2 mm
Final dimensions to be calculated and checked with calipers.

## Slide 10: Effect of Q on Operation

## Slide 11: RFQ1 Parameters
Parameter | Value
Fo | 352.2 MHz
QO, | 6772
QExt | 4250
β | 1.6
IBeam | 70 mA
Beam energy | 0.045 MeV
Beam output energy | 3.0 MeV
Beam Power, PBeam | 207 kW peak
Resistive losses, PLoss | 393 kW
Total losses, PTot | 600 kW
Input Power, PFor | ~600 kW peak
Taken from RFQ1. Cavity designed to be critically coupled with a ~70 mA beam.
Notes: Nominal values shown (beam/power not what are currently used in operation).

## Slide 12: RFQ2 Parameters
If Q0 = 6127, wall losses are 10.5% higher than in RFQ1, so with a 207kW beam:
The beta value with beam () will be:
Parameter | Value
Fo | 352.2 MHz
QO, | 6127
QExt | 4106
β | 1.49
IBeam | 70 mA
Beam energy | 0.045 MeV
Beam output energy | 3.0 MeV
Beam Power, PBeam | 207 kW peak
Resistive losses, PLoss | 1.105*393 = 434.265 kW
Total losses, PTot | 207+434.265 = 641.265 kW

## Slide 13: RFQ2 Parameters
The reflection coefficient is given:
Necessary klystron power and reflection calculated respectively as:
Hence, for same beam energy, an input power of 641.32 kW is required.
Parameter | Value
Fo | 352.2 MHz
QO, | 6772
QExt | 4106
β | 1.49
IBeam | 70 mA
Beam energy | 0.045 MeV
Beam output energy | 3.0 MeV
Beam Power, PBeam | 207 kW peak
Resistive losses, PLoss | 393 kW
Total losses, PTot | 207+(1.105*393) = 641.265 kW
Input Power, PFor | 641.265/(1-0.009^2) = 641.32 kW

## Slide 14: Effect on Operation
The consequences are:
6.9% (41 kW) more power required from klystron.
~10.5% increase in surface heating. Corresponds to an extra ~40 W for water cooling (434 kW instead of 393kW in copper, pulsed for 1 ms at ~1Hz).
Slightly overcoupled with 70 mA beam, very small (~0.01%) reflection.
Overall, due to the increase in Q the numbers are better than we had anticipated previously.

## Slide 15: Discussion

## Slide 16: Measurement Plan for Full Assembly
Tuner lengths fixed
Confirm bead-pull/Qex, antenna calibration
Tune Qex using 3 aluminum dummy irises
Assemble all modules and auxiliaries
Bead-pull measurement / Tuning
Tuner recutting, antenna spacers fabrication
Final bead-pull/tuning if necessary
Coupler iris fixed
Coupler (ridge1) fabrication & installation
Use Ø 12 mm dummy iris for coupler
Use copper RF plugs
Copper ridge2, waveguide, wg-coax transition.
with copper ridge1
(final configuration)
Drawing of coupler iris (ridge1 body)
Drawing of dummy RF plug body
Drawing of antenna spacer
Drawing of tuner body w/ antenna hole
Drawing of tuner body w/o antenna hole
Drawing of dummy RF plug assembly
Drawing of ridge1 assembly
✅
✅
✅
✅
✅
✅

## Slide 17: Discussion
The proposed next steps are:
Collect final tuner dimensions and send tuners for machining. Antenna spacers to be machined simultaneously. Tuner mechanisms packaged and moved to storage area?
Reinstall machined tuners, bead pull the cavity.
Install tuners and antennas with gaskets, bead pull.
Calibrate the antennas w.r.t. the bead pull.
Remove bead pull and perform vacuum test.
Hand RFQ2 over to Suitbert for test stand transport/installation (bead pull in the test stand? If so, time/space will be required.).