## Slide 1: MD10766: Crystal collimation performance with ion beams using different collimator settings
M. D’Andrea, R. Bruce, R. Cai, D. Mirarchi, S. Redaelli
27 September 2023 – LHC Studies Working Group – Ion MD Preparation

## Slide 2: Motivation
Crystal collimation used as baseline for 2023 operation with Pb ion beams
Operational settings for 2023 Pb ion run finalized during commissioning
  Assess cleaning performance in a wider variety of configurations → possible further improvement
  Complete characterization and gather data for benchmark of simulations and development of tools
Goals of the MD:
Collimator | Proposed settings
TCP | 6 σ
TCPC H / V | 4.75 σ / 5 σ
TCSG.B5[L/R]7.B[1/2], TCSG.A5[L/R]7.B[1/2] | 6.5 σ
TCLA | 8 σ
TCSP IR6 | 10.3 σ
TCT IR1 | 10.5 σ
TCT IR2 | 13 σ

## Slide 3: Beam requirements and plan
Up to 30 pilot bunches for both beams, respecting setup beam flag
Estimated time: 5 hours
Plan:
  Ramp to 6.8 Z TeV
  Optimize orientation of crystal collimators if needed
  Loss maps with different collimator settings → potential further cleaning improvement
    TCLAs at 7 σ
    Retraction of TCPs/TCSGs upstream of crystal and between crystal and absorber
  ͏͏Beam excitations with different ADT strengths → assessment of cleaning performance dependence on impact parameter at crystal, better understanding to improve simulation parameters
  Fast angular scans (~1 mrad at 50 µrad/s) → data for development of machine learning tools
  Linear scan of absorber for all crystals → characterization and reference for simulation benchmark
Same procedure as previous crystal tests with ion beams (e.g. MD4168)
During angular and linear scans, ADT used to excite 3 pilot bunches at the same time

## Slide 4
Thank you for your attention!