## Slide 1
Arthur CLAIREMBAUD
Plasma light measurements with fast cameras

## Slide 2
Plasma light set-up
5m
Consistency between signal of PMTs and cameras
Plasma light shape in the vapor source
Effect of a plasma density step
10 PMTs
2 Fast cameras
1 Basler camera
Rb vapor source
1us integration time
39us of no signal + 1us of signal
9.5m
3.5m
Motivation

## Slide 3
Signal of the cameras
16 bits camera : 2^16 = 65535
Lineout is taken for light in the window (remove reflections)
Background subtracted
Raw image – Fast camera
Reflections of the plasma light on the viewport
Lineout at the center of the image

## Slide 4
Wakefield light ?
Electronic background | Protons | Laser | Laser + Protons
Comes from kinetic energy lost by wakefield electrons after the passage of proton bunch
vmax = 400
vmax = 25000
Light observed comes from energy deposited by proton bunch when propagating in plasma

## Slide 5
Shape of the signal
Averaged over 20 events
Shape of plasma light column changes with bunch population or light intensity
FWHM from 3.5 to 5.8 mm
5 m
Uniform plasma density – npe = 3.7e14/cc
Bunch population scan
RIF position 3 sigma SMI (unseeded)
Integration

## Slide 6
Integrated signal
Proton bunch population scan
Error bars = r.m.s for 20 events
Signal increases with bunch population
Linear increase
From 1e11 to 3e11 – 3 times more signal
Uniform plasma density – npe = 3.7e14
RIF position 3 sigma SMI (unseeded)
5 m

## Slide 7
Reproducibility and RIF scan
9.5 m camera light
SSM
SMI
Uniform plasma density – npe = 3.7e14
Bunch population – Qb = 2.85e11
Different RIF position
Sigma = 180ps
Error bars = r.m.s for 20 events
Position of RIF along bunch determines signal level: number of protons driving wakefields
Position of RIF affects reproducibility in signal
Clear difference between seeded and unseeded (SSM vs SMI) in r.m.s. variations

## Slide 8
With and without step
3 % step at RIF position 1 sigma (180ps):
  Signal increase 52% at 3.5m
  Signal increase 50% at 5m
  Signal increase 69% at 9.5m
6 % step:
  Signal lower at any RIF position and at any position along plasma
n_pe = 3.7e14
Qb = 2.85e11
Step position : z = 1.75m
3.5 m
5 m
9.5 m
Lower reproducibility at 10m with 3% step ?

## Slide 9
Intensity variations
20 events – Plasma light intensity and transverse distribution of protons at IS2
9.5 m – 3% step
Halo 442 camera

## Slide 10
Intensity variations
Halo 442 camera - sorted
9.5 m – 3% step – sorted
Laser position at IS1 – VLC5
0.5 mm radius
circle centered on mean position
Asymmetric halos  less plasma light when seeded

## Slide 11
Consistency PMTs / Cameras
PMT and camera show same trends
Variations of signal usually larger with cameras than PMTs
Factor of 3 on camera 5m – factor of 1.3 on PMT5
Fast Camera vs PMT – 5m
Uniform plasma density – npe = 3.7e14
RIF position = 3 sigma (SMI)
Bunch population scan

## Slide 12
Summary and conclusion
Plasma light signal increases with bunch population
Plasma light column expands with signal intensity (at 5m and 10m – lower expansion at 3.5m)
Plasma light signal more reproducible with SSM – largest at intensity RIF = 1 sigma
3% at 1.75m (npe = 3.7e14) density step increases plasma light signal at all three positions (z = 3.5 m, z = 5 m, z = 9.5m) by 50% or more
6% density step decreases signal everywhere
Plasma light signal can be related to other diagnostics (halo cameras) when proton-laser alignment is off
Consistency in trends with PMTs but signal variations larger with cameras
We observe that:
Next run: 1 camera in front of each PMT