## Slide 1
www.cea.fr
STAARQ project
Station Test Aimant AccélérateuR Quadripole
MQ and MQYY Anti-cryostats
Hervé Allain, Jean-Marc Gheller
Visio CERN - 22/09/2023

## Slide 2
STAARQ project: anti-cryostat
7.65 meter
OUTLINE
ANTI-CRYOSTAT manufacturing
Next step
Hold point
Transport beam
Magnetic measurement system

## Slide 3
anti-cryostat manufacturing
Anti-cryostat manufacturing status?
Next steps
Hold point:
    before insertion of the inner tube in the outer tube
    Jean-Marc and Hervé will come to CERN
    Approximative date?
Remark:
  photographs of the different step of manufacturing would be appreciated
  Only one anti-cryostat needed for MQYYM test and STAARQ test
  Station commissionning

## Slide 4
Anti-cryostat arrival
(horizontal):
Transport and turning beam
Anti-cryostat
Anti-cryostat turning
to vertical position:
1
2
CERN supply
CEA supply
(turnaround plot)
Drawings needed
Once vertical, the anti-cryostats will always stay vertical (manipulation and storage)
Drawings needed
anti-cryostat transport beam

## Slide 5
Anti-cryostat storage
Plateform for magnet preparation
Anti-cryostat support for vertical storage
anti-cryostat storage

## Slide 6
Magnetic measurement system
Status
Insertion at CERN
Transport in the anti-cryostat on the transport beam

## Slide 7
Thank you for your attention

## Slide 8
Anti-cryostat (VIII)
2 T sensors
1 T sensor
1 T sensor
PCB heater
(0.65 m long)
Instrumentation:
  4 temperature sensors dispatched along the bottom part
  Of the anti-cryostats to control and regulate the temperature (placed
  Between inner and outer tube)
  3 flexible PCB heaters: 2 heaters 2.2 m long and 1 heater 0.65 m long, all on the internal tube to maintain room temperature inside the measuring tube (manufactured by CERN)
Helium flow:
  One small tube to feed and generate a helium mass flow in the
  measuring tube from the bottom (1.5 mm inner diameter, 0.25 mm
  Of wall thickness)
MLI:
  MLI will be wrapped around the inner tube to minimise the heat
  Load on the superfluid bath (15 layers minimum, more is better)
PCB heater
(2.2 m long)
PCB heater
(2.2 m long)