Emittance measurements
in LEIR
1. Maciej Slupecki, Theo Argyropoulos
2. 19 October 2023

---
Contents
  1. Preparation
  2. Measurement
  3. Meaning of HW settings
  4. Outlook

---
Preparation phase
1. IPM preparation: switching the HVs on
  1. Very slow ramp up
    1. optimistically: ~20 min
    2. realistically: ~1 h
      1. the present system requires constant supervision during this 1-h startup
  2. Issue:
    1. Frequent ‘no response from device?’ message that halts the ramp-up and OP needs to manually restart it
      1. The app will be rewritten during
         YETS23-24 (by Dwane Almeida
        1. thanks to SPSOP team for help
      2. Is it an underlaying hardware or FESA problem?

---
Present IPM measurements
  1. Monitoring
    1. quality of cooling
    2. beam size evolution after ecooler → OFF and RF on
  2. Is the reading at ramp and extraction reliable?

---
Meaning of HW settings
1. Which settings should we use?
  1. Bottom voltage: 5 kV
  2. MCP voltage: 1.45 kV
  3. Top voltage: 1.35 kV
2. Is vertical IPM always saturated?
  1. or plotting artifact?
Vertical
Horizontal

---
Schottky
LEIR NOMINAL cycle
  1. 7 injections
  2. Schottky shows beam energy distribution
    1. dragging the injected beam (with e-cooler) towards 4‰ lower energy to make space for the next injection
  3. IPM shows the beam position / size / intensity
    1. newly injected beam has different position (orbit) than the stacked beam,
    2. then it is dragged towards the well-centered stack (while getting cooled)
    → Nice complimentary information
IPM
DCBCT
1st inj
2nd inj
3rd inj
4th inj
5th inj
6th inj
7th inj
RF on

---
Outlook and new possibilities
  1. Continuous measurement is better
    1. Hard to define the specific points of interest along the injection plateau – the focus is rather on the continuous behaviour of the beam
    2. We could process the data from selected slices and publish them in nxcalls for offline performance checks
  2. The unclosed bump
    1. Better to close it, otherwise powering up the IPM changes orbit
      1. not a source of major losses, but still a headache

---
Further points to discuss
  1. Possibility to measure continuously through the whole run (= IPM always on)
    1. as online performance diagnostics
  2. Extend x/y range beyond 35 mm
  3. Reliability of data at RAMP
  4. Artifacts in the data
  5. Processing:
    1. show slices directly
       before/after injection
    2. help diagnose injection and cooling issues