## Slide 1: Cross Section Measurements (Detectors)
Deborah Harris
York/Fermilab
June 7, 2024
NuSTEC 2024 Summer School

## Slide 2: Summary from Yesterday, Plan for today
Particle Propagation through Materials
Examples of detector technologies
Today’s lecture:
  Segmented Active/Passive Detectors (leftover)
  Hybrid Detectors (T2K’s ND280, MINERvA)
  Estimating Backgrounds, constraining with data
  Estimating Efficiency, checking with data
  The challenge of migrating from measurement to truth
  From Inclusive to Exclusive Cross sections
  If time allows: how to measure

## Slide 3: Homework question #1:
How far does a proton with 100MeV Kinetic Energy go in
  Plastic Scintillator (could consider C alone)
  Iron
  Argon
How far does a muon with 2000 MeV Kinetic Energy go in
  Plastic Scintillator
  Iron
  Argon

## Slide 4: Homework question #1:
How far does a proton with 100MeV Kinetic Energy go in
  Plastic Scintillator (could consider C alone)
  Iron
  Argon
How far does a muon with 2000 MeV Kinetic Energy go in
  Plastic Scintillator
  Iron
  Argon
Target | Range (g/cm^2) | Density (g/cm^3) | Range (cm)
C | 8.67 | 0.92 | 9.4
H | 3.63 | 0.08 | 47.2
Fe | 11.3 | 7.90 | 1.4
Ar | 10.9 | 1.40 | 7.8
Target | dE/dx (min) (MeV/g/cm^3) | Density (g/cm^3) | dE/dx (MeV/cm) | Range (m)
Polystyrene | 1.9 | 1.1 | 2.1 | 10
Fe | 1.5 | 7.9 | 11.5 | 2
Ar | 1.5 | 1.4 | 2.1 | 10

## Slide 5: Homework question #2:
What is the shower max (in cm) for a 1GeV electron:
  Plastic Scintillator
  Iron
  Argon
  Lead
What is the shower max (in cm) for a 2GeV electron:
  Plastic Scintillator
  Iron
  Argon
  Lead

## Slide 6: Homework question #2:
What is the shower max (in cm) for a 1GeV electron:
  Plastic Scintillator
  Iron
  Argon
  Lead
What is the shower max (in cm) for a 2GeV electron:
  Plastic Scintillator
  Iron
  Argon
  Lead
 | Z | Ec (MeV) | X0 | ln(1000/Ec)-0.5 | t_max (cm)
Plastic Scintillator | 6 | 111 | 42 | 1.7 | 71.3
Iron | 26 | 29 | 1.76 | 3.0 | 5.3
Argon | 18 | 42 | 14 | 2.7 | 37.5
Lead | 82 | 10 | 0.56 | 4.1 | 2.3
 | Z | Ec (MeV) | X0 | ln(2000/Ec)-0.5 | t_max (cm)
Plastic Scintillator | 6 | 111 | 42 | 2.4 | 100.4
Iron | 26 | 29 | 1.76 | 3.7 | 6.5
Argon | 18 | 42 | 14 | 3.4 | 47.2
Lead | 82 | 10 | 0.56 | 4.8 | 2.7

## Slide 7
Module number
μ candidate
p candidate
Neutrino Events at Some Experiments

## Slide 8: Active/Passive Detectors

## Slide 9: From Fully Active to Sampling Detectors
Advantages to Sampling:
  Cheaper readout costs
  Fewer readout channels
  Denser material can be used
    More N, more interactions
    Could combine emulsion with readout
  Can use magnetized material!
Disadvantages to Sampling
  Loss of information
  Particle ID is harder (except emulsion for taus in final state)

## Slide 10: Sampling calorimeters
High Z materials:
  mean smaller showers,
  more compact detector
  Finer transverse segmentation needed
Low Z materials:
  more mass/X0 (more mass per instrumented plane)
  Coarser transverse segmentation
  “big” events (harsh fiducial cuts for containment)
Material | Xo (cm) | lINT (cm) | Sampling (Xo) | Xo (g/cm2)
L.Argon | 14 | 83.5 | 0.02 (ICARUS) | 20
Steel | 1.76 | 17 | 1.4 (MINOS) | 14
Scintillator | 42 | ~80 | 0.13 (NOnA) | 40
Lead | 0.56 | 17 | .2 (OPERA) | 6

## Slide 11: Steel/Scintillator Detector (MINOS)
8m octagon steel & scintillator calorimeter
  Sampling every 2.54 cm
  4cm wide strips of scintillator
  5.4 kton total mass
486 planes of scintillator
  95,000 strips

## Slide 12: MINOS Event Topologies
Long muon track + hadronic activity at vertex

CC Event
NC Event
e
CC Event
UZ
VZ
3.5m
1.8m
2.3m
Short showering event, often diffuse
Short event with typical EM shower profile
En = Eshower + Pm
Shower energy resolution: 55%/√E
Muon momentum resolution: 6% range; 13% curvature
Courtesy Chris Smith, FNAL Seminar

## Slide 13: (Oscillation) Detector Summary
Detector Technology | Largest Mass to Date (kton) | Event by Event Identification |  |  | +/-? | Ideal n Energy Range
 |  | ne | nm | nt |  | 
LAR TPC | 0.8 |  |  |  | Not yet | huge
Water Cerenkov | 50 |  |  |  |  | <2GeV
Emulsion/Pb/Fe | 0.27 |  |  |  |  | >.5GeV
Scintillator++ | 14 |  |  |  |  | huge
Steel/Scint. | 5.4 |  |  |  |  | >.5GeV

## Slide 14: Cross Section Detectors
Given the lengths of the muon tracks we saw earlier
Given the intense beams close to where neutrinos are produced
Will need to combine detector strategies to fit into allowed real estate for Near Detector Halls

## Slide 15
Experiments current releasing results (in 0.5-20GeV region)
MicroBooNE:
Liquid Argon TPC
Booster and NuMI (off axis) beamline!
T2K Near Detector:
CH, H2O
NOvA Near Detector: CH
MINERvA:
He, CH, C, H2O, Fe, Pb
NINJA:
CH, H2O, Fe

## Slide 16: Modern Cross Section Experiments
Experiment | Beam Energy | Target Nucleus | B field? | Granularity | Status
COHERENT | 25MeV, broad | CsI, Ar, …. | No | various | Data-taking
MINERvA | 3.5GeV and 6GeV, broad band | He, CH, C, H2O, Fe, Pb | For muons only | 1.6cm x3.3 cm triangles (scint) | Last data: 2019 Still analyzing
T2K (Wagasci) | 600MeV | CH, H2O | Yes! | ~few cm triangles + Gas TPC | Data-taking in 2023
NOvA | 2GeV | CH | No | 4cmx6cm (scint) | Data-taking in 2023
NINJA | 700MeV | Pb, H2O | For muons only | Emulsion! | 
MicroBooNE | 600MeV (BNB) and 2GeV (NuMI) | Ar | No | 3mm wire pitch | Data-taking ended in 2022 Still analyzing
ICARUS |  |  | No | 3mm wire pitch | Data-taking in 2023
SBND | 600MeV (BNB) |  | No | 3mm wire pitch | Data-taking soon!

## Slide 17: T2K Near Detector
Fine-Grained Detectors (FGD 1 & 2):
CH scintillator tracker
Target for
FGD2 contains water
Time Projection Chambers (TPC):
Excellent tracking
High-resolution charged-particle momenta
Accurate particle ID

## Slide 18: Upgrade to original T2K Near Detector

## Slide 19: MINERvA Detector
Core of detector was an active scintillator strip target, surrounded by calorimetry.
Passive targets interspersed with scintillator upstream.
Detector is mostly in trash cans now, but some has been recycled for DUNE tests.
Nucl.Instrum.Meth.A 743 (2014) 130 and beam test Nucl.Instrum.Meth.A 789 (2015) 28

## Slide 20: How to measure a Cross Section
Golden Rule in Cross Section Measurements:
More generally, consider an observable x that describes the interaction
And no detector is perfect, so what we really measure is as a function of “ , so there’s an additional step

## Slide 21: Quick word about units
What are the units of the different components?
  N: number of events, unitless
  s: cross section, area per target (for neutrinos, usually x10-38 cm2)
  F: flux, Neutrinos per unit area (for near detector location, cm-2)
    example: NOvA reports*: 87νμ/cm2/1010 POT or for 1020 POT, 1012 n/cm2
  e: efficiency, unitless
  M: ”mass” must be “number of targets” : recall this is 6.023x1023 if your detector weighed 1 gram
*Phys.Rev.D 107 (2023) 11, 112008

## Slide 22: How to measure a cross section
From the equation:
U written this way is a “smearing” step that translates
from the true quantity to a reconstructed quantity

## Slide 23: Solving for
And in real life, there are backgrounds: not every event you select is going to be the signal process you are looking for!
Integrate over the entire flux to find:

## Slide 24: Measuring Cross Sections: Simplify notation
Remove subscript from true variables, but t=bin of xtrue, m=measured
We’ll write phi but it really means “integrating over the flux”
Switch from to again just for simplicity, sometimes called “unfolding”
Deconstruct this piece by piece, from the easiest to the most complicated:

## Slide 25
: These are the backgrounds that are still in the event sample even after you make all your cuts.
You could predict what this background is from your simulation, but that prediction may have a large uncertainty!
  Background Process Cross Section uncertainties (have to sum over all processes!)
  Flux uncertainties (have to Sum over all fluxes!)
  Have to smear back: is that smearing matrix the same for all backgrounds?
Signal
Background

## Slide 26: Using data to predict B(xm)
Quasi-elastic neutrino scattering should have an easily-identifiable signature: one muon and one proton
Example from MINERvA: if you only require a muon (p>1.5GeV/c)
and NO other energy deposits far from the nucleus, no Michel electron, here are the backgrounds:
Phys.Rev.Lett. 130 (2023) 16, 161801

## Slide 27: Using Data to predict B(xm)
Remember: the CCQE process is probably the best known neutrino-nucleus process, how could you trust your simulation to tell you the background levels?
Solution: Use the data itself, but try to isolate each background by looking at the events you REMOVED from the signal process
How to find events with p+?
How to find events with p0?
Remember, red is signal: can’t always find event samples that have all one background, or no signal events in them…
Phys.Rev.Lett. 130 (2023) 16, 161801

## Slide 28
: This is the ”unsmearing matrix” that takes you from the measured variable to the true variable
We want to know, if an event is observed in bin m, what bin did it really happen in?
In other words, what’s the probability that an event observed in bin m (measured) actually occurred in bin t (true)?
We can use our Monte Carlo to form a migration matrix indicating what fraction of events generated in each true bin α were observed in each reconstructed bin j
If the detector has good resolution, the matrix should be close to diagonal
True distribution
Reconstructed (smeared)
distribution
Graphics courtesy C. Patrick

## Slide 29
To get the unsmearing matrix Utm, you have to invert the migration matrix
…in theory. In practice, it often gives poor results and we often need to use a more sophisticated method
Each row adds up to 100%
Diagonal corresponds to events reconstructed in the right bin
“Migration Matrix”
Graphics courtesy C. Patrick

## Slide 30: T2K: Letting vary
T2K: Showing 3 out of 5 samples
“CC0p” Analysis for nm
Try to get as many m as possible!
Phys.Rev.D 101 (2020) 11, 112001

## Slide 31: T2K: Letting vary
In order to incorporate systematic uncertainties on cross section model, T2K parameterizes the uncertainties and then lets them float in a fit that incorporates not only the signal region but also two control samples
Jesus-Valls, NuINT 2022, and Phys.Rev.D 101 (2020) 11, 112001

## Slide 32: T2K: Letting vary
In order to incorporate systematic uncertainties on cross section model, T2K parameterizes the uncertainties and then lets them float in a fit that incorporates not only the signal region but also two control samples
Jesus-Valls, NuINT 2022, and Phys.Rev.D 101 (2020) 11, 112001

## Slide 33
: Flux [neutrinos/cm2]
Usually the cross section is reported assuming you’ve integrated over all neutrino energies: so really means
For the rare cases where neutrino energy is measurable
Total Cross Section:
=

## Slide 34
: Efficiency [unitless]
The fraction of signal events that you retain after making all the analysis cuts to remove your backgrounds
In truth, this efficiency may depend not only on xt but also on neutrino energy, and remember you’re integrating over the flux
One way to check: Compare efficiencies from different generators
(Ref: T2K, Phys.Rev.D 98 (2018) 3, 032003)

## Slide 35: NOvA: Using Data to test
NOvA has produced first double differential cross section for electron neutrino charged current inclusive scattering
Use Boosted Decision Tree to identify electrons
How do they know that they model the efficiency of the BDT correctly given uncertainties in hadron energy? Use the Data! Can you guess how?
“Muon Removal” Technique: remove muon from nmCC data events, add electron at same angle and energy, then measure efficiency, and compare to the efficiency for original simulation.
Phys.Rev.Lett. 130 (2023) 5, 051802

## Slide 36
: Bin width [units of whatever x is]
How wide should this bin width be?
The more bins you have, easier to distinguish features of the distribution
The more bins you have, the worse the statistics are in each bin
BUT…Depends on your resolution: if you can’t measure something to better than d , you shouldn’t pick bins that are d/10!
10 bins
100 bins
Graphics courtesy C. Patrick

## Slide 37: Break, now that we’ve discussed every term in

## Slide 38: Easiest Cross Section to measure: “Inclusive Charged Current Interactions”
Say you want to measure total Charged Current neutrino cross section
What cuts would you use to isolate your signal?
  Require a muon-like energy or an electron-like energy
  If you have a magnetic field, might be able to cut on charge of final state lepton
What are your backgrounds?
  Antineutrino interactions (low if you have a B field)
  Neutral Current Interactions
    For muon neutrinos:
    For electron neutrinos: and recall that might look like electrons in your detector
Easiest Observables to measure: Muon Kinetic Energy (T) and angle (q) w/rt Neutrino beam

## Slide 39: One example of Inclusive Cross Section Result
NOvA nmCC Cross Section Result, vs. muon kinematics
Phys.Rev.D 107 (2023) 5, 052011
Even for a narrow range of neutrino energy (like NOvA) any one kinematic region still has a range of interactions that contribute.

## Slide 40: The Catch with Inclusive Cross Sections
NOvA nmCC Cross Section Result, vs. muon kinematics
Phys.Rev.D 107 (2023) 5, 052011
Even for a narrow range of neutrino energy (like NOvA) any one kinematic region still has a range of interactions that contribute.

## Slide 41: Using both Lepton and Hadron Information
Let’s say you have measured the following quantities:
  Final lepton charge and momentum 3-vector: can determine plep, Elep ,qlep
  Total hadronic energy (pretend you can see all of it, even the neutron energy) Ehad
Can define a few quantities:
  Estimated Neutrino Energy En = Elep + Ehad
  Estimated Momentum Transfer (squared) to the nucleus: (remember, W is virtual) -q2=Q2 = 2 En(Eμ – pμcos θμ) – Mμ2
  Estimated Energy transferred to the nucleus = w = Ehad
  3-momentum transferred to the nucleus: Q2+w2=q32

## Slide 42: Neutrino Observables w/hadrons & leptons
Remember this picture from e- scattering: e- beam (energy E) comes in, scatters, you measure the outgoing electron energy distribution (E’) at some angle, and w=E-E’
ω (GeV)
ω (GeV)
ω (GeV)
d2σ/dΩ/dω (nb/GeV/sr)
d2σ/dΩ/dω (nb/GeV/sr)
d2σ/dΩ/dω (nb/GeV/sr)
Phys. Rev. D 94, 013012 (2016)
Notes: You saw the middle plot in S. Dolan’s lecture. I’m showing it at three angles

## Slide 43: Neutrino Observables w/hadrons & leptons
Translating this picture to Neutrino Scattering
ω (GeV)
d2σ/dΩ/dω (nb/GeV/sr)
Initial and Final Electron energy and angle define a 3-momentum transfer
For neutrinos:
True Energy transfer: w
True 3-momentum transfer: Q2+w2=q32
Graphics courtesy R. Gran
Phys. Rev. D 94, 013012 (2016)

## Slide 44: Proxy for True Energy transfer to Hadronic system: “Available Energy” (answer to HW#4)
Visible in scintillator (and argon)
p+- deposit their kinetic energy, but not their mass
p0 deposit their total energy
Protons: deposit total kinetic energy
Neutrons: deposit very little.
“Available energy”: sum of visible energy
Phys. Rev. D 94, 013012 (2016)
Kinetic energy Kinetic energy
~0
Total energy
p
π+
n
π0
Figure courtesy P. Rodrigues
Example from MINERvA at right, 3.3cm plastic granularity
Similar in spirit to ~3cm wire pitch Liquid Argon (but different density, Z)
Notes: You saw the middle plot in S. Dolan’s lecture. I’m showing it at three angles

## Slide 45: What does the Data Look like in this space?
Look at inclusive sample of events as function of energy AND momentum transferred
Showing event distributions, but cross sections were extracted
Cross sections were also extracted from these distributions
Available Energy: “visible” energy in scintillator
Unfolding this was tricky!
M. Ascencio et al, Phys.Rev.D 106 (2022) 3, 032001
vs.

## Slide 46: From Inclusive to Exclusive
From these event displays, you know we can do better to isolate processes and look at only one (set of) final states
How would you isolate events that are quasielastic?
  Require one lepton (of the correct charge if possible)
  Do you require a proton track? Or do you only require NO pion tracks?
  What about Michel Electrons: what if you didn’t see a pion track but you saw a tiny em-like shower right near the vertex?

## Slide 47: New vocabulary: Quasielastic-like
After subtracting backgrounds, MINERvA has enough statistics to bin QE-like events along 3 axes: muon kinematics AND hadron energy
Many processes contribute to ”CC0 ”
  CCQE
  2p2h
  Resonance+p absorption
  DIS
Lots of discrepancies with the model
D. Ruterbories et al, Phys.Rev.Lett. 129 (2022) 2, 021803

## Slide 48: Different Detectors will have different cuts
MicroBooNE example: nm CC0p Cross section
Event with muon and proton candidate
Leading Muon candidate has p>100MeV/c
Leading Proton candidate has p<1.2GeV/c
  Proton candidate has to be shorter than muon candidate
Phys.Rev.D 102 (2020) 11, 112013

## Slide 49: CCQE versus “CCQE-like” versus “CC0p”
Since so many other processes can look like a CCQE event even if you have a perfect detector, we have defined a new term
How would you make a CCQE-like event that is not CCQE?
Example from MicroBooNE: breakdown of signal events after background subtraction:
Phys.Rev.D 102 (2020) 11, 112013

## Slide 50: Have to map on to Cross Section Models
Quasielastic Scattering
2p2h (correlated nucleon pairs) Scattering
Resonant Pion Production (D’s, etc.)
Continuum Pion Production
Coherent Pion Production
Shallow Inelastic Scattering (?)
Deep Inelastic Scattering
Plus models for initial and final state effects
S. Dolan, INSS 23

## Slide 51: QE-like processes and Unfolding Neutrino Energy
Solution to Homework #3: QE assumption, solve for Neutrino Energy

## Slide 52: What if you were to unfold to Neutrino Energy?
The energy resolution you get using this formula (or ANY FORMULA) depends on what you assume about the events that pass all your cuts
Plot at right is for T2K, one of their earliest oscillation papers
Phys.Rev.Lett. 112 (2014) 18
Moral of this story: Big model dependence in unfolding to Neutrino Energy

## Slide 53: New Neutrino Observables: Transverse Kinematic Imbalance (TKI)
If you know you’re starting with a neutrino, and you see a muon and a proton in the final state, you can calculate kinematics in the plane transverse to the neutrino direction if you measure 3-vector of both final state particles, and you are SURE they are a muon and a proton
Phys. Rev. C 94, (2016) 015503

## Slide 54: New Neutrino Observables: Transverse Kinematic Imbalance (TKI)
Hopefully all these different variables will give you a consistent story about what all the different quasielastic-like processes might be there in your data (T2K, Phys.Rev.D 98 (2018) 3, 032003)

## Slide 55: MicroBooNE: Looking at TKI in 2 dimensions
MicroBooNE split these distributions up into “QE-rich” samples and “everything else” samples
Plus: Another tool of the trade: “Fake Data Studies”
  Put in different interaction models see if your procedure extracts predictions from the new model or the one in your unfolding matrix
Phys.Rev.D 108 (2023) 5, 053002

## Slide 56: ”Initial Nucleon Momentum” as observable?
Another “transverse kinematic imbalance variable”: if you assume conservation of momentum for events with a final state proton and muon, can calculate the initial nucleon momentum
MINERvA Phys. Rev. Lett. 121, 022504 (2018)

## Slide 57: Challenges
Goal: make measurements that can constrain models
Why is this difficult?
  Given the flux, you never know precisely what neutrino energy you have for any one event
  Given the analysis cuts to isolate the signal you are trying to find, the detector limitations mean you may have backgrounds in your sample
  Given detector limitations you never know precisely what energy you missed from neutrons
  If that’s not bad enough, there’s also the fact that nuclear effects can make one process look like another even if your detector was perfect

## Slide 58: If only we could measure a cross section on H first…

## Slide 59: Using what you’ve learned to see H by itself
Consider antineutrino QE-like scattering:
  If you have a plastic target, you have C and H
  If you are trying to measure CCQE on H, then CCQE on C is a background
  Use nuclear effects to isolate H!
Nature, 614, 48–53 (2023)

## Slide 60: When life gives you lemons… make lemon meringue pie

## Slide 61: Different Reactions populate different regions
SIGNAL: Elastic on H
Background: QELike CCQE (on C)
Background: QELike Resonant
Background: QELike 2p2h
Regions of the 2D angular distribution used to fit the backgrounds proportion in the signal region.
NuFact23

## Slide 62: Validating the Background Prediction
CCQE is the dominant background. Small 2p2h, inelastic (absorbed), and Non-QELike contributions. The fitted model are well constrained by data.
NuFact23

## Slide 63: Another test: Neutrino Beam
Recipe: select events with trackable protons in a neutrino sample. Different final states and available kinematics. Apply same fitting mechanism. Data and MC mostly agree within uncertainty. Data and MC mostly agree. Disagreement can be explained by 2p2h uncertainty.
NuFact23

## Slide 64: Cross-section Extraction
Ingredients:
Unfolding matrix and efficiency from Data and Simulation studies
Flux from models and data measurements ()
Number of Hydrogen targets from the detector assay.
Measured signal from data – predicted background
[Nature 614, 48–53]
[Nature 614, 48–53]
NuFact23

## Slide 65: Uncertainties in the Axial Form Factor Cross-Sections
Dominated by statistical uncertainty after the background subtraction.
Systematic uncertainties from residuals of background subtraction
Particle responses in the “other” category, dominated by neutron systematics.
Always ask to see uncertainties!
NuFact23

## Slide 66: Free Nucleon Axial Form Factor
MINERvA found ~5800 such events on a background of ~12500.
Shape is not a great fit to a dipole at high Q2.
LQCD prediction at high Q2 is close to this result, but maybe not at moderate Q2.

## Slide 67: How to summarize this field?
Want to cover “current cross sections” but…
Consider the various combinations: 6x4x5x6
Interaction
Inclusive Scattering
CC 0 p Production
CC 1p+ Production
CC 1p0 Production
CC Shallow or Deep Inelastic Scattering
Rare Chanels (n-e, coherent scattering)
Flavour, Helicity
Flavour, Helicity
Target Nucleus
CH
H2O
H, He, C, Pb
Ar
Pb
Observable (xm)
Lepton Kinematics
Q2
q0 vs q3
Proton Kinematics
Pion Kinematics
Transverse Kinematic Imbalance variables (many)
“Neutrino Energy”
Number of Dimensions
1
2
3

## Slide 68: Summary of This Lecture
So many interactions, so little time!
Measuring Cross Sections all use the same formula
Challenges with making a robust measurement
  Flux
  Detector
  Cross section
Clever ideas of new observables and ways to reduce backgrounds are yours to discover!
All the tricks we’ve figured out to isolate different effects in Quasielastic interactins, we have to figure out for pion production!
Notes: If you look at the Technical design report, you will NOT see the techniques MINERvA used to make its most impactful results!

## Slide 69: Backup Slides

## Slide 70
M: ”Mass” [nucleons] Sounds easy, right?
Cross sections are usually reported “per nucleon” so…
BUT, it depends on what cross section you are trying to measure: are you trying to measure something “per nucleon”?
What if you are measuring something that (in principle) only happens on neutrons? (i.e. )
What if you are measuring something that (in principle) only happens on protons? (i.e. )

## Slide 71: Full Disclosure on calculating “M”
For Liquid Argon detector, it’s very pure so you can be sure the nucleus that is struck is Ar
For Water, at least at Super-K or Hyper-K those detectors are very pure H2O
But scintillator-based detectors may not always be all CH or CH2: for example NOvA:
Phys.Rev.D 107 (2023) 11, 112008
N
NOvA Image: https://doi.org/10.1016/j.nuclphysb.2016.04.027

## Slide 72: Observables in Quasielastic Interactions
If you have a quasielastic interaction, and the initial nucleon is at rest, you can estimate the neutrino energy and momentum transfer from the lepton kinematics ALONE
This is how T2K makes its (most precise) oscillation measurements!
  Require ONLY one lepton in the final state
  Require conservation of energy and momentum
You may hear from Stephen and Luke why this is a problem, but it’s still an observable
Just don’t call it true energy if you are scattering off a big nucleus!