## Slide 1
New Electronics for the Experimental Areas
Progress and points for discussion
Mark McLean 3rd Oct 2023

## Slide 2: Agenda
MWPC approach
HV Power supplies
DWC ???
Progress

## Slide 3: MWPC – The problem
Two problems:
  The local electronics fail quite often due to radiation damage
  We want to support 26 instruments during Run 4 for which we will need new readout electronics

## Slide 4: MWPC - Options
Do nothing at all
  Local Electronics (LE) will fail, but maybe not too often now they are powered down when un-used.
  Angleo readout boards cannot co-exist in the same crate as VFC or EAVP boards
Design RTM2 for EAVP
  This was the original plan. RTM2 would accept the signals from the current LE and pass them to the EAVP-VME board.
  Nothing wrong with this, except it is wasted work and money because the MWPCs will be replaced in LS4 and nothing of this solution will transfer to the RHFM. Also does nothing to address failure of LE.
Design RTM2 for VFC
  This could work. Same LE, VFC has sufficient RTM signals to readout LE and control HV PSUs. VFCs will migrate to RHFM, avoids waste of EAVP-VME boards. No fibres needed.
Design rad-hard LE for VFC
  This would provide a long-term solution until chambers are replaced by RHFM, and when that happens the VFCs will be used for the RHFM.
  No RTM required, new LE based on LpGBTx and a rad-hard multiplexer
  Need to qualify the mux relatively soon
  I reckon the design of the RTM2 is a similar amount of work to the design of new LE, and both need VFC firmware

## Slide 5: MWPC Local Electronic (LE) Ideas
Spaciroc, 64 charge sensitive inputs, LpGBT controlled
  Could be very similar to planned RHFM
LpGBT (with ADC) plus discrete amplifiers and mux
  Need to find a rad-hard mux
NanoXplore Ultra-300 device, rad-hard FPGA with ADCs
  Possibility of LE supporting both current cabling and future fibre readout

## Slide 6: HV Power supplies
Still trying to catch Christos to ask what BI plans are

## Slide 7: DWC
Inaki’s list shows that there will still be five of these after LS3. Is this true? I have no plans to support them with the EAVP.

## Slide 8: EAVP Progress
Welcome Stasa
6 prototypes of each of the VME board and the RTM1 are with the assembly company, delivery expected soon.
Stasa is working on a test board

## Slide 9: Backup info
LE: EDA-04708