## Slide 1: Subcooling HEX Contract Kick Off Meeting Introduction to CERN and High Luminosity project
CERN, 06/10/2023
V. Gahier

## Slide 2: Outline
Introduction to CERN
Introduction to Hi-Lumi project
Cryogenic system for Hi-Lumi project

## Slide 3
Push forward the frontiers of knowledge
E.g., the secrets of the Big Bang …what was the matter like within the first moments of the Universe’s existence?
Develop new technologies for accelerators and detectors
Information technology - the Web and the GRID
Medicine - diagnosis and therapy
Train scientists and engineers of tomorrow
Unite people from different countries and cultures
The Mission of CERN
Notes: 3

## Slide 4
CERN was founded 1954: 12 European States
“Science for Peace”
Today: 23 Member States
Member States: Austria, Belgium, Bulgaria, the Czech Republic, Denmark, Finland, France, Germany, Greece, Hungary, Israel, Italy, the Netherlands, Norway, Poland, Portugal, Romania, Serbia, Slovakia, Spain, Sweden, Switzerland and the United Kingdom
Associate Members in Pre-Stage to Membership: Cyprus, Slovenia
Associate Member States: Croatia, India, Lithuania, Pakistan, Turkey and Ukraine
Applications for Membership or Associate Membership: Brazil, Estonia, Latvia
Observers to Council: Japan, Russia, United States of America; European Union, JINR and UNESCO
Employees: ~2 700 staff, 800 fellows
Associates: ~11 800 users, 1 300 others
Budget (2019) ~ 1 200 MCHF
Notes: 4

## Slide 5
Accelerating Science and Innovation
CMS
ALICE
LHCb
ATLAS
LHC ring:
27 km circumference
Notes: 5

## Slide 6
Why the High Luminosity LHC project ?
Many questions remain !
Higgs properties [coupling]
More than one Higgs?
Beyond Standard Model Physics? Dark Matter & Dark Energy?
Need more Data and Statistics!!
The final focusing magnets will also need to be replaced because of radiation damage.
HL-LHC Goals
Extend the LHC lifetime by 15+ years
Prepare the machine for producing in that period 10 times more data as compared to the nominal LHC operation period
NB: doubling the accuracy for the experiments would require 4 times the data volume (over 20 Years of operation with current peak performance after end of Run 3)
dR/dt : number of events per second
L : luminosity
σp : event production cross section

## Slide 7
Basic performance indicators of a particle collider
Nominal luminosity
Peak Luminosity
=> Performance
“ The potential of the facility”
Integrated Luminosity
=> Qualification – Global availability - Time
“What allows science” (statistics)

## Slide 8
Towards higher collision rates
Luminosity = f * N2 / 4p s2
stronger focusing
LIU
More intensity
New discoveries and precision measurements need integrated luminosity !!!
NB. Plans as defined a few years ago, timing not up-to-date
Target for physics:
doubling integrated Luminosity for each new run
Need for more protons in a smaller cross section !!!
more powerful final focusing !

## Slide 9
Existing LHC
NC D1
SC D1
Corrector
Package
Q1
Q2a
Q2b
Q3
Final focussing at P1 and P5: from LHC to HL-LHC
D2
Q4
CC
HL-LHC relies on more powerful final focussing quadrupoles, associated recombination dipoles and crab cavities.
Local heat loads expected x5 w.r.t LHC

## Slide 10
Q1
Q2a
Q2b
Q3
D1
DFX
DFM
Connection to LHC (UL)
Service gallery (UR)
TAXS
Crab cavities
UA Gallery
Q4
TAXN
Service cavern
SC Links
D2
Collimators
CP
DFHX
DFHM
View of underground configuration at IP5
A truly international collaboration !

## Slide 11
UA57
US57
UR55
UL57
UPR57
PC IT
PCs IT Trims
DFX
DSHX
DFHX
CDBs
PIC,BIS
QDS
CLIQ
Warm Diodes
DCM
Q1
Q2A
Q2B
Q3
CP
D1
OC PCs
D1 PC
Cold Diodes
OC EE
DSHM
D2 PC
D2 OC EE
Cold box
CDBs
DFM
DFHM
DQHDS
D2
Q4
Q5
Q6
Valve box
D2 OC PCs
Crab
Cavities
RF Powering
UW57
TAXN
Cooling and Ventilation
View with the technical galleries

## Slide 12
Eu funded design study
Approval of HL-LHC project
Today
HL-LHC operation
Timeline of LHC and HL-LHC
Series production is well underway - or ready to be launched - for all components!
Ca. 1.1BCHF
Ca. 75% committed

## Slide 13
Q1
Q2a
Q2b
Q3
D1
DFX
DFM
Connection to LHC (UL)
Service gallery (UR)
TAXS
Crab cavities
UA Gallery
Q4
TAXN
Service cavern
SC Links
D2
Collimators
CP
DFHX
DFHM
What needs to be cooled
1.9 K
4.5 K
4.5 K – 20 K
20 K – 300 K
SC magnets beam screens are cooled at 60-80 K

## Slide 14
HL-LHC P1/P5 Cryogenic architecture
QSRG : 4.5K refrigerator providing supercritical helium at 3 bara and 4.6 K
QURCG : Cold compressor box providing cooling capacity at 1.8 K
Users at tunnel level
QPLG : Vertical transfer line (~100 m height)
QXL : Distribution line distributing C,E and returning B,D,F
70 m for the common branch
270 m for the long branch
60 m for the short branch
RM/JM : Return module and junction module at extremities for transient handling and back-up
QSRG : Compressor station providing gaseous helium 20 B

## Slide 15
Helium Refrigerators at LHC P1 and P5 for HL-LHC
Helium Refrigerators
LHC Helium Refrigerators
similar capacity required
for P1 and for P5,
in addition to 8 existing ones
Compressor station
(100t, 4MW input power)
Cold boxes from world wide leading industries
(>100t, Heat exchangers, expansion turbines, valves, controls)
2 x 14kW@4.5K, including 3.25kW@1.9K
P1-P5 Cryogenic Architecture

## Slide 16
Cryogenic distribution line at P1 and P5
2 x 750 m, 5 process pipes, vacuum insulated lines
Lines diam. 40 - 273 mm, 650 mm - 800 mm
~145 t
per point
LHC tunnel
Gallery
LHC Line
Tendering process Q1-Q2_2022
Contract signed Dec’22 with KrioSystem (PL)

## Slide 17
DN400
double gimbal joint
DN400
gimbal joint
HXI dome
HXI dome
Jumper interconnection
Magnet interconnection
Q2B magnet Service Module
QXL Service Module
Existing HXI
New HXI
Jumper elbow (IT side)
XB lines (pumping) ISO DN65
Interface to the magnet HX
LD line (quench)
EHE’H line (thermal shield)
CY lines (injection)
Cryogenic distribution line at P1 and P5: some details

## Slide 18: Thank you for your attention