## Slide 1
Francisco Rogelio Palomo Pintoa, Ricardo Ascazubic, Alexis C.Vilas Bòasc , Jorge Jiménez-Sáncheza , Caterina Soldadoe, Begoña Fernández-Martínezb, Carlos Guerrero-Sánchezb
fpalomo@us.es
aElectronic Engineering Dept. of School of Engineering, University of Seville, Spain
bNuclear Physics Dept. at Physics Faculty, University of Seville, Spain
cIntel Corp.
d Centro Universitario da Fei, Universidade de São Paulo, Brazil
eElectronics and NanoEngineering Dept., Aalto University, Finland
Learning HISPANoS, a new Neutron Beam Facility at CNA
Detector and SEE experiments

## Slide 2
Learning HISPANoS, a new neutron beam facility at CNA
Introduction
About the new HISPANoS neutron beam now open for experiments at the National Center of Accelerators, Sevilla, Spain
On a first experiment about detection of neutron induced nuclear reactions in silicon photodiodes and its intrincacies
Neutron induced Single Event Effects in an Intel MAX10 FPGA (55 nm)
Preparation of the Neutron Beam Line for the
experiment
SEU FPGA experiment
Photodiode Matrix
Experiment
Notes: Introduction:
Description of the Hispanos facility
Description of the Detector Experiment
Description of the SEU Experiment

## Slide 3
HiSPANoS is the first Accelerator-based neutron source in Spain and it is installed at the 3 MV Tandem Accelerator.
Operates since 2013 in continuous mode and since 2018 in pulsed mode.
Learning HISPANoS, a new neutron beam facility at CNA
more info at: https://indico.cern.ch/event/1132520/ ,Carlos Guerrero's presentation
Chopper
Buncher
Beam
Chopper:
Variable width: 40 ns-250 ns
RR: 31.25 kHz-2MHz
Switcher Voltage: 650 V
Buncher:
Needs tuning (delay & power) for synchronization
Pulsing system: p,d & α
Notes: Description of the Hispanos Facility

## Slide 4
HiSPANoS
monoenergetic
Learning HISPANoS, a new neutron beam facility at CNA
Neutron production targets/mechanisms
EJ301 @0o
EJ301 @30o
Be target
100 cm
PickUp
For our experiments we choose Fast Neutrons between up to 10 MeV,
2H on 9Be target (9Be(d,n)10B)
Reaction | Q-value (MeV) | Eth (MeV) | Target |  |  | Neutron spectra
 |  |  | Material | Thickness | Diameter | 
2H(d,n)3He | 3,27 | 0,0 | D/Ti | 546 µg/cm2 | 30 mm | Quasi-monoenergetic 2,2 – 6,1 MeV
9Be(p,n)9B | -1,85 | 2,06 | Be | 500 µm | 25 mm | Continuum up to 4 MeV
9Be(d,n)10B | 4,36 | 0,0 |  |  |  | Continuum up to10 MeV
7Li(p,n)7Be | -1,64 | 1,88 | Li | 500 µm | 25 mm | Continuum up to 4 MeV
7Li(d,n)8Be | 15,03 | 0,0 |  |  |  | Continuum up to 20 MeV
Projectiles
1H, 2H up to 6 MeV
4He up to 6 MeV
Continuous mode
Up to 10 uA
Pulsed mode
1-2 ns pulse width
32,5 kHz - 2 MHz
1- 4 m flight path
Monoenergetic and broad energy neutron beams
Notes: Experimento con FPGA's: descripción del montaje y de las FPGAs usadas

## Slide 5
Learning HISPANoS, a new neutron beam facility at CNA
Monoenergetic and Broad Energy Neutron Beams

## Slide 6
Neutron total, elastic and reaction cross-section of 28Si from JENDL/HE-2004
Nuclear data relevant to single event upsets in semiconductor memories induced by cosmic-ray neutrons and protons, Y. Watanabe, H. Nakashima, Proc. of 2006 Symposium on Nuclear Data, Jan 25-26, 2007, SND2006-III.03
Incidence of multiparticle events on soft error rates caused by n-Si Nuclear Reactions, F.Wrobel et al, IEEE TNS 47(6), 2000
Reaction | Threshold (MeV)
28Si(n,n)28Si | <keV
28Si(n,a) 25Mg | 2.75
28Si(n,p) 28Al | 4.00
28Si(n,n,a)24MgOff limits | 10.34 Off limits
Averaged emission energy for elastic recoil 28Si(n,n)28Si and main nuclear reactions 28Si(n,p)27Al, 28Si(n,a)24Mg
Learning HISPANoS, a new neutron beam facility at CNA
Expected Nuclear reactions in silicon

## Slide 7
Learning HISPANoS, a new neutron beam facility at CNA
Expected Nuclear reactions in silicon
Ion | IEL (eV/Å) | LET (MeV/cm2-mg) | Mean Range Long./Lateral (mm)
28Si (elastic recoil) | ~30 | ~1.3 | ~0.27/0.06
25Mg (from 28Si(n,a)25Mg) | ~50 | ~2.1 | ~1.4/0.3
27Al (from 28Si(n,p)27Al) | ~40 | ~1.7 | ~1.1/0.2
SRIM range/straggling simulation, IEL, NIEL 28Si 200 keV in silicon bulk
SRIM range/straggling simulation, IEL, NIEL 25Mg 1 MeV in silicon bulk
28Si(n,n)28Si
28Si(n,a)25Mg
SRIM range/straggling simulation, IEL, NIEL 27Al 750 keV in silicon bulk
28Si(n,p)27Al
SRIM simulations for Si, Mg and Al ions at different possible kinetic energies
from a nuclear reaction gives a hint about LET (minimum) and range in the
Silicon Detector Bulk: the ion gives all its energy to the bulk and is trapped.
Ionizing Energy Loss, IEL. Non-Ionizing Energy Loss, NIEL
Notes: estas simulaciones son para valores pequeños de energía cinética del ión. Muestran dos cosas: que son iones eficientes para dejar energía en el silicio (LET alto aunque K sea baja) y que su poder de penetración es minúsculo (menor de 1.5 um) por lo que si se generan en el detector, van a quedarse allí dentro, no importa lo delgado (20 um) de la zona de deplexión.

## Slide 8
Key to successful result is to achieve a very low noise, high speed pre-amplifier.
  Battery-powered pre-amp board (remove AC noise).
  Single trans-impedance amplifier, 500MHz BW, femtoA input bias, femtoF input cap (from Analog Devices Inc.).
  VREF-filtered voltage regulators for low noise (uV) high ripple rejection (68dB).
  Custom board layout to minimize parasitic capacitances
Multiple diodes to maximize exposed cross section/oscilloscope channel usage.
Hamamatsu S1336 series PIN detectors, 20 mm depletion depth
3.6 mm
3.6 mm
At bias=-1.5 V we
calculate depletion depth
from the Capacitance
Formula, d=20 mm
=4.7kW
Learning HISPANoS, a new neutron beam facility at CNA
Photodiode Experiment
Notes: Descripción de la electrónica

## Slide 9
Learning HISPANoS, a new neutron beam facility at CNA
Direct measurement (Trans Impedance Amplifiers) is useful to get signals in a straight manner but it is very sensitive to Electro Magnetic Interference. There is plenty of EMI in the accelerator room, with an amplitude no less than 30 mV. The EMI signal is the same in both detectors but the ionization signal, at an instant, happens in only one.
A typical signal from a nuclear reaction,
~100 ns long
Deuteron arrival to production target
Level trigger positive
Photodiode Experiment
CAEN N625
Quad Linear
Fan In/Fan Out
4ns delay line
Signal Inversion
(delay = 4ns)
+
coax
RF Signals
&
Neutrons
The synchronous difference signal shows only the ionization pulse when a neutron arrives at one detector. Changing Level Trigger Sign selects pulses
from one or the other
detector
Difference
Signal
Notes: Montaje de señales para evitar interferencia electromagnética

## Slide 10
Learning HISPANoS, a new neutron beam facility at CNA
Just for calibration we put the same setup under gamma radiation from a Co60 source (accelerator shut off). We detect no spike from gamma photons so we concluded the dataset from the experiment with the accelerator on was due to neutron induced nuclear reactions in the photodetectors silicon bulk.
Digital Signal Processing of the data set showed the same conclusion:
Digital Data
Processing
(low pass convolution
filter)
low pass filter kernel
Photodiode Experiment
Notes: Experimento de calibración con gammas, acelerador apagado

## Slide 11
Learning HISPANoS, a new neutron beam facility at CNA
blue: close to neutron source
Event distribution of
captured events
The analyzed data is consistent with the hypothesis that signals come from ions generated by neutron induced nuclear reactions in Silicon, as expected.
Photodiode Experiment
Notes: Descripción del montaje para el experimento de neutrones

## Slide 12
Learning HISPANoS, a new neutron beam facility at CNA
In this experiment the difficult part is at the digital design. Irradiation data analysis is very easy (just a disagreement in the fff... word received).
Controller FPGA
(off beam)
Target FPGA
(on beam)
The second experiment was oriented to evaluate the usefulness of HISPANoS for Single Event Upset experiments. The target was a MAX10 FPGA card, with another MAX10 FPGA out of beam as local controller. The MAX10 target had simple digital design: a memory controller and a RAM matrix, made with the flip-flop pool of the FPGA. A simple word (fff...) was recorded in the FPGA RAM memory. The memory controller readouts the RAM and send the data stream to the controller FPGA, from there to the control computer on a safe place. We used two uarts as a double check in the data transfer.
FPGA Experiment
Notes: Experimento con FPGA's: descripción del montaje y de las FPGAs usadas

## Slide 13
Learning HISPANoS, a new neutron beam facility at CNA
With the Target FPGA close to the neutron source we detected SEUs at a rate of one every couple of minutes, sometimes even a total failure of the readout (an indication of SEU in the memory controller). No stuck bits in any case were seen, with the Target FPGA in pristine condition after scrubbing (or reconfiguration). For future experiments we will design a Shift Register structure in the Target FPGA, without the internal memory controller block, now possible because the MAX10 is insensitive to Single Event Effects Stuck Bits.
FPGA Experiment
Controller
MAX10 FPGA
Target MAX10 FPGA
MAX10 FPGA experiment layout
FPGA RAM memory dump
Notes: Experimento con FPGA's: detalle de los autómatas implementados

## Slide 14
Learning HISPANoS, a new neutron beam facility at CNA
Conclusions
We learned about how to make neutron detection experiments in the new
HISPANoS neutron beam facility at CNA, Sevilla
The photodiode experiment opens the way to more sophisticated detector experiments in the facility. As a plus, we got straight signals from neutron (up to 10 MeV) induced nuclear reactions in silicon.
The MAX10 FPGA shows no stuck bits under neutron irradiation. New Neutron Single Event Effects experiments are planned.
Thanks to the funding programme H2020-ARIEL
Notes: Conclusiones generales

## Slide 15
Learning HISPANoS, a new neutron beam facility at CNA
Thanks for your attention!
fpalomo@us.es