## Slide 1
Alexej Grudiev on behalf of the CHART/FCCee Injector design collaboration
Slides (most of) are kindly provided by Paolo Craievich
THE FCC-ee INJECTOR COMPLEX: AN OVERVIEW

## Slide 2
Acknowledgements
2
This work was done under the auspices of CHART (Swiss Accelerator Research and Technology) Collaboration, https://chart.ch - CHART Scientific Report 2022: https://chart.ch/reports/
PSI | R. Zennaro, M. Schaer, N. Vallis, B. Auchmann, I. Besana, S. Bettoni, H. Braun, M. Duda, R. Fortunati, H. Garcia-Rodrigues, D. Hauenstein, E. Hohmann, R. Ischebeck, P. Juranic, J. Kosse, F. Marcellini, U. Michlmayr, S. Muller, G. L. Orlandi, M. Pedrozzi, J.-Y. Raguin, S. Reiche, M. Seidel, R. Rotundo, S. Sanfilippo, M. Zykova all the technical groups involved in the P3 experiment
IJCLab | I. Chaikovska, F. Alharthi, V. Mytrochenko, R. Chehab
CERN | A. Grudiev, A. Latina, S. Doebert, Z. Vostrel, Y. Zhao, B. Humann, A. Lechner, A. Kurtulus, R. Mena Andrade, J.L. Grenard, A. Marcone, M. Calviani, W. Bartmann, Y. Duthell, H. Bartosik, K. Oide, F. Zimmermann, M. Benedikt
INFN-LNF | C. Milardi, A. De Santis, O. Etisken, S. Spampinati
SLAC | T. Rauberheimen
KEK: | Y. Enomoto, K. Furukawa
and L. Bandiera, M. Soldani, A. Sytov (INFN/Ferrara), A. Bacci, M. Rossetti Conti (INFN/Milano) | 

## Slide 3
3
Content
Where we are in FCCee
Injector parameters (for the choice of key technology)
  Pre-requisite for linacs technology: conventional normal conducting technology based on the SwissFEL facility (at the Paul Scherrer Institut)
  FCC CDR0 as a starting point
Baseline layout: linacs, positron source and damping ring
Some remarks
Summary

## Slide 4
Where we are in FCCee
4
Injector complex, total length ~1.1 km
SPS to be used as a Pre-booster
Electron-Positron collider
~90.7 km

## Slide 5
5
Injector parameters (Z-mode)
K. Oide, FCC week 2023 talk
 | SPS | HE Linac | Unit
Injection energy | 6 | 20 | GeV
Bunch charge both species | 4.0* | 4.0* | nC
Repetition rate | 200 | 200 | Hz
Number of bunches | 2 | 2 | 
Bunch spacing | 25 | 25 | ns
Norm. emittance (x, y) (rms) | 10,10 | 10,10 | mm mrad
Bunch length (rms) | ~1 | ~1 | mm
Energy spread (rms) | 0.3 | ~0.1 | %
*Maximum charge to be injected into the collider rings 4 nC (bunch pop. 2.5x1010 particles)
Target bunch length and energy spread at the linac end, TL from HE linac to booster will include an energy compression (and bunch decompression)
The bunch-by-bunch intensity will arbitrarily vary from 0 to 100%, depending on the intensity balance between the collider rings
Bunch-by-bunch intensity fluctuation: 5% (Z mode), 3% (WW, ZH, tt)

## Slide 6
6
Injection time – HE linac option
5 ms
25 ns
Collider rings, 11200 bunches
Filling from scratch 305.4 s for each species (3.5 nC/bunch)
Total filling time from scratch 2x305.4 s = 610.8 s (~10 min)
Booster ring, 11200 bunches, Injection time 28 s, Ramp up 0.32 s, Flat-top 1.9 s, Ramp down 0.32 s
5600 rf pulses x 2 bunches (28 s)
1 injection
Booster ring
Cycle time 30.54 s
5600 rf pulses x 2 bunches (28 s)
≥ 2.54 s
Linac up to 20 GeV
Collider rings, top up (Z mode) – 200 Hz
Collider filling time 30.54 s for each species
In top up, the injector will run continuously, and the reliability becomes an important aspect for the Injector design.
Collider parameters from the mid-term review:
- Bunch charge 34.24 nC, bunch pop. 2.14E11
D = 5%, 1.712 nC (charge for top up)  is there margin on this 5%?
Lifetime (t2): 1240 s (~21 min)
ttop-up = Dt2 = 62 sec (D = ttop-up/t2)
Injection time for one specie: 30.54 s, top-up time for both species 61 sec

## Slide 7
7
Schematic layout of Injector complex – work breakdown structure
WP1. Electron source and linacs (A. Grudiev, CERN)
WP3. Positron source and capture system
(I. Chiakovska, IJCLab)
WP4. Damping ring and return transfer line
(C. Milardi LNF INFN)

## Slide 8
8
Electron source
Provide electrons for positron production and injection into CR, it is based on the SwissFEL gun
Two laser systems, each for one bunch (as in SwissFEL)
Top up injection scheme: Robust solution to preserve the emittance for different bunch charge
Bunch-by-bunch intensity fluctuation: 5% (Z mode), 3% (WW, ZH, tt)
SwissFEL RF gun
Courtesy of Zdenek Vostrel and Steffen Doebert

## Slide 9
Key properties listed in the table, reached
Courtesy of Zdenek Vostrel and Steffen Doebert
Bunch parameter | Simulation | Target
Transverse emittance | 3.14 mm mrad (rms) | < 4 mm mrad
Bunch length | 0.96 mm (rms) | ~ 1 mm (or shorter)
Energy | ~ 190 MeV | ~ 200 MeV
Energy spread | 390 keV (0.2 %) | < 0.5 %
Peak charge | 5 nC | 5 nC
Emittance evolution for 5 nC charge
Electron source

## Slide 10
Courtesy of Zdenek Vostrel and Steffen Doebert
Robust solution to preserve the emittance for different bunch charge
Large contribution from 5% particles
Cutting particles based on energy or transverse position
Emittance for different charges (nominal design charge is 5 nC)
Electron source

## Slide 11
Beam dynamics design (start-to-end simulations) provides specification for accelerating structure design: aperture, RF frequency, structure length, gradient, etc.
RF design of accelerating structures (S-, C-band, 2.0 GHz)
RF module layout and parameters are put together based on the above input and the parameters of the RF power sources
Klystron abbrev. | Linac | Freq. | Peak power specification | Rep. Rate | RF pulse length | Duty factor | Average power | Required numbers
 |  | [MHz] | [MW] | [Hz] | [ms] | [1e-3] | [kW] | 
Kly_p | p-linac + Ecomp | 2004 | 80 | 200 | 5 | 1 | 80 | 16 + 1
Kly_e | e-linac + e-source HE-linac S-band | 2806 | 80 | 200 | 3 | 0.6 | 48 | 10 + 1 82
Kly_c | c-linac | 2806 | 50 | 400 | 3 | 1.2 | 60 | 35
Kly_HE_C | HE-linac C-band | 5611 | 50 | 200 | 3 | 0.6 | 30 | 86
e-, common, e+ and HE-linacs: design steps
A. Grudiev, J.-Y. Raguin, S. Bettoni, M. Schär et al.

## Slide 12
12
Positron, Electron, Common, HE linacs
RF module summary table for all linacs
Inc. WG loss and 90% margin
Same for quads, corrs. and BPMs
Peak gradient  Average power: up to 7.5 kW/m, power density on outer wall radius up to 104 kW/m2
A. Grudiev, A. Kurtulus et al.

## Slide 13
13
Electron-, Common, Positron and HE-linacs
SwissFEL linac
RF technology: tuning-free from PSI
Each RF module: one klystron/modulator, rf WG network, 2 rf structures (3-m long), LLRF, cooling system, 2 BPMs, 2 quads and 2 correctors. Total length: 7.5 m
Common linac at 400 Hz during positron production

## Slide 14
High gradient & Breakdown rate
Tuning-free technology: PSI has developed a production line of high technological content for high-quality, high gradient C-band accelerating structures for the SwissFEL project (~120 structures) https://doi.org/10.1038/s41566-020-00712-8
  Gradient and BDR at 100 Hz: max 55 MV/m, BDR=1E-07, operation at 30 MV/m
Collaboration CERN-PSI on first-tuning-free X-band Accelerating Structures: CLIC X-band prototypes (max gradient ~120 MV/m at 100 Hz) https://doi.org/10.1109/TNS.2022.3230567
Collaboration Elettra-PSI: free tuning free S-band Accelerating Structures https://doi.org/10.1016/j.nima.2023.168543
  Gradient and BDR at 100 Hz: max 40 MV/m, BDR=1E-07, operation at 30 MV/m
  Max gradient was limited by the RF source
As a conclusion: present gradients (30 MV/m at 200 Hz, 21.5 MV/m at 400 MV/) are well supported by experiences, thermo-mechanical analysis to be performed with higher dissipated power density
3m-long S-band structure brazed in one piece

## Slide 15
15
Electron, Common, HE linacs – RF power density
400 Hz
200 Hz
200 Hz
Linac | Freq. | Peak gradient | Average power <Pin> | Structure length | Average power <Pin>/L*3/4 | Outer wall radius | Power density on outer wall radius
 | [GHz] | [MV/m] | [kW/structure] | [m] | [kW/m] | [mm] | [kW/m^2]
p-linac | 2.0 | 20 | 31 | 3 | 7.5 | 60 | 125
e-linac HE-linac S-band | 2.8 | 29.5 | 18 | 3 | 4.5 | ~40 | 112.5
c-linac | 2.8 | 23.4 | 22.5 | 3 | 5.6 | ~40 | 141
HE-linac C-band | 5.6 | 28.8 | 11 | 3 | 2.8 | ~20 | 140
SwissFEL C-band | 5.7 | 30 | 5 | 2 | 1.9 | ~20 | 95

## Slide 16
Positron source and capture linac
I. Chaikovska et al.
Accepted e+ yield is a function of primary beam characteristics + target + matching device + capture linac + beam transport + DR acceptance
Primary (drive) beam parmeters
Conventional target
Matching device (MD)
Capture linac and solenoid focusing

## Slide 17
17
Positron source: matching device
Flux concentrator (FC) - SuperKEKB source
SC solenoid (PSI)
FC: lower peak field and aperture, fixed target position, challenging power source working at 200 Hz, robust and reliable solution…
HTS solenoid: higher peak field and aperture, flexibility on the field profile and target position, DC operation, innovative solution in application for e+ capture…
Magnetic field profiles
18.2 T @15K@2kA reached

## Slide 18
N. Vallis et al., Proof-of-principle e + source for future colliders, accepted PR AB.
Design phase well advanced, several components are ordered
Installation on the Porthos extraction line ongoing
Ongoing collaboration with CERN STI for the target
Experiments in 2025/2026
PSI Positron Production (p-cubed) experiment

## Slide 19
Baseline structure: large-aperture (Φ = 60 mm) TW L-band @ 2 GHz, 9π/10, 3-m long, 20 MV/m. 5 RF structures are used to accelerate the e+ beam up to ~200 MeV where there is the electron/positron separation
Baseline solenoid configuration: 0.5 T NC solenoid, magnetic field uniformity, solenoid focusing first 50 m, quadrupole focusing downstream
Positron source: capture linac

## Slide 20
Safety margin for the acceptance in the DR and transport in the linac (13.5 nC)
Drive beam parameters have been also updated based on this safety margin
The studies on the positron source based on the SC solenoid are well advanced
Positron source and capture linac
I. Chaikovska et al.
@ 1.54 GeV (DR entrance)
Vertical Phase space
Horizontal phase space
Long. phase space

## Slide 21
21
Damping Ring and Return Transfer Lines
Damping Ring 1.54 GeV – C=242 m
Energy Compressor
Injection dogleg
Extraction dogleg
C. Milardi, A. De Santis, S. Spampinati, O. Etisken
Damping ring acceptance
R56 = 0.40 m
One S-band RF module to chirp the beam. Accelerating voltage 54 MV (70.5 MV available)
Two S-band RF modules to remove part of the chirp. Accelerating voltage 110 MV (140MV available)
LPS from positron linac
Bunch profile to c-linac
Before BC
After BC
Bunch Compressor
Analytical Energy Compressor

## Slide 22
22
Damping Ring and Return Transfer Lines
Layout in CDR0 for cost estimate: DR and TLs design has been complete
DR acceptance larger than 83% can be achieved with the help of the ECS installed between the p-linac and the DR injection line
A BCS has been included in the return line from DR to c-linac (max compression factor 5)
Alternative DR designs are being considered
  Different types of cells and magnets are being evaluated to reduce the number of elements
  Preliminary study for a DR at higher energy is on-going
106 x 53 m
400 MHz, RF cavity

## Slide 23
Summary
A baseline for the pre-injector layout was ready for the mid-term review (week 42)
  Cost estimates for the hardware, technical infrastructures and civil engineering are available for the project
Pre-Injector can fulfill the (partially new) requirements for the collider rings
  but there is still room for some optimizations
P3 project is underway, and will be a first step towards the FCCee positron source
Several presentations with more details were given at FCC week 2023
23

## Slide 24
Credits
24
This work was done under the auspices of CHART (Swiss Accelerator Research and Technology) Collaboration, https://chart.ch - CHART Scientific Report 2022: https://chart.ch/reports/
PSI | R. Zennaro, M. Schaer, N. Vallis, B. Auchmann, I. Besana, S. Bettoni, H. Braun, M. Duda, R. Fortunati, H. Garcia-Rodrigues, D. Hauenstein, E. Hohmann, R. Ischebeck, P. Juranic, J. Kosse, F. Marcellini, U. Michlmayr, S. Muller, G. L. Orlandi, M. Pedrozzi, J.-Y. Raguin, S. Reiche, M. Seidel, R. Rotundo, S. Sanfilippo, M. Zykova all the technical groups involved in the P3 experiment
IJCLab | I. Chaikovska, F. Alharthi, V. Mytrochenko, R. Chehab
CERN | A. Grudiev, A. Latina, S. Doebert, Z. Vostrel, Y. Zhao, B. Humann, A. Lechner, A. Kurtulus, R. Mena Andrade, J.L. Grenard, A. Marcone, M. Calviani, W. Bartmann, Y. Duthell, H. Bartosik, K. Oide, F. Zimmermann, M. Benedikt
INFN-LNF | C. Milardi, A. De Santis, O. Etisken, S. Spampinati
SLAC | T. Rauberheimen
KEK: | Y. Enomoto, K. Furukawa
and L. Bandiera, M. Soldani, A. Sytov (INFN/Ferrara), A. Bacci, M. Rossetti Conti (INFN/Milano) | 

## Slide 25
Thank for your attention!!
Warm autumn colours at the PSI Campus

## Slide 26
Common linac | Baseline | Option 1*
Repetion rate (Hz) | 400 | 400
Gradient (MV/m) | 23.4 | 16.5
Length (m) | 262.5 | 360
Cost for module (MCHF/module) | 1.840 | 2.455
# module | 35 | 26
Total cost (MCHF) |  | 
Cost per meter (kCHF/m) |  | 
Plug power red. |  | -26%
HE linac | Baseline | Option 1*
Repetion rate (Hz) | 200 | 200
Gradient (MV/m) | 29.5 | 20.9
Length (m) | 615 | 885
Cost for module (MCHF/module) | 1.805 | 2.415
# module | 82 | 59
Total cost (MCHF) |  | 
Cost per meter (kCHF/m) |  | 
Plug power red. |  | -28%
Reduction of gradient (and dissipated power)
*Option 1: four RF structures per klystron, total module length: 15 m

## Slide 27
Positron source: target
R. Mena Andrade (SY-STI) et al., FCC week 2023
After several iterations, the current beam parameters provide a solid baseline for the design of the FCC-ee positron source target.
A target made of pure tungsten now is a feasible option. The thermo-mechanical studies show values of temperature and stresses inside of the safety limits of tungsten.
As a next step, a R&D test campaign is foreseen to evaluate different manufacturing options for the target and the hipping of the tubes for the cooling system.
Radiation load to HTS coils
Up to 8MGy/year
Up to 8E-5 DPA/year
Cumulative dose in coils
(one year at Z-pole)
DPA in coils
(one year at Z-pole)
In general, no showstopper, but shielding design to be further optimized
DPA likely acceptable (with annealing cycles)
Limits for ionizing dose to be understood (if any)

## Slide 28
28
Injector layout with DR at higher energy
The present positron yield would allow positrons to be generated at a lower electron beam energy. Preliminary study showed no more stringent specifications for the target, compatibility with present target study.
Common linac: Rep rate 200 Hz instead of 400 Hz  less average rf power, higher accelerating gradient, shorter linac
Dedicated linac for electron and positron before the DR.
Overall, the cost of the hardware remains approximately the same, the costs of the CE and TI to be evaluated

## Slide 29
29
Some general remarks
RF systems at 2.0, 2.8 and 5.6 GHz to be developed: Pulsed RF sources are moving to higher repetition rate but still not mature, 400 Hz is challenging for klystrons and HV modulators  collaboration with suppliers for development of prototypes
RF structures: peak gradient vs dissipated power and breakdown rate (prototypes), high power density to be dissipated  thermo-mechanical analysis to be performed
Damping ring acceptance must be confirmed with collective effects, IBS, etc…
Positron source: AMD based on SC solenoid, demonstrator will provide several information, AMD based on FC to be verified the operation at 200 Hz in term of ohmic losses on the FC and high-power requirement for the pulsed PS
Electron source: stability and top-up scheme to be verified up to 5 nC

## Slide 30
BR
Trasfer line with bunch decompression/EC
With this option, the specifications for the linac end and for injection into the BR can be partially decoupled
More flexibility for the linac but more complex transfer line
Independent tuning of the bunch length (operating rf phase, R56, zero-crossing) and energy spread (RF voltage)
R56
Short linac
Energy compressor at linac end

## Slide 31
SPS vs HE linac performances
31
HE linac delivers beam with 4x small energy spread and 16x smaller transverse emittance. The Booster injection will be difficult and will need additional time at max energy to damp.
Collective effects in the SPS have not been evaluated for the FCC-ee bunch train (5 nC!)
HE linac allows for higher injection energy into the booster (e.g., 20 GeV versus 16 GeV from SPS) and injection into the booster would be much more flexible (low magnetic field at booster injection and impedance effects)
  further energy increases through linac extensions could be possible, should an even higher injection energy turn out to be desirable AND would be fully independent of any hadron beam operation, and it could serve for many additional applications.
  the construction and commissioning could proceed in parallel to any SPS or LHC hadron beam operation, while the reconstruction and use of the SPS could not begin before the end of the HL-LHC programme
SPS as a pre-booster during Z running would be used most of the time for lepton operation. HE linac would not impact hadron beam operation. SPS option would have major repercussions for any hadron beam programme in the SPS, and also implications for any use of the SPS as a future hadron beam injector to the LHC or FCC-hh