## Slide 1: Linear colliders Sustainability studies for LCs Life Cycle Assessments
Steinar Stapnes
CLIC mini workshop 11.12.23 – hence focus on CLIC

## Slide 2: Initial considerations
Resource optimization as traditionally done for accelerators:
  Length/complexity -> construction cost
  Power/energy consumption -> operating costs
  Traditionally we optimize for energy reach and luminosity wrt to cost and power
Sustainability in a wider sense adds new construction and operation optimization criteria:
  Energy use not only costs but also CO2, embedded CO2 in construction materials and components, rare earth usage, responsible sourcing in general for all parts, landscaping, integration in local communities, life cycle assessments including decommission and many more issues
Approaches to increase sustainability
Overall system design
  Compact accelerator -> high gradients (high field magnets for rings)
  Energy efficient -> low losses (wall-plug to beam)
  Effective -> small beam sizes to maximize luminosities
  Energy recovery concepts
  Civil engineering including landscaping and “community” integration
Subsystem and component design, e.g.
  High-efficiency cavities and klystrons
  Permanent magnets, HTS magnets
  Heat-recovery. e.g. in tunnel linings, possibly other components
  Responsible sourcing and material choices for all parts
Sustainable operation concepts
  Renewables
  Adapt to power availability
  Exploit energy buffering potential
  Recover low grade energy (heat)
Good progress on the red points (was also part of the our radiational approach), initial progress/focus on the yellow/black ones

## Slide 3: From costs and power to sustainability and life cycle assessments
Reduce power/energy (hand in hand with cost optimisation)
Operation energy use means carbon –> use the minimum energy, of the right type and at the right time, compensate
Life Cycle Assessments

## Slide 4
Power optimization – examples
Design Optimisation:
All projects aim to optimize – most often energy reach, luminosities and cost. Power is becoming at least as important, maybe even compromising ultimate performance for power saving.
Technical Developments:
Technical developments targeting reduced power consumptions at system level high efficiency klystrons and RF systems generally, RF cavity design and optimisation, magnets (traditional SC and HTS including cryo, and also permanents magnets).
Heat recovery:
Already implemented in point 8 for LHC
Tunnel heat recovery study by ARUP in 2022, results interesting but …
Parameter scans to find optimal parameter set, change acc. structure designs and gradients to find an optimum
The designs of CLIC, including key performance parameters as accelerating gradients, pulse lengths, bunch-charges and luminosities, have been optimised for cost and power

## Slide 5: Nanobeams
A very important part of increasing the energy efficiency of a collider is reducing the beamsizes at the collision point.
This involved optimisation of every part of the machine, from injectors to damping rings to main linacs/rings to beam-delivery/interaction point.
and covers in terms of design and technologies:
beam-dynamics, steering and feedback, precise instrumentation, alignment, stability (passive/active), injection, extraction, precise magnets, vacuum, studies of ground vibrations and stray-field, temperature control and more.
This has been extensively developed and prototyped in CLIC, ILC, FEL linacs.
Beyond studies and HW developments, test in beam facilities as ATF2, FACET, light sources and FEL linacs are essential.

## Slide 6
High Eff. Klystrons
L-band, X-band (for applications/collaborators and test-stands
High Efficiency implementations:
New small X-band klystron – recent successful prototype
Large X-band with CPI
L-band two stage, design done, prototype desirable
Drivebeam klystron: The klystron efficiency (circles) and the peak RF power (squares) simulated for the CLIC TS MBK (solid lines) and measured for the Canon MBK E37503 (dashed lines) vs total beam power. See more later.
Publication: https://ieeexplore.ieee.org/document/9115885

## Slide 7: Magnets also important in Higgs factories
ZEPTO (Zero Power Tuneable Optics) project is a collaboration between CERN and STFC Daresbury Laboratory to save power and costs by switching from resistive electromagnets to permanent magnets.
For CLIC the dominant power is in the drive-beam quadrupoles, successfully prototyped and tested as permanent (two different strengths) magnets, and also dipoles (in drivebeam turn arounds)
Longitudinal gradient dipole magnet for the CLIC DR (CIEMAT)
1.5 TeV CLIC power
Magnets second largest
doi:10.18429/JACoW-IPAC2018-MOPML048 CC-BY-3.0
HTS magnets might be of interests in all circular and linear Higgs factories to reduce power.

## Slide 8: R&D for Improved SRF Performance & Sustainability
Better surface treatments and cavity shapes improve cavity performance. Lots of progress in last 10 years
Raise gradient: fewer cavities for same beam energy. Short term goal: 31.5MV/m -> 35MV/m Medium term goal: 45MV/m Lab record: 59MV/m
Improve Q0: reduce cryogenic losses (1W @ 2K requires ~750W AC power!) Short term goal: 1E10 -> 2E10
New treatments reduce / avoid need for electropolishing treatments (involving aggressive chemicals)
R&D into replacement of bulk niobium cavities with Nb or Nb3Sn coated copper: reduce niobium consumption, increase performance (arXiv:2203.09718)

## Slide 9: From costs and power to sustainability and life cycle assessments
Reduce power/energy (hand in hand with cost optimisation)
Operation energy use means carbon –> use the minimum energy, of the right type and at the right time, compensate
Life Cycle Assessments

## Slide 10: Running on renewables and when electricity is cheap
Two studies in 2017:
Supply the annual electricity demand of the CLIC-380 by installing local wind and PV generators (this could be e.g. achieved by 330 MW-peak PV and 220 MW-peak wind generators) at a cost of slightly more than 10% of the CLIC 380 GeV cost.
  Study done for 200 MW, in reality only ~110 MW are needed
Self-sufficiency during all times can not be reached but 54% of the time CLIC could run independently from public electricity supply with the portfolio simulated.
Can one run an accelerator as CLIC in a mode where one turn “on” and “off” depending prices (fluctuating with weather, demand, availability etc) ?
Specify transition times (relatively fast for a LC) and the annual luminosity goal
Significant savings – but the largest saving is the obvious one, not running in the winter.
Flexibility to adjust the power demand is expected to become increasingly important and in demand by energy companies.
More information (link)
Victor Gleim CC-BY-SA-4.0
C. Gaunand, B. Remenyi: Introduction to Demand Side Flexibility
ESSRI Workshop 2022 https://indico.esrf.fr/event/2/contributions/94/
(Regenerative) Power availability varies
Linear accelerators have no stored beam -> ideal for flexible operation
Study by Fraunhofer institute considered running on renewables and participating in demand side flexibility

## Slide 11: Green ILC
Asurnipal CC-BY-SA-4.0
For ILC: renewable energy available (Tohoku Electric Power) in local grid at ~23% level, need 0.5-1 % for ILC. Additionally considers increased CO2 absorption to be fully neutral.

## Slide 12: Power and energy
Very uncertain but MTP assumes 120 MCHF/TWh beyond 2026.
With “standard” running scenario (on the right) every 100 MW corresponds to ~0.6 TWh annually, corresponding to ~75 MCHF annually (European costing)
Typical power numbers for Higgs factories on the right – see also table on page above.
The CERN “standard” running scenario is shown below right, used to convert to annual energy needs.

## Slide 13: Sustainability during operation
Operation costs dominated by energy (and personnel, not discussed in the following)
Reducing power use, and costs of power, will be crucial. Other consumables (gas, liquids, travels … ) during operation need to be well justified. Align to future energy markets, green and more renewables, make sure we can be flexible customer and deal with grid stability/quality.
Carbon footprint related to energy source, relatively low already for CERN (helped by nuclear power), expected to become significantly lower towards 2050 when future accelerators are foreseen to become operational (in Europe, US and Japan).
Provided we can run on green mixtures (PPA example at CERN, also (hopefully) built fully into the green ILC concept) we can also contractually chose green options. LCs are very suited for this (variable power load).
A rough estimate, assuming ~50% nuclear and ~50% renewables (as wind/sun/hydro):
1 TWh annually equals ~12.5 ktons CO2 equiv. annually
(note: this is factor ~3 below the current French summer month average)

## Slide 14: From energy to CO2 – in 2040-50
From: https://app.electricitymaps.com/zone/FR
Contains also g/kWh per source
What is the carbon intensity of energy in ~2050 (operation):
50% nuclear and 50% renewable give ~10-15g/kWh
France summer-months are today ~40g/kWh
ILC has a green implementation concept including compensation and contracting renewable energy
Reductions predicted (LINK)

## Slide 15: From costs and power to sustainability and life cycle assessments
Reduce power/energy (hand in hand with cost optimisation)
Operation energy use means carbon –> use the minimum energy, of the right type and at the right time, compensate
Life Cycle Assessments

## Slide 16: Sustainable Construction – Life Cycle Assessment
Responsible purchasing – and understanding the impact on our supply chain, costs and potential for changes – will be essentials for future projects (CERN implementation information from E.Cennini)
For carbon emission the construction impact will be much earlier and might be more significant (also rare earths and many other issues etc):
  Construction: CE, materials, processing and assembly – not easy to calculate
  Markets will push for reduced carbon, responsible purchasing crucial (see right) – construction costs likely to increase
Decommissioning – how do we estimate impacts ?
The report: https://edms.cern.ch/ui/#!master/navigator/document?D:101320218:101320218:subDocs

## Slide 17
Only B6 discussed in all the slides above, now discuss A1-A5 for the CE
Missing A1-A5 for accelerator, some surface installations, all maintenance and upgrades, all EoL activities

## Slide 23
CLIC around 11km, ILC around 20 km
A1-A3 material only dominates
Around 6kton/km for CLIC DB and ILC

## Slide 26
Include all tunnels (access, transfer, damping rings), shafts and caverns.
A1-A5
Scaling to main linac tunnel lengths we are now at 11-14 kton/km for the CLIC DB and ILC

## Slide 30: Looking at the impact of the accelerator components
Study to estimate the Green House Gas emissions from raw materials in CLIC 2-beam module, including waveguides and supports
~2.5t CO2-eq / m: -> about half of CO2 for tunnel
Half of CO2 impact is steel for supports -> optimization potential
Services (power, cabling, cooling, ventilation) not included
Situation in magnet-heavy sections (e.g. turn-arounds, bends, damping rings) may be different
CO2 impact of accelerator components is comparable to CO2 of main tunnel – to be studies but easily 5 kton/km
Note: Careful with material processed away, recycled or not ?

## Slide 31
A1-A5: Tunnel construction (ILC and CLIC DB dimensions) is around 6kton/km
Add shafts, caverns , access tunnels, DR, etc + from 30 to 60%
Add transports, power used in construction, etc + 25%
= > ILC (20km) around 270 kton, CLIC (11 km) around 125 kton
Possible savings (but at a cost to be defined) of ~40%
Adding accelerator components and injectors more consistently (possibly 50% increase – very early days)
Operation (in ~2050)
Nuclear 5g/kWh and re-newables (sun/wind/hydro) 20g/kWh – suitable for Europe, what is suitable as goal for Japan ?
Can be higher with poor energy mix, can be lower with good contracting (good mix)
Assume 50/50 mix => Energy use estimated for LCs 0.6-0.8 TWh annually, i.e. around 10 kton CO2
France in summer months are at ~40 g/kWh, a factor three better towards 2050 within reach ?
In Japan this is much harder, contracting on low carbon energy an important tool
A green field site offers more flexibility for compensation (as in the green ILC approach)
Power nevertheless has huge cost impact, and secondary effects on CO2 (more material)
Wrap-up

## Slide 32
Towards Carbon Accounting with LCA
Work in progress – this example is closest to the CLIC drive-beam parameters, detectors and computing (and travels) not considered

## Slide 33
Thanks:
CLIC and ILC teams
Benno List, Maxim Titov, Shin Michizono, Tomoyuki Sanuki, Nobuhiro Terunuma, Takayuki Saeki
John Osborne, Liam Bromiley and the entire ARUP team
Among them slides from Suzanne Evans ARUP talks at LCWS 2023 and yesterday
… many more
Concluding:
Construction in the 2030’ies the most (time)critical carbon emission to address (A1-A5)
LCA methodology is the way to go for sustainability studies, also for other parts (many missing) and other phases. Provides us with handles for optimisation.
  Very good to see all the examples in this workshop of using or thinking about using this methodology
Upgrades removing components and decommissioning likely other major CO2 sources
All other factors to be considered, e.g. radiation, acidity, etc

## Slide 35: Power and energy
CERN “standard” running scenario used to convert to annual energy use
Power at 250-380 GeV in the 100-150 MW range for the projects above, reaching ~500 MW at 3 TeV for CLIC
With a running scenario on the right this corresponds to 0.6-0.8 TWh annually
CERN is currently consuming 1.2 – 1.3 TWh annually
Includes studies of overall designs optimisation to reduce power, SRF cavities (grad,Q), cryo efficiency, RF power system (klystrons, modulators, components), RF to beam efficiencies, permanent magnets, operation when power is abundant, heat recovery, nanobeam and more.
Recent overview (LINK)

## Slide 36: Sustainability: towards a Life Cycle Assessment (LCA) for LCs
Recent C3 paper using the LCA “methodology”, also including considerations for other projects, is also well worth studying: LINK
What is the carbon intensity of energy in ~2050 (operation):
50% nuclear and 50% renewable give ~10-15g/kWh
France summer-months are today ~40g/kWh
ILC has a green implementation concept including compensation and contracting renewable energy
Reductions predicted (LINK)
Around 11-12 kton/km main linac (CLIC DB and ILC)
LCA report for Civil Engineering: LINK