## Slide 1
The LDG RF Activities
Giovanni Bisoffi, INFN
CLIC Mini Week, CERN
December 12,2023

## Slide 2: European Particle Physics Strategy and its updates
Strategy 14 July 2006
Update 30 May 2013
Update 19 June 2020
“(…) cornerstone of Europe’s decision-making process for the long-term future of the field. Mandated by the CERN Council, it is formed through a broad consultation of the grass-roots particle physics community (…) and it is developed in close coordination with similar processes in the US and Japan (…)”
Chairperson
1/CERN Member State,
1/lab of the major European Laboratory Directors’ Group, LDG
CERN Director-General,
SPC Chairperson,
ECFA Chairperson.
Invitees:
President of the CERN Council,
1/Associate Member States,
1/Observer State,
1/European Commission, JINR
Chairs of ApPEC, FALC, ESFRI, and NuPECC
Members of Physics Prep Group
European Strategy Group

## Slide 3: European Laboratory Directors Group (LDG)
Dialogue among Lab Directors and CERN
Input to the ESPP, liaise with EU Commission and national funding agencies, institutes and universities
Maximise national benefits of investment in fundamental research and in CERN
Look at activities outside CERN’s Member States, and of other groups in PP and related fields
Draw up and maintain a prioritised accelerator R&D roadmap towards future large-scale facilities for PP
Coordinate the accelerator R&D activities on the roadmap, until the next SU
Lab representatives from NIKHEF, INFN, STFC, CIEMAT, CERN, DESY, RAL, CNRS, PSI
Standing observers: ECFA Chair, SPC Chair, CERN Directorate

## Slide 4: Approved R&D strategy and its implementation
Accelerator R&D Roadmap presented to SPC in March 2022 and adopted by the Council
Each technology area deeply surveyed
Key R&D objectives, deliverables (at 5 and 10 years)
Resource estimates, needed facilities
Emphasis on: e+e- programme and sustainability
https://doi.org/10.23731/CYRM-2022-001
After that: expert coordination panels, working with LDG (“extended LDG”) and accelerator R&D community to begin implementation of roadmap recommendations
Lab representatives from NIKHEF, INFN, STFC, CIEMAT, CERN, DESY, RAL, CNRS, CEA, PSI - Standing observers: ECFA Chair, SPC Chair, CERN Directorate
Extended LDG members: on HF-Magnets , Muon C, ERL, Laser Plasma Acc , RF

## Slide 5: LDG and the and Acc R&D Coordination panels
High-field magnets
High-gradient plasma and laser accelerators
Bright muon beams and muon collider
Energy Recovery Linacs
High-gradient RF structures and systems
The 5 R&D Themes
(~ feasible start dates)
Scope
R&D needs
Teams
Time horizon

## Slide 6: 1. High Field Magnets
HFM Key for new colliders, beyond the LHC
Goals (on conductor and magnets):
16 T Nb3Sn technology (large-scale, industry-optimised) for FCC-hh, demonstration before 2026
20 T at 10÷20K with HTS (proof-of-principle, tapes and cables with industry)
Decades needed, broad expertise and coordination, infrastructures, industry: CARE, EUCARD, EUCARD2, ARIES, now I-FAST, CERN-High Field Magnet and US-MDP
Cross-cutting activities: materials, powering and protection, infrastructures and instruments, quench detection and protection
New infrastructures needed!
12 T prototypes expected in INFN-Ge and CERN by 2025; CEA: a 16 T prototype plan
Focus on stress/strain sensitivity and degradation of Nb3Sn: mech. strength, higher JC, stress-adapted magnet design
Hybrid LTS/HTS magnets: ReBCO tapes or Bi-2212 cables (still a long way to go for 16 T)
Panel chairs: P. Vedrine, M. Lamont
Notes: Nb3Sn: production scale through robust design, industrial manufacturing processes and cost reduction, taking as a reference the HL-LHC magnets, i.e. 12 T
Rare earth Barium Copper Oxide
INFRASTRUCTURES: The cross-cutting technology activities will be a key seed for innovation. The scope includes materials
and composites development using advanced analytics and diagnostics, new engineering solutions
for the thermal management of high-field magnets, and the development of modelling tools within a
unified engineering design framework. We propose to explore alternative methods of detection and protection
against quench (especially important for HTS) including new measurement methods and diagnostics.
Finally, dedicated manufacturing and test infrastructure required for the HFM R&D programme,
including instrumentation upgrades, needs to be developed, built and operated through close coordination
between the participating laboratories.
Hybrid LTS/HTS SC - In transient conditions, rather lower minimum propagation currents have also been observed due to the long magnetic diffusion time constant in the pure aluminum compared with the steady-state recovery currents [3], [4]. To solve these problems, a new kind of LTS/HTS superconductor is proposed where HTS is used as a stabilizer in place of low resistive metals, such as pure aluminum. By this modification, the steady-state cold-end recovery currents can be improved as the HTS has very low resistance as compared with pure aluminum.

## Slide 7: 2. Muon Collider
5 GeV p → p → m,
cooled and
accelerated
at 3/10 TeV
After the target: 200 mm bore 15÷20 T solenoid
(synergy with fusion)
Cooling channel demonstrator is key:
HG room-T cavity in
high-field SC solenoid
3/10 TeV m acceleration via RLA/FFAG and RCS (with 14 T
Magnets)
For long-term sustainability of collider physics: strong suppression of synchrotron radiation (m vs. e) power consumption at 10 TeV lower than CLIC at 3 TeV; L/Pbeam increasing with collision energy
Needed: a fully integrated design (on target, detector, cooling and accelerator chain)
Needed from RF technology: e.g. HG room-T cavity in high-field SC solenoid, 20 T solenoids (HFM), ERL linac
MuCol Collaboration: 32 partners Institutions in Europe, plus USA (waiting for P5), China, India: 7-15 M€ thus far
After 2026, CDR R&D with a m-cooling demonstrator
Panel chairs: S. Stapnes, D. Schulte
Notes: 3 → 10 TeV with added accelerator ring and with a new collider ring

## Slide 8: 3. Colliders based on Energy Recovery Linacs
ERL-based colliders: LHeC, FCC-eh, CERC, ERLC
Current facilities: S-DALINAC (Darmstadt), MESA (Mainz), CBETA (Cornell, US), cERL (KEK), Recuperator facility (BINP)
New ERLs: Berlin-PRO, PERLE, CEBAF5, ERL-ecool at EIC
Collaboration: iSAS project approved (July 10, 2023): 1000 person*months, 12.6 M€, 4 years
Needed from SRF technology: Q~1011 at higher T (4K); HOM extraction at high-T; FE-FRT to control transient beam loading and microphonics; dual-axis cavities; ...
Circular ER Collider
LHC/FCC-based
electron-hadron
Collider
Energy Recovery Linear Collider
Multipass accel/decel (energy efficient)
«Linac» beam quality, «ring» high Iave
Panel chairs: J. D’Hondt, M. Klein
Notes: electron-hadron versions of LHC and FCC (LHeC and FCC-eh)
Luminosity increase for physics applications by one or more orders of magnitude at a power consumption comparable comparable to classic lower luminosity solutions
Using Energy Recovery Linacs (ERL) located in the same-size 100 km tunnel would allow a large reduction of the beam energy losses, and therefore a reduction of the power consumption, while providing higher luminosity. Recovers beam energy loss (by recovering the energy); higher L, higher energy (final stage of acceleration without going around and more efficient in accelerating/losing energy); recycles particles, not only energy

## Slide 9: 4. High-gradient plasma and laser accelerators
Electron bunch or laser (v~c) induce wave-like separations of electrons from ions (~ at rest)
Experimental studies on key R&D: e+ bunch acceleration, sufficient bunch charge, nm-scale emittance, staging of multiple structures, spin-polarisation preservation, high rep-rate and power handling, high rep-rate lasers, energy efficiency.
Pre-CDR and Collider Feasibility Report (2025), CDR in 2026-2030 with demo of technical parameters.
A collider option beyond 2050 (after FCC-hh)
HALHF
HALHF, with both RF and PBA: e- 500GeV electrons onto e+ 31GeV positrons
Driving discipline is photon/material science: ELI and EuPRAXIA distributed facilities.
R&D strategies at CERN (AWAKE), CLARA, CNRS, DESY, Helmoltz’s, INFN, RAL, and abroad.
HEP-related programmes: EU (EuroNNAc), the US (DOE) and world-wide (ALEGRO).
Panel chairs: W. Leemans, R. Patahill
Notes: Hybrid Asymmetric Linear Higgs Factory (HALHF)

## Slide 10: RF = increase beam energy efficiently and reliably
Per year: 10 M€, 90 FTE (nominal, ~30% higher than actual - ref. Accelerator R&D strategy)
GOAL
Notes: Including: 3 M€ and 18 FTE in 5 years for MC test stand (obsolete)

## Slide 11: SRF Cavities: reduce operational cost (Q0 ↑) and capital cost (Eacc ↑)
Higher Eacc
ILC – higher Eacc  smaller linac (= lower capital cost)
MC – quick acceleration (vs m-lifetime)
FCC – fewer cavities  smaller RF installation
Higher Q0
FCC, ERL, ILC – lower RF losses, cryogenic power minimised.
Others: Reproducibility, cost, industrial manufacturing
Niobium (Tc=9.2K, Tcryo= 2K is mandatory)
Eacc > 40 MV/m, Q0 > 1010
Theoretical limits close? ≤ 57 MV/m s.h. ….
Thin films (higher-TC materials)
Eacc x 2 higher than Nb (≤100 MV/m); Q0>1010 at Tcryo=4.2K (66% saving in Pele,cryo) – 40% cryo-plant cost saving (cryocoolers?))
Cavity types – mostly elliptical: 1.3 GHz (3.9 GHz), 802 MHz (401 MHz), 704 MHz (352 MHz), 650 MHz (325 MHz).
NEEDS:
vs. Eacc
Pdiss, ref
(R&D goal)
(mature)
Notes: cryogenic power reduced by factor > 2 with high measured Q0
Grassellino: we discover that the addition during the mild bake of a step at 75deg for few hours, before the 120deg, increases systematically the quench fields up to unprecedented values of 49 MV/m.

## Slide 12: WG2 – Thin film Cavities C. Antoine (CEA) and O. Malyshev (STFC)
1.`Further increase Q and Eacc: surface polishing, treatment (N doping), low/mid/2-step baking, H degas).
2. Improve reproducibility of high-Eacc fields: robots in clean room, in-situ plasma processing.
3. Reduce the cost: Fine → Medium Grain
4. Risk of losing manufacturing capability?
Maintain SRF technology skills in both labs & industry.
Invest in industrial processes (FCC – ~1000 cavities, ILC - 8000 cavities).
CERN (CH), CEA and IJCLab (F), DESY, HZB, Hamburg-Uni (D), INFN (LASA, LNF, LNL), STFC (UK)
  Goals: high Q0 @ 4.2K; much higher Eacc.
  A15 materials: Nb3Sn-on-Nb (USA). Nb3Sn-on-Cu (IFAST EU project, on going)
  SIS (multi-layer): higher performance, less defect-sensitive (sample→cavity, CEA).
  Cu cavity base production R&D: spinning (CERN, INFN), 3D-printing; Cu-surface preparation.
Nb3Sn/Nb
CEA-Saclay, CERN, HZB, HZDR, INFN, STFC, USI, Hamburg U. (DESY), (I.FAST-WP) JLAB, KeK and FNAL
WG1 –Bulk Nb Cavities M. Baylac (IJCLab), C. Madec (CEA) and L. Monaco (INFN)
Notes: medium grain : grain size < 1 mm; large grain : grain size >> 1 cm (: material 35% cheaper, full cavity 5% cheaper)
Few Nb suppliers (1 in China, perhaps 2 in Japan/USA).
Few cavity suppliers (2 in Europe, 2-3 in China, 1 in Japan)
Reduce contamination during assembly (Eacc , field emission-FE)
**************************************************************************
→ higher TC material allows Tcryo = 4.2K instead of 2K, which reduces Pplug by a factor 3.
SIS: . If the superconducting film is deposited with a thickness d < lambda, the Meissner state can be retained at a magnetic field much higher than the bulk Hc1. The strong increase of Hc1 in films allows utilization of RF fields higher than the critical field Hc of Nb but lower than those at which the flux penetration at grain boundaries may create a problem.
A superconductor with little or no magnetic field within it is said to be in the Meissner state. The Meissner state breaks down when the applied magnetic field…
medium grain : grain size < 1 mm; large grain : grain size >> 1 cm (: material 35% cheaper, full cavity 5% cheaper)
Few Nb suppliers (1 in China, perhaps 2 in Japan/USA).
Few cavity suppliers (2 in Europe, 2-3 in China, 1 in Japan)
Reduce contamination during assembly (Eacc , field emission-FE)
**************************************************************************
𝑃_𝑝𝑙𝑢𝑔∝"h" _𝑇 ∝𝑇_𝑐𝑟𝑦𝑜/(300𝐾−𝑇_𝑐𝑟𝑦𝑜 ) → higher TC material allows Tcryo = 4.2K instead of 2K, which reduces Pplug by a factor 3.

## Slide 13: WG3: Fundamental Power Couplers (FPC) and HOM F. Gerigk (CERN), A, Neumann (HZB) and E. Montesinos (CERN)
Transmitting hundreds of kW (W’s in the cold mass) reliably through thin ceramic windows (diameter ~ 5÷ 50 cm) into SRF cavities.
1. Ceramic window! No leak allowed vs. cavity and entire machine, low losses at operating f and T, but brazed, low T-gradient
FCCee (Z→W,H → ttb modes): 112→864 couplers, CW, 400-800 MHz, P = 165 - 900 kW
MC (SC driver, NC RF, SC RCS): 250, 7000, 4500 couplers, dc 0.05% → 4%, 325-1300 MHz, P = 100 - 4000 kW
(for ILC and CLIC: FP specs achieved)
HOMs couplers (see iSAS proposal): R&D on 800, 1300 MHz multicell; ~ kW RF power out of the cold mass
FABRICATION CAPABILITIES, TEST STAND
CERN: for future colliders, long-term expertise; couplers for Soleil, ESRF, PERLE, … - CEA: couplers on request for XFEL, ESS DESY: 1.3 GHz CW couplers RI company
EIC (USA): couplers with challenging specs, developments will benefit next colliders.
2. CERN SPS resonant ring
3. Fast Reactive Tuners (potential game changer for tuning, transient beam loading, microphonics)
Notes: A resonant ring is a closed loop of a waveguide system that can amplify power, and it is widely used for the breakdown test of the RF components under high power
FerroElectric Fast Reactive Tuners (FE-FRTs) are a novel type of tuner that may be able to achieve near perfect compensation of microphonics in the near future. This would eliminate the need to design over-coupled fundamental power couplers and thus significantly reduce RF power, particularly for low beam current applications.

## Slide 14: WG4: HG Normal-Conducting RF W. Wuensch (CERN) and D. Alesini (INFN)
CLIC
HG (70 to 100 MV/m), X-Band with very low breakdown rate, key for cost (linac length) and efficiency (BD).
Good alignment mitigates HG/BD interplay (wakefields).
Muon Collider
Muon capture: HG with high external magnetic field.
FCC-ee 20 GeV NC injector; FCC-hh E-separators (S and C-Band).
Synergic with applications outside HEP (60 - 70 MV/m)
Operational test infrastructures: CERN (n.3, 50 MW, 12 GHz), Trieste (45 MW, 3 GHz), Valencia (7.5 MW, 3 GHz), Frascati (50 MW, 12 GHz), Uppsala (cryo pulsed DC sys)
X-band linearizers and deflectors: PSI, DESY, STFC
Linac design, operation: INFN (Roma and LNF), CERN, PSI, Eindhoven, Elettra, Medical VHEE, FLASH
Achieved: Gradient; understanding of fundamentals physics; industry on NC RF components/systems; synergies (XFEL, Eupraxia, ICS, medical, plasma accelerator, RFQ, …)
Generated: dielectric structures, short pulse acceleration and HT superconductors.
Required: systems engineering, integration, mechanics R&D, design, m-level alignment.
Fundamentals of breakdown: on materials, plasma, surface physics, …
Notes: Funding for CLIC from 4 to 2 nowadays

## Slide 15: WG5: High Efficiency Amplifiers I. Syratchev (CERN), G. Burt (Lancaster U) and M. Jensen (ESS)
High efficiency RF power sources for future large-scale particle accelerators (LHC and FCCee first)
In collaboration with industry to secure to ensure decades of industry support.
Klystrons (CERN, Lancaster, ESS, CEA): R&D expensive, today done solely with industry (3 qualified vendors!). 50-100% cost increase in last ~5 yrs. SSPA (CERN, Uppsala, CEA Saclay, INFN-Legnaro, NCBJ (Swierk), CIEMAT): industry on transistor (and h) R&D; labs contribute with combination/matching techniques
Only large projects can afford R&D costs and risks,
which benefit many applications; for small labs
energy savings are not worth R&D investment.
105 MW
FCCee
3.0 TeV CLICe+e- ; pulsed, 1.0 GHz, PRF, total = 180 MW
from 380 klystrons
and 600 SSPAs
Notes: The cavity combiner is a symmetrical device, which means that it can be used to combine the power of several inputs into one common output, but also to divide the power of a common input into several outputs. Therefore, it is possible to perform the validation indistinctly working as a combiner or as a divider.

## Slide 16: WG6: RF Control – LLRF, ML and AI G. Zheqiao (PSI) and W. Cichalewski (DMCS)
Accelerator sections with different beam patterns and fRF high-level AI automation/optimisation.
ILC/FCC/MC SC RF cavities → RF control vs. vibrations and heavy BL
Lower energy consumption → RF/operation control
Long construction and operation cycles → optimal architecture and framework suited for long-term standardised HW/SW
RF stability figures achieved! (FEL specs ~ 0.01 % amplitude and 0.01° phase; ILC: 0.07 % and 0.24°); real-time stabilization with AI automation/optimization alogorithms (telecom industry providing high-res fast ADCs and high-performance DSPs.
Availability, reliability and operability (FCC, ILC, MC, …) with many RF stations & cavities (ILC, > 560 RF stations and 14500 cavities), ML algorithms will decrease operation/maintenance costs.
Standardise LLRF system design and gain long-term industry support to labs (HW/SW platforms like VME, ATCA to MicroTCA, System-on-Chip): it will facilitate in-kind for large scale projects
Comprehensive, intelligent, highly automated, and standardised LLRF system
is essential for the success of the RF systems of future colliders.

## Slide 17: RF-to-ERL Panel link
ERL/RF Panel collaboration: iSAS project 1000 person*months, 12.6 M€, 4 years
(Approved July 10, 2023, Start March 1, 2024):
CNRS, CERN, ESS, DESY, VUB, CEA,
HZB, INFN
M. Baylac (CNRS)
(WG2-Thin films, WG3-Couplers, WG5-Power Sources, WG6-LLRF, ML and AI)
RF items

## Slide 18: RF-to-MC link: high Ea in high B
Study of RF breakdown (BD) under strong magnetic fields for muon ionisation cooling
So far (FNAL): 50 MV/m at 3 T
Four test stands being considered:
UHF test facility (CEA)
Higher frequencies - 3 GHz, 12 GHz (INFN, CERN and Cockcroft): smaller, quicker, act as guideline
DC field breakdown test stands (CERN, Cockroft, Uppsala): cheaper, compact, short gap
New compact klystrons (with WG5)
MC/RF Panel coordination → survey sent to each institute involved, responses awaited on capabilities and physics targeted by each facility; joint meeting to follow
G. Burt (STFC)
(WG4-NC High Grad, WG5-Power Sources)
Notes: 50 MV/m at 3 T , using Be elements inside the cavity (to limit plastic deformation/pulsed heating).
cheaper, compact, short gasp (altering the physics in strong B-fields?)
LASA setup: due blocchi di Cu spaziati da un gap di 0.1 mm, Delta-V 10 kV pulsato
INFN – 3 GHz in 7 T SC magnet

## Slide 19: Outlook - Progress of the LDG RF Panel
+
=
Nov22 – Mar23: watch future collider needs and RF goals
From Apr23:
Outreach (Community Forum-July 2023; special session at HG2023), priorities revised
Apr23 – Oct23:
Who is doing what/progress on the Roadmap milestones: survey of national teams
Continue coordination with ERL and MC panels
Jan-Jun 24:
Coordinate teams vs priorities, explore funding routes: national and EU
Zoom meeting with RF coordinators in Snowmass-P5 (February 2024)
Promote RF developments/needs towards HEP-physicists and funding agencies
Idea, a superWP on RF in I.FAST2 ← EU funds, national matching funds, more cohesion in the RF community at large
Jul-Dec 24, … : report on progress in the field and impact of above actions
Notes: MC: this infrastructure (Graeme is comparing the test stands, as an exercise with proponents), plus related cavity design and RF Power Source items

## Slide 20: Spare slides

## Slide 21: Outlook - lobbying for more funds
How to address the funding agencies after the survey?
Highlight priority areas; identify best lab candidates to address them
Elaborate a overall investment proposal
Coordinate within the extended-LDG on the overall fund requests to the funding agencies
«IFAST-2»
Initial contacts to develop a super-workpackage clustering several R&D activities in RF (now in I.FAST: thin films, HE power sources, C-guns, AM).
Additional funds for RF by EU
National FAs to add matching funds.
It encourages RF coordination across Europe → one community
Notes: "to support development of new concepts, new ideas and to prove their feasibility"

## Slide 22: Outlook
Done:
Future collider RF needs well focused
European contributing teams identified, along with available infrastructures; Progress/challenges in RF theme areas followed up
Next:
The Nov-2023 progress report to the CERN council, as basis for periodic updates
Correlate needs - candidate labs to fulfill them → coordinate (at LDG level) towards national funding agencies
Elaborate on a super-RF-WP in the “I.FAST2” proposal

## Slide 23: European Particle Physics Strategy and its updates
Strategy 14 July 2006
Update 30 May 2013
Update 19 June 2020
“(…) cornerstone of Europe’s decision-making process for the long-term future of the field. Mandated by the CERN Council, it is formed through a broad consultation of the grass-roots particle physics community (…) and it is developed in close coordination with similar processes in the US and Japan (…)”
Chairperson
1/CERN Member State,
1/lab of the major European Laboratory Directors’ Group, LDG
CERN Director-General,
SPC Chairperson,
ECFA Chairperson.
Invitees:
President of the CERN Council,
1/Associate Member States,
1/Observer State,
1/European Commission, JINR
Chairs of ApPEC, FALC, ESFRI, and NuPECC
Members of Physics Prep Group
European Strategy Group (ESG)

## Slide 24: European Laboratory Directors Group (LDG)
Remit by CERN Council:
Dialogue among Lab Directors and CERN
Input to the ESPP, liaise with EU Commission and national funding agencies, institutes and universities
Maximise national benefits of investment in fundamental research and in CERN
Look at activities outside CERN’s Member States, and of other groups in PP and related fields
Draw up and maintain a prioritised accelerator R&D roadmap towards future large-scale facilities for PP
Coordinate the accelerator R&D activities on the roadmap, until the next SU
‣ S. Bentvelsen (NIKHEF)
‣ F. Bossi (LNF)
‣ J. Clarke (DL)
‣ N. Colino (CIEMAT)
‣ F. Gianotti (CERN)
‣ B. Heinemann (DESY)
‣ D. Newbold (RAL)
‣ E. Previtali (LNGS)
‣ F. Sabatie (IRFU)
‣ M. Seidel (PSI)
‣ A. Stocchi (IJCLab)
‣ K. Jakobs (ECFA Chair)
‣ M. Lamont (CERN Directorate)
‣ J. Mnich (CERN Directorate)
‣ H. Montgomery (SPC Chair)
Standing observers
‣ G. Bisoffi (for RF) + P. Macintosh
‣ W. Leemans (for LPA) + R. Patahill
‣ S. Stapnes (for Muons) + D. Schulte
‣ J. D’Hondt (for ERL) + M. Klein
‣ P. Vedrine (for HFM) + M. Lamont
Secretary
‣ E. Tsesmelis (CERN)
Extended LDG members

## Slide 25: European Strategy Update and Accel R&D
What R&D? which priorities?
How long might it take? How much will it cost?
Which science with demonstrators, or intermediate-scale facilities?
Which new infrastructures?
Superconducting RF: bulk niobium cavities, surface preparation, thin films
NC structures: fundamental limitations, surface preparation, manufacturing techniques
High power RF sources, accelerating structures ancillaries (couplers, tuners…), LLRF and AI
Authors of RF R&D strategy: S. Bousson (IJCLab), Hans Weise (DESY). G. Burt (Lancaster University); G. Devanz (CEA); A. Gallo (INFN LNF); F. Gerigk (CERN); A. Grudiev (CERN); D. Longuevergne (IJCLab); T. Proslier (CEA); R. Ruber (Uppsala University), plus added experts
Large-scale accelerator R&D plan to inform and support future decision-making in the field
HF magnets
HG RF structures and systems
HG plasma and laser accelerators
Muon colliders,
Energy Recovery Linacs
Key questions during the 2020 Strategy Update on R&D for future collider options:

## Slide 26: Strategy update process timeline
End of 2024,
start of the next exercise !
→ 2020÷2027
CERN Council: decision making body, coordinating particle physics in Europe (23 Member States)
Notes: ECFA - EUROPEAN COMMITTEE FOR FUTURE ACCELERATORS (https://ecfa.web.cern.ch/ecfa-terms-reference). It is a broader representation of physicists, involved at high level in CERN activities

## Slide 27: Example: INFN-Projects for ESPP Accelerator R&D
Damping Ring and Transfer Lines for FCC-ee Injector
FCC-ee IR and MDI full-scale experimental validation
Muon Collider R&D activities
High-Q/high-G SRF R&D
SRF R&D for FCC-ee
HFM Italy
GANDALF (GaN-baseD AmpLiFier)
(*) Allocated funds (for 3 years, 2023-2026): 4929 k€
- 2125 k€ (of which RF: 1730 k€)
- Temporary personnel 552k€ p (of which RF: 288 k€)
- 2252 k€ staff
Approved (*)
On-hold

## Slide 28
Notes: LEP and FCCee: With two independent 100-kmcircumference rings for e+ and e− , a total synchrotron power fixed to 100 MW, and two interaction points (IPs), a yearly integrated luminosity more than five orders of magnitude larger than that of LEP can be achieved at the Z pole, as shown in Fig. 2

## Slide 29: ERL RF topics

## Slide 30: Extended LDG role