## Slide 1: ICS experimental studies in CTF2 CLIC Mini Week
Vlad Musat, Andrea Latina, Eduardo Granados, Steffen Döbert

## Slide 2
Introduction
RF-Track simulations of the CTF2 gun
Experimental development
Contents
2

## Slide 3
= The scattering of a low energy photon from an EM field to a high-energy photon (X-ray or gamma ray) during the interaction with a charged particle.
Compton backscattering
3
Total flux
Photon bandwidth
Photon energy
Average brilliance

## Slide 4: The CTF2 gun
S-band standing wave 1.5 cell RF-gun intended for the new AWAKE injector.
Prototype constructed by INFN-Frascati and commissioned at CTF2.
Fabricated with brazing free technology [1].
[1] D. Alesini, et al., PRAB, vol. 21, n. 11, November 2018
0.3 m
0.57 m
CLINXBT_0001
Spectrometer + Faraday cup

## Slide 5
Experimental set-up
5
Laser beam
Electron beam
X-ray beam
2.1 mJ, 1030 nm, 112 fs
6 MeV, 400 pC

## Slide 6: Gun simulations

## Slide 7
A model of the CTF2 gun was implemented in RFT. The model comprised the cathode, gun, and solenoid.
Optimisation goals:
  Maximise flux
  Minimise background
Simulations of CTF2 injector
7
0 – 20 mm/c
30 – 200 mm/c
Evolution of the phase space from cathode to screen
Cathode | Gun | Solenoid
Bunch charge (laser intensity) | RF phase | B field
Laser spot size (Gaussian) | RF gradient | 

## Slide 8
8
Gun
Solenoids
Gun
Solenoids
On-crest phase in RFT: 120°
Results: Flux optimisation (cathode screen)
Distance from cathode to IP = 0.57 m
Setup | Unit | 100 pC | 200 pC | 300 pC | 400 pC
Gun phase (RFT) | Deg | 100.5 | 108.5 | 99.0 | 94.0
Gun gradient | MV/m | 120 | 120 | 120 | 120
Max B field | T | 0.350 | 0.355 | 0.350 | 0.336
Laser RMS size | mm | 0.438 | 0.482 | 0.502 | 0.567
Parameter at IP | Unit | 100 pC | 200 pC | 300 pC | 400 pC
Beam energy | MeV | 5.77 | 5.84 | 5.77 | 5.75
 | mm mrad | 1.88 | 2.77 | 4.00 | 6.14
 | mm | 1.27 | 1.68 | 1.78 | 1.80
 | µm | 42 | 46 | 61 | 94
 | ps | 0.4 | 0.6 | 0.90 | 1.1
Ph/bunch | # | 14,000 | 35,000 | 37,000 | 29,000
Parameter at IP | Unit | 100 pC | 200 pC | 300 pC | 400 pC
Beam energy | MeV | 5.77 | 5.84 | 5.77 | 5.75
 | mm mrad | 1.88 | 2.77 | 4.00 | 6.14
 | mm | 1.27 | 1.68 | 1.78 | 1.80
 | µm | 42 | 46 | 61 | 94
 | ps | 0.4 | 0.6 | 0.90 | 1.1
Ph/bunch | # | 14,000 | 35,000 | 37,000 | 29,000

## Slide 9
9
Results: Flux optimisation (cathode screen)
On-crest phase in RFT: 120°
Distance from cathode to IP = 0.57 m
Setup | Unit | 100 pC | 200 pC | 300 pC | 400 pC
Gun phase (RFT) | Deg | 100.5 | 108.5 | 99.0 | 94.0
Gun gradient | MV/m | 120 | 120 | 120 | 120
Max B field | T | 0.350 | 0.355 | 0.350 | 0.336
Laser RMS size | mm | 0.438 | 0.482 | 0.502 | 0.567
Parameter at IP | Unit | 100 pC | 200 pC | 300 pC | 400 pC
Beam energy | MeV | 5.77 | 5.84 | 5.77 | 5.75
 | mm mrad | 1.88 | 2.77 | 4.00 | 6.14
 | mm | 1.27 | 1.68 | 1.78 | 1.80
 | µm | 42 | 46 | 61 | 94
 | ps | 0.4 | 0.6 | 0.90 | 1.1
Ph/bunch | # | 14,000 | 35,000 | 37,000 | 29,000
Parameter at IP | Unit | 100 pC | 200 pC | 300 pC | 400 pC
Beam energy | MeV | 5.77 | 5.84 | 5.77 | 5.75
 | mm mrad | 1.88 | 2.77 | 4.00 | 6.14
 | mm | 1.27 | 1.68 | 1.78 | 1.80
 | µm | 42 | 46 | 61 | 94
 | ps | 0.4 | 0.6 | 0.90 | 1.1
Ph/bunch | # | 14,000 | 35,000 | 37,000 | 29,000

## Slide 10: Optimal beam parameters
Laser beam IP parameter | Value
Wavelength | 1030 nm
Laser pulse energy | 0.9 mJ
RMS pulse length | 112 fs
M2 | 1.3
Laser waist at IP | 15 µm
Electron beam parameter | Value
Beam energy | 5 MeV
Bunch charge | 400 pC
RMS beam size at IP | 94 µm
RMS bunch length | 1 ps
Repetition rate | 10 Hz
Input parameters | Value
Laser RMS on cathode | 0.56 mm
Gun solenoid field | 0.3 T
Gun phase | (wrt on-cr st)
Gun field | 100 MV/m
Input parameters | Value
Laser RMS on cathode | 0.56 mm
Gun solenoid field | 0.3 T
Gun phase | 
Gun field | 100 MV/m
0.75 m
13.5 mm
18mrad
Collection angle of photon detector

## Slide 11
Simulated X-ray parameters
11
X-ray beam parameter | Value
Photon energy | 220 eV
Wavelength | 5.6 nm
Crossing angle | 90
RMS beam size on detector | 6.7 mm
RMS pulse length | 0.23 ps
Nb photons per pulse (total) | 29,000
Nb photons per pulse (18 mrad) | 1,200
Bandwidth | 2.2%

## Slide 12: Water Window X-ray source
Water window is a region in the electromagnetic spectrum where water is invisible.
The region spans the K-edge of Carbon (282 eV) to Oxygen (533 eV).
Only microscopy allowing for 10 nm range 3D imaging of cellular samples in their near-native state quantitative characterisation of (sub)cellular organisation in single cells and cell-cell interaction [1].
https://doi.org/10.1364/OPTICA.393014
[1] V. Weinhardt, J.-H. Chen, A. Ekman, G. McDermott, M. A. Le Gros, and
C. Larabell, “Imaging cell morphology and physiology using x-rays,”
Biochem. Soc. Trans. 47, 489–508 (2019).
Most water window microscopes have been implemented as part of synchrotrons.

## Slide 13: Experimental set-up

## Slide 14: The detector set-up
Provides 106 gain with a 27 mm effective diameter
Dimensions: 81 by 36 mm
Operated in vacuum (< 1e-4 Pa)
Capable of time-of-flight measurements (900 ps FWHM pulse width)
High absorption of soft X-rays in air prevents us from placing the photon detector in-air
(air)

## Slide 15
To maximise the scattered photon flux we need:
  High bunch charge (> 200 pC)
  High laser pulse energy (1 mJ from frequency doubler)
  Small laser pulse length (100 fs RMS)
  High beam energy to reduce angular spread of ICS photons (> 5 MeV)
  Small spot size (< 150 µm RMS)
Configuring the CTF2 gun for the ICS experiment
15
Total flux
“Beam based procedures for RF guns”, PAC2005
As indicated from the optimisation of the simulation:
  Use a small RF phase
  Use a laser spot size with RMS size
  Align UV laser beam on the cathode, along with the solenoid

## Slide 16: Alignment of laser spot on cathode with solenoid
Method: scan the laser position on the cathode, and for each point, made a solenoid scan and determined the beam drift select laser coordinates with smallest drift.
Stable beam region accuracy set by drift distance of the laser spot within 160 .
Stable point
x
y
d1
d2
Total drift = d1 + d2
0.28 T
0.27 T
0.29 T
Electron beam position drift

## Slide 17: Alignment of laser spot on cathode with solenoid
Stable beam for a large range of solenoid strengths was obtained.
Solenoid current [A]
Solenoid current [A]
Solenoid current [A]
Solenoid current [A]

## Slide 18: Stable beam point found
0.351 T
0.329 T
0.307 T
0.285 T
0.263 T
0.241 T
0.219 T
0.197 T

## Slide 19: Centering the laser on cathode
Want to align the laser position on the cathode to be on-axis with the gun.
The RF was used to focus the electron beam with the solenoid turned off. To achieve this, used:
  low beam energy (1.5 MeV) reduce dark current
  low bunch charge (5 pC) get small spot
A stability map of the laser position was made after setting a high RF phase (215 deg).

## Slide 20: Centering the gun solenoid
To further reduce the emittance from the gun, the position of the electron beam can be tracked through a solenoid scan
solenoid position and angle offset can be inferred by fitting the beam trajectory to simulations. Preliminary results predict a transverse misalignment less than 1 mm.
Solenoid X offset
Solenoid Y offset

## Slide 21: Small spot working point
Used a small RF phase and a laser RMS spot of 200 µm.
An electron RMS spot of 100 µm was obtained for a bunch charge of 200 pC.
At 400 pC, a 200 µm RMS spot was obtained.
Note the presence of an electron beam halo, inducing a non-Gaussian beam profile.
Is this profile optimal for generating a high photon flux?

## Slide 22: Optimum beam profile for high photon flux
Simulations indicate that non-Gaussian beam distributions with a sharp peak and space charge-induced halo achieve the highest flux.

## Slide 23: Conclusions
The CTF2 gun serves as an ideal test bench for an ICS proof of concept experiment.
The obtainable X-ray parameters are compatible with water window microscopy.
Working points have been defined to allow the generation of high flux photons.
Installation and experiment to be completed during the first half of next year.
End goal: experiment with a CLIC X-band structure-accelerated beam and Fabry-Perot cavity.
Thanks to CTF2 team: Steffen Döbert, Edu Granados, Miguel Calderon.

## Slide 25
Impact of RF phase on electron spot size at IP
25
100 pC
200 pC
300 pC
400 pC
Simulation
Q = 200 pC
Measurement
Negligible change in electron spot = 190 um

## Slide 26: Tolerance study (Cathode)
Cathode
Determine the impact of offsets in injector parameters on the total flux from CBS.
Tolerance study done for 200 pC with Copper cathode.
Bunch charge
Laser pulse length
Laser spot
position
Laser spot
size

## Slide 27: Tolerance study (RF Gun)
RF Gun
Gradient
Phase
The RF gradient controls the beam energy at the injector exit.
Difference with respect to nominal energy leads to poor focusing flux is most sensitive to the gun gradient.

## Slide 28: Tolerance study (Gun Solenoid)
Solenoid
B-field
amplitude
Offset
Transverse & Angular
Due to the strong focusing involved, the CBS photon flux is sensitive to offsets of the gun solenoid.

## Slide 29: Tolerance study (IP region)
Electron beam phase space at the IP
2 deg
crossing angle