## Slide 1: Large-Scale Comprehensive Thermal Simulation of the CBM Silicon Tracking System (STS) on the Virgo Cluster at GSI

## Slide 2: Compressed Baryonic Matter (CBM) Experiment
BEAM
F. Matejcek. CBM-MVD Integration. FTDM 2023 | Link

## Slide 3: Silicon Tracking System (STS) Detector Structure
M. Teklishyn. CBM-STS Integration. FTDM 2022 | Link

## Slide 4: Challenges for the Thermal Simulations
How does every silicon sensor perform in complex 3D geometry?
How does irradiation scenarios affect the sensors thermal performance?
Can particles physics related effects be integrated in the thermal performance?
Can a broad group of scientists, students and engineers be involved?

## Slide 5: Open Source Computational Software
OpenFOAM (Open Field Operation And Manipulation) is the free, open source computational software that utilizes finite volume method for thermofluidic simulations
Allows parallel computations, as a result, suitable for high performance computing in computer clusters
Can be easily customized for specific tasks
The Salome platform is an open-source software for pre-processing
Allows for simplifying geometry for simulations and initial meshing
Power open source visualization engine
Allows for results analysis

## Slide 6: High Performance Computing at GSI – Green IT Cube
Partition | CPUs max | RAM max [TB] | Time limit
debug | 2048 | 8 | 30 minutes
main | 2048 | 8 | 8 hours
high_mem | 2048 | 16 | 7 days
The Green IT Cube is one of the largest high-performance data centers in the world
Chart: Elapsed time [min]
| Meshing time | Solving (100 iterations)
AMD Ryzen 7 7745HX 8 cores Windows 11 w/ WSL 2 | 35.1 | 108.9
Virgo cluster 512 processors | 3.06 | 12.78
Two regions (conjugate heat transfer)
Region VolAir 20,4 million cells
Region VolSiliconSensors: 1 million cells

## Slide 7: Customization for STS: Non-Ionizing Energy Loss (NIEL)
FLUKA diagrams in Root-format can be converted into OpenFOAM directly
[neq/cm2]

## Slide 8: Customization for STS: Thermal Model for Sensors
Conjugate heat transfer solver was modified to account power dissipation caused by radiation damage
Q = I x U
Radiation damage properties are combined in one file
The solver prints power dissipation every time step for controlling computation

## Slide 9: Analytical Noise Estimation Model
Sensor
CT=Csensor + Ccable
Source: Rodriguez Rodriguez, Adrian “STS FRONT-END ELECTRONICS ENC measurements & estimation”
Electronics
Sensor
Cable
Electronics
From sensors thermal model
Need to know heights of sensors and lengths of cables

## Slide 10: Work on the STS Detector’s Model: Geometry
Thermal enclosure
C-Frame
Cooling plate
Silicon sensors
Front-end electronics (FEB) box
Front-end electronics PCB with chips
Front-end electronics Box
STS detector simplified geometry

## Slide 11: First Results from the Detector Thermal Simulation: Sensors
Power dissipation
Non-ionizing energy loss
Temperature field

## Slide 12
First Results from the Detector Thermal Simulation: Air Convection
Air velocity field inside the thermal enclosure
Air temperature around the cooling plate

## Slide 13: First Results from the Detector Thermal Simulation: Supplementary Results
Temperature field: Thermal enclosure walls
Temperature field: C-Frame

## Slide 14: First Results from the Detector Thermal Simulation: Noise analytical model
Series voltage noise
[arbitrary units]
Silicon sensor module

## Slide 15: Experimental Verification of the Model
Geometry of the thermal demonstrator prepared for the simulation
Actual assembly of the thermal demonstrator

## Slide 16: First Simulation Results of the Thermal Demonstrator: Pressure Loss
 | Pressure difference, Pa
Mesh w/o inflation layers | 47462
Mesh w/ inflation layers | 54403,7
Cooling plate

## Slide 17: Results from thermal demonstrator
Preliminary simulation of the STS sensors temperatures
Thermal demonstrator measurements of the sensors dummies temperatures
Courtesy of K. Agarwal

## Slide 18: Summary
A comprehensive thermal model of the STS detector is being prepared
OpenFOAM® allows for implementation of the specific features for the detector
Power dissipation of the silicon sensors with respect to irradiation and signal-to-noise model is implemented
This model is suitable for high performance computing on the Virgo cluster at GSI
Utilizing open-source software allows for the broad usage of the model and results analysis
Outlook and future work
Experimental results have been acquired from the thermal demonstrator
These results will be used for cross-validation of our detector model
Geometry of the thermal demonstrator was prepared for the simulation
Simulated results has been acquired for the pressure loss in the cooling plates
The results of this work (know-how) is foreseen as a contribution for DRD8