## Slide 2: Status Update from ISOLDE
J. Alberto Rodriguez on behalf of ISOLDE operations and other technical teams

## Slide 3
Outline:
Introduction to the ISOLDE facility and the 2023 Physics campaign.
The REX/HIE-ISOLDE post-accelerator.
What do the users of the facility request?
  Variety and purity of the beams.
  Beam intensity and number of shifts dedicated to Physics.
  Beam energy.
  Beam time structure.
  Transverse and longitudinal emittances and beam stability.
Summary.
J. Alberto Rodriguez – JAP Workshop 2023, Montreux – 07.12.2023

## Slide 4
ISOLDE is the Radioactive Ion Beams (RIBs) production facility at CERN.
ISOLDE receives ~ 50 - 70 % of the protons produced in the complex.
RIBs are produced when 1.4 GeV protons from the PSB are transferred to the facility via the BTY line and impinge in one of the two targets.
Introduction to the ISOLDE facility and the 2023 Physics campaign:
J. Alberto Rodriguez – JAP Workshop 2023, Montreux – 07.12.2023
Ions
Radioisotopes
Protons
Vacuum
Air
The just-created radioactive isotopes diffuse out of the target when it is heated to ~ 2000 C.
They are ionized using different mechanisms (surface, plasma, laser).
They are extracted out of the target unit that is floating at 30-60 kV.

## Slide 5
ISOLDE is able to produce and deliver ~1500 different isotopes with a very large range of beam intensities (i.e. often difficult beam characterization and optimization).
J. Alberto Rodriguez – JAP Workshop 2023, Montreux – 07.12.2023
2023 Physics Schedule (K. Johnston, H. Heylen). Experiments in green for GPS and in blue for HRS
Nuclear chart and production yields at ISOLDE
Introduction to the ISOLDE facility and the 2023 Physics campaign:
More than a hundred different beams delivered to complete the 59 experiments scheduled in 2023.
Experiments last 1 day - 1 week and are scheduled sequentially alternating target positions (although solid state physics normally done in parallel).
Each experiment generally requires a different target (multiple target changes every week), ionization mechanism and/or beam characteristics (i.e. dedicated “mini-commissioning” and machine set-up for every experiment).

## Slide 6
J. Alberto Rodriguez – JAP Workshop 2023, Montreux – 07.12.2023
Introduction to the ISOLDE facility and the 2023 Physics campaign:
MEDICIS facility
Nanolab
Low energy experimental stations:
IDS
ISOLTRAP
CRIS
COLLAPS
SSP stations
VITO
MIRACLS / PUMA
WISARD
Cryoplant
Water plant
Control room
User labs
High energy experimental stations:
Miniball
ISS
SEC
REX/HIE-ISOLDE post-accelerator
BTY line
Target stations
GPS separator
HRS separator
Isotopes extracted from one of the two front-ends are transported using electrostatic elements to a separator (GPS or HRS) where the RIB of interest is selected. A beam switch yard is used to distribute the beam.
The RIB of interest is transported to one of the experimental stations either directly or after being accelerated in the REX/HIE-ISOLDE post-accelerator.

## Slide 7
J. Alberto Rodriguez – JAP Workshop 2023, Montreux – 07.12.2023
Ions are accumulated and transversely cooled in the REX-TRAP and charge bred in the REX-EBIS.
The charge state of interest is selected in the REX separator before injection into the REX/HIE-ISOLDE linac for acceleration.
The REX/HIE-ISOLDE post-accelerator:
REX-TRAP
REX-EBIS
REX Separator

## Slide 8
J. Alberto Rodriguez – JAP Workshop 2023, Montreux – 07.12.2023
The REX room temperature linac:
Beam from the charge breeder with 5 keV/u energy is accelerated to 2.8 MeV/u.
Cavities: Seven RF structures: f = 101.28 MHz (except for 9gap at 202.56 MHz) up to 10% duty cycle.
Nominal charge state acceptance: 2.5 < A/q < 4.5. Operational 2023: 1.75 < A/q < 4.0
Beam instrumentation: 3 diagnostic boxes (FCs, silicon detectors, beam attenuators and collimators).
The REX/HIE-ISOLDE post-accelerator:
RF structure | Ef [MeV/u] | βf [%] | P [kW] for A/q=4.0 | A/q acceptance
RFQ | 0.3 | 2.5 | 29 | < 5.5
Buncher | 0.3 | 2.5 | 1.3 | > 2.5
IHS | 1.2 | 5.1 | 40 | < 4.5
7gap1 | 1.55 | 5.7 | 60 | > 2.5
7gap2 | 1.88 | 6.3 | 60 | > 2.5
7gap3 | 2.2 | 6.8 | 60 | > 2.5
9gap | 2.85 | 7.8 | 71 | > 2.5
REX-EBIS
REX-TRAP
REX linac
REX separator

## Slide 9
J. Alberto Rodriguez – JAP Workshop 2023, Montreux – 07.12.2023
The HIE-ISOLDE superconducting linac and HEBT lines (project completed in 2018):
Cavities: Quarter Wave Resonators (QWR) made of a copper substrate with sputtered niobium.
Cryomodule: one SC solenoid and 5 QWR that can be phased independently.
Nominal energy: 9.2 MeV/u (A/q = 4.5), 14.2 MeV/u (A/q = 2.5). Operational 2023: ~7.2 MeV/u (A/q = 4.5).
Diagnostics: scanning slits, collimators, stripping foils, silicon detectors and FCs.
The REX/HIE-ISOLDE post-accelerator:
REX-EBIS
REX-TRAP
REX linac
REX separator
2018
2017
2016
2015
HIE-ISOLDE linac
f [MHz] | 101.28
Geometrical beta (βg) | 10.3
Eacc [MV/m] | 6
Quality factor (Qo) at Eacc | 5∙108
Active length [m] | 0.3
Beam aperture [cm] | 2
Max. Transit Time Factor (TTF) | 0.9
Miniball
ISS
SEC

## Slide 10
J. Alberto Rodriguez – JAP Workshop 2023, Montreux – 07.12.2023
Variety and purity of the beams.
Beam intensity and number of shifts dedicated to Physics.
Beam energy.
Beam time structure.
Transverse and longitudinal emittances and beam stability.
…
What do the users of the facility request?

## Slide 11
J. Alberto Rodriguez – JAP Workshop 2023, Montreux – 07.12.2023
Variety and purity of beams:
Nuclear chart and production yields at ISOLDE
Mass resolving power not enough to separate isobaric contaminants. Some experimental stations equipped with a MR-ToF. But no plans to redesign the GPS or HRS separators at this time.
Excellent work by SY/STI developing new targets and ionization mechanisms to increase the variety and purity of the RIBs. (e.g. LIST targets, RILIS new ionization schemes, molecular beams…)
New regions of the nuclear chart  Additional Physics!
Short half-life. Not a lot we can do. Intrinsic limitation of ISOL facilities. Diffusion of isotopes out of target takes > few milliseconds.
Period
Slow release
Fast release
Pulsing beam gates to change contaminant ratios if release times are different
  In combination with supercycle structure, they can be used to improve beam purity.
  Supercycle structure kindly accommodated by PSB colleagues.
  Issues with the hardware since LS2. Work-around in place.
  Meeting to address this problem planned for next week.
Beam gates system (system to start/stop the transport of beams outside the separator zones):
Stable beam contaminants due to ionization of residual gas in the REX-EBIS charge breeder greatly reduced during after LS2 thanks to the excellent vacuum level. Stripping foils in HEBT lines available and used for low A beams when needed.
A/q spectrum out of the REX-EBIS

## Slide 12
J. Alberto Rodriguez – JAP Workshop 2023, Montreux – 07.12.2023
Beam intensity and number of shifts dedicated to Physics:
Improved operational efficiency (BE-OP, SY-STI-RBS/LP). Despite the shorter Physics campaign:
  59 experiments in 2023 compared to 52 experiments in 2022.
  Comparable number of protons to ISOLDE in 2023 and in 2022.
  Note: Even though is not sustainable in the long-term and a correction to a reasonable middle point will be needed in 2024, it is still a remarkable achievement by all ISOLDE technical teams.
  In the long-term: Development and validation of optics model for low-energy beam lines (SY-ABT), adoption of LSA, EPA project and additional software applications to automate tasks.
Pulsing of the central line.
  With the notable exception of the SSP experiments, the central line blocks simultaneous beam delivery from GPS and HRS separators.
  Pulsing this line will reduce the effective set-up time and increase the number of Physics shifts.
Beam intensity for all RIBs proportional to proton beam intensity. Up to a factor x5 higher intensity for multiple RIBs expected with 2 GeV proton energy. Keeping the 1.4 GeV option needed.
  Linac4 and PSB high-intensity MDs extremely valuable and very welcome by the user community.
  Beam dumps consolidation and 2 GeV upgrade of the BTY line needed (hopefully during LS3).
  Additional target (and possibly front-end) developments may be needed to cope with the new p beam.
  In the meantime: 1.7 GeV p to GPS target will be used for physics and higher than 2 uA p current may be occasionally requested (RP and SY-STI assessment to define authorized beam power limit).
Higher RIBs intensities  “New” isotopes and more experiments in a year!
Central line
SSP experimental stations

## Slide 13
J. Alberto Rodriguez – JAP Workshop 2023, Montreux – 07.12.2023
Beam energy:
In the short-term:
  Experimental proposals may be rejected by the TAC or not scheduled.
  Pushing accelerating gradient. Consequences: Additional trips. Downtime increases quickly!
  Boosting the charge state of the beam. Possible only because of the excellent performance of the new electron gun developed by BE-ABP during LS2. Consequences: Longer breeding time reducing repetition rate and worsens the time structure of the beam. In some cases, saturation of the REX-TRAP.
In the long-term:
  Keeping the cryomodules cold during the YETS. Under investigation by SY-RF and TE-CRG.
  Additional cryomodule (hopefully, shortly after LS3). Major effort by SY-RF, TE-VSC and other groups.
  Consolidation of existing cryomodules. Major effort (i.e. clean room in SM18). Cannot be done during a normal YETS without impact on the Physics campaign unless an additional cryomodule is used as a “hot” spare.
Accelerating gradient of superconducting cavities limited in average to ~70 % of the nominal 6 MV/m. In addition, it is degrading over time (believed to be caused by the yearly thermal cycles).
Higher beam energies increase the cross-section of some reaction and it is required for many high-energy experiments.
Maximum nominal (orange) and operational (blue) beam energy for different A/q ratios

## Slide 14
J. Alberto Rodriguez – JAP Workshop 2023, Montreux – 07.12.2023
Beam time structure:
Non-optimal time structure. A/q acceptance limited to 4.0 (compared to nominal 4.5) because of instabilities of REX RF systems at high peak powers. In addition, RF pulse lengths limited to ~ 1.2 ms due to the average power limit in the 9gap.
In the short-term: Limiting Physics with heavy isotopes, pushing the REX-EBIS (possible only because of the excellent performance of the new electron gun developed by BE-ABP during LS2), slow extraction (~1 ms long pulses) from the REX-EBIS.
In the long-term: New solid-state RF amplifiers and digital LLRF system (LS3). In my view, a study (beam dynamics and RF EM designs) to replace some of the REX RF cavities should also be launched.
The time structure of the beam defined by the supercycle structure, the RIB release time and the configuration of the beam gates.
The ISOLDE cooler/buncher in the HRS separator is required to bunch and change the time structure.
Even though the situation has improved significantly after LS2 (e.g. remote He gas injection system, new RF amplifiers…), some issues remain (e.g. possible misalignment of extraction system, limited RF power, hysteresis in gas supply…)
In the longer term, removing the HRS one and adding dedicated cooler/bunchers for each experimental station that needs them should be studied.
Low-energy users often require bunched beams.
High-energy users generally request the highest possible average beam intensity with the lowest possible peak intensity to avoid pile-up in their DAQ.
ISOLDE cooler/buncher
Slow-extracted beam pulse from REX-EBIS

## Slide 15
J. Alberto Rodriguez – JAP Workshop 2023, Montreux – 07.12.2023
Transverse / longitudinal emittances and beam stability:
Trips of the target and line heating. Slow ramping to limit thermal stresses in target units. Significant source of downtime. Root cause not clear. Difficult diagnosis.
Beam characterization. Excellent consolidation work by SY-BI since LS2. Dozens of devices already replaced or added (FCs, scanning wires, linac slits and attenuators…). Several others (e.g. BTY SEMgrids, low-energy slits systems) planned for the coming years.
Limited support for some critical systems. Day-time support for the REX RF systems and best effort for the front-end HT may result in loss of an experiment if the system fails during afterhours. Improving the level of support would be greatly appreciated by OP and the user community.
Instabilities of the aging electrostatic power converters result in effective emittance growth (electrostatic benders are excellent energy spectrometers).
Phase and field instabilities of the REX RF and SRF systems result effective growth of both longitudinal and transverse emittance (after HEBT dipoles).
In the long-term:
Consolidation of electrostatic and HRS dipoles power converters (SY-EPC) over the next few years.
Development of optics model for low-energy beam lines (SY-ABT) should help improving quality of beam set-ups and reducing growth effective emittance.
New solid-state RF amplifiers and digital LLRF system (LS3).
Users need small transverse & longitudinal emittance beams.
Jitter due to faulty power converter visible in beam profile.
Other possible improvements:

## Slide 16
J. Alberto Rodriguez – JAP Workshop 2023, Montreux – 07.12.2023
Summary:
Very demanding but successful 2023 Physics campaign:
More experiments than in 2022 and comparable number of protons despite the shorter length.
Several work-arounds in place to deal with aging equipment.
Multiple systems consolidated and improved since LS2:
Target front-ends.
Tape station.
REX and low-energy beam instrumentation.
REX-EBIS electron gun.
Lots of improvements planned or being evaluated for the coming years:
Consolidation of the beam dumps.
2 GeV upgrade of the BTY line.
Consolidation of the electrostatic and HRS dipoles power converters.
Pulsing of the central line.
Development of the optics model of the low-energy beam lines.
New solid-state amplifiers for REX.
New digital LLRF system for REX.
Consolidation of SRF cavities.
Additional cryomodule.
System of keep SRF cavities cold during the YETS.
Consolidation of several BTY and low-energy lines beam instrumentation.
RILIS lab extension and upgrade.