## Slide 1: HL-LHC Crab-Cavities LLRF project LLRF Integration
G. Hagmann
HL-LHC CC LLRF project, December 11, 2023

## Slide 2: Crab-Cavities underground layout
Fig – HL-LHC point 1 or 5 underground layout. Top view, Courtesy S. Maridor
UAX7
USX7
URX5
UAX3
ULX3
ULX7
URx5 Faraday cage
USx7 Faraday cage

## Slide 3: US17 or US57 gallery
Faraday cage
6 racks
Access from the stairs to the platform /FC
Fig – HL-LHC USx7 gallery, Courtesy S. Maridor

## Slide 4: Patch panel – USx7 faraday-cage
Two patch panels required
  Missing Fiber-feed through
  Missing N-type connectors (new cable request from Andy)
  Reasonnable amont of spare required
Or extension possible
  Final spec to be discussed with FC supplier.
Space reservation is important today
Faraday cage
6 racks
Fig – HL-LHC USx7 gallery, Courtesy S. Maridor
Existing patch AJFC01
New patch AJFC02

## Slide 5: Patch panel – USx7 faraday-cage
Current design
  550x1500mm
  75 N-type connectors
    69 signals, 6 spare
Second patch panel required
  AJFC01: 550x1500mm (unchanged)
    75 coaxial connectors
    61x N type
    14x 7/16 type (for 7/8’’: pickup, ANT, spare)
    69 signals, 6 spare
  AJFC02: 550x ~1000mm
    N type
    4 fiber feed-throughs
    EMI multi-conductors with remaing space
    Space reservation of 1500mm
  Cable allocation might still changed
Fig – HL-LHC USx7 patch panels
Fiber feed-throughs

## Slide 6: USx7 Faraday cage layout
Current design (v5)
  5800x2900mm (proposal from the issue of the staires outside)
Final design
  Back to 5600x2900mm
  Door at 250mm
  Door moved at the same place than in UR
  Uniformization of the FCs between UR/US
5600mm
2900mm
Fig – HL-LHC USx7 FC drawing V5, Courtesy S. Maridor

## Slide 7: USx7 Faraday cage False-floor
External Platform required
  Height H0=250mm
  Area > door open at 90°
  Door : 900mm
H0 False floor:
  Height H0=250mm
  FC bottom structure not even
  Protection of FC floor
H2 false floor
  Height H2 = H0+450mm
  Behind the racks
  For cables from patch panel AJFC01 to the racks
  One step required (H1=H0+225mm)
New size: 5600mm
Single step of 250mm
Ok for HSE
after correction 12.12.2023

## Slide 8: USx7 Faraday cage Racks allocation
New allocation (optimized for cabling)
after correction 12.12.2023

## Slide 9: UR15 or UR55 gallery
UR15
UA13
UL13
Faraday cage
6 racks
Fig – HL-LHC URx5 gallery, Courtesy S. Maridor

## Slide 10: Patch panel – UR faraday-cage
Patch panel
  New size: 450x1300mm
  N connectors
  7/16 connectors (for critical signal to minimize réflexion)
  Fiber-optics feedthrough (AJFC02)
  multi-conductors EMI feedthrough (AJFC02)
  Distribution depending on the destination inside FC
Faraday cage
6 racks
patch panel
AJFC01
patch panel
AJFC02
Fig – HL-LHC URx7 FC, Courtesy S. Maridor

## Slide 11: URx5 Faraday cage layout
Current design
  Size 5600x2900mm (no change)
Final design
  Door at 250mm
5600mm
2900mm
Fig – HL-LHC URx5 FC drawing V5, Courtesy S. Maridor

## Slide 12: UR15 & UR55 Faraday cage False-floor
External Platform required
  Height H0=250mm
  Area > door open at 90°
  Door : 900mm
H0 False floor:
  Height H0=250mm
  FC bottom structure not even
  Protection of FC floor
H1 False floor
  Height H1=H0+225mm
  For cables from patch panels to the racks
H2 false floor
  Height H2=H1+225mm
  Behind the racks
  For cables from patch panels to the racks
  One step required (H1)
225mm
800mm
Ramp slope: 16 deg (28%)
Ok for HSE
Single step of 250mm
Ok for HSE

## Slide 13: URx7 Faraday cage Racks allocation
New allocation (optimized for cabling)
after correction 12.12.2023

## Slide 14: False floors - Stairs
False floor stairs
  ISO 14122-3:2016(E)
  Height h: 225mm (max)
  Going g: 210mm
  Overlap r: 30mm
H0=250mm (door height)
OK for HSE
External platform to be approved by integration

## Slide 15: Head room – UR faraday-cage
Rounded air dict (blue, 400mm)
Rectangle air duct (yellow , 400mm)
H0=250mm
OK for HSE
HSE recommendations:
  Reduce size of air duct (H2 false floor)

## Slide 16: Head room – US faraday-cage
Rounded air dict (blue, 400mm)
Rectangle air duct (yellow , 400mm)
H0=250mm
OK for HSE
HSE recommendations:
  Reduce size of air duct (H2 false floor)

## Slide 17: Head room – CV
Air ducts size
  Assuming 400mm
  400mm height from FC hard ceiling?
lighting, false-ceiling
  150mm space needed for
Space needed for cable tray at the top of the racks
Positioning of the aeration grid:
  Lower than 150mm
  at the bottom?
Can we reduce air duct height? (HSE)

## Slide 18: FC monitoring
FC environnement monitoring
  Space reservation needed
  400x400x200mm
USx7
URx5

## Slide 19: Fiber feed-throughs
For fiber-optics
Dimensions
  L=120mm (80mm outside)
  inner diameter=30mm
  Outer diameter=36mm
4x feed-throughs in AJFC02
Fig – SPS BA3 fiber feed-throughs

## Slide 20: Cabling - Couplers Patch panel
New patch panels on Circulator guirder
14x N type connectors/ patch
1 patch / girder (2 patchs / UA)
Missing patch panel name
Cable tray layout?
8x LLRF signal per UA (4x LLRF signals / patch):
2x IcFWD (CGN50B, 7/8’’)
2x IcREV (CD50A, 3/8’’)
Under SY-RF-AC responsability (design & fabrication)
Patch panel
Fig – HL-LHC UA gallery, Circulator and patch panel, Courtesy L. Ciampo

## Slide 21: Cabling - Tunnel patch panel
Patch panel
44 RF cables (assuming RF cables only)
  36 LLRF signals
  8x HLRF signals
Currently 60x connectors
  Connector spacing (currently 80mm) can be optimized to ease the cabling?
ANT, PU cables (extension)
  16x 7/8’’ cables => Same length
  7/16 connector type on PP side
  N connector type on PU/ANT side
HOM cable (extension)
  16x 3/8’’ cables (CD50A) for HOM
  N connector (both side)
Fig – HL-LHC Crab-cavity, tunnel patch panel, Courtesy N. Bruti
Fig – HL-LHC Crab-cavity, tunnel patch panel, , Courtesy S. Maridor

## Slide 22: Cabling - Tunnel patch panel
Cable tray required from patch-panel to
  Pickup, Cavity antenna, HOM (extension)
High radiation area
  Access required for cables exchange campaign
  150kGy after 10 years expected
Pickup
  Last 2.5m: SIO2 cables provided by BI
  Situation unknown for RF loads
HOM
  3/8’’ cables directly connected to the RF port.
LLRF Cavity antenna
  Below the cryostat (1 per cavity)
  Last centimeters with RF semi-rigid patch cable
Fig – HL-LHC Crab-cavity, tunnel patch panel, , Courtesy S. Maridor

## Slide 23: Specifications for LLRF
Fig – Phase offset leading to transverse displacement on one beam only [16]
Crabbing closure
  Cavity phase on bunch core. Phase offset → transverse displacement (x or y) of bunch core
  Coherent phase shift Requirement: <100ps phase error (14.4°) [1] (2% peak luminosity reduction)
  In Coherent phase shift Requirement : <15ps phase error (2°) [1] (1% peak luminosity reduction)
  Precise crabbing-uncrabbing voltage (V)
  Counter-phasing on both side of the IP during filling/ramping (V=0)

## Slide 24: Underground temperature
Thermal simulation in UR
High temperature gradient
  1m height: ~19°C
  3m height: ~25°C
Fig – Steady temperation profile UR tunnel, Phase modulation of LHC ACS cavities along the batch for 2.21011 [5]

## Slide 25: Underground temperature
Tunnel ΔT=±1.5°K
8°K daily variation in UR [5]
No simulation available in UA
Operational scenario of RF heat load variation in UA?
Heat load varying with LHC cycle (WP6b, WP7, WP17.2)
Figs – Transient temperature at 2m height [3, 5]
8°K
5°K

## Slide 26: Cables
Tunnel PP to faraday-cage PP
  Draka cables (93m)
    CGN50B : 7/8’’ : 0.0042 RFdeg / °K / m
    CD50A: 3/8’’ : 0.0016 RFdeg / °K / m
  CGN50B example:
    L=93m for 8K => 3.12 RFdeg (spec 2RFdeg)
  tentative budget
    0.1 RFdeg (10%)
    8°K for 3m => 0.1RFdeg
Budget also for
  Cable inside FC, in the tunnel
±1.5
Fig – Draka phase stability wrt Temperature, 7/8’’, 3/8’’

## Slide 27: Cabling
Differential measurement with pickup-cavity
Same cable type/ length
Fig – LLRF differential measurement

## Slide 28: Cabling
Cabling rules required
  Same cable type (CGN50B), length, routing for PU (12x 7/8’’), ANT(4x 7/8’’), IcFWD, IcREV and SPARE (4x 7/8’’).
    Dedicated cable tray for these temperature sensitive cables.
    Keep same temperature variation for all cables (Simulation required?)
    identical cable drum preferred
  From FC to amplifiers: cables as short as possible per cavity (no cable length matching), optimize for latency
  HOM cables (3/8’’) on a different cable tray than PU, ANT, IcFWD and SPARE (Fc to Tunnel)
after correction 12.12.2023
Drive, IgFwd, IgREV, Spare
IcFWD, IcREV
PU
ANT
SPARE HOM

## Slide 29: Fire detection
Pending issue
  Electrical power supply switch off in case of fire detection?
Concern for Machine protection and HSE
  Possible damage in the machine in case of CC voltage uncontrolled
  Beam-dump within 3-turns
Current status
  Request pending to HSE
  Machine protection to be contacted

## Slide 30: References
[1] T. Mastoridis et al., Cavity voltage phase modulation to reduce the high-luminosity Large Hadron Collider rf power requirements, PRAB Oct 2017 Phys. Rev. Accel. Beams 20, 101003 (2017) - Cavity voltage phase modulation to reduce the high-luminosity Large Hadron Collider rf power requirements (aps.org)
[2] E. Yamakawa et al., Luminosity reduction caused by phase modulations at the HL-LHC crab cavities, NIMA 2018, https://www.sciencedirect.com/science/article/pii/S0168900218310325
[3] Rahul, CFD Results of the Transient Thermal analysis of UR15 Gallery, HL-MCF Meeting # 87, CERN 2021, https://indico.cern.ch/event/1053324/
[4] SMB/SC, Technical Description 19” Instrument Rack , EDMS 1967612
[5] F. Dragoni, A. Mejica, P. Pepinster, WP17.3 - COOLING AND VENTILATION USERS’ REQUIREMENTS FOR P1 AND P5, EDMS EN-CV-2018-081, Doc N°1572976
[6]H. Schönbacher, M. Tavlet, Absorbed doses and radtion damage during the 11 years of LEP operation, CERN-TIS-2002-010-DI-PP, CERN, Geneva 2002 DOI: 10.1016/j.nimb.2003.09.034
[7] https://edms.cern.ch/ui/file/2669584/LAST_RELEASED/SSI-FS-2-1_EN.pdf