## Slide 1: Update on Task 3.2 Concept of a HTS solenoid
Michal Duda on behalf of HTS solenoid team
9/11/2023

## Slide 2
Experimental setup
HTS solenoid assembly
Warm wide bore through tube
Vacuum chamber
Thermal shielding
Cryo coolers
Electrical and thermal Leads
Thermal lead buffers
Support structure
Ground support frame
Backbone frame for vacuum chamber
HTS solenoid for P3 experiment
Components status
power supply – delivery next month
cryocoolers - delivered
HTS tape - delivered
cryostat – main components - delivered
cryostat support – delivered

## Slide 3: Specification Requirements
DN40CF gate valve
Lead shield
DN40CF bellow
Shielding
Chamber
Needs of fine adjustment
of vacuum chamber
144 mm
Courtesy of Thomas Uli Michlmayr

## Slide 4: Solenoid Access Bore
DN160CF
Bellow
one side rotatable
W target insertion
upstream side
DN63CF-R
wide bore
upstream
flange
O-ring sealed
retention groove
DN40CF-R
wide bore
downstream
flange
Courtesy of Thomas Uli Michlmayr

## Slide 5: Support Structures
Weight of chamber assembly ~ 1 Ton
Force between NC and SC solenoids 30 kN
Welded frames from ▢80 / D6 and ▢100 / D8 stainless steel tubes
Solenoid support directly in contact with backbone plate
Earthquake and deviation analysis
Girder brackets (D10)
Sub mm adjustment
Vertical / horizontal
Tilt
1200 mm
Remachined support plates for precise repositioning
Crane hooks
Courtesy of Thomas Uli Michlmayr

## Slide 6: P3 Main Assembly
Air side cabling and leads
Water cooler with 50W heater
A = 3 * 300mm2 J = 1.3A/mm2 @ I = 1.17kA
G10 separator
Thermal shielding case EN AW-1050 and 3 x 10 layer MLI
7 G10 support pillars
Supports only Al shield D2 and MLI (7kg)
Remachined vacuum chamber
Cryo cooler 1
Leads
Thermal shield
Thermal lead buffers
Warm wide bore 72 through pipe
Cryo cooler 2
Coil assembly
Right buffer
Courtesy of Thomas Uli Michlmayr

## Slide 7: Coil winding
Courtesy of Henrique Garcia

## Slide 8: Coil soldering
Courtesy of Henrique Garcia

## Slide 9: Coil soldering
Ready for testing!
Courtesy of Henrique Garcia

## Slide 10: Coil verification
Courtesy of Henrique Garcia