## Slide 1: New understanding of longitudinal (bunched) beam instabilities and comparison with measurements
Ivan Karpov
Acknowledgments:
Elena Shaposhnikova, Theodoros Argyropoulos, Alexandre Lasheen, Heiko Damerau (CERN)
Alexey Burov (FNAL), Maxime Gadioux (UCD), Sigurd Nese (UiB)
HB Flash Seminar, 16.11.2023

## Slide 2: Loss of Landau damping (LLD)
LLD threshold depends not only on impedance strength but also on cut-off frequency **
*Y. H. Chin, K. Satoh, and K. Yokoya, Instability of a bunched beam with synchrotron frequency spread, 1983 and A. Burov, Van Kampen modes for bunch longitudinal motion, 2010 **IK, T. Argyropoulos, E. Shaposhnikova, Thresholds for loss of Landau damping in longitudinal plane, 2021
H. Timko et al, Beam instabilities after injection to the LHC, 2018
LLD threshold
Undamped mode
Long-lasting oscillations were observed in SPS, RHIC, Tevatron, LHC, …
van Kampen modes* for broadband impedance above transition energy
Synchrotron frequency spread
LLD threshold for LHC at 6.5 TeV with MV
J.F. Esteban Müller, PhD thesis, 2016

## Slide 3: Single-bunch instability in SPS (long bunches)
*F. J. Sacherer, Bunch lengthening and microwave instability, 1977
**K. Oide and K. Yokoya, Longitudinal single bunch instability in electron storage rings, 1990
***IK, Longitudinal mode-coupling instabilities of proton bunches in the CERN Super Proton Synchrotron, 2023
Classical azimuthal mode-coupling instability* is predicted at extremely high intensity
RF nonlinearities reduce the threshold by a factor of 5 (consistent with SPS measurements)***
Coupling of radial modes** is actual mechanism of instability
Classical approach* (no frequency spread)
Self-consistent approach** (frequency spread with potential-well distortion + RF nonlinearity)
Mode coupling

## Slide 4: Generalized multi-bunch instability threshold
Growth rates of most unstable modes for 9 bunches (MELODY - lines, BLonD - crosses)
Instability develops below the LLD threshold
Theory is supported by observations in SPS and is relevant for HL-LHC
Threshold coupled-bunch instability (CBI) for a combination of narrowband (nb) and broadband (bb) impedance can be evaluated using stability diagrams*
*F. J. Sacherer, A longitudinal stability criterion for bunched beams, 1973
**IK and E. Shaposhnikova, Generalized threshold of longitudinal multi-bunch instability in synchrotrons, 2023
Valid approach only for very short bunches
A self-consistent approach was developed, and an approximate expression was proposed**