## Slide 2: Beam performance with the LHC Injectors Upgrade (LIU)
Giovanni Rumolo
S. Albright, R. Alemany, M.E. Angoletta, C. Antuono, T. Argyropoulos, F. Asvesta, M. Barnes, H. Bartosik, P. Baudrenghien, G. Bellodi, N. Biancacci, C. Bracco, N. Bruchon, E. Carlier, J. Coupard, H. Damerau, G.P. Di Giovanni, E. de la Fuente Garcia, A. Findlay, M. Fraser, A. Funken, R. Garoby, S. Gilardoni, B. Goddard, G. Hagmann, K. Hanke, A. Huschauer, G. Iadarola, V. Kain, I. Karpov, J.B. Lallement, A. Lasheen, T. Levens, K. Li, A. Lombardi, E. Maclean, D. Manglunki, I. Mases Sole, M. Meddahi, L. Mether, B. Mikulec, E. Montesinos, Y. Papaphilippou, G. Papotti, K. Paraschou, C. Pasquino, F. Pedrosa, T. Prebibaj, S. Prodon, D. Quartullo, F. Roncarolo, B. Salvant, M. Schenk, R. Scrivens, E. Shaposhnikova, L.Sito, P. Skowronski, A. Spierer, R. Steerenberg, M. Sullivan, F. Velotti, R. Veness, C. Vollinger, R. Wegner, C. Zannini, LIU teams, OP crews & all equipment experts

## Slide 3: The LHC Injectors Upgrade (LIU) goal
2023
Run 3
2021
Only injectors
Run 2
Long Shutdown 2
2019
2020
2016
2017
2018
2015
2014
Only injectors
Long Shutdown 1
2013
Run 1
2010
2011
2012
2009
2024
2025
2022
Run 4
Long Shutdown 3
2026
2027
HL-LHC installation
(+ ATLAS & CMS upgrade, NA cons, ECN3, …)
2028
2029
2030
Pre-LIU performance:
Nb=1.1 – 1.3 x 1011 p/b
ex,y=2.5 – 3.0 mm
A gap by a factor 2 in intensity and brightness to be filled
HL-LHC target
Nb=2.3 x 1011 p/b
ex,y=2.1 mm

## Slide 4: The LHC Injectors Upgrade (LIU) goal
Peak installation phase in Long Shutdown 2 (LS2)
Project closure with performance ramp-up plan and back-up items
2023
Run 3
2021
Only injectors
Run 2
Long Shutdown 2
2019
2020
2016
2017
2018
2015
2014
Only injectors
Long Shutdown 1
2013
Run 1
2010
2011
2012
2009
2024
2025
2022
Run 4
Long Shutdown 3
2026
2027
HL-LHC installation
(+ ATLAS & CMS upgrade, NA cons, ECN3, …)
2028
2029
2030
(2010 – 2021)

## Slide 5: The LIU installation
Connection of PSB to Linac4 and acceleration to 2 GeV in PSB
PS & SPS RF upgrades + e-cloud & impedance reduction, new SPS optics, new dumps & stoppers, etc.
PS longitudinal damper
New SPS RF amplifier towers
New SPS beam dump
PSB new power supply building
PSB injection Line from Linac4

## Slide 6: LIU beam commissioning in Run 3: ramp-up plan
Year-by-year intensity goals of the ramp-up at SPS extraction
  Pre-LS2 beam parameters recovered by the end of 2021 – 1.3e11 p/b
  1.8e11 p/b in MD by the end of 2022 – to be ready for LHC in 2023 (operation)
  2.1e11 p/b in MD by the end of 2023 – to be ready for LHC in 2024 (MD)
  2.3e11 p/b in MD by the end of 2024 – to be ready for HL post-LS3
A. Huschauer et al., LIU workshop 2020

## Slide 7: Actual progress in Run 3
LIU-PS achieved
LIU-SPS achieved
Nb = 2.6 ∙ 1011 p/b 4sz<4 ns
MKP-L heating
Pressure spikes in MKP-L and MKDH
Thanks to new MKP-L + efficient scrubbing

## Slide 8: Actual progress in Run 3
LIU-PS achieved
LIU-SPS achieved
2 eVs
3 eVs

## Slide 9: Summary & outlook
LIU project ended on time & budget
LIU beam commissioning is advancing well and is currently ahead of schedule both in terms of achieved beam intensity and brightness
Some surprises encountered on the way but no major showstoppers!