## Slide 1: Scaling of Micro-Fabricated Penning Ion Traps
Kilian Hanke
Tobias Sägesser, Silke Auchter, Nina Megier , Matthias Dietl,
Shreyans Jain, Pavel Hrmo, Yingying Cui, Matteo Simoni, Clemens Rössler, Daniel Kienzler, Yves Colombe,
Jonathan Home

## Slide 2: Penning traps – quick review
Radially-symmetric static quadrupolar potential:
Homogenous static magnetic field:
Trajectory can be decomposed into modified-cyclotron (), magnetron () & axial () motion
anti-confining potential
harmonic well

## Slide 3: Penning traps – macroscopic to micro-fabricated
[Hendricks2008] Hendricks et al. (2008) Laser cooling in the Penning trap: an analytical model for cooling rates in the presence of an axializing field
[Stahl2004] S. Stahl et al. (2004). A planar Penning trap. European Phys. Journal D Vol. 32
[Jain2020] S. Jain et al. (2020). Scalable Arrays of Micro-Penning Traps for Quantum Computing and Simulation. Phys. Rev. X 10, 031027
adapted from [Jain2024]
Ideal Penning Trap
Simplified Penning Trap
(incl. axialization electrodes)
Planar Penning Trap
(incl. axialization electrodes)

## Slide 4: Why Penning traps might be a good alternative.
Full 3D transport
Not restricted to RF nulls i.e., grid of RF nulls
No need for junctions
  Saves chip area
  No engineering of complicated geometry
No more high power RF
RF voltages on the order of 1 V instead of 100 V
Reduced dissipation on chip → potentially lower heating rate
Usage of silicon substrate more feasible → easier to handle in industrial CMOS fab
No need for resonator circuit
[Jain2024]
[Kielpinski2002]
Paul-trap: QCCD
Penning: full 2D transport
[Kielpinski 2002] Kielpinski D, Monroe C, Wineland DJ. Architecture for a large-scale ion-trap quantum computer. Nature. 2002. doi: 10.1038/nature0078
Substrate
RF loss

## Slide 5: Penning Trap Experiment, TIQI, ETH
First surface-electrode Penning ion trap:
  Fabricated by PTB
  Single layer
  12 µm gold metallization
  Sapphire substrate
  25 electrodes
3 T magnetic field
Single 9Be+ ion
First micro-fabricated Penning ion trap. Fabricated by Amado Bautista-Salvador at PTB.
[Jain2024]

## Slide 6
Courtesy of Tobias Sägesser
optical access
50 cm

## Slide 7: Next generation of the Penning ion trap
8 mm
5 mm
2.25 mm
1 mm

## Slide 9
Loading zone
  19 DC electrodes
  2 axialization electrodes
  Simulated trapping velocity: 2

## Slide 10
Working zone
  Goal: trap 2x2 grid of 9Be+ ions
  56 DC electrodes
  min. 25 µm x 40 µm in size
  3 axialization electrodes
Courtesy of Tobias Sägesser

## Slide 11
Intermediate zone
  24 DC electrodes
  Transport: loading → working zone
  & stray-field compensation

## Slide 13: Layer stack
Si
SiOx
Al
W
MC
Substrate: silicon
Metallization: aluminum
  3 structured metal layers
  1 shielding layer
Planarized dielectric layers
Tungsten plugged vias (tbd.)

## Slide 14: Steps towards scalable ion trap design software
Number of electrodes increases rapidly:
  2020 (PTB): 25 electrodes
  2024: 104 electrodes
  202x: ~1000 electrodes?

## Slide 15: Steps towards scalable ion trap design software
Issue: manual routing becomes unfeasible
Solution: programmatic chip layout
Foundation: KQCircuits [Heinsoo2023]
  Python package for superconducting circuit design
  Extends KLayout
  Developed by IQM
We added features for ion trap design
  Multi-layer routing incl. vias
  Electrode structures
[Heinsoo2023] J. Heinsoo et al. (2023). KQCircuits. 10.5281/ZENODO.4944796

## Slide 16: Steps towards scalable ion trap design software
[Heinsoo2023] J. Heinsoo et al. (2023). KQCircuits. 10.5281/ZENODO.4944796
45°
Issue: manual routing becomes unfeasible
Solution: programmatic chip layout
Foundation: KQCircuits [Heinsoo2023]
  Python package for superconducting circuit design
  Extends KLayout
  Developed by IQM
We added features for ion trap design
  Multi-layer routing incl. vias
  Electrode structures

## Slide 17: Steps towards scalable ion trap design software
[Heinsoo2023] J. Heinsoo et al. (2023). KQCircuits. 10.5281/ZENODO.4944796
Issue: manual routing becomes unfeasible
Solution: programmatic chip layout
Foundation: KQCircuits [Heinsoo2023]
  Python package for superconducting circuit design
  Extends KLayout
  Developed by IQM
We added features for ion trap design
  Multi-layer routing incl. vias
  Electrode structures

## Slide 18: Steps towards scalable ion trap design software
[Heinsoo2023] J. Heinsoo et al. (2023). KQCircuits. 10.5281/ZENODO.4944796
Issue: manual routing becomes unfeasible
Solution: programmatic chip layout
Foundation: KQCircuits [Heinsoo2023]
  Python package for superconducting circuit design
  Extends KLayout
  Developed by IQM
We added features for ion trap design
  Multi-layer routing incl. vias
  Electrode structures

## Slide 19: Summary & Outlook
Micro-fabricated Penning traps provide promising alternative to Paul traps
  Full 3D transport capabilities
  No high-power RF
Next trap is currently in fabrication at Infineon Villach
  2x2 grid of 9Be+ ions
  Silicon substrate on multi-layer stack
Routing of high electrode numbers requires algorithm based routing
Outlook: Installation of new trap until end of 2024
For more details: Check out the paper & feel free to reach out.
Chip carrier PCB
Prerunner wafer
Prerunner chip

## Slide 20: Thanks to the whole team!
Pavel Hmro
Matteo Simoni
Yingying Cui
Prof. Jonathan Home
Daniel Kienzler
Tobias Sägesser
Shreyans Jain
Nina Megier
Silke Auchter
Matthias Dietl
Yves Colombe
Clemens Rössler

## Slide 21
For more details:
Check out the paper & feel free to reach out e.g.,
kilian.hanke@infineon.com

## Slide 22: Raman beams are used to address the different transitions.

## Slide 23: Motional coherence is reduced significantly, when the electrodes are disconnected during the measurement.
 |  |  | (detached)
modified-cyclotron | 0.05(1) | 0.49(5) | 0.58(2)
magnetron | 0.03(2) | 3.8(1) | 1.8(3)
axial | 0.007(3) | 0.088(9) | 0.10(1)
modified-cyclotron | 0.05(1) |  | 
magnetron | 0.03(2) |  | 
axial | 0.007(3) |  | 

## Slide 24: The choice of 9Be+ ion was made due to the simple structure and advantageous mass for Penning traps.
Pro:
High mass:
  High-frequency for same strength of trapping potential
  Lower magnetic field strength required for Penning trap
  Lower Doppler limit
Relatively simple electronic structure
Only two wavelengths required: 313 nm & 235 nm?
Contra:
Has nucler spin
Transitions are UV
Ground state qubit is in MW regime (~80 GHz)

## Slide 25
Pavel Hmro
Matteo Simoni
Yingying Cui
Prof. Jonathan Home
Daniel Kienzler
Tobias Sägesser
Shreyans Jain
Nina Megier
Silke Auchter
Matthias Dietl
Yves Colombe
Clemens Rössler
Kilian Hanke

## Slide 26: The Team
Pavel Hmro
Matteo Simoni
Yingying Cui
Prof. Jonathan Home
Daniel Kienzler
Tobias Sägesser
Shreyans Jain
Silke Auchter
Matthias Dietl
Yves Colombe
Clemens Rössler
Kilian Hanke
Nina Megier

## Slide 27: Penning Trap Experiment, TIQI, ETH - Setup
Single 9Be+ ion
3 T magnetic field from superconducting coils
First Surface-electrode Penning trap:
  Fabricated by PTB
  single layer
  12 µm gold metallization
  Sapphire substrate
  25 electrodes
First micro-fabricated Penning ion trap. Fabricated by Amado Bautista-Salvador at PTB.
[Jain2024]

## Slide 28: Penning Trap Experiment, TIQI, ETH - Results
Full quantum control of single ion
Transport in 2D plane
Heating rates
Spin coherence
  Vibrations
  Magnetic field fluctuations
[Jain2024] S. Jain, T. Sägesser, P. Hrmo et al. (2024). Penning micro-trap for quantum computing. Nature 627, 510–514
[Jain2024]

## Slide 29: Current status of chip Penning traps
Socket 2.0 Assembly

## Slide 30: Current status of chip Penning traps
Si
SiOx
Al
W
Silicon substrate
Pure Al metallization
1 unstructured shielding layer
3 structured routing & electrode layers
Planarized dielectric layers
(tbd.) tungsten plugged vias

## Slide 31
Axialization electrodes
  5 electrodes
  3 RF signals
  phase matched routing

## Slide 32: Towards scalable trap design software
Number of electrodes increases rapidly:
  2020 (PTB): 25 electrodes
  2024: 104 electrodes
  202x: ~1000 electrodes?
Issue: manual routing is unfeasible
Solution: programmatic chip layout
Foundation: KQCircuits [Heinsoo2023]
  Python package for superconducting circuit design
  Extends KLayout
  Developed by IQM
Added features for ion trap design
  Multi-layer routing incl. vias
  Electrode structures
[Heinsoo2023] J. Heinsoo et al. (2023). KQCircuits. 10.5281/ZENODO.4944796
straight = (cell_refs["port_LZ_DC1,3_n“], (1, 0.74))
for el_ref, launcher_ref in electrode2launcher.items():
intersect1 = compute_intersection_from_direction(…)
intersect2 = compute_intersection_from_direction(…)
self.insert_cell(WaveguideComposite,
nodes=[
Node(launcher_ref),
Node(intersect1),
Node(intersect2),
Node(el_ref),
],
**waveguide_dc_wide_params,
)