## Slide 1
Design and construction of
ALFA fibre detector

## Slide 2
Construction of fibre detectors shared by:
JLU Giessen  Fibre tracking modules, mechanics and final assembly
Desy Hamburg  Metrology of fibre plates and MAPMTs
Desy Zeuthen  Triggers
LIP Lisbon  Fibres machining, coating and characterisation
HUB Berlin  Machining of Ti substrates
CERN  Design, prototyping work, fibre coating, fibre end machining quality check, final adjustments and metrology.
PH/DT was also in charge of assembly and integration of RP stations, motor control, vacuum, tunnel installation, …
PH/DT contribution from:
Adrian, Alessandro, Christian, Claude, Jerome, Luc, Miranda, Patrick, Sune, Sylvain, Thomas, Tonio, Xavier...
Thanks to Hasko and Sune providing most of the illustrations for the slides

## Slide 3
  Requirements
● Detector size 30 x 30 mm2
● No dead edge zones
● Resolution sx =sy ~ 30 mm
● Uniform trigger/detection efficiency
● Compatibility with operation in vacuum
● Easy and quick to install and remove
● Moderate radiation hardness
(detector removed during high-L runs)
● Relative position of upper and lower detector
to be known within ~10 mm precision
Must fit inside Roman Pots !
(RP stations developed for TOTEM)

## Slide 4
Scintillating fibers
Type Kuraray SCSF 78
10mm
Cladding PMMA
Core PS
500 mm
500 mm
MAPMT
R7600-00-M64
Aluminium side coating
Large bending radius to avoid cracks
No clear fibre !
the scintillating fibre is routed directly to the MAPMT
Absorption length measured:
120 – 170 cm
Machined fibre end, well positioned wrt MAPMT
Mirror coating
Light yield is critical!
Cracks on the surface of a fiber after a few minutes bending at R = 15 mm.
Specified dimensional tolerance ±2%

## Slide 5
Fibers conditioning
● Fibre end is machined and aluminum coated by sputtering at LIP Lisbon
  ● Fibre body is aluminum coated by evaporation at CERN
  ● Fibre dimensions are measured to allow a selection

## Slide 6
Layout of scintillating fibres
Black surface
Pot window
Central view :
On scale, fibres detectors close to beam position
(10-15 s ~1.5mm)
Beam (f~100mm)
200 mm
150 mm
1.15 mm
10 planes of U and V fibres staggered by 1/10 of fiber pitch
 larger fibres bending radius highest edge sensitivity
XY configuration rejected !
Poor edge sensitivity
Small fibre bending radius
U
V
Al coating:
● Suppression of cross talk
● Reflector on sides of 45° cut fibres
● Reflector on ends of 90° cut fibres

## Slide 7
Design of first prototype
U and V fibre layers (64 fibres each )glued on two sides of a thin ceramic substrate
Ceramic substrate 170 mm thick
Support arm with reference and alignment precision pin holes
Ceramic precision wedge glued on the central ceramic plate
● Staggering given by accurate positioning of the support arm on the fibre plates

## Slide 8
Prototype construction

## Slide 9
Concept validation in test beam

## Slide 10
The ALFA fiber detector
Main detector
(10 fibre plates)
Staggered fiber planes:
Main detector fiber plate:
Construction of 8+2(spares) fiber detectors:
 100 fiber plates  12800 fibers !

## Slide 11
Design of Fibre plates
Reference and alignment pin holes
(f6 +0.01 +0.005mm)
Overall substrate thickness
(2mm +0 -0.15mm)
Offset for staggering
(± 0.005mm)
Step for fiber gluing
  (0.75±0.05mm)
● Based on precision machining of a titanium substrate
Overall substrate flatness
(± 0.1mm)
Angle of reference edges (45 ± 0.01 deg.)
300mm G10 subsrate + 100mm polyimid pad coating on both sides
(Promote insertion of glue by capillarity)

## Slide 12
Assembly of fibre plates
1) Selection of fibres
2) Fibre positioning (straight, U+V)
3) Glue fibres in crossing area
4) Bend fibres to 45° + glue
5) Metrology
6) Fiber ends machining
Fiber ends machining at CERN

## Slide 13
Metrology
A
B
C
D
origin (0,0)
X
Y
side U
fiber #1
fiber #1
point (X,Y)
E
Metrology for serial production done at DESY HH
Metrology for prototyping work done at CERN
Determine the fibre equations (ax+b) needed for space point reconstruction.
Fibre positioning accuracy has a direct impact on the spatial resolution.

## Slide 14
Metrology
typical good modules
rare bad modules

## Slide 15
Assembly
Procedure:
Before we assemble a detector consisting of 10 Plates we run a G4 Monte Carlo
simulation (Prague) of elastic scattering events through the detector using the
measured fibre positions as input (real geometry). Then the resolution is
calculated and if good (~30 µm) this configuration is actually assembled.
Detector | Proto2 | A10 | A11
Resolution [µm] | 32 | 28 | 27
series production

## Slide 16
Overlap detector
Construction of 8+2(spares) fiber detectors:  30 fiber plates  1800 fibers !
The overlap detector

## Slide 17
Overlap detectors
3 planes of horizontal fibres staggered by 1/3 of fibre pitch
Beam halo
Determine the vertical distance between up and down detectors
Accuracy < 10 mm with large number of tracks recorded
Extrusions for overlap detectors

## Slide 18
Assembly of overlap fibre plates
1) Hot bending of fibers at 80 -90 °C
2) Fibre positioning (straight, horizontal)
3) Glue fibres on Ti substrate
4) Metrology

## Slide 19
Trigger tiles
Main trigger tiles
Overlap trigger tiles
2 overlap trigger tiles
Standard plastic scintillator technology. Two independently read tiles suppress noise or give redundancy.
Light transport to PMT by means of clear fibres.
Titanium substrate
2 main
trigger tiles
 Tiles define active surface of detector. Positioning precision of main trigger tile is as important as fibre positioning.

## Slide 20
Detector assembly
   Fiber and trigger plates aligned on an adjustable support arm equipped with precision pins.
   Routing of 1460 fibres and trigger lightguide bundles to connectors
   Mounting LED and PT100 sensors
   Gluing fibres and lightguides in the connectors
   Machining & polishing of connectors
  (10 tracking modules, 3 overlaps and 2 triggers)
Reference and alignment
pin holes
Adjustable support arm:
Feedthrough for test LEDS and temperature sensors

## Slide 21
Detector adjustment and metrology
Reference pin hole
Alignment pin hole
Base plate reference surface
Detector reference & alignment pins
 Check the overall dimensions of the fibre detector
 Adjustment of the detector position relative to the base plate ( best fit into individual pot)
 edge 150mm from pot window!
 Accurate measurement of the detector position

## Slide 22
Detector final survey
 Survey spheres (mirrors) mounted directly on the detectors
 3 survey points used on each detector (4th backup survey point)
 Same survey points on all detectors
 The survey point have be measured ±10mm in the coordinate system of the detector/Roman Pot (TESA 3D metrology)

## Slide 23
Insertion into Roman Pot

## Slide 24
MAPMTs
HAMAMATSU R7600-00-M64
Grid of 8x8 anodes, size 2x2mm2 pitch 2.3mm
 Anode grid not centred to the metal case !
Plastic shims to compensate for the misalignment of the anode grid
23 MAPMTs per module
HV divider and front-end electronics (PMF) attached to the pins
Accurate positioning inside the m-metal frame. Anode grid aligned to the fibres connector.

## Slide 25
Photo-detector module
Photo-detector module under black box
MAPMTs
PMFs
Kapton flat cable (readout)
m-metal frame
Roman Pot
Spring loaded bracket

## Slide 26
Installation of the photo-detector module in the LHC tunnel

## Slide 27
Survey in tunnel
Survey of fibre detectors in the LHC coordinate system with a laser tracker