## Slide 1: Electronics and DAQ
CERN Summerstudent Programme 2011
Niko Neufeld, CERN-PH
(final version of slides)

## Slide 2: Contents
Lecture 1: Mostly electronics, some triggering
Lecture 2: More electronics, basics of Data Acquisition
Lecture 3: Data acquisition at the LHC, odds and ends
Topics are related, no 100% separation between the 3
We want to fill in some of the blanks from Werner Riegler’s “Detectors” lectures to Jamie Boyds’s “From raw data to physics”. Triggering will be only treated in so far it is relevant for the electronics and DAQ. The “physics” of the trigger is treated in “Triggers for LHC physics” by Bryan Dahmess

## Slide 3: Physics, Detectors, Electronics Trigger & DAQ
rare, need many collisions
High rate collider
Fast electronics
Big data acquisition
trigger

## Slide 4: Disclaimer
Electronics, Trigger and DAQ are vast subjects covering a lot of physics and engineering
Based entirely on personal bias I have selected a few topics
While most of it will be only an overview at a few places we will go into some technical detail
Some things will be only touched upon or left out altogether – information on those you will find in the references at the end
  Quantitative treatment of detector electronics & physics behind the electronics
  Derivation of the “physics” in the trigger
  DAQ of experiments outside HEP/LHC
  Management of large networks and farms &High-speed mass storage

## Slide 5: Thanks
Some material and lots of inspiration for this lecture was taken from lectures by my predecessors: P. Mato, P. Sphicas, J. Christiansen
In the electronics part I learned a lot from H. Spieler (see refs at the end)
Trigger material I got from H. Dijkstra
Many thanks to S. Suman for his help with the animations

## Slide 6: Lecture 1/3
Mostly electronics

## Slide 7: Electronics in a nutshell

## Slide 8: Electronics: introduction
Why do we care about electronics?
  As physicists?
  As computer scientists?
The Readout Chain
  Shaping, Amplifying
  Digitizing, Transmitting, Noise and all that
Timing and Synchronization
Systems
  Power, Cooling & Radiation

## Slide 9: Physicists stop reading here
It is well known that
“Only technical details are missing”
Werner Heisenberg, 1958
A physicist is someone who learned Electrodynamics from Jackson

## Slide 10: Computer scientists wonder…
Why bother with this gruesome analogue electronics stuff
The problem is that Turing machines are so bad with I/O and it is important to understand the constraints of data acquisition and triggering

## Slide 11: The bare minimum
From Maxwell’s equations derive:
Ohm’s law and power
The IV characteristics of a capacitance
Kirchhoff’s laws
where: Q = charge (Coulomb), C = Capacitance (Farad), U = V = Voltage (Volt), P = Power (Watt), I = Current (Ampere)

## Slide 12: Detector Frontend Electronics (FEE)

## Slide 13: Seeing the data
Notes: What does “see” mean? How do we visualize particles, which are as small as an electron, which have actually no internal structure, no size!

## Slide 14: Once upon a time…
from Wikipedia
Notes: COUPP experiment – searching for WIMPs with a bubble-chamber!

## Slide 15: ...experiment-data were read

## Slide 16: Looking at ATLAS
Beam pipe
Tracking (in solenoid field)
Muon chambers
Electromagnetic Calorimetry
Hadronic Calorimetry

## Slide 17: Tracking
Separate tracks by charge and momentum
Position measurement layer by layer
  Inner layers: silicon pixel and strips  presence of hit determines position
  Outer layers: “straw” drift chambers  need time of hit to determine position

## Slide 18: Calorimetry
Particles generate showers in calorimeters
  Electromagnetic Calorimeter (yellow): Absorbs and measures the energies of all electrons, photons
  Hadronic Calorimeter (green): Absorbs and measures the energies of hadrons, including protons and neutrons, pions and kaons
amplitude measurement
position information provided by segmentation of detector

## Slide 19: Muon System
Electrons formed along the track drift towards the central wire.
The first electron to reach the high-field region initiates the avalanche, which is used to derive the timing pulse.
Since the initiation of the avalanche is delayed by the transit time of the charge from the track to the wire, the detection time of the avalanche can be used to determine the radial position(*).
Principle also used in straw tracker – need fast timing electronics
Track
Δt
ATLAS Muon drift chambers have a radius of 3 cm and are between 1 and 6 m long
(*) Clearly this needs some start of time t=0 (e.g. the beam-crossing)

## Slide 20: Different detectors: similar requirements
Sensors must determine several or all of the following:
  presence of a particle
  magnitude of signal
  time of arrival
Some measurements depend on sensitivity, i.e. detection threshold, e.g.: silicon tracker, to detect presence of a particle in a given electrode
Others seek to determine a quantity very accurately, i.e. resolution, e.g. : calorimeter – magnitude of absorbed energy; muon chambers – time measurement yields position
All have in common that they are sensitive to:
signal magnitude
fluctuations

## Slide 21: The “front-end” electronics`
Front-end electronics is the electronics directly connected to the detector (sensitive element)
Its purpose is to
  acquire an electrical signal from the detector (usually a short, small current pulse)
  tailor the response of the system to optimize
    the minimum detectable signal
    energy measurement (charge deposit)
    event rate
    time of arrival
    insensitivty to sensor pulse shape
  digitize the signal and store it for further treatment
Shaping
Detector
Amplifier
Digitization
DSP
Buffering
Triggering
Multiplexing
ETC.
DAQ
Interface
shaping
detector
pre-amplifier
digitization
DSP
buffering
triggering
multiplexing
etc.
DAQ
Interface
incident radiation

## Slide 22: The read-out chain
Amplifier
Filter
Shaper
Range compression
clock (TTC)
Sampling
Digital filter
Zero suppression
Buffer
Format & Readout
Buffer
Feature extraction
Detector / Sensor
to Data Acquisition System

## Slide 23: The read-out chain
Amplifier
Filter
Shaper
Range compression
clock (TTC)
Sampling
Digital filter
Zero suppression
Buffer
Format & Readout
Buffer
Feature extraction
Detector / Sensor
to Data Acquisition System

## Slide 24: The signal
The signal is usually a small current pulse varying in duration (from ~ 100 ps for a Si sensor to O(10) μs for inorganic scintillators)
There are many sources of signals. Magnitude of signal depends on deposited signal (energy / charge) and excitation energy
Signal | Physical effect | Excitation energy
Electrical pulse (direct) | Ionization | 30 eV for gases 1- 10 eV for semiconductors
Scintillation light | Excitation of optical states | 20 – 500 eV
Temperature | Excitation of lattice vibrations | meV

## Slide 25: A very simple example: Scintillator
from H. Spieler “Analog and Digital Electronics for Detectors”
Photomultiplier has high intrinsic gain (== amplification)  no pre-amplifier required
Pulse shape does not depend on signal charge  measurement is called pulse height analysis

## Slide 26: Acquiring a signal
Interesting signal is the deposited energy  need to integrate the current pulse
  on the sensor capacitance
  using an integrating pre-amplifier, or
  using an integrating Analog Digital Converter (ADC)
The signal is usually very small  need to amplify it
  with electronics
  by signal multiplication (e.g. photomultiplier, see previous slide)

## Slide 27: A first approach
The detector is essentially a capacitance Cd (This is valid for solid-state detectors! For other detectors the equivalent circuit can have reisistive and inductive elelments)
A particles puts QS into the detector
Add an amplifier and amplify Vi
Not so practical! Response depends
on sensor capacitance

## Slide 28: Charge sensitive amplification
Feedback amplifier with gain –A
Assume infinite input impedance  no current flows into the amplifier and all signal charge builds up on Cf
Input signal produces vi at the input of the amplifier generating –Avi on output
Charge gain depends only on Cf
Ci = Cf x (A+1) needs to be large compared to Cd

## Slide 29: How good can we get?
Noise

## Slide 30: Fluctuations and Noise
There are two limitations to the precision of signal magnitude measurements
  Fluctuations of the signal charge due to a an absorption event in the detector
  Baseline fluctuations in the electronics (“noise”)
Often one has both – they are independent from each other so their contributions add in quadrature:
Noise affects all measurements – must maximize signal to noise ration S/N ratio

## Slide 31: Signal fluctuation
A signal consists of multiple elementary events (e.g. a charged particle creates one electron-hole pair in a Si-strip)
The number of elementary events fluctuates where F is the Fano factor (0.1 for Silicon), Ei the energy of an elementary event
r.m.s.

## Slide 32: Full Width at Half Maximum (FWHM)
from Wikipedia
FWHM = 2.35 σ for a Gaussian distribution

## Slide 33: Electronics Noise
Thermal noise
  created by velocity fluctuations of charge carriers in a conductor
  Noise power density per unit bandwidth is constant: white noise  larger bandwidth  larger noise (see also next slide)
Shot noise
  created by fluctuations in the number of charge carriers (e.g. tunneling events in a semi-conductor diode)
  proportional to the total average current

## Slide 34: SNR / Signal over Noise What do we actually care about?
Need to optimize Signal over Noise Ratio (SNR)

## Slide 35: SNR and detector capacitance
For a given signal charge Qs: Vs = Qs/(Cd + Ci)
Assume amplifier has an input noise voltage Vn, then
SNR =
SNR is inversely proportional to total capacitance on the input  thicker sensor gives more signal but also more noise

## Slide 36: The read-out chain
Amplifier
Filter
Shaper
Range compression
clock (TTC)
Sampling
Digital filter
Zero suppression
Buffer
Format & Readout
Buffer
Feature extraction
Detector / Sensor
to Data Acquisition System

## Slide 37: Two important concepts
The bandwidth BW of an amplifier is the frequency range for which the output is at least half of the nominal amplification
The rise-time tr of a signal is the time in which a signal goes from 10% to 90% of its peak-value
For a linear RC element (amplifier):
BW * tr = 0.35
For fast rising signals (tr small) need high bandwidth, but this will increase the noise  shape the pulse to make it “flatter”

## Slide 38: The pulse-shaper should “broaden”…
Sharp pulse is “broadened” – rounded around the peak
Reduces input bandwidth and hence noise

## Slide 39: …but not too much
Broad pulses reduce the temporal spacing between consecutive pulses
Need to limit the effect of “pile-up”  pulses not too broad
As usual in life: a compromise, in this case made out of low-band and high-band filters

## Slide 40: The read-out chain
Amplifier
Filter
Shaper
Range compression
clock (TTC)
Sampling
Digital filter
Zero suppression
Buffer
Format & Readout
Buffer
Feature extraction
Detector / Sensor
to Data Acquisition System

## Slide 41: Analog/Digital/binary
After amplification and shaping the signals must at some point be digitized to allow for DAQ and further processing by computers
Analog readout: analog buffering ; digitization after transmission off detector
Digital readout with analog buffer
Digital readout with digital buffer
Binary: discriminator right after shaping
  Binary tracking
  Drift time measurement
control
1) Analog memory
Mux
ADC
ADC
ADC
ADC
ADC
Mux
3) Digital memory
control
2) Analog memory
Mux
ADC
Mux

## Slide 42: Analog to digital conversion
There is clearly a tendency to go digital as early as possible
  This is extensively done in consumer goods
The “cost” of the ADC determines which architecture is chosen
  Strongly depends on speed and resolution
Input frequencies must be limited to half the sampling frequency.
  Otherwise this will fold in as additional noise.
High resolution ADC also needs low jitter clock to maintain effective resolution

## Slide 43: An inconvenient truth
A solution in detector-electronics can be:
  fast
  cheap
  low-power
Choose two of the above: you can’t have three
Cost means:
  Power consumption
  Silicon area
  Availability of radiation hard ADC

## Slide 44: Time measurements
Time measurements are important in many HEP applications
  Identification of bunch crossing (LHC: 25ns)
  Distinguishing among individual collisions (events) in continuous beam like experiments (or very short bunch interval like CLIC: ~250ps)
  Drift time
    Position in drift tubes ( binary detectors with limited time resolution: ~1ns)
    Time projection chamber (both good time and amplitude)
    Time Of Flight (TOF) detectors (very high time resolution: 10-100ps)
Time walk: Time dependency on amplitude
  Low threshold (noise and pedestal limited)
  Constant fraction discrimination
    Works quite well but needs good analog delays (cable delay) which is not easy to integrate on chip.
  Amplitude compensation (done in DAQ CPU’s)
    Separate measurement of amplitude (expensive)
    Time measurements with two thresholds: 2 TDC channels
    Time over threshold (TOT): 1 TDC channel measuring both leading edge and pulse width
Time Over Threshold (TOT) can even be used as a poor mans ADC
  E.g. ATLAS Pixel
TH1
TH2
1/k
delay
Th
D
R
delay
delay
Constant fraction discriminator
Vi
TOT1
TOT1
T=Tr – f(TOT)

## Slide 45: Time to digital conversion
Counter
  Large dynamic range
  Good and cheap time references available as crystal oscillators
  Synchronous to system clock so good for time tagging
  Limited resolution: ~1ns
Charge integration (start – stop)
  Limited dynamic range
  High resolution: ~1-100 ps
  Sensitive analog circuit needing ADC for final conversion.
  Sensitive to temperature, etc. so often needs in-system calibration
  Can be combined with time counter for large dynamic range
Start
Stop
ADC
Start
Stop
Counter
Clock
Register
Hit
Reset
Time tagging type
Counter
Clock
Start
Stop
Start-stop type

## Slide 46: Readout

## Slide 47: After shaping and amplifying
As usual  what you do depends on many factors:
Number of channels and channel density
Collision rate and channel occupancies
Triggering: levels, latencies, rates
Available technology and cost
What you can/want to do in custom made electronics and what you do in standard computers (computer farms)
Radiation levels
Power consumption and related cooling
Location of digitization
Given detector technology

## Slide 48: Single integrator
Simple (only one sample per channel)
Slow rate (and high precision) experiments
Long dead time
Nuclear physics
Not appropriate for HEP
ADC
DAQ
Collect charge from event
Convert with ADC
Send data to DAQ

## Slide 49: Double buffered
Use a second integrator while the first is readout and reset
Decreases dead time significantly
Still for low rates
ADC
DAQ

## Slide 50: Multiple event buffers
Good for experiments with short spills and large spacing between spills (e.g. fixed target experiment at SPS)
Fill up event buffers during spill (high rate)
Readout between spills (low rate)
ADC can possibly be shared across channels
Buffering can also be done digitally (in RAM)
ADC
DAQ
Shaping
Channel mux.

## Slide 51: Constantly sampled
Needed for high rate experiments with signal pileup
Shapers and not switched integrators
Allows digital signal processing in its traditional form (constantly sampled data stream)
Output rate may be far to high for what following DAQ system can handle
With local zero-suppression this may be an option for future high rate experiments (SLHC, CLIC)
ADC
DAQ
Shaping
Sampling clock
DSP
(zero-sup.)

## Slide 52: Excursion: zero-suppression
Why spend bandwidth sending data that is zero for the majority of the time ?
Perform zero-suppression and only send data with non-zero content
  Identify the data with a channel number and/or a time-stamp
  We do not want to loose information of interest so this must be done with great care taking into account pedestals, baseline variations, common mode, noise, etc.
  Not worth it for occupancies above ~10%
Alternative: data compression
  Huffman encoding and alike
TANSTAFL (There Aint No Such Thing As A Free Lunch)
  Data rates fluctuates all the time and we have to fit this into links with a given bandwidth
  Not any more event synchronous
  Complicated buffer handling (overflows)
  Before an experiment is built and running it is very difficult to give reliable estimates of data rates needed ( background, new physics, etc.)

## Slide 53: Synchronous readout
All channels are doing the same “thing” at the same time
Synchronous to a global clock (bunch crossing clock)
Data-rate on each link is identical and depends only on trigger -rate
On-detector buffers (de-randomizers) are of same size and there occupancy (“how full they are”) depends only on the trigger-rate
 Lots of bandwidth wasted for zero’s
  Price of links determine if one can afford this
 No problems if occupancy of detectors or noise higher than expected
  But there are other problems related to this: spill over, saturation of detector, etc.
Trigger
Zero-
suppression
Data
formatting
MUX
DAQ
On-detector
Off-detector
Global clock
Data buffering during trigger
Derandomizer buffer

## Slide 54: Trigger & DAQ (Sneak Preview)

## Slide 55: What is a trigger?
An open-source 3D rally game?
The most famous horse in movie history?
An important part of a Beretta

## Slide 56: What is a trigger?
Wikipedia: “A trigger is a system that uses simple criteria to rapidly decide which events in a particle detector to keep when only a small fraction of the total can be recorded. “

## Slide 57: Trigger
Simple
Rapid
Selective
When only a small fraction can be recorded
Notes: This is not a scientific precise definition, but it catches what most physicists think about, when they hear “trigger”
Simple: because you want to be able to understand what the trigger did to your measurement – a selection of data will influence the result!
Rapid: because the data you want to keep, might be lost if you wait to long to decide
Decide to keep: a trigger is a selection mechanism, depending on what you want and what your apparatus is
When only a small fraction can be recorded: most of the time we are a looking for rare event and consider all events, which create similar signals in our detectors as “background”, the cheap & dumb approach would be to record everything and then try to select in the analysis the good events. Even though sometimes this would be nice, in practice we do not have enough money to do that.

## Slide 58: Trivial DAQ
ADC Card
External View
sensor
sensor
CPU
disk
ADC
storage
Physical View
Logical View
Proces-
sing

## Slide 59: Trivial DAQ with a real trigger
ADC
Sensor
Delay
Proces-
sing
Interrupt
Discriminator
Trigger
Start
storage
What if a trigger is produced when the ADC or
processing is busy?

## Slide 60: Trivial DAQ with a real trigger 2
ADC
Sensor
Delay
Proces-
sing
Interrupt
Discriminator
Trigger
Start
Deadtime (%) is the ratio between the time the DAQ
is busy and the total time.
Set
Q
Clear
and
not
Busy Logic
Ready
storage

## Slide 61: Trivial DAQ with a real trigger 3
ADC
Sensor
Delay
Proces-
sing
Discriminator
Trigger
Start
Buffers are introduced to de-randomize data,
to decouple the data production from the data
consumption. Better performance.
Busy Logic
FIFO
Full
DataReady
and
storage

## Slide 62: Triggered read-out
Trigger processing requires some data transmission and processing time to make decision so front-ends must buffer data during this time. This is called the trigger latency
For constant high rate experiments a “pipeline” buffer is needed in all front-end detector channels: (analog or digital)
  Real clocked pipeline (high power, large area, bad for analog)
  Circular buffer
  Time tagged (zero suppressed latency buffer based on time information)
ADC
DAQ
Shaping
Channel mux.
Trigger
Constant writing

## Slide 63: Trigger rate control
Trigger rate determined by physics parameters used in trigger system: 1 kHz – 1MHz for LHC experiments
  The lower rate after the trigger allows sharing resources across channels (e.g. ADC and readout links)
Triggers will be of random nature i.e. follow a Poisson distribution  a burst of triggers can occur within a short time window so some kind of rate control/spacing is needed
  Minimum spacing between trigger accepts  dead-time
  Maximum number of triggers within a given time window
Derandomizer buffers needed in front-ends to handle this
  Size and readout speed of this determines effective trigger rate

## Slide 64: (Large) Systems

## Slide 65: New problems
Going from single sensors to building detector read-out of the circuits we have seen, brings up a host of new problems:
  Power, Cooling
  Crosstalk
  Radiation (LHC)
Some can be tackled by (yet) more sophisticated technologies

## Slide 66: Radiation effects
In some experiments large amounts of electronics are located inside the detector where there may be a high level of radiation
  This is the case for 3 of the 4 LHC experiments (10 years running)
    Pixel detectors: 10 -100 Mrad
    Trackers: ~10Mrad
    Calorimeters: 0.1 – 1Mrad
    Muon detectors: ~10krad
    Cavern: 1 – 10krad
Normal commercial electronics will not survive within this environment
  One of the reasons why much of the on-detector electronics in the LHC experiment are custom made
Special technologies and dedicated design approaches are needed to make electronics last in this unfriendly environment
Radiation effects on electronics can be divided into three major effects
  Total dose
  Displacement damage
  Single event upsets
1 Rad == 10 mGy
1 Gy = 100 Rad

## Slide 67: Total dose
Generated charges from traversing particles gets trapped within the insulators of the active devices and changes their behavior
For CMOS devices this happens in the thin gate oxide layer which have a major impact on the function of the MOS transistor
  Threshold shifts
  Leakage current
In deep submicron technologies ( <0.25um) the trapped charges are removed by tunneling currents through the very thin gate oxide
    Only limited threshold shifts
No major effect on high speed bipolar technologies

## Slide 68: Displacement damage
Traversing hadrons provokes displacements of atoms in the silicon lattice.
Bipolar devices relies extensively on effects in the silicon lattice.
  Traps (band gap energy levels)
  Increased carrier recombination in base
Results in decreased gain of bipolar devices with a dependency on the dose rate.
No significant effect on MOS devices
Also seriously affects Lasers and PIN diodes used for optical links.

## Slide 69: Single event upsets
Deposition of sufficient charge can make a memory cell or a flip-flop change value
As for SEL, sufficient charge can only be deposited via a nuclear interaction for traversing hadrons
The sensitivity to this is expressed as an efficient cross section for this to occur
This problem can be resolved at the circuit level or at the logic level
Make memory element so large and slow that deposited charge not enough to flip bit
Triple redundant (for registers)
Hamming coding (for memories)
  Single error correction, Double error detection
  Example Hamming codes: 5 bit additional for 8 bit data
    ham[0] = d[1] $ d[2] $ d[3] $ d[4]; ham[1] = d[1] $ d[5] $ d[6] $ d[7]; ham[2] = d[2] $ d[3] $ d[5] $ d[6] $ d[8]; ham[3] = d[2] $ d[4] $ d[5] $ d[7] $ d[8] ; ham[4] = d[1] $ d[3] $ d[4] $ d[6] $ d[7] $ d[8]; $ = XOR
  Overhead decreasing for larger words 32bits only needs 7hamming bits
Example of SEU cross section

## Slide 70: Powering
Delivering power to the front-end electronics highly embedded in the detectors has been seen to be a major challenge (underestimated).
The related cooling and power cabling infrastructure is a serious problem of the inner trackers as any additional material seriously degrades the physics performance of the whole experiment.
A large majority of the material in these detectors in LHC relates to the electronics, cooling and power and not to the silicon detector them selves (which was the initial belief)
How to improve
  Lower power consumption
  Improve power distribution

## Slide 71
Data Aquisition

## Slide 72: Introduction: DAQ
Data Acquisition is a specialized engineering discipline thriving mostly in the eco-system of large science experiments, particularly in HEP
It consists mainly of electronics, computer science, networking and (we hope) a little bit of physics

## Slide 73: Tycho Brahe and the Orbit of Mars
First measurement campaign
Systematic data acquisition
  Controlled conditions (same time of the day and month)
  Careful observation of boundary conditions (weather, light conditions etc…) - important for data quality / systematic uncertainties
I've studied all available charts of the planets and stars and none of them match the others. There are just as many measurements and methods as there are astronomers and all of them disagree. What's needed is a long term project with the aim of mapping the heavens conducted from a single location over a period of several years. Tycho Brahe, 1563 (age 17).

## Slide 74: The First Systematic Data Acquisition
Data acquired over 18 years, normally e every month
Each measurement lasted at least 1 hr with the naked eye
Red line (only in the animated version) shows comparison with modern theory

## Slide 75: Tycho’s DAQ in Today’s Terminology
Bandwith (bw) = Amount of data transferred / per unit of time
  “Transferred” = written to his logbook
  “unit of time” = duration of measurement
  bwTycho = ~ 100 Bytes / h (compare with LHCb 40.000.000.000 Bytes / s)
Trigger = in general something which tells you when is the “right” moment to take your data
  In Tycho’s case the position of the sun, respectively the moon was the trigger
  the trigger rate ~ 3.85 x 10-6 Hz (compare with LHCb 1.0 x 106 Hz)

## Slide 76: Some More Thoughts on Tycho
Tycho did not do the correct analysis of the Mars data, this was done by Johannes Kepler (1571-1630), eventually paving the way for Newton’s laws
Morale: the size & speed of a DAQ system are not correlated with the importance of the discovery!

## Slide 77: Publicité / Commercial

## Slide 79: The ISOTDAQ permanent lab
In February 2010 the first ISOTDAQ school was held in Ankara
See: http://isotdaq.web.cern.ch/isotdaq/isotdaq/2010.html
Slides and videos can be found at:
http://indico.cern.ch/conferenceTimeTable.py?confId=68278#20100201
Some of the exercises that were prepared for this school were (or will soon be) installed at CERN
Interested students can register themselves to do some of these exercises. To register:
  Add yourself to: https://twiki.cern.ch/twiki/bin/view/Sandbox/DaqSchoolLab#Requests_for_access
  Or write an e-mail to markus.joos@cern.ch
It is recommended to have a look at the slides / videos before doing an exercise
NOTE: We cannot guarantee that all the exercises will take place. So, don’t be disappointed, if you favourite is not in
Publcite
Advertisement

## Slide 80: A Very Simple Data Acquisition System

## Slide 81: Measuring Temperature
Suppose you are given a Pt100 thermo-resistor
We read the temperature as a voltage with a digital voltmeter

## Slide 82: Reading Out Automatically
Note how small the sensor has become.
In DAQ we normally need not worry about the details of the things we readout
USB/RS232
#include <libusb.h>
struct usb_bus *bus;
struct usb_device *dev;
usb_dev_handle *vmh = 0;
usb_find_busses(); usb_find_devices();
for (bus = usb_busses; bus; bus = bus->next)
for (dev = bus->devices; dev; dev = dev->next)
if (dev->descriptor.idVendor == HOBBICO) vmh = usb_open(dev);
usb_bulk_read(vmh ,3,&u,sizeof(float),500);

## Slide 83: Read-out 16 Sensors
Buy 4 x 4-port USB hub (very cheap) (+ 3 more voltmeters)
Adapt our little DAQ program
No fundamental (architectural) change to our DAQ

## Slide 84: Read-out 160 Sensors
For a moment we (might) consider to buy 52 USB hubs, 160 Voltmeters
…but hopefully we abandon the idea very quickly, before we start cabling this!
Expensive, cumbersome, fragile  our data acquisition system is not scalable

## Slide 85: Read-out with Buses

## Slide 86: A Better DAQ for Many (temperature) Sensors
Buy or build a compact multi-port volt-meter module, e.g. 16 inputs
Put many of these multi-port modules together in a common chassis or crate
The modules need
  Mechanical support
  Power
  A standardized way to access their data (our measurement values)
All this is provided by standards for (readout) electronics such as VME (IEEE 1014)
Backplane Connectors
(for power and data)
VME Board
Plugs into Backplane
7U VME Crate
(a.k.a. “Subrack”)
19”
7U

## Slide 87: DAQ for 160 Sensors Using VME
Readout boards in a VME-crate
  mechanical standard for
  electrical standard for power on the backplane
  signal and protocol standard for communication on a bus
Notes:     modules (6U x 200 mm, 9U x 400 mm)
    Crates 19’’ wide

## Slide 88: A Word on Mechanics and Pizzas
The width and height of racks and crates are measured in US units: inches (in, '') and U
  1 in = 25.4 mm
  1 U = 1.75 in = 44.45 mm
The width of a "standard" rack is 19 in.
The height of a crate (also sub-rack) is measured in Us
Rack-mountable things, in particular computers, which are 1 U high are often called pizza-boxes
At least in Europe, the depth is measured in mm
Gory details can be found in IEEE 1101.x (VME mechanics standard)
49 U
19 in
1 U

## Slide 89: Communication in a Crate: Buses
A bus connects two or more devices and allows the to communicate
The bus is shared between all devices on the bus  arbitration is required
Devices can be masters or slaves (some can be both)
Devices can be uniquely identified ("addressed") on the bus
Device 1
Master
Data Lines
Slave
Select Line
Device 2
Device 4
Device 3
Device 2
Device 4
Master
Data Lines
Slave
Select Line
Device 1
Device 3
Notes: Address and data signals can be on separate electrical lines or share the same lines (multiplexed)

## Slide 90: Advantages of buses
Relatively simple to implement
  Constant number of lines
  Each device implements the same interface
Easy to add new devices
  topological information of the bus can be used for automagically choosing addresses for bus devices: this is what plug and play is all about.

## Slide 91: Buses for DAQ at LHC?
A bus is shared between all devices (each new active device slows everybody down)
  Bus-width can only be increased up to a certain point (128 bit for PC-system bus)
  Bus-frequency (number of elementary operations per second) can be increased, but decreases the physical bus-length
Number of devices and physical bus-length is limited (scalability!)
  For synchronous high-speed buses, physical length is correlated with the number of devices (e.g. PCI)
  Typical buses have a lot of control, data and address lines (look at a SCSI or ATA cable)
Buses are typically useful for systems < 1 GB/s

## Slide 92: Moving on to Bigger Things…
The CMS Detector

## Slide 93: Moving on to Bigger Things…
?
15 million detector channels
@ 40 MHz
= ~15 * 1,000,000 * 40 * 1,000,000 bytes
= ~ 600 TB/sec

## Slide 94: Network based DAQ
In large (HEP) experiments we typically have thousands of devices to read, which are sometimes very far from each other  buses can not do that
Network technology solves the scalability issues of buses
  In a network devices are equal ("peers")
  In a network devices communicate directly with each other
    no arbitration necessary
    bandwidth guaranteed
  data and control use the same path
    much fewer lines (e.g. in traditional Ethernet only two)
  At the signaling level buses tend to use parallel copper lines. Network technologies can be also optical, wire-less and are typically (differential) serial

## Slide 95: Network Technologies
Examples:
  The telephone network
  Ethernet (IEEE 802.3)
  ATM (the backbone for GSM cell-phones)
  Infiniband
  Myrinet
  many, many more
Note: some of these have "bus"-features as well (Ethernet, Infiniband)
Network technologies are sometimes functionally grouped
  Cluster interconnect (Myrinet, Infiniband) 15 m
  Local area network (Ethernet), 100 m to 10 km
  Wide area network (ATM, SONET) > 50 km

## Slide 96: Connecting Devices in a Network
On an network a device is identifed by a network address
  eg: our phone-number, the MAC address of your computer
Devices communicate by sending messages (frames, packets) to each other
Some establish a connection lilke the telephone network, some simply send messages
Modern networks are switched with point-to-point links
  circuit switching, packet switching

## Slide 97: Switched Networks
In a switched network each node is connected either to another node or to a switch
Switches can be connected to other switches
A path from one node to another leads through 1 or more switches (this number is sometimes referred to as the number of "hops" )

## Slide 98: A Switched Network
While 2 can send data to 1 and 4, 3 can send at full speed to 5
2 can distribute the share the bandwidth between 1 and 4 as needed
5
4
1
2
3

## Slide 99: Data Acquisition for a Large Experiment

## Slide 100: Designing a DAQ System for a Large HEP Experiment
What defines "large"?
  The number of channels: for LHC experiments O(107) channels
    a (digitized) channel can be between 1 and 14 bits
  The rate: for LHC experiments everything happens at 40.08 MHz, the LHC bunch crossing frequency (This corresponds to 24.9500998 ns or 25 ns among friends)
Sub-systems: tracking, calorimetry, particle-ID, muon-detectors, are of very different size from the point of view of the DAQ (the amount of data from the Muon system is normally small compared to the pixel detectors)

## Slide 101: What Do We Need to Read Out a Detector (successfully)?
A selection mechanism (“trigger”)
Electronic readout of the sensors of the detectors (“front-end electronics”)
A system to keep all those things in sync (“clock”)
A system to collect the selected data (“DAQ”)
A Control System to configure, control and monitor the entire DAQ
Time, money, students

## Slide 102: Trigger for LHC
No (affordable) DAQ system could read out O(107) channels at 40 MHz  400 TBit/s to read out – even assuming binary channels!
What’s worse: most of these millions of events per second are totally uninteresting: one Higgs event every 0.02 seconds
A first level trigger (Level-1, L1) must somehow* select the more interesting events and tell us which ones to deal with any further
Black magic happening here
(*) See “Triggers for LHC Physics”
Notes: c.f. 2 500 000 000 simultaneous(!) phone conversations (practically everybody on the planet is on the phone - like 31st of December 23:59)

## Slide 103: Challenges for the L1 at LHC
N (channels) ~ O(107); ≈20 interactions every 25 ns
  need huge number of connections
Need to synchronize detector elements to (better than) 25 ns
In some cases: detector signal/time of flight > 25 ns
  integrate more than one bunch crossing's worth of information
  need to identify bunch crossing...
It's On-Line (cannot go back and recover events)
  need to monitor selection - need very good control over all conditions

## Slide 104: Clock Distribution and Synchronisation
An event is a snapshot of the values of all detector front-end electronics elements, which have their value caused by the same collision
A common clock signal must be provided to all detector elements
  Since the c is constant, the detectors are large and the electronics is fast, the detector elements must be carefully time-aligned
Common system for all LHC experiments TTC based on radiation-hard opto-electronics
Plus:
Trigger decision
Bunch cross ID

## Slide 105: Distributing the L1 Trigger
Assuming now that a magic box tells for each bunch crossing (clock-tick) yes or no
  Triggering is not for philosophers – “perhaps” is not an option
This decision has to be brought for each crossing to all the detector front-end electronics elements so that they can send of their data or discard it
Global Trigger 1
Accept/Reject LV-1
Front-End Digitizer
Local level-1 trigger
Primitive e, g, jets, µ
Pipeline delay
( ≈ 3 µs)
≈ 2-3 µs latency loop
Trigger
Primitive Generator

## Slide 106: High Level Trigger
And that, in simple terms, is what we do in the High Level Trigger

## Slide 107: After L1: What’s next?
Where are we after L1
  ATLAS and CMS : rate is ~75 to 100 kHz, event size ~ 1 - 2 MB
  LHCb: rate is 1 MHz, event size 40 kB / ALICE: O(kHz) and O(GB)
Ideally
  Run the real full-blown physics reconstruction and selection algorithms
  These application take O(s). Hence: even at above rates still need 100 MCHF server farm (Intel will be happy!)
In Reality:
  Start by looking at only part of the detector data seeded by what triggered the 1st level
  LHCb: 1st level Trigger confirmation" algorithms: < 10 ms/event
  Atlas: Region of Interest" (RoI): < 40 ms/event
 Reduce the rate by factor ~ 30, and then do offline analysis

## Slide 108: The High Level Trigger is …
SWITCH
HLT farm
Detector
TTC
System
SWITCH
SWITCH
SWITCH
SWITCH
SWITCH
SWITCH
READOUT NETWORK
LHC clock
Event building
Front
-
End
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
C
P
U
Readout
Board
Experiment Control System (ECS)
VELO
ST
OT
RICH
ECal
HCal
Muon
L1
Trigger
C
P
C
P
U
P
U
C
P
U
Readout
Board
Readout
Board
Readout
Board
Readout
Board
Readout
Board
Readout
Board
FE
Electronics
FE
Electronics
FE
Electronics
FE
Electronics
FE
Electronics
FE
Electronics
FE
Electronics
HERE
The question is: How do we get the data in?

## Slide 109: Event Building (providing the data for the High Level Trigger)

## Slide 110: Two philosophies
Send everything, ask questions later (ALICE, CMS, LHCb)
Send a part first, get better question Send everything only if interesting (ATLAS)

## Slide 111: Event Building
Data Acquisition
Switch
To Trigger
Algorithms
1
Event fragments are received from detector front-end
2
Event fragments are read out over a network to an event builder
3
Event builder assembles fragments into a complete event
4
Complete events are processed by trigger algorithms
Event Builder 3
Event Builder 3
Event Builder 3

## Slide 112: Push-Based Event Building
Switch Buffer
Data Acquisition
Switch
1
Readout Supervisor tells readout boards where events must be sent (round-robin)
2
Readout boards do not buffer, so switch must
3
No feedback from Event Builders to Readout system
“Send next event to EB1”
“Send next event to EB2”
Event Builder 2
Event Builder 1
Readout
Supervisor

## Slide 113: Congestion
2
1
3
2
2
Bang
"Bang" translates into random, uncontrolled packet-loss
In Ethernet this is perfectly valid behavior and implemented by very cheap devices
Higher Level protocols are supposed to handle the packet loss due to lack of buffering
This problem comes from synchronized sources sending to the same destination at the same time

## Slide 114: Pull-Based Event Building
Event Builder 1
Data Acquisition
Switch
1
Event Builders notify Readout Supervisor of available capacity
2
Readout Supervisor ensures that data are sent only to nodes with available capacity
3
Readout system relies on feedback from Event Builders
“Send next event to EB1”
“Send next event to EB2”
EB1:
EB2:
EB3:
0
0
0
“Send me
an event!”
“Send me
an event!”
1
1
1
“Send me
an event!”
“Send me
an event!”
0
1
1
0
0
1
“Send next event to EB3”
1
0
1
Event Builder 1
Event Builder 2
Event Builder 3

## Slide 115: AACL
ALICE, ATLAS, CMS, LHCb
DAQs in 4 slides

## Slide 116: ALICE DAQ
GDC
GDC
GDC
GDC
CTP
LTU
TTC
FERO
FERO
LTU
TTC
FERO
FERO
LDC
LDC
BUSY
BUSY
Rare/All
Event
Fragment
Sub-event
Event
File
Storage Network 1250 MB/s
TDS
PDS
L0, L1a, L2
L0, L1a, L2
342 DDLs
EDM
LDC
Load Bal.
LDC
LDC
HLT Farm
FEP
FEP
DDL
H-RORC
10 DDLs
10 D-RORC
10 HLT LDC
144 DDLs
TDS
DS
DS
Event Building Network 2500 MB/s
416 D-RORC
194 Detector LDC
50 GDC
25 TDS
5 DSS
Two stage hardware trigger L0 + L1
High Level Trigger (HLT) on separate farm

## Slide 117: ATLAS DAQ
117
ATLAS
L1 selects events at 100 kHz and defines regions of interest
L2 pulls data from the region of interest and processes the data in a farm of processors L2 accepts data at ~ 1 kHz
Event Filter reads the entire detector (pull), processes the events in a farm and accepts at 100 Hz
Notes: 117

## Slide 118: CMS DAQ

## Slide 119: LHCb DAQ
40 GB/s
80 MB/s
Average event size 40 kB
Average rate into farm 1 MHz
Average rate to tape 2 kHz

## Slide 120: Trigger/DAQ parameters
No.Levels Level-0,1,2 Event Readout HLT Out
Trigger Rate (Hz) Size (Byte) Bandw.(GB/s) MB/s (Event/s)
4 Pb-Pb 500 5x107 25 1250 (102)
p-p 103 2x106 200 (102)
3 LV-1 105 1.5x106 4.5 300 (2x102)
LV-2 3x103
2 LV-1 105 106 100 ~1000 (102)
2 LV-0 106 3.5x104 35 70 (2x103)
ALICE
ATLAS
CMS
LHCb
Notes: Trigger levels include HLT which is operating on entire events

## Slide 121: The end

## Slide 122: Further Reading
Electronics
  Helmut Spielers web-site: http://www-physics.lbl.gov/~spieler/
Buses
  VME: http://www.vita.com/
  PCI http://www.pcisig.com/
Network and Protocols
  Ethernet “Ethernet: The Definitive Guide”, O’Reilly, C. Spurgeon
  TCP/IP “TCP/IP Illustrated”, W. R. Stevens
  Protocols: RFCs www.ietf.org in particular RFC1925 http://www.ietf.org/rfc/rfc1925.txt “The 12 networking truths” is required reading
Wikipedia (!!!) and references therein – for all computing related stuff this is usually excellent
Conferences
  IEEE Realtime
  ICALEPCS
  CHEP
  IEEE NSS-MIC
Journals
  IEEE Transactions on Nuclear Science, in particular the proceedings of the IEEE Realtime conferences
  IEEE Transactions on Communications

## Slide 123: More Stuff
Data format, DIY DAQ, run-control

## Slide 124: Overcoming Congestion: Queuing at the Input
Two frames destined to the same destination arrive
While one is switched through the other is waiting at the input port
When the output port is free the queued packet is sent
2
1
3
2
2

## Slide 125: Head of Line Blocking
2
1
3
2
2
4
4
Packet to node 4 must wait
even though port to node 4 is free
The reason for this is the First in First Out (FIFO) structure of the input buffer
Queuing theory tells us* that for random traffic (and infinitely many switch ports) the throughput of the switch will go down to 58.6%  that means on 100 MBit/s network the nodes will "see" effectively only ~ 58 MBit/s
*) "Input Versus Output Queueing on a Space-Division Packet Switch"; Karol, M. et al. ; IEEE Trans. Comm., 35/12

## Slide 126: Output Queuing
In practice virtual output queueing is used: at each input there is a queue  for n ports O(n2) queues must be managed
Assuming the buffers are large enough(!) such a switch will sustain random traffic at 100% nominal link load
2
1
3
2
2
4
4
Packet to node 2 waits at output to
port 2. Way to node 4 is free

## Slide 127: Binary vs Text
11010110 Pros:
  compact
  quick to write & read (no conversion)
Cons:
  opaque (humans need tool to read it)
  depends on the machine architecture (endinaness, floating point format)
  life-time bound to availability of software which can read it
<TEXT></TEXT> Pros:
  universally readable
  can be parsed and edited equally easily by humans and machines
  long-lived (ASCII has not changed over decades)
  machine independent
Cons:
  slow to read/write
  low information density (can be improved by compression)

## Slide 128: A little checklist for your DAQ
Remember:
YMMV

## Slide 129: Runcontrol
© Warner Bros.

## Slide 130: Run Control
The run controller provides the control of the trigger and data acquisition system. It is the application that interacts with the operator in charge of running the experiment.
The operator is not always an expert on T/DAQ. The user interface on the Run Controller plays an important role.
The complete system is modeled as a finite state machine. The commands that run controller offers to the operator are state transitions.
LHCb DAQ /Trigger Finite State Machine diagram (simplified)

## Slide 131: Finite State Machine
State A
Each component, sub-component of the system is modeled as a Finite State Machine. This abstraction facilitates the description of each component behavior without going into detail
The control of the system is realized by inducing transitions on remote components due to a transition on a local component
Each transition may have actions associated. The action consist of code which needs to be executed in order to bring the component to its new state
The functionality of the FSM and state propagation is available in special software packages such as SMI
State B
State C
State D
Component 1
Component 2
Component 1 can only
complete the transition to
State B if Component 2 is
in state D.

## Slide 132: Detector Control
The detector control system (DCS) (also Slow Control) provides the monitoring and control of the detector equipment and the experiment infrastructure.
Due to the scale of the current and future experiments is becoming more demanding: for the LHC Experiments: » 100000 parameters
Experiment
Control
Run / DAQ
Control
Detector
Control
Control hierarchy

## Slide 133: Run Control GUI
Main panel of the LHCb run-control
(PVSS II)

## Slide 134: Control and monitoring
Access to setup registers (must have read-back)
Access to local monitoring functions
  Temperatures, power supply levels, errors, etc.
Bidirectional with addressing capability (module, chip, register)
Speed not critical and does not need to be synchronous
  Low speed serial bus: I2C, JTAG, SPI
Must be reasonably reliable (read-back to check correct download and re-write when needed)
SPECS
Example: ELMB

## Slide 135: Gallery
CMS on-line computing center
ATLAS Online Network Infrastructure
ALICE Storage System

## Slide 136: Even more stuff

## Slide 137: Transistors
Exampe: bi-polar transistor of the NPN type
C collector, E emitter, B Base
EB diode is in forward bias: holes flow towards np boundary and into n region
BC diode is in reverse bias: electrons flow AWAY from pn boundary
p layer must be thinner than diffusion length of electrons so that they can go through from E to C without much recombination
from Wikipedia

## Slide 138: Multilevel triggering
First level triggering.
  Hardwired trigger system to make trigger decision with short latency.
  Constant latency buffers in the front-ends
Second level triggering in DAQ interface
  Processor based (standard CPU’s or dedicated custom/DSP/FPGA processing)
  FIFO buffers with each event getting accept/reject in sequential order
  Circular buffer using event ID to extracted accepted events
    Non accepted events stays and gets overwritten by new events
High level triggering in the DAQ systems made with farms of CPU’s: hundreds – thousands. (separate lectures on this)
Trigger L1
Trigger L2
Zero-
suppression
Data
formatting
DAQ
MUX
Front-end
DAQ interface

## Slide 139: ADC architectures
Flash
  A discriminator for each of the 2n codes
  New sample every clock cycle
  Fast, large, lots of power, limited to ~8 bits
  Can be split into two sub-ranging Flash 2x2n/2 discriminators: e.g. 16 instead of 256 plus DAC
    Needs sample and hold during the two stage conversion process
Ramp
  Linear analog ramp and count clock cycles
  Takes 2n clock cycles
  Slow, small, low power, can be made with large resolution
1
2
3
2n
Linear to binary encoder
Vref
1
Counter
Start
Clock
Start
Stop
Ramp
Vin
I
Vin
Vin
Flash1
DAC
-
Flash2
Vin
S&H

## Slide 140: ADC architectures
Successive approximation
  Binary search via a DAC and single discriminator
  Takes n clock cycles
  Relatively slow, small, low power, medium to large resolution
Pipelined
  Determines “one bit” per clock cycle per stage
    Extreme type of sub ranging flask
  n stages
  In principle 1 bit per stage but to handle imperfections each stage normally made with ~2bits and n*2bits mapped into n bits via digital mapping function that “auto corrects” imperfections
  Makes a conversion each clock cycle
  Has a latency of n clock cycles
    Not a problem in our applications except for very fast triggering
  Now dominating ADC architecture in modern CMOS technologies and impressive improvements in the last 10 years: speed, bits, power, size
100
010
011
DAC code
DAC voltage
DAC
Aprox reg.
Vin
ADC code

## Slide 141: ADC imperfections
Quantization (static)
  Bin size: Least significant bit (LSB) =Vmax/2n
  Quantization error: RMS error/resolution:
Integral non linearity (INL): Deviation from ideal conversion curve (static)
  Max: Maximum deviation from ideal
  RMS: Root mean square of deviations from ideal curve
Differential non linearity (DNL): Deviation of quantization steps (static)
  Min: Minimum value of quantization step
  Max: Maximum value of quantization step
  RMS: Root mean square of deviations from ideal quantization step
Missing codes (static)
  Some binary codes never present in digitized output
Monotonic (static)
  Non monotonic conversion can be quite unfortunate in some applications. A given output code can correspond to several input values.