## Slide 1: IBS simulations benchmark
Benchmark IBS codes (CERN – INFN)
  SLS as example
  Nominal energy (2.411GeV ) and 1.6GeV
  Use perfect lattice with misalignments for getting some vertical emittance
  Zero-current vertical emittance of 2pm in both cases
  Zero-current bunch length of 3.8mm in both cases
  Bunch current of 3e10 @2.411GeV and 6e9 @1.6GeV
  Fanouria will provide the MADX file
  Compare h/v and bunch length as a function of time and final distribution
Parameter | Value
Energy [GeV] | 2.411
Circumference [m] | 288
Energy loss/turn [MeV] | 0.54
RF voltage [MV] | 2.1
Mom. Comp. factor | 6.05e-4
Damping times h/v/l [ms] | 8.59/8.55/4.26
Hor. emittance [nm rad] | 5.6
Vert. emittance [pm rad] | 2
Bunch length [mm] | 3.8
Energy spread [%] | 0.086

## Slide 2: IBS simulation improvements
Include high-order terms in tracking
  High-order sector map may be problematic due to lack of symplecticity
  Need to use MADX-PTC – discuss with Etienne Forest during his visit at CERN (May 2011)
Remove effective angle approximation and use real Coulomb interaction
  May become extremely time consuming
Parallelisation using CMAD (contact with Mauro) and/or MADX-PTC (E. Forest)

## Slide 3: IBS measurements
The theoretical predictions indicate that the effect could be measured at the SLS but not for the nominal energy and beam.
  The effect is visible at lower energies and/or higher bunch current
In order to disentangle the effect from other collective effects  run the machine in one bunch mode (or few bunches)
  Issues with BPM calibration at different current (MD time)
  Issues with other diagnostics (profile measurements?)
There is the possibility to use the 3rd harmonic cavity in bunch shortening mode but:
  The 3rd harmonic cavity needs to be retuned
  Retuning of the RF cavity needed in order to be able to go at nominal current for lower energies (high-order modes)
  Measurements in the horizontal plane where the effect is more visible
  SLS colleagues mentioned that some MD shifts may be possible during August (to be confirmed)

## Slide 4: TIARA issues
Edit web-space
  Include picture of SLS
  Milestones and deliverables
  MD report (Simone), Interim report on Instrumentation (Andreas), Minutes of IBS meeting
Schedule a webex meeting before TIARA Steering committee meeting (May 10th)
  Proposed date May 2nd (tbc)
Confirm date of next MD
  Data exchange optimisation
Meeting on Beam Instrumentation at SLS (tbc)
Abstract for IPAC (Yannis) to be partially used as the report on existing hardware limitations (due for 09/2011)