## Slide 1
Error Tolerances, Girder Errors and long range errors from a beam dynamics point of view
S.M.Liuzzo, ESRF, Grenoble, 27th June 2023, on behalf of the beam dynamics group
The message of this presentation is, for an HMBA-like upgrade project:
Girder-Girder == Magnet-Magnet
IF ANY, USE SIMULATED SURVEYs INSTEAD OF GIRDER-GIRDER and LONG RANGE ERRORS

## Slide 2: Tolerance estimates objective
TARGET
Septum
>10h
Touschek Lifetime
@ 200mA uniform, 5pm
Injected
beam
2 main parameters to achieve,
Absolute values depend on facility layout.
-10mm (-8.1mm @INJECTION)
~100% Injection Efficiency
Also :
Emittance variation < 2pm
Feasible correction strengths
Orbit < 100um rms
etc…

## Slide 3: LifEtime and dynamic apertures vs error sources
10h
17h
DA=-10mm
Lifetime = 10h
A CLUSTER is crucial for this analysis. Each error set to analyze requires 1CPUx4h
CAoPAC Workshop l GSI, Darmstadt 10-13 March 2015 l S.M.Liuzzo
How tolerances were defined
How to determine the ”tolerance” ?  DRAW A LINE (relative impact of each error), RESCALE globally.
The line where I should have placed it.
The line where I should have placed it.
Sext. Alignment do more on DA than on TLT ;
Moderate gradient are irrelevant compared to high gradient ;
Etc. etc.

## Slide 4: Comparable tolerance table
DQ (combined function dipoles) behave as quadrupoles concerning errors. Evident the impact on vertical dispersion compared to the other quadrupoles (defocussing quadrupoles).
Quadrupoles have large impact on orbit and horizontal dispersion, also in this case, lifetime and DA are strongly affected. QF6 and QF8 are dominant.
Sextupoles have the largest impact on DA, they are also the strongest source of beta-beating and emittance as expected.
Octupoles influence is limited compared to quadrupole and sextupoles, nevertheless they do have an impact on DA. Their effect on lifetime is very small.
Rotations up to 100urad have impact on the various parameters but limited.
How tolerances were defined
In RED
The worst crossing of the “line” for each performance parameter

## Slide 5: Tolerable random errors
Each error, on each magnet family, is studied individually looking at the dependence of DA, lifetime, emittances and all relevant parameters vs error amplitude.
Required: | DX | DY | DS | DPSI | DK
 | mm | mm | mm | mrad | 10^-4
DL | >100 | >100 | 1000 | 500 | 10
DQ, QF[68] | 70 | 50 | 500 | 200 | 5
Q[DF][1-5] | 100 | 85 | 500 | 500 | 5
SFD | 70 | 50 | 500 | 1000 | 35
OF | 100 | 100 | 500 | 1000 | 
Sextupoles and high gradient quadrupoles are the most relevant limitations, nevertheless, this alignment specifications are currently achievable.
(DX=DY=60mm, 84 mm between two magnets).
How tolerances were defined

## Slide 6: Girder Errors
Girder displacements and rotations
Girder displacements and rotations
+ random errors Quad. and Sext.
4 girders, BPMs are moved with the girder.
l 30-31 May 2014 l S.M.Liuzzo
How GIRDER
tolerances were defined

## Slide 7: Dynamic aperture @S3 septum vs errors for s28A + RDT correction
-20%
l WP1 ESRF upgrade l May 2014 l S.M.Liuzzo
26/07/2013
How GIRDER
tolerances were defined
All is NOT the sum of each error

## Slide 8: error values for a reduction of 20% of Hor. Dynamic Aperture @S3
No influence on emittances
Strong impact of quadrupole errors
RDT correction
How GIRDER
tolerances were defined

## Slide 9: Girder Errors
(g) Stands for girder errors,
no (g), are quadrupole and sextupole individual misalignments
10h
17h
Hor. DA @ QFI, X0.81 to scale at S3,
8mm required at S3, 10mm accepted at QFI
How GIRDER
tolerances were defined
In terms of DA girders and magnet alignment approx. sum up. In terms of lifetime, magnets+girder have a stronger impact.
Girders+Magnets
Girders+Magnets
GOOD
BAD
Girders only
girders

## Slide 10: Summary Table of Girder Errors
(g) Stands for girder errors, no g, are quadrupole and sextupole individual misalignments
How GIRDER
tolerances were defined
Commissioning-like correction sequence to get these data
Cluster, Average over several (10) error seeds.
Computing cluster

## Slide 11: The measured position of the lattice
nominal
current
How GIRDER
tolerances were excluded
This is where the machine is. Let’s use this information!
ESRF 1994-2018
EBS 2019-?? We placed EBS where the old SR used to be. Everyone is happy.

## Slide 12: Survey errors PLUS random errors
Random Gaussian DX DY in quadrupoles and sextupoles on top of the survey errors.
The blue curve represents the current ESRF storage ring position.
The x symbols are the interpolated positions on this curve for the S28A lattice.
BPM are positioned on the same curve.
DX and DZ and girder rotations are applied.
Errors are ramped in steps of 20% up to the nominal value.
Added random errors to account for unknown magnetic center position
l ESRF Upgrade l June 2014 l S.M.Liuzzo
How GIRDER
tolerances were excluded
D.Martin, G.Gatta

## Slide 13: Long range errors
Error “waves” applied to the lattice: DX, DY, Rotations for quad and sext.
Correction performed for each frequency and amplitude set as:
Open trajectory correction
Orbit correction
RDT correction
storage ring survey data
simulated 1st harmonic,
Simulations performed on the OAR asd cluster, 8h-600cpu
26/07/2013
How GIRDER
tolerances were excluded
10 years AGO!

## Slide 14: displacements and global tilt
--------------------------------------------------
------ total std corrector values applyed --------
------ --------
HK (288) [1/m]: 0.00e+00 -> 1.06e-04
VK (288) [1/m]: 0.00e+00 -> 1.19e-04
SK (288) [1/m2]: 0.00e+00 -> 0.00e+00
QK (514) [1/m2]: 0.00e+00 -> 0.00e+00
HKL (288) [rad]: 0.00e+00 -> 1.08e-05
VKL (288) [rad]: 0.00e+00 -> 8.25e-06
SKL (288) [T/m]: 0.00e+00 -> 0.00e+00
QKL (514) [T/m]: 0.00e+00 -> 0.00e+00
------ --------
------ residual orbit and dispersion --------
------ --------
OH (288) [m]: 3.78e-05 -> 9.02e-06
OV (288) [m]: 1.48e-04 -> 9.05e-07
DH (288) [m]: 3.80e-04 -> 1.18e-04
DV (288) [m]:1.38e-03 -> 3.33e-04
BBH (288) %: 0.9 -> 0.3
BBV (288) %: 0.6 -> 0.3
PhH (288) : 2.09e-02 -> 1.75e-02
PhV (288) : 1.70e-02 -> 1.07e-02
------ --------
------ tune and emittance --------
------ --------
Qx [0.580]: 0.580 -> 0.580
Qy [0.620]: 0.619 -> 0.619
EX [147.528 pm]: 147.506 -> 147.545
EY [0.000pm]: 0.986 -> 0.049
------ --------
--------------------------------------------------
----- ----- -- -- -- -- ------ -----
initial (ex, ey): 147.53, 0.00,
errors (ex, ey): 147.51, 0.99,
corrected (ex, ey): 147.54, 0.05,
Freq 1, every 32

## Slide 15: every 16 cells
--------------------------------------------------
------ total std corrector values applyed --------
------ --------
HK (288) [1/m]: 0.00e+00 -> 1.51e-04
VK (288) [1/m]: 0.00e+00 -> 1.68e-04
SK (288) [1/m2]: 0.00e+00 -> 0.00e+00
QK (514) [1/m2]: 0.00e+00 -> 0.00e+00
HKL (288) [rad]: 0.00e+00 -> 1.54e-05
VKL (288) [rad]: 0.00e+00 -> 1.17e-05
SKL (288) [T/m]: 0.00e+00 -> 0.00e+00
QKL (514) [T/m]: 0.00e+00 -> 0.00e+00
------ --------
------ residual orbit and dispersion --------
------ --------
OH (288) [m]: 6.01e-05 -> 1.28e-05
OV (288) [m]: 2.61e-04 -> 1.31e-06
DH (288) [m]: 5.95e-04 -> 1.75e-04
DV (288) [m]:2.41e-03 -> 5.84e-04
BBH (288) %: 1.4 -> 0.5
BBV (288) %: 0.9 -> 0.5
PhH (288) : 1.77e-02 -> 1.28e-02
PhV (288) : 1.42e-02 -> 8.11e-03
------ --------
------ tune and emittance --------
------ --------
Qx [0.580]: 0.579 -> 0.580
Qy [0.620]: 0.618 -> 0.619
EX [147.528 pm]: 147.487 -> 147.563
EY [0.000pm]: 2.806 -> 0.137
------ --------
--------------------------------------------------
Freq 2, evry 16 cells

## Slide 16: every 8 cells
--------------------------------------------------
------ total std corrector values applyed --------
------ --------
HK (288) [1/m]: 0.00e+00 -> 1.37e-04
VK (288) [1/m]: 0.00e+00 -> 1.63e-04
SK (288) [1/m2]: 0.00e+00 -> 0.00e+00
QK (514) [1/m2]: 0.00e+00 -> 0.00e+00
HKL (288) [rad]: 0.00e+00 -> 1.54e-05
VKL (288) [rad]: 0.00e+00 -> 1.14e-05
SKL (288) [T/m]: 0.00e+00 -> 0.00e+00
QKL (514) [T/m]: 0.00e+00 -> 0.00e+00
------ --------
------ residual orbit and dispersion --------
------ --------
OH (288) [m]: 8.79e-05 -> 1.31e-05
OV (288) [m]: 1.35e-03 -> 1.67e-06
DH (288) [m]: 2.59e-03 -> 2.61e-04
DV (288) [m]:1.02e-02 -> 3.12e-03
BBH (288) %: 3.9 -> 0.5
BBV (288) %: 2.2 -> 0.5
PhH (288) : 2.95e-02 -> 6.91e-03
PhV (288) : 2.13e-02 -> 5.69e-03
------ --------
------ tune and emittance --------
------ --------
Qx [0.580]: 0.574 -> 0.580
Qy [0.620]: 0.612 -> 0.619
EX [147.528 pm]: 147.077 -> 147.596
EY [0.000pm]: 67.039 -> 4.014
------ --------
--------------------------------------------------
----- ----- -- -- -- -- ------ -----
initial (ex, ey): 147.53, 0.00,
errors (ex, ey): 147.08, 67.04,
corrected (ex, ey): 147.60, 4.01,
Freq 4, every 8 cells

## Slide 17: every 4 cells
--------------------------------------------------
------ total std corrector values applyed --------
------ --------
HK (288) [1/m]: 0.00e+00 -> 1.24e-04
VK (288) [1/m]: 0.00e+00 -> 1.63e-04
SK (288) [1/m2]: 0.00e+00 -> 0.00e+00
QK (514) [1/m2]: 0.00e+00 -> 0.00e+00
HKL (288) [rad]: 0.00e+00 -> 1.59e-05
VKL (288) [rad]: 0.00e+00 -> 1.14e-05
SKL (288) [T/m]: 0.00e+00 -> 0.00e+00
QKL (514) [T/m]: 0.00e+00 -> 0.00e+00
------ --------
------ residual orbit and dispersion --------
------ --------
OH (288) [m]: 6.11e-05 -> 1.40e-05
OV (288) [m]: 1.37e-04 -> 1.84e-06
DH (288) [m]: 7.00e-04 -> 2.83e-04
DV (288) [m]:1.72e-03 -> 3.68e-04
BBH (288) %: 3.8 -> 2.4
BBV (288) %: 1.8 -> 2.5
PhH (288) : 2.23e-02 -> 1.34e-02
PhV (288) : 1.19e-02 -> 1.38e-02
------ --------
------ tune and emittance --------
------ --------
Qx [0.580]: 0.583 -> 0.580
Qy [0.620]: 0.622 -> 0.620
EX [147.528 pm]: 147.809 -> 147.692
EY [0.000pm]: 1.477 -> 0.133
------ --------
--------------------------------------------------
----- ----- -- -- -- -- ------ -----
initial (ex, ey): 147.53, 0.00,
errors (ex, ey): 147.81, 1.48,
corrected (ex, ey): 147.69, 0.13,
Freq 8, every 4 cells

## Slide 18: Misalignment pattern, every 2 cells
--------------------------------------------------
------ total std corrector values applyed --------
------ --------
HK (288) [1/m]: 0.00e+00 -> 1.05e-04
VK (288) [1/m]: 0.00e+00 -> 5.10e-05
SK (288) [1/m2]: 0.00e+00 -> 0.00e+00
QK (514) [1/m2]: 0.00e+00 -> 0.00e+00
HKL (288) [rad]: 0.00e+00 -> 1.07e-05
VKL (288) [rad]: 0.00e+00 -> 6.21e-06
SKL (288) [T/m]: 0.00e+00 -> 0.00e+00
QKL (514) [T/m]: 0.00e+00 -> 0.00e+00
------ --------
------ residual orbit and dispersion --------
------ --------
OH (288) [m]: 4.93e-05 -> 8.49e-06
OV (288) [m]: 3.13e-05 -> 1.60e-06
DH (288) [m]: 5.04e-04 -> 3.98e-04
DV (288) [m]:3.92e-04 -> 1.69e-04
BBH (288) %: 1.1 -> 0.6
BBV (288) %: 0.8 -> 0.2
PhH (288) : 7.76e-03 -> 2.97e-03
PhV (288) : 9.02e-03 -> 3.40e-03
------ --------
------ tune and emittance --------
------ --------
Qx [0.580]: 0.582 -> 0.579
Qy [0.620]: 0.616 -> 0.622
EX [147.528 pm]: 147.483 -> 141.513
EY [0.000pm]: 0.301 -> 13.404
------ --------
--------------------------------------------------
----- ----- -- -- -- -- ------ -----
initial (ex, ey): 147.53, 0.00,
errors (ex, ey): 147.48, 0.30,
corrected (ex, ey): 141.51, 13.40,
Freq 16, Every 2 cells

## Slide 19: Long range errors: error envelope function
Impact of error “waves” on horizontal orbit
At a wavelength of L/128~6m
30um errors amplitude give
30 um residual orbit distortion.
At a wavelength of L/2~422m
7mm errors amplitude give
30 um residual orbit distortion.
26/07/2013
How GIRDER
tolerances were excluded
SLOW, LARGE VARIATIONS HAVE LIMITED IMPACT ON THE OPTICS

## Slide 20: Emittance, dispersion and beta-beating vs wavelength
How GIRDER
tolerances were excluded

## Slide 21: Comparison of various Error Sources to obtain 30 um orbit

## Slide 22: Comparison of various Error Sources (other parameters)

## Slide 23: DRAFT table of tolerable rms of error distributions
Error (S28 Table) | TDS value | New value
Dipole DPSI | 300 mrad | Splitted
Dipole DX | 50 mm | Splitted
Dipole DY | 50 mm | Splitted
Quadrupole DX | 50 mm | Splitted
Quadrupole DY | 100 mm | Splitted
Quadrupole DPSI | 350 mrad | Splitted
Sextupole DX | 50 mm | 70
Sextupole DY | 75 mm | 50
Sextupole DPSI | - | 500 mrad
Girder DX | 50 mm | Removed
Girder DY | 50 mm | Removed
Girder DPSI | 200 mrad | Removed
BPM X-offset | 50 mm | Separated
BPM Y-offset | 50 mm | Separated
Dipole DK0/DK0 | 10 10-4 | 10 10-4
Quadrupole DK1/K1 | 5 10-4 | 5 10-4
Sextupole DK2/K2 | 35 10-4 | 35 10-4
Error (S28 Table) | TDS value | New value
DL DPSI | 300 | 500 mrad
DL DX | 50 | 100 mm
DL DY | 50 | 100 mm
DL DS | - | 1000 mm
DQ and QF6-8 DPSI | 300 | 200 mrad
DQ and QF6-8 DX | 50 | 50 mm
DQ and QF6-8 DY | 50 | 70 mm
DQ and QF6-8 DS | - | 500 mm
Octupole DX | - | 100 mm
Octupole DY | - | 100 mm
Octupole DPSI | - | 500 mrad
Octupole DS | - | 1000 mm
Q [D-F] [1-5] DPSI | 350 | 500 mrad
Q [D-F] [1-5] DX | 50 | 100 mm
Q [D-F] [1-5] DY | 100 | 85 mm
Q [D-F] [1-5] DS | - | 500 mm
Sextupole DS | - | 1000 mm
DS = longitudinal displacement
DX = radial displacement
DY = vertical displacement
DPSI = rotation about beam axis
Girder errors replaced by smooth wave summing first 4 long wavelengths with 0.6mm amplitude.

## Slide 24: d.A. and lifetime: Table above + waves + Bpm errors 50 um rms
DA about 7mm at S3 septum.
Some seeds have bad DA and some are lost. Work in progress to recover them. this may change the above list of tolerable errors.
Lifetime is about 7h.
“Closed” continuous waves

## Slide 25: The measured position of the lattice
nominal
current
This is where the machine is. Let’s use this information!
ESRF 1994-2018
EBS 2019-?? We placed EBS where the old SR used to be. Everyone is happy.
How GIRDER and LONG RANGE
tolerances were excluded

## Slide 26: Simulated survey errors current positions (from ALGE group)
Simulated survey errors about the current position of the lattice.
Rotations are random, but for a 21urad systematic outward tilt.
Data provided in 320 points for the current lattice.
26/07/2013
50 cases
WHERE WILL THE SR BE
if we remove it and reinstall it?
horizontal
Longitudinal (electrons path)
vertical
DATA from ALIGNMENT GROUP
How GIRDER and LONG RANGE
tolerances were excluded
D.Martin, G.Gatta
D.Martin, G.Gatta
D.Martin, G.Gatta
IDEA by P.Raimondi

## Slide 27: Simulated survey errors nominal positions (from ALGE group)
Simulated survey errors about the nominal position of the lattice.
Rotations are random, but for a 21urad systematic outward tilt.
Data provided in 320 points for the current lattice.
PREVIOUS
horizontal
Longitudinal (electrons path)
vertical
How GIRDER and LONG RANGE
tolerances were excluded
D.Martin, G.Gatta
D.Martin, G.Gatta
D.Martin, G.Gatta
DATA from ALIGNMENT GROUP

## Slide 28: Dynamic aperture and lifetime
The above curves are interpolated to set the errors in the S28A lattice.
-10mm (-8.1mm @S3)
Lifetime: 16.6h
range:[16.4 17.1]
26/07/2013
MEASURED SURVEY + simulated alignment errors
SET IN THE LATTICE
AND TESTED FOR DA/LIFETIME AFTER CORRECTION
TARGET
nominal
current
On the blue curve
How GIRDER and LONG RANGE
tolerances were excluded

## Slide 29: Additional Random errors
-10mm (-8.1mm @S3)
Lifetime goes from 16.6h to about 12h with many lost seeds and increasing range.
As above + RANDOM ERRORS SET IN THE LATTICE
AND TESTED FOR DA/LIFETIME AFTER CORRECTION
Increasing random errors
TARGET
Additional random errors are still required to describe the error on the position of the magnetic centers of the magnets.
How GIRDER and LONG RANGE
tolerances were excluded

## Slide 30: Dynamic aperture and lifetime
The above curves are interpolated to set the errors in the S28A lattice.
-10mm (-8.1mm @S3)
Lifetime: 16.7h
range:[16.6 17]
IDEAL SURVEY SET IN THE LATTICE
AND TESTED FOR DA/LIFETIME AFTER CORRECTION
TARGET
nominal
current
On the red curve
How GIRDER and LONG RANGE
tolerances were excluded

## Slide 31: Additional Random errors
-10mm (-8.1mm @S3)
Lifetime goes from 16.7h to about 13h with many lost seeds and increasing range.
IDEAL SURVEY + RANDOM ERRORS SET IN THE LATTICE
AND TESTED FOR DA/LIFETIME AFTER CORRECTION
TARGET
Increasing errors
Additional random errors are still required to describe the error on the position of the magnetic centers of the magnets.
How GIRDER and LONG RANGE
tolerances were excluded

## Slide 32
X-ray beam position at ID (60 meters) : decision to place the new SR where the old was.
All ID are assumed to be at 60m from the source.
The position of the beam after 60m is very similar for ESRF and S28A considering the current survey measurement.
The position if the ring was aligned on the reference circumference would be about (0,0) for al ID.
Current (simulated) position of the X-ray at the beamline
position of the X-ray at the beamline for S28A on the same survey
4TH APAC 2014
S28
ESRF
“on theory geom”.
Good choice. During commissioning (Jan2019): ALL beamlines but one could see the x-ray beam at the white beam viewers at very first Front End opening.

## Slide 33: In practice
We have no specific beam dynamics interest in the girder-girder tolerance themselves.
Those are not precisely defined among different groups and may lead to lack of understanding.
From beam dynamics, we can say that: large, slow, smooth, variations of position are not detrimental.
In order to model the lattice at the location where it will be installed, we included in all “predictive” (DA, LT, IE,etc) simulations the Simulated Survey Position provided by the alignment group.
From a beam dynamics point of view, as long as magnet-magnet tolerances (actually, single magnets rms position errors) are achieved at every location in the machine, including between magnets standing on neighboring girders, we will get the foreseen Dynamic Aperture and LIFETIME.
We let the alignment group decide how to achieve this requirement.
For ESRF-EBS It worked extremely well, largely exceeding expectations/simulations.
Expected magnet-to-magnet
60-70 mm
From steerers/orbit data
Achieved magnet-to-magnet
25-55 mm
rms DX DY
alignment
Conclusion

## Slide 34: Tolerable random errors
Required: | DX | DY | DS | DPSI | DK
 | mm | mm | mm | mrad | 10^-4
DL | >100 | >100 | 1000 | 500 | 10
DQ, QF[68] | 70 | 50 | 500 | 200 | 5
Q[DF][1-5] | 100 | 85 | 500 | 500 | 5
SFD | 70 | 50 | 500 | 1000 | 35
OF | 100 | 100 | 500 | 1000 | 
Sextupoles and high gradient quadrupoles are the most relevant limitations, nevertheless, this alignment specifications are currently achievable.
(DX=DY=60mm, 84 mm between two magnets).
GIRDERS
SAME AS worst case MAGNET-MAGNET
What girder-girder tolerances did you use?
Conclusion
60
Many simulations for 1 number needed
Long range
Survey simulations
How far can be two magnets on opposite sides of the ring?

## Slide 35: conclusions
The definition of alignment tolerance can be done in a quasi deterministic way, to give relative impact on final parameters of each source of errors. Finally this is NOT directly usefull for alignment. Unless some specification is really demanding, everything will be alignment to the minimum value found: one single number.
Running Girder-to-girder simulations is also not really useful. For compact machines girder-to-girder is the same as magnet-to-magnet. Using simulated Survey data is more realistic, simpler and efficient.
Large, slow, SR position variations are not an issue for beam dynamics. Magnet to magnet is what really counts.
For upgrade project using the measured positions of the SR and hypothetical positions after dismantling and reinstallation, shares well the contribution of alignment and magnet center fiducialization error sources. Simulations of the measured survey may be included in the model simply, sparing a lot of time and effort, and simplifying the communication among colleagues.

## Slide 36: BACKUP

## Slide 37: Comparable tolerance table
This table provides a deterministic way to compare error impact on lattices.
It is used also to asses the performances of correction schemes and correction algorithms
Further reduction of this data is needed to provide a tolerance table.
How tolerances were defined

## Slide 38: definition of a List of tolerable errors
Compare magnet groups for the same error
Compare error sources for the same magnet group
Tolerated errors
beta beating = 1%
Hor. Disp. = 1mm
How tolerances were defined

## Slide 39: error amplitude giving 30um orbit after correction vs wavelength
Amplitude is X, Y and rotation about s (rad) simultaneously

## Slide 40: Estimated Alignment is better then expected/required from tolerances !
After optics corrections: Db/bH,V = 1.5 ± 1 % ,
DhH,V = 1.0 ± 0.1 mm
From simulations the estimated SR alignment errors are:
H 30-45 mm, V 20-55 mm
Today: 0.2 % std(quad gradients),
~ 65mrad, ~30mrad, std(H V steerers)
Simulations: 0.26 % std(quad gradients),
~160mrad, ~120mrad, std(H V steerers)
Correction strengths in the SR:
IPAC 2021

## Slide 41: Girder to girder: an historical exchange after >2 years of PhD simulations
Dear Alignment group colleagues,
we would like the girders to have an alignment error of
78.656 mm rms in the X plane
73.421 mm rms in the Y plane
Thank you
Best regards
Beam Dynamics
Dear Beam Dynamics colleagues,
What do you mean?
2 girders one at the injection and one on the opposite side of the SR should be aligned within 75 mm?
We think it would be better to meet and discuss.
Could you give us the tolerated alignment envelope over 10cm, 1m, 10m, 100m, 1km?
By the way, X for us is the longitudinal direction.
Thank you
Best regards
Alignment
Dear Alignment colleagues,
Indeed, we would appreciate a meeting on the topic.
Best regards
Beam Dynamics
In purpose missing “Thank you”
Lesson learnt:
TALK with YOUR COLLEAGUES BEFORE RUNNING YEARS OF SIMULATIONS

## Slide 42: Girder to girder: an historical exchange after >1month of simulations
Dear Alignment group colleagues,
we would like the girders to have an alignment error in the transverse plane with
L/1-L/8 wavelengths and up to 2mm amplitude on a closed trajectory.
Thank you
Best regards
Beam Dynamics
Dear Beam Dynamics colleagues,
What do you mean?
What do you mean by “wavelength”?
We think it would be better to meet and discuss.
Could you give us the tolerated girder-to-girder alignment envelope over 10cm, 1m, 10m, 100m, 1km?
What about the longitudinal direction, X?
Thank you
Best regards
Alignment
Dear Alignment colleagues,
Indeed, we would appreciate a meeting on the topic.
Beam Dynamics
In purpose missing “Thank you”
In purpose missing “best regards”
Lesson learnt:
TALK again with YOUR COLLEAGUES BEFORE RUNNING YEARS OF SIMULATIONS

## Slide 43: Girder to girder: an historical exchange after >1month of simulations
Dear Alignment group colleagues,
Thanks to the simulated SR positions you provided we can say that the SR may be aligned on the theoretical survey or on a smooth line interpolating the existing measured positions, without detriment on the final beam performances.
Thank you
Best regards
Beam Dynamics
Dear Beam Dynamics colleagues,
That is great news!
Thank you
Best regards
Alignment
Lesson learnt:
speak the same language or
find an interpret or
first think and discuss what would be the easiest for everyone.
Notice the disappearance of the word “girder” from the conversation.