MD10724
BFPP Quench Test
P. Hermes, A. Abramov, G. Broggi, R. Bruce, M. D’Andrea,
M. Jebramcik, J. Jowett,
A. Lechner, C. Maccani, S. Morales Vigo, C. E. Montanari, T. Persson,
S. Redaelli, B. Salvachua,
J. Uythoven, D. Wollmann
LSWG Meeting on Heavy-ion MDs
21.11.2023

---
MD Overview
Time Slot Assigned 30-10-2023 00:00 - 30-10-2023 06:00
Very efficient injection
“Success-oriented” planning materialized
Everything went according to plan

---
MD Overview
208Pb81+
208Pb81+
Ultraperipheral collisions → pair production
208Pb82+ + 208Pb82+ + e- + e+ → 208Pb81+ + 208Pb82+

---
Overview
Idea: use secondary BFPP beam to probe quench limit of dipoles
Change orbit bump to steer BFPP beam into magnet
Configuration validated with LM and asynch. dump beforehand
Increase luminosity in steps
Identify luminosity at which magnet quench occurs
Very well defined power deposition
Initially planned 11R1 – discovered non-conformity: switched to 11L1

---
MD Overview
MB.B11L1
Steered losses here for quench test
Empty cryostat: BFPP loss location in operation

---
BLM Signal
MB.B11L1
Empty cryostat
Nominal

---
BLM Signal
MB.B11L1
Empty cryostat
Bump +6mm
(Prepared beforehand)

---
Procedure
BLM thresholds changed beforehand
QPS crates reset before fill
Injection of 960 bunches per beam
Ramp, Squeeze
Establish collisions at low luminosity
Trim new orbit bump to steer BFPP into MB.B11L1

---
Procedure
Increased ATLAS luminosity in ten steps
0.2 × 1027 cm-2 to 2.0 × 1027 cm-2 (quench)
Curious Facts
FASER was able to see the test (see next slide)

---
Slide: Courtesy of J. Boyd

---
Conclusions
Test very smooth and successful (excellent preparation by all experts)
Quench achieved: next step power deposition simulations