## Slide 2: Particle Detectors
History of Instrumentation ↔ History of Particle Physics
The ‘Real’ World of Particles
Interaction of Particles with Matter
Tracking Detectors, Calorimeters, Particle Identification
Detector Systems
Summer Student Lectures 2024
Werner Riegler, CERN, werner.riegler@cern.ch

## Slide 3
Detectors based on Ionization
Gas detectors:
  Wire Chambers
  Drift Chambers
  Time Projection Chambers
  Transport of Electrons and Ions in Gases
Solid State Detectors
  Transport of Electrons and Holes in Solids
  Si- Detectors
  Diamond Detectors

## Slide 4
Gas Detectors
In gaseous detectors, a charged particle is liberating electrons from the atoms, which are freely bouncing between the gas atoms.
An applied electric field makes the electrons and ions move,
which induces signals on the metal readout electrodes.
For individual gas atoms, the electron energy levels are discrete.
Solid State Detectors
In solids (crystals), the electron energy levels are in ‘bands’.
Inner shell electrons, in the lower energy bands, are closely bound to the individual atoms and always stay with ‘their’ atoms.
In a crystal there are however energy bands that are still bound states of the crystal, but they belong to the entire crystal. Electrons in these bands and the holes in the lower band can freely move around the crystal, if an electric field is applied.
Solid State Detectors

## Slide 5
Solid State Detectors
Free Electron Energy
Unfilled Bands
Conduction Band
Band Gap
Valance Band
Conductor, Insulator, Semiconductor
In case the conduction band is filled the crystal is a conductor.
In case the conduction band is empty and ‘far away’ from
the valence band, the crystal is an insulator.
In case the conduction band is empty but the distance to the valence band is small, the crystal is a semiconductor.

## Slide 6
Band Gap, e-h pair Energy
The energy gap between the last filled band – the valence band – and the conduction band is called band gap Eg.
The band gap of Diamond/Silicon/Germanium is 5.5, 1.12, 0.66 eV.
The average energy to produce an electron/hole pair for Diamond/Silicon/Germanium is 13, 3.6, 2.9eV.
Temperature, Charged Particle Detection
In case an electron in the valence band gains energy by some process, it can be excited into the conduction band and a hole in the valence band is left behind.
Such a process can be the passage of a charged particle, but also thermal excitation  probability is proportional Exp(-Eg/kT).
The number of electrons in the conduction band is therefore increasing with temperature i.e. the conductivity of a semiconductor increases with temperature.
Solid State Detectors
Band Gap

## Slide 7
Electron, Hole Movement:
It is possible to treat electrons in the conduction band and holes in the valence band similar to free particles, but with an effective mass different from elementary electrons not embedded in the lattice.
This mass is furthermore dependent on other parameters such as the direction of movement with respect to the crystal axis. All this follows from the QM treatment of the crystal (solid state physics).
Cooling:
If we want to use a semiconductor as a detector for charged particles, the number of charge carriers in the conduction band due to thermal excitation must be smaller than the number of charge carriers in the conduction band produced by the passage of a charged particle.
Diamond (Eg=5.5eV) can be used for particle
detection at room temperature,
Silicon (Eg=1.12 eV) and Germanium (Eg=0.66eV)
must be cooled, or the free charge carriers
must be eliminated by other tricks  doping  see later.
Solid State Detectors

## Slide 8
Primary ‘ionization’:
The average energy to produce an electron/hole pair is: Diamond (13eV), Silicon (3.6eV), Germanium (2.9eV)
Comparing to gas detectors, the density of a solid is about a factor 1000 larger than that of a gas and the energy to produce and electron/hole pair e.g. for Si is a factor 7 smaller than the energy to produce an electron-ion pair in Argon.
Solid State vs. Gas Detector:
The number of primary charges in a Si detector is therefore about 104 times larger than the one in gas  while gas detectors need internal charge amplification, solid state detectors don’t need internal amplification.
While in gaseous detectors, the velocity of electrons and ions differs by a factor 1000, the velocity of electrons and holes in many semiconductor detectors is quite similar  very short signals.
Solid State Detectors
Diamond  A solid state ionization chamber

## Slide 9
Diamond Detector
Velocity:
μe=1800 cm2/Vs, μh=1600 cm2/Vs
Velocity = μE, 10kV/cm  v=180 μm/ns  Very fast signals of only a few ns length !
Typical thickness – a few 100μm.
<1000 charge carriers/cm3 at room temperature due to large band gap.
I1
I2
q,vh
-q, ve
z
Z=D
Z=0
Z=z0
E
I1(t)
T=2-3ns
A single e/h par produced in the center

## Slide 10
Diamond Detector
I1
I2
q,vh
-q, ve
Z=D
Z=0
E
I1(t)
T=2-3ns
I1(t)
T=2-3ns
However, charges are trapped along the track, only about 50% of produced primary charge is induced 

## Slide 11
Silicon Detector
Velocity:
μe=1450 cm2/Vs, μh=505 cm2/Vs, 3.63eV per e-h pair.
~33000 e/h pairs in 300μm of silicon.
However: Free charge carriers in Si:
T=300 K: e,h = 1.45 x 1010 / cm3 but only 33000 e/h pairs in 300m produced by a high energy particle.
Why can we use Si as a solid state detector ???

## Slide 12
doping
p
n
Doping of Silicon
In a silicon crystal at a given temperature the number of electrons in the conduction band is equal to the number of holes in the valence band.
Doping Silicon with Arsen (+5) it becomes and n-type conductor (more electrons than holes).
Doping Silicon with Boron (+3) it becomes a p-type conductor (more holes than electrons).
Bringing p and n in contact makes a diode.

## Slide 13
At the p-n junction the charges are depleted and a zone free of charge carriers is established.
By applying a voltage, the depletion zone can be extended to the entire diode  highly insulating layer.
An ionizing particle produces free charge carriers in the diode, which drift in the electric field and induce an electrical signal on the metal electrodes.
As silicon is the most commonly used material in the electronics industry, it has one big advantage with respect to other materials, namely highly developed technology.
Si-Diode used as a Particle Detector !

## Slide 14
Zone without free charge carriers positively charged.
Sensitive Detector Volume.
Under-Depleted Silicon Detector
n
p
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
+
-
Zone with free electrons. Conductive.
Insensitive to particles.
Electric Field

## Slide 15
Zone without free charge carriers positively charged.
Sensitive Detector Volume.
Fully-Depleted Silicon Detector
n
p
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
+
-
Electric Field
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+

## Slide 16
Zone without free charge carriers positively charged.
Sensitive Detector Volume.
Over-Depleted Silicon Detector
n
p
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
+
-
Electric Field
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
In contrast to the (un-doped) diamond detector where the bulk is neutral and the electric field is therefore constant, the sensitive volume of a doped silicon detector is charged (space charge region) and the field is therefore changing along the detector.
 Velocity of electrons and holes is not constant along the detector.

## Slide 17
300mm
SiO2
passivation
readout capacitances
ca. 50-150 mm
Silicon Detector
Fully depleted zone
N (e-h) = 11 000/100μm
Position Resolution down to ~ 5μm !

## Slide 18
Silicon Detector
Every electrode is connected to an amplifier 
Highly integrated readout electronics.
Two dimensional readout is possible.
CMS Outer Barrel Module

## Slide 20
CMS Tracker

## Slide 21
Pixel-Detectors
Problem:
2-dimensional readout of strip detectors results in ‘Ghost Tracks’ at high particle multiplicities i.e. many particles at the same time.
Solution:
Si detectors with 2 dimensional ‘chessboard’ readout. Typical size 50 x 200 μm.
Problem:
Coupling of readout electronics to the detector
Solution:
Bump bonding for correcting a sensor to the readout electronics chip
Monolithic silicon sensors that incorporate the sensor and the electronics inside one substrate

## Slide 22
ATLAS: 108 pixels
ALICE: 1010 pixels
Pixel-Detectors
Bump bonding of pixels to readout electronics.
‘Hybrid Pixel Detectors’
Sensitive element and electronics on the same silicon wafer produced with ‘standard’ electronics fabrication process. ‘Monolithic Pixel Detectors’

## Slide 23
Radiation Effects ‘Aging’
Increase in leakage current
Increase in depletion voltage
Decrease in charge collection efficiency due to under-depletion and charge trapping.

## Slide 24
Summary on Solid State Detectors
Solid state detectors provide very high precision tracking in particle physics experiments (down to 5um) for vertex measurement but also for momentum spectroscopy over large areas (CMS, ATLAS+CMS Phase-II).
Technology is improving rapidly due to rapid Silicon development for electronics industry.
Typical numbers where detectors start to strongly degrade are 1015-1016 hadron/cm2.
‘Clearly, monolithic solid state detectors are an ultimate goal.

## Slide 25
Calorimetry

## Slide 26
Bremsstrahlung + Pair Production  EM Shower

## Slide 27
Electro-Magnetic Shower of High Energy Electrons and Photons

## Slide 28
Calorimetry: Energy Measurement by total Absorption of Particles
Only Electrons and High Energy Photons show EM cascades at current GeV-TeV level Energies.
Strongly interacting particles like Pions, Kaons, produce hadonic showers in a similar fashion to the EM cascade
Hadronic calorimetry
Momentum Spectrometer: Δp/p α p
Calorimeter: Δ E/E α 1/ √ E
Energy measurement improves with higher particle energies – LHC !

## Slide 29
Liquid Nobel Gases
(Nobel Liquids)
Scintillating Crystals,
Plastic Scintillators
Calorimetry: Energy Measurement by total Absorption of Particles

## Slide 30
Calorimetry
Calorimeters can be classified into:
Electromagnetic Calorimeters,
to measure electrons and photons through their EM interactions.
Hadron Calorimeters,
Used to measure hadrons through their strong and EM interactions.
The construction can be classified into:
Homogeneous Calorimeters,
that are built of only one type of material that performs both tasks, energy degradation and signal generation.
Sampling Calorimeters,
that consist of alternating layers of an absorber, a dense material used to degrade the energy of the incident particle, and an active medium that provides the detectable signal.
C.W. Fabjan and F. Gianotti, Rev. Mod. Phys., Vol. 75, N0. 4, October 2003

## Slide 31
Calorimetry
Calorimeters are attractive in our field for various reasons:
In contrast with magnet spectrometers, in which the momentum resolution deteriorates linearly with the particle momentum, on most cases the calorimeter energy resolution improves as 1/√E, where E is the energy of the incident particle. Therefore calorimeters are very well suited for high-energy physics experiments.
In contrast to magnet spectrometers, calorimeters are sensitive to all types of particles, charged and neutral. They can even provide indirect detection of neutrinos and their energy through a measurement of the event missing energy.
Calorimeters are commonly used for trigger purposes since they can provide fast signals that are easy to process and interpret.
They are space and therefore cost effective. Because the shower length increases only logarithmically with energy, the detector thickness needs to increase only logarithmically with the energy of the particles. In contrast for a fixed momentum resolution, the bending power BL2 of a magnetic spectrometer must increase linearly with the particle momentum.
C.W. Fabjan and F. Gianotti, Rev. Mod. Phys., Vol. 75, N0. 4, October 2003

## Slide 32
EM Calorimetry
Approximate longitudinal shower development Approximate transverse shower development
Radiation Length X0 and Moliere Radius are two key parameters for choice of calorimeter materials

## Slide 33
Crystals for Homogeneous EM Calorimetry
In crystals the light emission is related to the crystal structure of the material. Incident charged particles create electron-hole pairs and photons are emitted when electrons return to the valence band.
The incident electron or photon is completely absorbed and the produced amount of light, which is reflected through the transparent crystal, is measured by photomultipliers or solid state photon detectors.

## Slide 34
Crystals for Homogeneous EM Calorimetry
CMS@LHC, 25ns bunch crossing,
high radiation dose
L3@LEP, 25us bunch crossing,
Low radiation dose
Barbar@PEPII,
10ms interaction rate, good light yield, good S/N
KTeV@Tevatron,
High rate,
Good resolution

## Slide 35
Crystals for Homogeneous EM Calorimetry

## Slide 36
When a charge particle traverses these materials, about half the lost energy is converted into ionization and half into scintillation.
The best energy resolution would obviously be obtained by collecting both the charge and light signal. This is however rarely done because of the technical difficulties to extract light and charge in the same instrument.
Krypton is preferred in homogeneous detectors due to small radiation length and therefore compact detectors. Liquid Argon is frequently used due to low cost and high purity in sampling calorimeters.
Noble Liquids for Homogeneous EM Calorimetry

## Slide 37
Noble Liquids for Homogeneous EM Calorimetry
I1
I2
q,ve
-q, vI
Z=D
Z=0
E
I1(t)
T~1μs
E.g. Liquid Argon, 5mm/ μs at 1kV/cm, 5mm gap  1 μs for all electrons to reach the electrode.
The ion velocity is 103 to 105 times smaller  doesn’t contribute to the signal for electronics of μs integration time.

## Slide 38
Homogeneous EM Calorimeters, Examples
1%
0.8%
0.6%
1%
0.8%
0.6%
NA48 Experiment at CERN and KTeV Experiment at Fermilab, both built for measurement of direct CP violation. Homogenous calorimeters with Liquid Krypton (NA48) and CsI (KTeV). Excellent and very similar resolution.
NA48/62 Liquid Krypton
2cmx2cm cells
X0 = 4.7cm
125cm length (27X0)
ρ = 5.5cm
KTeV CsI
5cmx5cm and
X0 = 1.85cm
2.5cmx2.5cm crystals
50cm length (27X0)
ρ = 3.5cm

## Slide 39
Sampling Calorimeters
Energy resolution of sampling calorimeters is in general worse than that of homogeneous calorimeters, owing to the sampling fluctuations – the fluctuation of ratio of energy deposited in the active and passive material.
The resolution is typically in the range 5-20%/Sqrt[E(GeV)] for EM calorimeters. On the other hand they are relatively easy to segment longitudinally and laterally and therefore they usually offer better space resolution and particle identification than homogeneous calorimeters.
The active medium can be scintillators (organic), solid state detectors, gas detectors or liquids.
Sampling Fraction = Energy deposited in Active/Energy deposited in passive material.

## Slide 40
EM Calorimetry  Hadron Calorimetry
Similar process for Hadrons.
The equivalent to EM Bremsstrahlung is Pion radiation.
The equivalent to the radiation length is the nuclear interaction length.

## Slide 41
Hadronic Calorimetry

## Slide 42
Hadron Calorimeters are Large because λ is large
Hadron Calorimeters are large and heavy because the hadronic interaction length λ, the ‘strong interaction equivalent’ to the EM radiation length X0, is large (5-10 times larger than X0)
Because part of the energy is ‘invisible’ (nuclear excitation, slow nucleons), the resolution of hadron calorimeters is typically worse than in EM calorimeters 20-100%/√E(GeV).

## Slide 43
A few Reasons why you want to become an Experimental Particle Physicist
The Standard Model of Particles Physics, a theory that was established in the early 1970ies, is in excellent agreement with experiments. Experiments at LEP/Tevatron/LHC/KEK etc. verified the theory to impressive precision.
The Higgs Particle, a necessary element of the standard model, was found at the LHC.
Although the standard model is perfectly fitting the experiments, we know/think that it cannot be the final answer:
CP violation and the other CKM matrix elements are put into the model explicitly and they are not derived from a theory.
The Matter- Antimatter asymmetry in the Universe cannot be explained by the level of standard model CP violation.
The masses of the particles are unexplained.
We do not know what dark matter is.
The cosmological constant predicted by the standard model differs by many orders of magnitude from the observed one.
The Higgs mass renormalization requires fine tuning etc. etc.

## Slide 44
Substantial theory efforts did not really advance on these questions and did not touch base with experiment.
It is very difficult to find out what is wrong with the theory if all experimental results are in agreement with the theory.
The next step in advancing our knowledge will most likely come from experiment. Maybe LHC or some telescope, or some astrophysics experiment or some other future accelerator …
We have to invent new technologies for future accelerators and experiments !
A few Reasons why you want to become an Experimental Particle Physicist

## Slide 45
1.5V
+
_
e-
You
have to develop the tricks and technologies to advance on the most fundamental questions in Physics !
x 1013  LHC

## Slide 47
Detector Systems

## Slide 48
CMS Detector

## Slide 49
ALICE

## Slide 50
0 1 2 3 4 5 p (GeV/c)
1 10 100 p (GeV/c)
TPC (rel. rise) p /K/p
TRD e /p
PHOS g /p0
TPC + ITS
(dE/dx)
p/K
p/K
p/K
K/p
K/p
K/p
e /p
e /p
HMPID
(RICH)
TOF
Alice uses ~ all
known techniques!
p/K
K/p
ALICE Particle ID

## Slide 51
800 tons of mineral oil
1280 photomultipliers
MiniBooNE detector, Neutrinos

## Slide 52
Super-Kamiokande, Neutrinos

## Slide 53
20 tons of liquid scintillator
Daya Bay, Neutrinos

## Slide 54
NEXT experiment, double β decay

## Slide 55
CERN Neutrino Gran Sasso
(CNGS)

## Slide 56
ne
nt
nm
If neutrinos have mass:
CNGS
Muon neutrinos produced at CERN.
See if tau neutrinos arrive in Italy.

## Slide 57: CNGS Project
CNGS (CERN Neutrino Gran Sasso)
  A long base-line neutrino beam facility (732km)
  send nm beam produced at CERN
  detect nt appearance in OPERA experiment at Gran Sasso
 direct proof of nm - nt oscillation (appearance experiment)

## Slide 58
CNGS

## Slide 59
CNGS

## Slide 60
CNGS

## Slide 61
E. Gschwendtner, CERN
typical size of a detector at Gran Sasso
Flat top: 500m
FWHM: 2800m
Radial Distribution of the nm-Beam at GS
5 years CNGS operation, 1800 tons target:
30000 neutrino interactions
~150 nt interactions
~15 nt identified
< 1 event of background

## Slide 62: Neutrinos at CNGS: Some Numbers
For 1 year of CNGS operation, we expect:
protons on target 2 x 1019
pions / kaons at entrance to decay tunnel 3 x 1019
nm in direction of Gran Sasso 1019
nm in 100 m2 at Gran Sasso 3 x 1014
nm events per day in OPERA  2500
nt events (from oscillation)  2

## Slide 63
Lead plates: massive target
Emulsions: micrometric precision
10.2 x 12.7 x 7.5 cm3
8.3kg
brick
Brick
Pb
Couche de gélatine photographique 40 mm
n
t
1 mm
Basic unit: brick
56 Pb sheets + 56 photographic films (emulsion sheets)
Opera Experiment at Gran Sasso

## Slide 64
31 target planes / supermodule

Targets
Magnetic Spectrometers
First observation of CNGS beam neutrinos : August 18th, 2006
SM1
SM2
In total: 206336 bricks, 1766 tons
Opera Experiment at Gran Sasso
Notes: Lead makes target mass, emulsions allows to see tracks!
Walls are made of bricks, bricks are made of sandwiches, sandwiches are made of lead and emulsion sheets. (type of photographic film)

## Slide 65
Scintillator planes 5900 m2
8064 7m long drift tubes
Second Super-module
3050 m2 Resistive Plate Counters
2000 tons of iron for the two magnets
Details of the first spectrometer
Opera Experiment at Gran Sasso
Notes: 2 photos of OPERA, so we see, experiment exists!

## Slide 66
Opera Experiment at Gran Sasso

## Slide 67
First Tau Candidate !

## Slide 68: AMS
Alpha Magnetic Spectrometer
Try to find Antimatter in the primary cosmic rays.
Study cosmic ray composition etc. etc.

## Slide 69: AMS
Installed on the space station.

## Slide 70
AMS

## Slide 71
AMS