## Slide 1: Future High-Energy Collider Projects
Part 1
Roderik Bruce

## Slide 2: Introductory remarks
This lecture is based on a collection of materials from many colleagues that I would like to acknowledge:
  W. Bartmann, M. Benedict, M. Boscolo, H. Burkhardt, R. Corsini, B. Dalena, O. Etisken, F. Gianotti, M. Giovannozzi, B. Harer, B. Holzer, J. Jowett, R. Kersevan, A. Lechner, M. Lamont, J. Pfingstner, T. Pieloni, M. Rakic, S. Redaelli, D. Schulte, L. Rossi, R. Ruber, M. Schaumann, J. Wenninger, F. Zimmermann
  In particular, a lot of material comes from D. Schulte – thanks! – who in turn used material from S. Stapnes, L. Rossi, Ralph Assmann, J-P. Delahaye, L. Linssen, S. Doebert, A. Grudiev, F. Tecker, W. Wuensch, S. Poss, J. Strube, J. Wenninger, M. Benedikt, F. Zimmermann, B. Holzer, R. Kersevan, Ph. Lebrun
  This is an accelerator lecture. For particle physics, e.g., physics goals etc., please see physics lectures
  I will use concepts introduced in other lectures:
    Foteini Asvesta: Accelerators and Beam Dynamics
    Susana Izquierdo Bermudez: Magnet Superconductivity
  Focus on machines studied at CERN

## Slide 3: Outline
Introduction
  Considerations for collider design: particle type, energy, circular/linear…
  Limitations for future colliders
  European strategy for particle physics
ILC (International Linear Collider)
CLIC (Compact Linear Collider)
HL-LHC (High-Luminosity Large Hadron Collider)
FCC-hh (Future Circular collider, hadrons)
FCC-ee (Future Circular collider, e+e-)
CEPC/SppC (Chinese Electron-Positron Collider / Super proton-proton Collider)
Muon collider
First lecture
Second lecture
Linear
Circular

## Slide 4: Particle colliders
Particle colliders have been instrumental for scientific discoveries in high energy physics for more than half a century
  Key for establishing the standard model in particle physics
Technological innovation made it possible to increase energy at a much faster pace than the costs
LHC has the highest energy among colliders built so far
  Circular collider, designed to collide 7 TeV protons and heavy ions
“Livingstone plot” of collider energy vs time (source)

## Slide 5: LHC timeline
Present LHC will operate for a few more years
High-Luminosity LHC (HL-LHC) upgrades foreseen for next long shutdown
HL-LHC planned to operate into early 2040’s
What happens next?
  Nobody knows, but there are many ideas on the table
It took ~25 years to design and build the LHC, so need to start thinking now about future options
Tentative schedule, could well change (source https://edms.cern.ch/document/2311633/4.0 )
Run 3
Run 3
Run 4
Run 4
Run 5
Run 6
HL-LHC installation
Run 5
Run 6

## Slide 6
3 main complementary ways to search for (and study) new physics at accelerators
e.g.: Higgs production at future e+e- linear/circular colliders
at √s ~ 250 GeV through the HZ process
 need high E and high L
look for (tiny) deviations from SM expectation from quantum effects (loops, virtual particles)
sensitivities to E-scales Λ>> √s  need high E and high L
production of a given (new or known) particle
Direct
E.g. K+  π+νν decay (NA62 experiment)
Proceeds via loops  suppressed in the SM : BR~ 10-10
Can be enhanced by new particles running in the loop.
Theoretically very clean.
Rare processes
suppressed in SM  could be enhanced by New Physics
Indirect
precise measurements of known processes
X*
 -
 +
E.g. top mass predicted by LEP1 and SLC in 1993:
mtop = 177  10 GeV; first direct evidence
at Tevatron in 1994: mtop = 174  16 GeV
√s ~ 90 GeV
e.g. neutrino interactions, rare decay modes  need intense beams and/or ultra-sensitive (massive)
detectors (“intensity frontier”)
Slide from
F. Gianotti
Main focus

## Slide 7: Considerations for new colliders
So, we want high energy and high luminosity
  When we say high luminosity, we implicitly mean high event rate
  Reminder: The luminosity directly determines the event rate
How do we get there? Several choices to be made:
  What to collide: lepton vs hadron
  How to collide:
    fixed target or colliding beams
    linear vs circular collider
  Acceleration technology
    DC, RF, wakefield…
  Magnet technology
    Superconducting (what conductor?), normal conducting
  Acceptable cost of construction, power consumption, site
Think about various limitations to energy and luminosity and how to overcome them
Event rate
Luminosity
(determined by
and collider design:
can be influenced)
Cross section
(given by physics,
cannot be
influenced)
Higgs cross section:
(Centre-of-mass energy)
Notes: Cross section for hadronic Higgs production is order of pico barn
LHC total integrated lumi : Run1 28/fb, Run2 160/fb, Run 3 (2022 39/fb, 2023 32/fb July 2024 45/fb) => Total 304/fb
Total number of Higgs produced ~3E5

## Slide 8: Leptons vs hadrons
Hadrons (protons or ions)
Mix of quarks, anti-quarks and gluons:
  variety of processes
  not all nucleon energy available in collision
  Energy spread between partons – spread in collision energy
  huge QCD background
Can typically achieve highest collision energy
Good for discoveries at the frontier of new physics
p
p
LEP II e+e- collision, DELPHI
LHC Pb-Pb collision, CMS
Leptons (electrons, positrons, maybe muons)
Elementary particles colliding - very well defined centre-of-mass energy
Low background
Good for high-precision measurements
Higher energy loss from synchrotron radiation influences accelerator design  see next slides
e+
e-

## Slide 9: Synchrotron radiation
Classical electrodynamics: an accelerating charge radiates
  Radiation carries off energy, which is taken away from the kinetic energy
  Radiated energy needs to be replenished by accelerating RF cavities => could lead to very high power consumption
  Radiated photons impact on vacuum chamber => causes heating, maybe even damage for high power loads
For a relativistic charged particle, radiation is forward – it sweeps around like a locomotive's headlight as the particle moves
Imposes limitations on
collider design
Notes: Griffiths p11:16 p481 pdf,
Jackson p688 eq 14.13-14.14

## Slide 10: Radiated power
For full derivation, see e.g. Jackson, Classical electrodynamics, chapter 14
Very short summary
  Write down electric and magnetic fields of moving point charge (at relativistic speed)
  Power radiated is given by integral of Poynting vector over closed surface around charge, let R∞ (only 1/R terms in fields contribute)
  Integrate …. don’t be in a hurry
Result:
  Energy loss is negligible for longitudinal acceleration, except for extreme (unphysical) gradients
  For transverse acceleration (as in circular colliders), energy loss could be significant - 4th power dependence on energy and mass
  Effect is much more limiting for light particles, such as electrons/positrons
    Electrons are 2000 times lighter than protons!
… meaning…
force
force
Longitudinal
acceleration
Transverse
acceleration
Energy loss per turn from radiation

## Slide 11: Radiation damping
Emitted photons along betatron trajectory – particle loses both longitudinal and transverse momentum
Energy losses compensated by RF, giving purely longitudinal momentum kick
Increases longitudinal momentum and not transverse => decrease in angle
  Smaller betatron amplitudes => smaller emittance, “radiation damping”
  Remember: emittance determines phase space area occupied by beam
On the other hand: photon emission gives small random energy (and very small angle) change => blowup, “quantum excitation”
Equilibrium between radiation damping and quantum excitation exists: equilibrium emittance
  Time needed for the beam to reach the equilibrium emittance: “Damping time”
  Equilibrium emittance is typically smaller in vertical than horizontal plane => “flat” lepton beams
M. Sands, SLAC-121 UC-28

## Slide 12: Collider vs fixed target experiments
To achieve the highest possible centre-of-mass energy, need a collider
Fixed Target
Collider

## Slide 13: Circular vs linear collider
source
main linac
N
S
N
S
accelerating cavities
Circular Collider
multi-pass => Accelerate beam in many turns, let beam collide many times
many magnets, few accelerating cavities
Bending of beam trajectory => synchrotron radiation losses important for light particles
Linear Collider
single pass => need to be very efficient
few magnets, many accelerating cavities
Not limited by synchrotron radiation – promising choice for reaching highest lepton energies

## Slide 14: Increasing beam energy
Hadron beams: energy limited by ability of to keep particle on circular orbit
  Maximum achievable dipole field (superconductor technology)
  Radius of ring (cost, site)
Lepton beams: radiation losses
  RF power consumption
  Disposal of radiated power
  Radius of ring (cost, site)
Circular Collider
Linear Collider
(see lecture F. Asvesta)
Energy depends on
  Accelerating gradient (RF technology)
    Plasma wakefield acceleration promises large advancement, but not yet mature to produce required beam quality
  Length (cost, site)
To push energy boundary: improve technology (B-fields, RF gradient) or build a larger machine
For protons:
Ecm ≈ Llinac Gacc
Notes: 9 gev lost per turn in FCC-ee 182.5 GeV

## Slide 15: Increasing luminosity
Increase F: shorter bunches, smaller crossing angle
Smaller β*
Smaller normalized emittance
Smaller beam size
Higher intensity
Increase number of bunches
Increase bunch intensity
Reminder: luminosity depends on beams and optics (see lecture F. Asvesta)
Expression for round beams:
In addition:
Potential limitations on luminosity from losses and showers from the collisions
Elliptic beams:

## Slide 16: Some limitations on intensity and beam size
Intensity
  Limitations in beam production scheme
  Collective effects and instabilities, e.g. space charge, impedance effects, electron cloud, beam-beam effects (detrimental non-linear electromagnetic field acting on opposing beam)
  In circular lepton machines, limitations on RF power (compensate synchrotron radiation losses)
  Detrimental effects of beam losses
Beam size
  β* (β-function around collision point) limited by magnet focusing strength and aperture in final focus quadrupoles
  Emittance: limitations in beam production, larger risk for instabilities, blowup (intra-beam scattering); not easy to reduce emittance of existing beam, need dedicated cooling
    Lepton machines: equilibrium emittance determined by accelerator lattice
    Can use damping rings to shrink emittance
  Beam-beam effects
β-function around collision point:
(not exhaustive list)
Long-range
Head-on

## Slide 17: Geometric reduction factor
Bunches typically collide with an angle, ”crossing angle” – otherwise we get unwanted collisions outside interaction point if they arrive closely in time
  Crossing angle need to be large enough so that bunches are not perturbed by electromagnetic field at parasitic encounters (long-range beam-beam effect)
Fewer collisions when overlap is not perfect – geometric reduction factor
  Depends on crossing angle, bunch length, and transverse size
Long-range
Head-on

## Slide 18: Considerations for future collider choices
Physics potential
The collider energy
The collider luminosity
Particle type
Feasibility
The technical maturity
The risk
The schedule
Affordability
The collider cost
The collider power consumption
Availability of site
D. Schulte

## Slide 19: European strategy for particle physics
Common strategy worked out in Europe to guide future decision-making in field: “European strategy for particle physics”
  endorsed by the CERN council
Based on bottom-up approach:
physics community is invited to submit proposals for near-term, mid-term and longer-term projects  community discussion in open symposium, Physics briefing book
  Based on this input, the European Strategy Group formulates the strategy
    consists of scientific delegates from CERN Member States, Associate Member States, directors of major European laboratories, representatives of various European organizations, some invitees from outside the European Community
Initiated in 2006, updated in 2013 and 2020, next update foreseen around 2027
  2020 update: Key takeaway messages

## Slide 20: Some recommendations in European strategy
Some points relevant to future high-energy colliders - see full document here
[about LHC] “The successful completion of the high-luminosity upgrade …. should remain the focal point of European particle physics, together with continued innovation in experimental techniques. The full physics potential of the LHC and the HL-LHC …. should be exploited. “
“An electron-positron Higgs factory is the highest-priority next collider”
“Europe, together with its international partners, should investigate the technical and financial feasibility of a future hadron collider at CERN with a centre-of-mass energy of at least 100 TeV and with an electron-positron Higgs and electroweak factory as a possible first stage. “
“The particle physics community should ramp up its R&D effort focused on advanced accelerator technologies, in particular that for high-field superconducting magnets, including high-temperature superconductors”
Notes: Summary from DG presentation to personnel, sept 2020

## Slide 21: High-energy colliders studied at CERN
HL-LHC: luminosity upgrade of the LHC.
  Approved and financed - production and installation of upgrades already in full swing
  pp collisions with 14 TeV energy in centre-of-mass system (CMS) and heavy ions as in LHC, 27 km ring
Future Circular Collider (FCC) in different stages
  Conceptual design report released
  Circular e+e- collider in ~100 km tunnel, up to 365 GeV CMS: FCC-ee
  Re-use tunnel for 100 km hadron collider, ~100 TeV pp CMS: FCC-hh
  2-step approach inspired by successful LEP – LHC programs at CERN
Compact Linear Collider (CLIC)
  Linear e+e- collider, conceptual design report released
  Up to ~50 km and 3 TeV CMS energy
Other projects that are being studied
  Muon collider
  LHeC (hadron-electron collisions at the LHC)
LHC
FCC
CLIC

## Slide 22: Initiatives in the rest of the world
International Linear Collider (ILC)
  Linear e+e- collider, technical design report released – mature design
  up to 500 GeV CMS, 31 km
  Potentially hosted by Japan – waiting for political decisions
Chinese initiative for circular collider
  First: e+e- collider (CEPC), up to 240 GeV CMS energy, 100 km ring
  followed by a 100 km hadron collider (SppC), 75 TeV CMS energy (proposals for extensions to ~150 TeV)
Electron-Ion Collider (EIC) to be built at Brookhaven, US
  Circular, up to 140 GeV CMS energy, ~3.4 km
  Range of ions: p-U
  Use existing RHIC with some upgrades for ions
  New electron storage ring and injector
  Project approved, announced timeline to completion of ~10-15 years
ILC
CEPC / SppC

## Slide 23
ILC

## Slide 24: ILC basics
International Linear Collider: e+e- collider, aiming at 100-250 GeV beam energy (up to 500 GeV centre of mass)
  Extendable to 1 TeV (requires doubling the length)
Foreseen length at 500 GeV CMS energy of 31 km
Possibly to be built in Japan – waiting for political decisions and agreements on funding

## Slide 25: ILC layout and concept
Undulator
CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=537945
First, create e- (photocathode DC gun)
Accelerate, send to circulate in 3.2 km damping ring
  Shrinking emittance under radiation damping
e- sent to main linac, accelerate
To create e+: Electrons pass undulator – magnets with many periodic bends
  Radiated photons impact on Ti-alloy target, creating e+e- pairs.
  Capture e+, accelerate, send to damping ring
Send e+ to main linac, accelerate
Collide e+e- inside detector
From ILC design report

## Slide 26: ILC main parameters
From ILC design report

## Slide 27: Luminosity comparison
Comparing luminosity between different future lepton colliders
  Circular and linear
At high energies, linear lepton colliders can achieve higher luminosity than circular ones
  Intensity in circular colliders limited by synchrotron radiation

## Slide 28: ILC Cavities
Superconducting cavity (Ni at 2 K)
RF frequency is 1.3 GHz, 23 cm wavelength
Length is 9 cells = 4.5 wavelengths = 1 m
Standing wave structure, achieving gradients of 31.5 MV/m
Theoretical field limit around 50-60 MV/m
  In reality, reaching about 30-40 MV/m with imperfections
Need about 8000 cavities

## Slide 29: Further documentation
ILC technical design report

## Slide 30
CLIC

## Slide 31: CLIC basics
Linear e+e- collider, to be built in stages of increasing centre-of-mass energy:
  380 GeV – 3 TeV
  Length between ~11 km and ~50 km
Aiming at highest lepton energies
30 MW of beam power at 3TeV

## Slide 32: CLIC Staged Scenario
Central complex on Prevessin site
Luminosity evolution
3 stages foreseen:

## Slide 33: CLIC parameters
Parameter | Symbol [unit] | ILC 250 | CLIC | CLIC
Centre of mass energy | Ecm [GeV] | 250 | 380 | 3000
Luminosity | L [1034cm-2s-1] | 1.35 | 1.5 | 6
Luminosity in peak | L0.01 [1034cm-2s-1] | 1 | 0.9 | 2
Gradient | G [MV/m] | 31.5 | 72 | 100
Particles per bunch | N [109] | 20 | 5.2 | 3.72
Bunch length | σz [μm] | 300 | 70 | 44
Collision beam size | σx,y [nm/nm] | 516/7.7 | 149/2.9 | 40/1
Vertical emittance | εx,y [nm] | 35 | 30 | 20*
Bunches per pulse | nb | 1312 | 352 | 312
Bunch distance | Δz [mm] | 554 | 0.5 | 0.5
Repetition rate | fr [Hz] | 5 | 50 | 50
D. Schulte

## Slide 34: Flat beams in lepton colliders
Naturally smaller vertical beam size from radiation damping
  Often true also for linear colliders due to horizontal bending in damping rings, transfer lines etc.
Beam-beam effect
  Focusing of e+e- beams due to each others’ fields => higher luminosity
  Bending of particles => synchrotron radiation, “beamstrahlung” => unwanted energy spread in collisions
To avoid energy spread and keep luminosity high: collide “flat” beams, with much smaller beam size in one plane
M.A. Valdivia García et al.,
doi:10.18429/JACoW-IPAC2019-MOPMP035
M. Sands, SLAC-121 UC-28
average number of photons per collision depends on sum of beam sizes:
Luminosity depends on product of beam sizes:

## Slide 35: CLIC layout
Concept: beam generation  pre-acceleration  damping rings  booster linac  main linacs collisions
CLIC aims at gradients of 100 MV/m, 20 times higher than the LHC
  Compare 30 MV/m at ILC
Different acceleration concept in main LINAC from ILC :
  drive-beam acceleration, with RF power taken from another e- beam

## Slide 36: CLIC cavities
To reach 100 MV/m: different type of cavity from ILC
12 GHz, 23 cm long, normal conducting
  Much worse conductor than SC, but allows reaching higher fields
  Problem: power is very rapidly lost in the walls
  Need to put in very intense and short RF pulses timed to the passage of the beam
Power flow
1/3 lost in cavity walls
1/3 in filling the structure and into load
1/3 into the beam
Average RF power about 3 kW/m
About 1 kW/m into beam
D. Schulte

## Slide 37: Drive beam acceleration
To produce very rapid pulses: use two-beam acceleration scheme
A very long beam pulse at 4A, 140 us produced in LINAC
Use combiner rings to decrease bunch spacing of drive beam => produce very short and intense 100 A pulse
Send to decelerating structure
Drive Beam Accelerator
efficient acceleration in fully loaded linac
Power Extraction
Drive Beam Decelerator Sector
Combiner Ring x 3
Combiner Ring x 4
pulse compression &
frequency multiplication
pulse compression &
frequency multiplication
Delay Loop x 2
gap creation, pulse compression & frequency multiplication
RF Transverse
Deflectors
140 µs train length - 24 x 24 sub-pulses - 4.2 A
2.4 GeV - 60 cm between bunches
240 ns
24 pulses – 100 A – 2.5 cm between bunches
240 ns
5.8 µs
Drive beam time structure - initial
Drive beam time structure - final
R. Ruber

## Slide 38: Two-beam acceleration scheme
The high-current drive beam is decelerated in special power extraction structures (PETS)
Generated EM field can be transferred in RF waveguides to the other beam => power is used to accelerate the main beam

## Slide 39: CLIC Test Facility (CTF3)
Experimental tests carried out in test facility at CERN to demonstrate drive beam concept
Accelerating gradient of >100 MV/m achieved

## Slide 40: CLIC power consumption
Power and energy consumption at 380 GeV is well within the existing parameters and installations at CERN
At 1.5 TeV: power will surpass the current CERN usage (2017) by ~30%
At 3 TeV the energy consumption will be a factor two of the current CERN usage (2017)
Development work ongoing to further improve energy efficiency
Estimated power consumption of CLIC in MW at 380 GeV (total: 252 MW)
https://clic.cern

## Slide 41: CLIC reference documents
More information:
  Conceptual design report (2012)
  Updated CLIC baseline document (2016)

## Slide 42: Outline
Introduction
  Considerations for collider design: particle type, energy, circular/linear…
  Limitations for future colliders
  European strategy for particle physics
ILC (International Linear Collider)
CLIC (Compact Linear Collider)
HL-LHC (High-Luminosity Large Hadron Collider)
FCC-hh (Future Circular collider, hadrons)
FCC-ee (Future Circular collider, e+e-)
CEPC/SppC (Chinese Electron-Positron Collider / Super proton-proton Collider)
Muon collider
First lecture
Second lecture
Linear
Circular

## Slide 43: Coffee break – some fruit?
Source: https://xkcd.com/1949/